## Slide 1: Human Factors Applications of Biomechanical Modeling June 18, 2019 Beth Lewandowski Chris Gallo Aaron Godfrey Brad Humphreys William Thompson NASA Glenn Research Center

## Slide 2: Operational Volume Methodology Applications

## Slide 3: Operational Volume - Methodology
Z
Y
X
Infrared Illuminators
Laboratory motion capture system:
  BTS Bioengineering (Brooklyn, NY) Smart-DX 12 camera system
  Reflective markers placed on subjects
  BTS tracker software produces (x,y,z) vs. time for all markers
  Live video

## Slide 4: Operational Volume - Methodology
“Low Resolution,” small foot print, motion capture system for Zero-Gravity Flights, ISS and other operational settings
  Uses commercially available video cameras and software
  Custom software developed to perform calibration, tracking, identify kinematics and operational volume

## Slide 5: Operational Volume - Methodology
X
Y
Z
Plot of convex hull volume containing all markers
Plot of all markers at all time steps within a rectilinear volume

## Slide 6: Operational Volume - Methodology
Summary of maximum dimensions and maximum volume for various tasks for inclusion in volume data bases

## Slide 7: Operational Volume - Applications
How much space is required to perform a task?
  Exercise operational volume on HULK
  Exercise operational volume on ATLAS
  Medical station operational volume
Can a task be performed within a specified volume?
  Will the motion used to perform a task fit within an allocated volume?
  The space used may not be the minimum space needed
Example: Determine if the volume allocated for exercise within the MPCV adequately accommodates exercise performance

## Slide 8: Operational Volume - Applications
Data collection and processing

## Slide 9: Operational Volume - Applications
Findings:
  Orientation of the exerciser was a factor in how well the exercise was accommodated
  An adjustable footplate was recommended

## Slide 10: Operational Volume - Applications
Example: Provide procedure simulations, operational volume, video, event plots to aid the development of the medical station design and guidance
Findings:
  The operational volume decreased when volume restrictions were in place, but care was still successfully provided
  The caregiver primarily occupied volume at the patient’s side and at the patient’s head
  The ultrasound machine placement needs to factor in the dominant hand of the caregiver
  When giving care the feet stayed in general locations either by the patient’s side or at the patient’s head, the limiting factor becomes the extent to which the caregiver can reach for equipment and supplies.
Unrestricted Volume
Large Restricted
Small Restricted

## Slide 11: Estimates of Internal Loading Methodology Applications

## Slide 12: Estimates of Internal Loading - Methodology
Biomechanical data collection

## Slide 13: Estimates of Internal Loading - Methodology
Laboratory based biomechanical modeling process
  Kinematic data
  Ground reaction force data
  Other external forces
  Biomechanical modeling software to solve equations of motion and force
Biomechanical modeling outcome
  Joint torque estimates
  Muscle force estimates
Y
Z
X

## Slide 14: Estimates of Internal Loading - Methodology
If there is no availability to ground reaction forces and moments (GRF&M) in an operational setting, can internal forces be estimated with kinematics and exercise device loads alone?
Four key assumptions about GRF&M used to reduce the number of unknowns
  Ground reaction moments are negligible
  The lateral/medial location of the center of pressure (COP) is fixed
  The fore/aft location of the COP between the feet is equal
  The ground reaction force vector relative to the vertical in the frontal plane is constant

## Slide 15: Estimates of Internal Loading - Methodology
Comparison of joint torques resulting from squat and deadlift exercises estimated with traditional methods and this method resulted in
  Comparable flexion/extension joint moments
  Larger errors for abduction/adduction and rotational joint moments
Squat Knee Flexion
Deadlift Hip Flexion
Squat Hip Adduction
Deadlift Hip Adduction

## Slide 16: Estimates of Internal Loading - Methodology
Calculation of muscle dynamics without motion or force data through optimization routines
Instead formulate muscle dynamics in an implicit form and solve through optimization

## Slide 17: Estimates of Internal Loading - Methodology
Model the interaction of the human with an object
Example: a biomechanical model of an exerciser linked to a mechanical model of the advance resistive exercise device
What is the effect of the human-device interaction on posture, forces and torques at anatomical sites

## Slide 18: Estimates of Internal Loading - Applications
Questions that were answered using biomechanical modeling:
  Will the small exploration exercise devices provide comparable mechanical stimulus to Earth-based free weight exercise?
  What is the difference in mechanical stimulus between a harness interface and an exercise bar interface?
  How does differences in the load profile provided by an exercise device influence the resulting mechanical stimulus?

## Slide 19: Estimates of Internal Loading - Applications
How does the internal loading generated during performance of a task compare to injury thresholds?
How do the joint forces generated compare to ultimate bone strength?
How do the muscle forces generated compare to values associated with muscle strain injuries?

## Slide 20: This presentation provided methodologies and applications for: - operational volume estimation - internal loading estimation Thank you, Questions?