## Slide 1: CubeSat Proximity Operations Demonstration (CPOD) Overview
In-Space Inspection Workshop 2014
Houston, TX
07/16/2014
Austin Williams
CPOD Vehicle Bus Lead

## Slide 2: Operational View - CubeSat Proximity Operations Demonstration (CPOD)
S-Band Ground Network
Mission Operations Center (MOC)
UHF Ground Stations
RSO
Chaser
Notes: CubeSat Prox Ops Flight Experiment Study

## Slide 3: System View - CubeSat Proximity Operations Demonstration (CPOD)
S-Band Tracking Stations
S-Band
VPN
User /
Customer
GPS
GPS
Signal
Launch
Platform / Orbit Insertion
NASA-Tyvak 6U Dispenser
Mission Operations Center
SPACE SEGMENT
GROUND SEGMENT
LAUNCH / ORBIT INSERTION SEGMENT
USER SEGMENT
CubeSat Bus
CMD / TLM
CPOD Spacecraft A
Rendezvous, Proximity Operations (RPO) Payload
RPO Sensors and Image Software
RPO Sensors
CPOD Spacecraft B
Inter-Satellite Link w/ Ranging
UHF
Hosted UHF Remote Station

## Slide 4: CONOPS - Designed to Maximize Mission Success Probability
Ground Network
Mission Operations Center
1
2
Mission-Planning / Pre-Launch
Launch
3
Release together from 6U dispenser
Initial SOH Checkout
5
CubeSat A performs RPO relative to CubeSat B
Increased Range RPO Scenarios
Residual Ops
CMD /TLM
CMD /
TLM
CMD / TLM
CMD / TLM
CMD
TLM
CMD / TLM
4a
Disposal
Orbit Maneuvering to Initial Proximity Distance (Walking Safety Ellipse)
Main RPO Experiment Phases
A
B
Decreased Range RPO & Docking Scenarios
10
6
9
7
11
4b-c
Separate and Continue Checkout
A
B
Non-passively Safe Maneuvers
8

## Slide 5: Deployment Configurations and Vehicle Checkout
Connected “6U” Configuration
First Panel Deploy
Deploy UHF Antenna
Initial SOH Checkout
Vehicle Separation
Second Panel Deploy
Complete Checkout
4a
3
4b-c
Notes: CubeSat Prox Ops Flight Experiment Study

## Slide 6: CONOPS Overview
ISL Ranging
∆GPS via ISL
ISL Ranging
NFOV Bearings
100s m
Vbar
Rbar
NFOV Ranging
Drift km’s during checkout
Initiate Safety Ellipse
5.1
4
Inject into Walking Safety Ellipse
5.2
Stabilize into Safety Ellipse about CubeSatB
5.3
A
B
Reduce Size Safety Ellipses & NFOV checkout
6
Rendezvous
Docking
NFOV Bearings & Ranging
Vbar
Rbar
B
A
Docking Ranging
IR1 B & R
IR2 B & R
7.1
6.3
Reduced Size NMC
Transfer to V-bar
Approach to WP1
Reduce Size Safety Ellipse & Docking Sensor checkout
7.3
7.5
Docking Bearings
7.2
Approach & Dock
7.6
7.4
Approach to WP2
Transfer to InPlane NMC

## Slide 7: Space Vehicle Architecture
EPS
SYSTEM PROCESSOR
ADCS
State Estimation & Control Processor
3-axis IMU
Star Trackers w/ dedicated processing
3-axis Magnetometer Set
3-axis Sun Sensor Set
3-axis Reaction Wheel Set
3-axis
Mag. Torquer Set
COMM
S-BAND (downlink)
UHF
GPS
Inter-Satellite link (Comm / Ranging)
Power Sequencing
Heater
Health & State Sensors
RPO
Maneuver Planning Processor (GN&C)
Wide Field
Visible Imager
Infrared Imager
Docking
Sensor
Infrared Imager
Relative Position Estimation Processor (Imaging Processor)
Docking Mechanism
Optical Target Aid
8-thruster Cold Gas
CONTRIBUTIONS
Tyvak Nano-Satellite Systems
Applied Defense Solutions
406 Aerospace
VACCO

## Slide 8: Vehicle Configuration - External Arrangement, Isometric Views
Docking Mechanism
UHF Antennas
Separation Devices
S-Band
Patch
GPS
Patch
Thermal
Radiators
Solar Panel Arrays
with MPPTs
Thermal
Radiator
Star Trackers
Notes: CubeSat Prox Ops Flight Experiment Study

## Slide 9: Remote Proximity Operations and Docking Module (RPOD)
RPOD
Module
50mm IR Camera
70mm Visible Camera
35mm IR Camera
ISL Patch Antenna
LED
LED
LED
Notes: CubeSat Prox Ops Flight Experiment Study

## Slide 10: Vehicle Configuration - Internal Arrangement and Packaging
S-Band Transmitter
Battery Module
Cold Gas
Thrusters (8)
GPS Receiver
RPOD Module
Inertial Reference Module (IRM)
UHF Radio
Propulsion
Module
Endeavour Bus
Battery Module
Notes: CubeSat Prox Ops Flight Experiment Study

## Slide 11: 1U Endeavr Avionics
Star Trackers (2x)
Torque Coils (3x)
Endeavour C&DH
UHF Radio and Antenna
S-Band Radio
Battery Module
C&DH and ADCS
Reaction Wheels (3x)
IMU
Control Processor

## Slide 12: Algorithm Simulations
Actual Range
20.53 m
Calculated Range1
20.52 m
Calculated Range 2
19.38 m
Range 1 Error
0.05%
Range 2 Error
5.93%
Two Solutions

## Slide 13: CPOD Performance Summary
Capability | Specification | Comments
Average Power Generated | ~17W to 30W OAP | Polar Sun-Sync
Average Load | ~15W | Fully Active
Pointing Accuracy | <0.15 degrees | Star Trackers available under all mission scenarios
Mission Data Downlink | ~60MB / day | UHF and S-Band
Delta-V | ~20 m/s | Cold Gas
Total Mass | 5.990kg | Wet Mass (13% Margin)

## Slide 14: CPOD Integrated Flat-Satellite
Accomplishments to date
  EDU avionics bring-up complete with 100% of subsystems functionally verified using software driver implementations
  Complex low-level bus protocols functionally verified with flight data rates and electrical connectivity
  Initial EMI compatibility testing complete
  Vibration and Thermal Vacuum survivability tests
  Reaction Wheel life testing complete
  Star Tracker outdoor testing complete

## Slide 15: Summary and Status
State of the art Proximity, Rendezvous and Docking system
  Scalable architecture
Leverage on Tyvak’s Endeavour bus architecture
Sensor suite and algorithms created to interact with Tyvak’s vehicle
Great flexibility of operations
Design phase complete
  Leveraging on multiple quick iterations with hardware evaluation
Main interface risks retired through early adoption of FlatSat and dedicated risk reduction environmental tests
Final iteration of Engineering Development hardware is on order
  Qualification unit completed by November
Extensive mission assurance campaign through testing and ground demonstration

## Slide 16
Questions?
For additional inquiries, please contact:
Dr. Marco Villa
CPOD Program Manager
Marco.Villa@tyvak.com
310-956-5973