## Slide 1: Gas Bottle Blow-Down Analysis

## Slide 2: Introduction
This lesson provides the means to estimate the gas state in a pressure vessel during or after depressurization (blow-down) from a known state, a uniform-flow thermodynamic process.

## Slide 3: Overview
For the given thermodynamic problem of depressurization of a pressure vessel, the governing thermodynamic equations are derived.
Solutions are described for 3 methods: two using the simplifying process assumptions, isentropic and isothermal, and a third using more a generalized approach.

## Slide 4: Scope
In a propulsion testing system, pressure vessels (or bottles) supply propellants or pressurize liquid propellant tanks for a rocket engine test.
During the preliminary design, it may be important to estimate the capability of the bottles.
Gas Bottles
Control Valve
To Test Article
Run Tank
Gas Bottle
Control Valve
To Test Article

## Slide 5: Lesson Breakdown
Bottle Blow Down Problem Description
Governing Thermodynamic Equations
Example Problems
Concluding Remarks
Acknowledgements
References/Credits

## Slide 6: Lesson Roadmap
Problem Description
Conservation of Mass
1st Law of Thermodynamics
2nd Law of Thermodynamics
Example Problems
Isothermal Assumption
Isothermal Example
Generalized 1st Law Algorithm Example
Isentropic Assumption
Isentropic Example
Concluding Remarks
References/ Credits
Spreadsheet Excerpt
Acknowledgements

## Slide 7: Bottle Blow-Down Problem Description
Problem: Find the final state of a real gas in a control volume (CV) following a Uniform-Flow process.
Solution: Use the 1st and 2nd Laws of Thermodynamics for a control volume.

## Slide 8: Fundamentals

## Slide 9: Nomenclature
E = energy
Q = heat transfer
W = work
ke = specific kinetic energy
pe = specific potential energy
h = specific enthalpy
u = specific internal energy
m = mass
S = entropy
Sgen = entropy generation
T = boundary temperature
s = specific entropy

## Slide 10: Conservation of Mass
The Conservation of Mass Principle is needed in the derivation of the 1st and 2nd Law equations and is defined by the statement below:
The net mass transfer to or from a system during a process is equal to the net change in the total mass of the system during that process (Ref. 1).
Also known as the Continuity Equation.

## Slide 11: Conservation of Mass (Cont.)
Rate form of the Continuity Equation:
(Adapted from Ref. 1)
Or for a single inlet and a single outlet:

## Slide 12: 1st Law of Thermodynamics
The 1st Law of Thermodynamics is defined by the following statements:
Energy cannot be created or destroyed; it can only change forms. Energy is defined as the ability to cause change. The total energy is a property of a system (Ref. 1).
The Conservation of Energy Principle is the result.

## Slide 13: 1st Law Energy Balance
The Conservation of Energy Principle:
  The change in energy content of a body or any other system is equal to the difference between the energy input and the energy output, and the energy balance (Ref. 1).
Rate Form of the Energy Balance Equation:
(Adapted from Ref. 1)

## Slide 14: 1st Law Energy Balance (Cont.)
Rate Form of the Energy Balance for a Control Volume:
(Adapted from Ref. 1)
where
and

## Slide 15: 1st Law Energy Balance for Bottle Blow-Down
No Work
0
No Mass In
0
No
Work
0
No
Heat
0
mass flow out
T1 = Known
P1 = Known
heat in

## Slide 16: 1st Law Energy Balance for Bottle Blow-Down (Cont.)
No ke
0
No pe
0
No ke
0
No pe
0
No ke
0
No pe
0

## Slide 17: 1st Law Energy Balance for Bottle Blow-Down (Cont.)
Often, heat transfer can be neglected for short duration processes or well-insulated vessels.
When the process duration and heat transfer are sufficiently large, the process can be isothermal.

## Slide 18: Isothermal Blow-Down
The isothermal assumption is valid when process duration is such that gas temperatures remain approximately constant or return to the initial temperature (recovery state).
Final state fixed by density and temperature.
  Use thermodynamic tables or software such as Refprop (Ref. 2) to find final state properties.

## Slide 19: 2nd Law of Thermodynamics
The 2nd Law of Thermodynamics is defined by the following statements:
Energy has a quality as well as a quantity. Processes have a direction and occur in the direction of decreasing quality of energy or increasing entropy (adapted from Ref. 1).

## Slide 20: 2nd Law of Thermodynamics (Cont.)
Entropy is a property of a system and is defined as the quantitative measure of microscopic disorder for a system generated by heat transfer, mass flow, and irreversibilities (Ref. 1).
The Entropy Balance Equation can be derived from the Clausius Inequality and the Definition of Entropy.

## Slide 21: 2nd Law Entropy Balance
Rate form of the Entropy Balance:
(Adapted from Ref. 1)
Rate form of the Entropy Balance for a control volume:
(Adapted from Ref. 1)
where

## Slide 22: 2nd Law Entropy Balance for Adiabatic Bottle Blow-Down
Adiabatic means no heat transfer
No Mass In
0
No Entropy Generated Due to Frictional Losses
0
mass flow out
T1 = Known
P1 = Known
No Heat
0
Adiabatic

## Slide 23: 2nd Law Entropy Balance for Adiabatic Bottle Blow-Down (Cont.)
Often, heat transfer can be neglected for short duration processes or well-insulated vessels
When the process heat transfer and entropy generation can be neglected, the process is isentropic.
where
therefore

## Slide 24: Isentropic Blow-Down
The isentropic assumption is valid when the process duration is short or the bottle is well-insulated.
Final state fixed by density and entropy
  Use thermodynamic tables or software such as Refprop (Ref. 2) to find final state properties.

## Slide 25: Examples

## Slide 26: Example Problems
Problem Statement:
  A 28 m3 nitrogen bottle at 20 MPa and 300 K undergoes a process where mass exits at 15 kg/sec for 150 sec.
  Find final temperature and pressure, assuming the process is:
  Isothermal
  Isentropic
  Heat transfer rate = 1800 kW

## Slide 27: Isothermal Example (A)
State 1 is defined by temperature and pressure:
  r1 = 212.5 kg/m3  m1 = 5951 kg
  2250 kg is removed from the bottle, leaving 3701 kg. Final density is calculated from final mass and volume. Temperature of the nitrogen in the vessel is constant due to the isothermal assumption.
  State 2A defined by temperature and density:
      r2A = 132.2 kg/m3
      T2A = T1 = 300 K

## Slide 28: Isothermal Example (A) (Cont.)
    Final pressure can be found by using the thermodynamic tables in Reference 3 or software such as Refprop (Ref. 2):
      P2A = 11.9 MPa
      This is also the recovery pressure of the vessel if the vessel is depressurized and then allowed to heat back up to the initial temperature.

## Slide 29: Isentropic Example (B)
State 1 is defined by temperature and pressure:
  r1 = 212.5 kg/m3  m1 = 5951 kg
  s1 = 5.163 kJ/kg*K
  2250 kg is removed from the bottle, leaving 3701 kg. Final density is calculated from final mass and volume. Entropy of the nitrogen in the vessel is constant due to the isentropic assumption.
      State 2B defined by density and entropy:
      r2B = 132.2 kg/m3
      s2B = s1 = 5.163 kJ/kg*K

## Slide 30: Isentropic Example (B) (Cont.)
    Final temperature and pressure can be found by using the thermodynamic tables in Reference 3 or software such as Refprop (Ref. 2):
      T2B = 234.2 K
      P2B = 8.6 MPa

## Slide 31: Generalized Problem (C)
This problem must be solved numerically using the above equation derived from the Energy Balance Equation for a control volume.
mass flow out
T1 = Known
P1 = Known
heat in

## Slide 32: Generalized Problem (C) (Cont.)
State 1 is defined by temperature and pressure:
  r1 = 212.5 kg/m3  m1 = 5951 kg
The final temperature and pressure of the nitrogen were found to be:
T2C = 300 K
  P2C = 11.9 MPa

## Slide 33: Generalized Problem (C) (Cont.)
The heat rate into the vessel, 1800 kW, was chosen to produce the isothermal result, giving us the average heating rate needed to keep the nitrogen at a constant temperature.
This solution was obtained using a spreadsheet with a thermodynamic properties subroutine (Refprop.xls) and a time step of 0.1 sec.
Refprop.xls is included with the installation of Refprop (Ref. 2).

## Slide 34: Energy Balance Algorithm
With initial temperature (T1) and initial pressure (P1), find initial mass (m1), initial internal energy (u1), and initial enthalpy (h1 = hout).
With chosen time step, mass flow rate, and heat rate in (Qdotin), solve for the resulting total internal energy (U2) and mass (m2), using the 1st Law energy balance and the continuity equation, respectively.
With U2, m2, and volume calculate resulting internal energy (u2) and density (d2).

## Slide 35: Energy Balance Algorithm
With u2 and d2, find resulting temperature (T2) and pressure (P2) and other thermodynamic properties if required.
Update T1 and P1 with T2 and P2, then find next u1 and h1 = hout for the next time step.
Repeat for next time step.

## Slide 36: Energy Balance Algorithm (Cont.)
1
2
3
4
5
6

## Slide 37: Energy Balance Algorithm (Cont.)
1

## Slide 38: Energy Balance Algorithm (Cont.)
2

## Slide 39: Energy Balance Algorithm (Cont.)
3

## Slide 40: Energy Balance Algorithm (Cont.)
4

## Slide 41: Energy Balance Algorithm (Cont.)
5
6

## Slide 42: Energy Balance Algorithm (Cont.)
Notes:
Algorithm assumes user has numerical means of solving for thermodynamic properties
Can be programmed in an Excel spreadsheet using the Refprop.xls worksheet (Ref. 2)
Recommend an initial run without heat transfer and check against isentropic process

## Slide 43: Concluding Remarks
When the Blow-Down process can be approximated as isothermal or isentropic, final state properties can be found using thermodynamic tables (or thermodynamic software).
When heat transfer is a significant factor, the energy balance equation must be solved numerically, but a simple algorithm can be used to solve for the final state.

## Slide 44: Acknowledgements
Special acknowledgement is given to Steven Rickman, Ruth Amundsen, and David Gilmore for their assistance and review of this lesson.
This author is grateful to the NESC Passive Thermal Technical Discipline Team (TDT) for their contributions and technical review of this lesson.

## Slide 45: References/Credits
  “Thermodynamics: An Engineering Approach”, 4th ed., Cengel and Boles, McGraw-Hill, 2002.
  Lemmon, E.W., Huber, M.L., McLinden, M.O. NIST Standard Reference Database 23: Reference Fluid Thermodynamic and Transport Properties-REFPROP, Version 9.0, National Institute of Standards and Technology, Standard Reference Data Program, Gaithersburg, 2010.
  “Fundamentals of Thermodynamics”, 5th ed., Sonntag, Borgnakke and van Wylen, Wiley, 1998.
  Microsoft® Clip Art was used in the presentation.