## Slide 1
Generalized Fluid System Simulation Program (Version 701)
Alok Majumdar & Andre LeClair
NASA/Marshall Space Flight Center
GFSSP Training Class for SATERN
April 12 – 14, 2016

## Slide 2
Course Abstract
This three-day hands-on course provides basic introduction as well as advanced capabilities of GFSSP. GFSSP is a general-purpose computer program developed at Marshall Space Flight Center for analyzing steady state and time-dependent flow rates, pressures, temperatures, and concentrations in a complex flow network. For more information about GFSSP, please visit http://gfssp.msfc.nasa.gov/. The version 701 (Beta) of the code will be taught in this course. The course quickly teaches new users to use GFSSP to solve engineering flow network problems through lectures and tutorial problems. There are eight core lectures (CL), nine lectures on application (LA) and six step-by-step tutorials (TP) and several challenge tutorials.
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 3: BACKGROUND
GFSSP stands for Generalized Fluid System Simulation Program
It is a general-purpose computer program to compute pressure, temperature and flow distribution in flow network with solid to fluid (conjugate) heat transfer
It was primarily developed to analyze
  Internal Flow Analysis of Turbopump
  Transient Flow Analysis of Propulsion System
GFSSP development started in 1994 with an objective to provide a generalized and easy to use flow analysis tool
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 4
BACKGROUND
DEVELOPMENT HISTORY & ONGOING DEVELOPMENTS
Version 1.4 (Steady State) was released in 1996
Version 2.01 (Thermodynamic Transient) was released in 1998
Version 3.0 (User Subroutine) was released in 1999
Graphical User Interface, VTASC was developed in 2000
Selected for NASA Software of the Year Award in 2001
Version 4.0 (Fluid Transient and post-processing capability) is released in 2003
Version 5.0 (Conjugate Heat Transfer capability) is released in 2006.
Educational Version was released in 2011
Version 6.0 (Multi-Dimensional Capability) has been released in 2014
Version 701 (Beta) ( Psychrometric Property, Integrated Property Package, MLI Heat Transfer, Animation Capability) has been released in December, 2015
Uncertainty Analysis & Separated Flow for Multiple Species are under development
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 5
COURSE OUTLINE
Day 1 Morning
1. Introduction & Overview (CL-1)
Pre & Post Processor – Part I (CL-2)
Compressible Flow (LA-1)
Tutorial on Converging-Diverging Nozzle (TP-1)
Day 1 Afternoon
Resistance & Fluid Options (CL-4)
Pre & Post Processor – Part 2 (CL-3)
Fluid Transient (LA-2)
Tutorial on Water hammer (TP-2)
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 6
COURSE OUTLINE
Day 2 Morning
Mathematical Formulation (CL-5)
Tank Pressurization,Control & Relief Valve (LA-3)
3. Tutorial on Tank Pressurization & Control Valve (TP-3)
Day 2 Afternoon
Pressure & Flow Regulator (LA-4)
Tutorial on Pressure Regulator (TP-4)
6. Cryogenic Propellant Loading (LA-5)
7. Tutorial on Transfer Line Chilldown (TP-5)
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 7
COURSE OUTLINE
Day 3 Morning
Data Structure (CL-6)
User Subroutine (CL-7)
Fluid Mixture & Two-phase Flow (LA-6)
Tutorial on Propellant Recirculation (TP-6)
Day 3 Afternoon
Rotating Flow ,Turbopump & Heat Exchanger (LA-7)
Multi-Dimensional Flow Modeling (LA-8)
7. Psychrometric Properties and Multi-Layer Insulation (LA-9)
8. Model Integration & Future Developments (CL-8)
9. Open Session
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 8
NETWORK FLOW OR NAVIER STOKES ANALYSIS
Computational Fluid Dynamics (CFD)
Navier Stokes Analysis (NSA)
Network Flow Analysis (NFA)
Finite Difference
Finite Element
Finite Volume
Finite Volume
Finite Difference
GFSSP
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 9: NETWORK FLOW OR NAVIER STOKES ANALYSIS
Navier Stokes Analysis
Suitable for detailed flow analysis within a component
Requires fine grid resolution to accurately model transport processes
Used after preliminary design
Network Flow Analysis
Suitable for flow analysis of a system consisting of several components
Uses empirical laws of transport process
Used during preliminary design
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 10
Nitrogen
250 º F
Nitrogen
70 º F
Dinner= 2 inches
Douter= 4 inches
L= 2 ft
Internal Node
Boundary Node
Solid Node
Solid-Fluid Conductor
Solid-Solid Conductor
NETWORK DEFINITION
Branch
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 11
Network:
  Boundary node
  Internal node
  Branch
At boundary nodes, all dependent
variables must be specified
At internal nodes, all dependent variables
must be guessed for steady flow and specified for transient flow.
NETWORK DEFINITIONS
Series
Parallel
Combination
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 12
Units External (input/output) Internal (inside GFSSP)
  Length - inches - feet
  Area - inches2 - feet2
  Pressure - psia - psf
  Temperature - °F - °R
  Mass injection - lbm/sec - lbm/sec
  Heat Source - Btu/s OR Btu/lbm - Btu/s OR Btu/lbm
Sign Convention
  Mass input to node = positive
  Mass output from node = negative
  Heat input to node = positive
  Heat output from node = negative
UNITS AND SIGN CONVENTIONS
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 13
Network
Internal Node
Solid Node
Branch
Ambient Node
Boundary Node
Conductor
Fluid
Solid
Solid to Solid Conduction
Solid to Solid Radiation
Solid to Fluid
Solid to Ambient
DATA STRUCTURE
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 14: MATHEMATICAL FORMULATION
Principal Variables:
Unknown Variables Available Equations to Solve
1. Pressure 1. Mass Conservation Equation
2. Flowrate 2. Momentum Conservation Equation
3. Fluid Temperature 3. Energy Conservation Equation of Fluid
4. Solid Temperature 4. Energy Conservation Equation of Solid
5. Specie Concentrations 5. Conservation Equations for Mass Fraction of Species
6. Mass 6. Thermodynamic Equation of State
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 15: MATHEMATICAL FORMULATION
Auxiliary Variables:
Thermodynamic Properties, Flow Resistance Factor & Heat Transfer Coefficient
Unknown Variables Available Equations to Solve
Density
Specific Heats Equilibrium Thermodynamic Relations
Viscosity [GASP, WASP & GASPAK Property Programs]
Thermal Conductivity
Flow Resistance Factor Empirical Relations
Heat Transfer Coefficient
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 16: MATHEMATICAL FORMULATION
BOUNDARY CONDITIONS
Governing equations can generate an infinite number of solutions
A unique solution is obtained with a given set of boundary conditions
User provides the boundary conditions
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 17
PROGRAM STRUCTURE
Graphical User Interface (VTASC)
Solver & Property Module
User Subroutines
Input Data
File
New Physics
Time dependent
process
non-linear boundary
conditions
External source term
Customized output
New resistance / fluid
option
Output Data File
Equation Generator
Equation Solver
Fluid Property Program
Creates Flow Circuit
Runs GFSSP
Displays results graphically
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 18
GRAPHICAL USER INTERFACE - 1
MODEL BUILDING
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 19
GRAPHICAL USER INTERFACE
MODEL RUNNING
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 20
GRAPHICAL USER INTERFACE
MODEL RESULTS
GFSSP Version 6.05 Training Course Introduction & Overview
20

## Slide 21
1. Pipe Flow
2. Flow Through a Restriction
3. Non-Circular Duct
4. Pipe Flow with Entrance
& Exit Losses
5. Thin, Sharp Orifice
6. Thick Orifice
7. Square Reduction
8. Square Expansion
9. Rotating Annular
Duct
RESISTANCE OPTIONS
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 22
RESISTANCE OPTIONS
10. Rotating Radial Duct
11. Labyrinth Seal
12. Face Seal
13. Common Fittings
& Valves
14. Pump Characteristics
15. Pump Power
16. Valve with Given Cv
17. Viscojet
P
18. Control Valve
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 23
RESISTANCE OPTIONS
U
19. User Defined
20. Heat Exchanger Core
21. Parallel Tube
22. Compressible Orifice
23. Labyrinth Seal (Egli Correlation
24. Fixed Flowrate
25. Cartesian Grid
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 24
FLUID OPTIONS
GFSSP Version 7.01 Training Course Introduction & Overview
ID Number | Gas | ID Number | Gas | ID Number | Gas
1 | GASP He | 51 | GASPAK He | 71 | GASPAK Xe
2 | GASP CH4 | 52 | GASPAK CH4 | 72 | GASPAK R-11
3 | GASP Ne | 53 | GASPAK Ne | 73 | GASPAK R-12
4 | GASP N2 | 54 | GASPAK N2 | 74 | GASPAK R-22
5 | GASP CO | 55 | GASPAK CO | 75 | GASPAK R-32
6 | GASP O2 | 56 | GASPAK O2 | 76 | GASPAK R-123
7 | GASP Ar | 57 | GASPAK Ar | 77 | GASPAK R-124
8 | GASP CO2 | 58 | GASPAK CO2 | 78 | GASPAK R-125
9 | GASP F2 | 59 | GASPAK H2 (para) | 79 | GASPAK R-134A
10 | GASP H2 (para) | 60 | GASPAK H2 (normal) | 80 | GASPAK R-152A
11 | WASP H2O | 61 | GASPAK H2O | 81 | GASPAK N2F3
12 | RP-1 Tables | 62 | GASPAK RP-1 (liq) | 82 | GASPAK NH3
 |  | 63 | GASPAK Isobutane | 84 | GASPAK H2O2
33 | Ideal Gas | 64 | GASPAK Butane | 86 | GASPAK Air
 |  | 65 | GASPAK Deuterium |  | 
37 | User Fluid 1 | 66 | GASPAK Ethane |  | 
38 | User Fluid 2 | 67 | GASPAK Ethylene |  | 
39 | User Fluid 3 | 68 | GASPAK H2S |  | 
 |  | 69 | GASPAK Kr |  | 
 |  | 70 | GASPAK Propane |  | 

## Slide 25
FLUID OPTIONS
Fluids not available in GASP/WASP or in GASPAK can be modeled by providing property tables
GFSSP needs Molecular Weight and tables for following thermodynamic and transport properties:
  Enthalpy
  Entropy
  Density
  Viscosity
  Thermal Conductivity
  Specific Heat
  Specific Heat Ratio
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 26: ADDITIONAL OPTIONS
Variable Geometry
Variable Rotation
Variable Heat Addition
Turbopump
Heat Exchanger
Tank Pressurization
Control Valve
Valve Open/Close
Conjugate Heat Transfer
Pressure Regulator
Flow Regulator
Relief Valve
Multi-dimensional flow
GFSSP Version 7.01 Training Course Introduction & Overview
Fluid Mixture
Psychrometric Calculation
Multi-Layer Insulation
Sub-modeling Features
  Model Import
  Model Integration

## Slide 27
Example Problems
GFSSP User’s Manual includes thirty two example problems
The Purpose is to:
Demonstrate the major features of the code
Validate the solution by comparing with Textbook solution, Experimental data, if available
GFSSP Version 7.01 Training Course Introduction & Overview
27
 |  |  |  |  |  |  |  |  | EXAMPLE |  |  |  |  |  |  |  |  | 
FEATURE |  | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | FEATURE
Conjugate Heat Transfer |  |  |  |  |  |  |  |  |  |  |  |  |  | 13 | 14 |  |  | Conjugate Heat Transfer
Constant Property |  |  | 2 |  |  |  |  | 7 |  |  |  |  |  |  |  |  |  | Constant Property
Cyclic Boundary |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Cyclic Boundary
Fixed Mass Flow |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Fixed Mass Flow
Flow Regulator |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Flow Regulator
Gravity |  | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Gravity
Heat Exchanger |  |  |  |  |  | 5 |  |  |  |  |  | 11 |  |  |  |  |  | Heat Exchanger
Ideal Gas |  |  |  |  |  |  |  |  | 8 |  |  |  |  |  |  |  | 16 | Ideal Gas
Long Inertia |  |  |  | 3 |  |  | 6 |  |  |  |  |  | 12 |  |  |  |  | Long Inertia
Fluid Mixture |  |  |  |  | 4 |  |  |  |  |  | 10 |  | 12 |  |  |  |  | Fluid Mixture
Model Import |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Model Integration
Moving Boundary |  |  |  |  |  |  |  | 7 |  | 9 |  |  |  |  |  |  |  | Moving Boundary
Multi-Layer Insulation |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Multi-Layer Insulation
Multi-dimensional Flow |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Multi-dimensional Flow
Non-Circular Duct |  |  |  |  |  |  |  | 7 |  |  |  |  |  |  |  |  |  | Non-Circular Duct
Phase Change |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 14 |  |  | Phase Change
Pressurization (Tank) |  |  |  |  |  |  |  |  |  |  | 10 |  | 12 |  |  |  |  | Pressurization (Tank)
Pressure Regulator |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 16 | Pressure Regulator
Pressure Relief Valve |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Pressure Relief Valve
Pump |  | 1 |  |  |  |  |  |  |  |  |  |  | 12 |  |  |  |  | Pump
Solid Rocket Motor |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Solid Rocket Motor
Turbo Pump |  |  |  |  |  |  |  |  |  |  |  | 11 |  |  |  |  |  | Turbo Pump
Turbo Pump-Internal Flow |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | Turbo Pump-Internal Flow
Unsteady |  |  |  |  |  |  |  |  | 8 | 9 | 10 |  | 12 |  | 14 | 15 | 16 | Unsteady
User Fluid |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | User Fluid
User Subroutine |  |  |  |  |  |  |  |  |  |  | 10 |  | 12 |  |  |  |  | User Subroutine
Valve O/C |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 15 |  | Valve O/C
Variable Geometry |  |  |  |  |  |  |  |  |  | 9 |  |  |  |  |  |  |  | Variable Geometry
Fluid Transient (Water Hammer) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 15 |  | Fluid Transient (Water Hammer)

## Slide 28
Example Problems (Continued)

## Slide 29: Example Problems
In this class we will study the following example models in closer detail:
Simple Flow Systems
  Ex1: Steady-state Water Pumping System
  Ex2: Water Distribution Network
  Ex4: Mixing of Hot Combustion Gases with a Cold Gas Stream
  Ex8: Blow Down of a Pressurized Tank
  Ex16: Pressure Regulator Downstream of a Pressurized Tank
  Ex17: Flow Regulator Downstream of a Pressurized Tank
  Ex18: Fluid Network with the Fixed Flow Rate Option
  Ex24: Relief Valve in a Pressurized Tank
Compressible Flow
  Ex3: Converging-Diverging Nozzle
  Ex18: Subsonic Fanno Flow
  Ex19: Rayleigh Flow
Fluid Transient
  Ex15: Waterhammer after Sudden Valve Closure
  Ex26: Fluid Transient after Sudden Valve Opening
Tank Pressurization
  Ex10: Simple Tank Pressurization
  Ex12: Multiple Tank Pressurization with Control Valves
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 30: Example Problems (cont.)
Conjugate Heat Transfer
  Ex13: Steady-state Conduction through a Rod with Convection
  Ex14: Chilldown of Cryogenic Pipeline
  Ex29: Self-Pressurization of a Cryogenic Propellant Tank Due to Boil-Off
Turbomachinery Applications
  Ex6: Radial Flow on a Rotating Disk
  Ex11: Power Balancing of a Turbopump Assembly
  Ex21: Axial Thrust Calculation in the Simplex Turbopump
Miscellaneous
  Ex5: Simple Heat Exchanger
  Ex20: Lithium Loop Model
  Ex23: Helium-Assisted, Buoyancy-Driven Flow in a LOx Recirculation Line
  Ex25: Two-Dimensional Recirculating Flow in a Driven Cavity
  Ex27: Boiling Water Reactor
  Ex31: Psychrometrics of Air-Water Vapor Mixture
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 31
Feature: Moving Boundary, Comparison with Test Data
Example 7 - Flow in a Long Bearing Squeeze Film Damper
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 32
Feature: Variable Geometry, Moving Boundary, and Comparison with Analytical Solution
Example 9 - A Reciprocating Piston-Cylinder
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 33
Feature: Conjugate heat transfer with phase change, Fixed Flowrate option and Loading of Tank
Example 28 – No-Vent Tank Chill & Fill Model
GFSSP Version 7.01 Training Course Introduction & Overview

## Slide 34
GFSSP Version 7.01 Training Course Introduction & Overview
Feature: Modeling propellant burning as mass & energy source, flow in rocket nozzle and thrust calculation
Example 30 – Modeling Solid Propellant Rocket Motor Ballistic

## Slide 35
GFSSP Version 7.01 Training Course Introduction & Overview
Feature: Modeling of Longitudinal Inertia in Momentum Equation to calculate flow distribution in a dividing flow manifold
Example 32 – Flow Distribution in Manifold

## Slide 36: SUMMARY
GFSSP is a finite volume based Network Flow Analyzer
Flow circuit is resolved into a network consisting of nodes and branches
Mass, energy, and species conservation are solved at internal nodes. Momentum conservation is solved at branch
Generalized data structure allows generation of all types of flow network
Modular code structure allows user to add new capabilities with ease

## Slide 37: SUMMARY
Unique mathematical formulation allows effective coupling of thermodynamics and fluid mechanics
Numerical scheme is robust; adjustment of numerical control parameters is seldom necessary
Intuitive Graphical User Interface makes it easy to build, run, and evaluate numerical models
GFSSP has been successfully applied in various applications that included
  Incompressible & Compressible flows
  Phase change (Boiling & Condensation)
  Fluid Mixture
  Thermodynamic transient (Pressurization & Blowdown)
  Pressure and Flow Regulator
  Fluid Transient (Waterhammer)
  Conjugate Heat Transfer
  Model Integration
Thirty-two example problems illustrate use of various code options