## Slide 1: Conjugate Heat Transfer- Modeling Heat Transfer Between Solid and Fluid

## Slide 2
Contents
Why we need to analyze Conjugate Heat Transfer
Typical Example
Mathematical Formulation
Solution Algorithm
Input/Output
Examples

## Slide 3
Conjugate Heat Transfer
Why do we need it?
    In many applications fluid flow and heat transfer are strongly coupled
    Typical examples in Propulsion Systems are:
      Pressurization of cryogenic propellant tank
      Chilldown of cryogenic transfer line
      Regenerative cooling of engine nozzle
    Integration of separate models of fluid flow and heat transfer is difficult to construct and converge to a correct solution
    A better approach is to build a conjugate model using one solver module to solve for fluid and solid properties

## Slide 4
Heat Conduction Equation
Conservation Equation
Successive Substitution Form
Solid Node
Ambient Node
Fluid Node

## Slide 5
Mass conservation
Momentum Conservation
Equation of State
Flow chart of Solution Algorithm
Start
READIN - Reads input data from data file generated by VTASC
INIT – Generate Trial Solution
GASP & Wasp or GASPAK – A routine for thermodynamic properties
Obtain a trial solution
Simultaneous (S) solution of pressure, flowrate, and resident maas
NEWTON – Controls the iteration loop of Newton-Raphson scheme
COEF – Constructs the coefficient matrix of the correction equation
SOLVE – Solve correction equation by Gaussian elimination method
UPDATE – After applying corrections update each variable (11)
Successive Substitution (SS) solution of enthalpy & concentration
ENTHALPY – Solves enthalpy by SS method
MASSC – Solves concentration by SS method
Calculate flow resistances
RESIST – Calculates resistances for all branches
DENSITY – Calculates density and other properties
GASP & Wasp or GASPAK – A routine for thermodynamic properties
KFACT1 – KFACT21 Calculates branch resistances
Convergence check
Iteration loop
EQNS – Calculates residuals of three governing equations
Energy Conservation
Specie Conservation
BOUND – Supply Time-dependant boundary conditions
Solution of Temperature of Solid
TSOLID or TSOLIDNR – Solves temperature by SS or S method
Solid Temperature
repeated for each time step

## Slide 6
Solid Node Input

## Slide 7
Material Properties
The GFSSP installation directory contains temperature-dependent properties (k and Cp) for 40 common materials.
CAUTION: Not all library materials contain properties at cryogenic temperatures.
Up to 5 user-defined material properties may be defined in short text files:
  User1k.prp and user1cp.prp
  User2k.prp and user2cp.prp
  Etc.
Units are:
  T: R
  K: BTU/s-ft-R
  Cp: BTU/lbm-R

## Slide 8
Ambient Node Input

## Slide 9
Ambient to Solid Conductor
Input
Output

## Slide 10
Solid to Solid Conduction Conductor
Input
Output

## Slide 11
Mixing Materials
When a solid-to-solid conductor connects two different materials, the effective conductivity is the harmonic mean of the two conductivities.
This relationship holds true only if the length of the solid-to-solid conductor is ½ material A and ½ material B.
Example: A tank wall is 0.25 inches thick and covered with 1.0 inch of insulating foam.
Wall (0.2”)
Foam (0.95”)
Interface (0.1”)
(0.05” + 0.05”)

## Slide 12
Solid to Solid Radiation Conductor
Assumes two diffuse, gray surfaces that form an enclosure.
Example: a pipe surrounded by a vacuum jacket (Fij = 1.0)

## Slide 13
Solid to Fluid Conductor
Input
Output

## Slide 14
Heat Transfer Coefficient
May be user-specified to a constant value set in VTASC
May be calculated by a correlation defined in a user subroutine
May be calculated by the built-in Dittus-Boelter correlation:

## Slide 15
Heat Transfer Coefficient
May be calculated by the built-in Modified Miropolski Correlation
  Film-boiling correlation for two-phase flow
  Switches to Dittus-Boelter correlation for single-phase flow
  Suitable for chilldown problems
  Not accurate for nucleate boiling regime

## Slide 16
Verification of Conjugate Heat Transfer Results
Problem Considered
GFSSP Model
Comparison with Analytical Solution

## Slide 17: Advanced Applications
Modeling Cryogenic Transfer Line
  Validation of CHT Capability
Modeling of Propellant Loading
  Model Verification by comparing with Space Shuttle Data
Pressurization of Space Shuttle’s LH2 Tank
  Model Verification by comparing with Space Shuttle Data

## Slide 18
NBS Test Set-up of Cryogenic Transfer Line

## Slide 19
GFSSP Model of Cryogenic Transfer Line

## Slide 20
Comparison with Test Data
Saturated LH2 chilldown time for various driving pressures
Subcooled LH2 chilldown time for various driving pressures. LH2 is subcooled at –424.57 ºF
Saturated LN2 chilldown time for various driving pressures
Subcooled LN2 chilldown time for various driving pressures. LN2 is subcooled at –322.87 ºF

## Slide 21
p=36.74 psia
p=61.72 psia
p=86.7 psia
p=161 psia
Comparison of temperature histories for subcooled LH2 for various driving pressures
Station #1 (violet)
—20 ft from tank inlet
Station #2 (red)
—80 ft from tank inlet
Station #3 (green)
—141 ft from tank inlet
Station #4 (blue)
—198 ft from tank inlet

## Slide 25
ET LH2 Tank Properties

## Slide 29
29
Diffuser
Liquid level at start of prepress
Liquid level at end of prepress
Pressurization of Space Shuttle’s LH2 Tank

## Slide 30
GFSSP Model of ET Hydrogen Tank Pressurization
Ullage
Diffuser
Dome
LH2 Surface
Control Valve
He Supply

## Slide 31
Ullage Pressure History in LH2 Tank (STS-109)
0.00E+00
5.00E+00
1.00E+01
1.50E+01
2.00E+01
2.50E+01
3.00E+01
3.50E+01
4.00E+01
4.50E+01
5.00E+01
0.00E+00
1.00E+01
2.00E+01
3.00E+01
4.00E+01
5.00E+01
6.00E+01
7.00E+01
8.00E+01
Time (sec)
Pressure (psia)
GFSSP
Test Data (STS-109)
Heat Transfer Coeff (Ullage -> Wall) = 2.38 Btu/hr-ft^2-F
Heat Transfer Coeff (Ullage -> LH2) = 2.38 Btu/hr-ft^2-F
Condensation Heat Transfer Coeff =14 btu/hr-ft^2-F

## Slide 32
Helium flowrate history in to ullage for base case
0.00E+00
2.00E-01
4.00E-01
6.00E-01
8.00E-01
1.00E+00
1.20E+00
1.40E+00
0.00E+00
1.00E+01
2.00E+01
3.00E+01
4.00E+01
5.00E+01
6.00E+01
7.00E+01
8.00E+01
Time (sec)
Flowrate (lb/sec)
9 cycles in 45 seconds after prepress

## Slide 33
Summary
GFSSP allows Users to model Conjugate Heat Transfer (CHT)
Solid to Solid and Solid to Fluid Heat Transfer capability was added in the GFSSP framework
GFSSP’s Graphical User Interface VTASC allows user to construct, run and view results for network consisting of fluid and solid nodes
For Heat Transfer Coefficients, Dittus-Boelter and Miropoloski Correlations (For Two Phase Flow) have been included
Other correlations can be implemented through User Subroutine
GFSSP’s CHT capability has been validated by comparing with test data
Examples 13 and 14 illustrate the use of Conjugate Heat Transfer applications