## Slide 1
Tutorial – 5 CHILLDOWN OF CRYOGENIC TRANSFER LINE

## Slide 2
CHILLDOWN OF TRANSFER LINE SCHEMATIC
Problem Considered:
Time dependent Pressure, Temperature and Flow Rate history during chilldown

## Slide 3
Set Up Options
Select Advanced/Enable Conjugate Heat Transfer
User Information
  Input File: Tut5.dat
  Output File: Tut5.out
Unsteady Options
  Time Step: 0.0015 s
  Final Time: 50.0 s
Output Control
  Winplot binary output
  MultiPlot; Plot Frequency: 100

## Slide 4
Set Up Options (cont.)
Circuit Options
  Solid-Fluid Heat Transfer Coeff.
  Miropolski Correlation
Fluid Options
  Hydrogen

## Slide 5
Build Model on Canvas
Solid Node
Fluid-Solid
Convection
Solid-Solid
Conduction
Now is a good time to save your Tut5.vts file.

## Slide 6
Set Up Transient Boundary Conditions
Node 1: Inlet from Dewar
  P = 75 psia
  T = -411 °F
Node 7: Outlet to Ambient (Boulder, CO)
  P = 12.05 psia
  T = 44 °F

## Slide 7
Set Up Internal Node Initial Conditions
Nodes 2-6
  P = 12.05 psia
  T = 44 °F
  Volume not required – GFSSP will calculate from pipe dimensions
Shortcut method to set all initial conditions:

## Slide 8
Set Up Fluid Branches
Branch 12: Inlet valve
  A = 0.3068 in2, CL = 0.6
Branch 67: Exit
  A = 0.3068 in2, CL = 1.0
Branch 23, 34, 45, 56: Pipes
  L = 200 ft / 4 = 50 ft = 600 in
  D = 0.625 in
  Smooth pipe: ε = 0

## Slide 9
Set Up Solid Nodes
Pipe is 65 lbm of SS304
Nodes 8 – 12
  Initial T = 44 °F
  Mass = 65 lbm / 5 = 13 lbm
  Material 29
Shortcut method for setting all solid node initial conditions:

## Slide 10
Set Up Conductors
Fluid-Solid Convection
  Total Wetted Area:
  Area per convector: 942.5 in2
Solid-Solid Conduction
  Cross-Sectional Area:
  Length per conductor: 50 ft = 600 in

## Slide 11
Fluid Temperature

## Slide 12
Solid Temperature

## Slide 13
Quality (Vapor Mass Fraction)

## Slide 14
STUDY OF THE RESULTS
Plot pressure, flowrate and fluid and solid temperature history
Estimate the predicted chilldown time
Observe the phase change behavior

## Slide 15
ANIMATE THE RESULTS
In VTASC, click the “M” button to start MultiPlot
In MultiPlot, click the “Next” button to step through line plots of the pressure in each node.
Click the “Start Cycling” button to animate the changing pressure.
Time and
Frame Number

## Slide 16
ANIMATE THE RESULTS (Cont.)
Click Options/Animation Options.
Change Function from PRESS to TEMP.
Click “Show Min Line” and “Show Max Line”.
Click “Exit”.
Click “Start Cycling” to animate the Fluid Temperature drop over time.

## Slide 17
ANIMATE THE RESULTS (Cont.)
To plot solid node properties, Click File/Load MultiPlot File.
Select the file Tut5SN.MPL and click “Open”.
Under Options, select TS, “Show Min Line” and “Show Max Line”.
Click “Start Cycling” to animate the Solid Temperature drop over time.