## Slide 1: USER SUBROUTINE

## Slide 2: Contents
Motivation & Benefit
Program Structure
Solution Algorithm
Solver-User Subroutine Interaction
Data Structure
Indexing Subroutines
Utility Subroutines and Functions
Compiling and Linking
Examples
Demo 3: Tank Blowdown with Heat Transfer

## Slide 3
MOTIVATION AND BENEFIT
  Motivation: To allow users to access GFSSP solver module to develop additional modeling capability
  Benefit: GFSSP users can work independently without Developer’s active involvement

## Slide 4
How do they work?
  A series of subroutines are called from various locations of solver module
  The subroutines do not have any code but include the common block
  The users can write FORTRAN code to develop any new physical model in any particular node or branch
What do users need to do?
  Users need to compile a new file containing all user routines and link that with GFSSP to create a new executable

## Slide 5
GFSSP – Program Structure
Graphical User
Interface
(VTASC)
Solver & Property
Module
User Subroutines
Input Data
File
New Physics
•
Time dependent
process
•
non
-
linear boundary
conditions
•
External source term
•
Customized output
•
New resistance / fluid
option
Output Data File
•
Equation Generator
•
Equation Solver
•
Fluid Property Program
•
Creates Flow Circuit
•
Runs GFSSP
•
Displays results graphically
Graphical User
Interface
(VTASC)
Solver & Property
Module
User Subroutines
Input Data
File
New Physics
•
Time dependent
process
•
non
-
linear boundary
conditions
•
External source term
•
Customized output
•
New resistance / fluid
option
Output Data File
•
Equation Generator
•
Equation Solver
•
Fluid Property Program
•
Creates Flow Circuit
•
Runs GFSSP
•
Displays results graphically

## Slide 6
Start
READIN - Reads input data from data file generated by VTASC
INIT – Generate Trial Solution
GASP & Wasp or GASPAK – A routine for thermodynamic properties
Obtain a trial solution
Simultaneous (S) solution of pressure, flowrate, and resident maas
NEWTON – Controls the iteration loop of Newton-Raphson scheme
COEF – Constructs the coefficient matrix of the correction equation
SOLVE – Solve correction equation by Gaussian elimination method
UPDATE – After applying corrections update each variable (11)
Successive Substitution (SS) solution of enthalpy & concentration
ENTHALPY – Solves enthalpy by SS method
MASSC – Solves concentration by SS method
Calculate flow resistances
RESIST – Calculates resistances for all branches
DENSITY – Calculates density and other properties
GASP & Wasp or GASPAK – A routine for thermodynamic properties
KFACT1 – KFACT21 Calculates branch resistances
Convergence check
Iteration loop
EQNS – Calculates residuals of three governing equations
Mass conservation
Momentum Conservation
Equation of State
Energy Conservation
Species Conservation
BOUND – Supply Time-dependant boundary conditions
Solution of Temperature of Solid
TSOLID or TSOLIDNR – Solves temperature by SS or S method
Solid Temperature
repeated for each time step
Flow Chart of Solution Algorithm

## Slide 7: Description of User Subroutines
Twenty-three User Subroutines are provided.
The most commonly used are:
  BNDUSER: Variable boundary condition during transient run
  KFUSER: New resistance option
  SORCEQ: External Heat source
  SORCETS: External Heat Source in Solid Node
  USRHCF: New Heat Transfer Correlation
  USRADJUST: Solution adjustment to satisfy design requirement
  KFADJUST: Adjust resistance factor Kf, if necessary

## Slide 8: Description of User Subroutines
Less Commonly Used:
  SORCEM: External Mass Source
  SORCEF: External Force
  SORCEC: External Concentration source
  PRPUSER: Overwrite fluid properties; call other fluid packages such as REFPROP
  TSTEP: Variable time step during a transient run
  USRINT: Provide initial values and steady state boundary conditions
  PRNUSER: Additional print out or creation of additional file for post processing
  FILNUM: Assign file numbers; users can define new file numbers

## Slide 9: Description of User Subroutines
  USRSET: User can supply all the necessary information by writing their own code
  PRPADJUST: Adjust Thermodynamic or Thermophysical Property
  TADJUST: Adjust Temperature, if necessary
  PADJUST: Adjust Pressure, if necessary
  FLADJUST: Adjust Flowrate, if necessary
  HADJUST: Adjust Enthalpy, if necessary
  SORCEHXQ Add heat sources to component Enthalpy Equation in Mixture (Enthalpy Option -2)
  USRMDG: Adjust Input Parameters for Multi-D Flow

## Slide 10
MAIN
Controls program
FILENUM
Defines input and output files numbers within the code
TSTEP
Allows user to overwrite the input deck defined time step
READIN
Reads input data file
USRSET
Allows user to redefine input file to custom format
INIT
Provides initial value
and steady state
boundary conditions
USRINT
Allows user to overwrite initial values and
steady state boundary conditions
BOUND
Provides time-dependant
boundary conditions
from history file
BNDUSER
Allows user to define time-dependant boundary conditions
Solver Module/function
User Subroutine/function
USRADJUST
Allows user to iteratively adjust solution to satisfy design requirement
Solver-User Subroutine Interaction (Partial List)

## Slide 11
Solver Module/function
User Subroutine/function
ENTHALPY/
ENTROPY
Generates and solves the
energy conservation
equation
SORCEQ
Allows user to provide an external heat source
MASSC
Generates and solves the
specie conservation
equation
SORCEC
Allows user to provide an external specie source
RESIST
Calculates the flow
resistance coefficient
KFUSER
Allows user to define new resistance options
DENSITY
Calculates the
fluid properties
PRPUSER
Allows user to define new fluid properties
EQNS
Generates mass &
momentum conservation
equations along with
equation of resident mass
SORCEM
Allows user to provide an external mass source
SORCEF
Allows user to provide an external momentum source

## Slide 12
PRINT
Generates the Output files
PRNUSER
Allows user to provide any additional output file(s)
TSEQNS
Generates conservation equations
of solid temperature
TSOLID
Solves solid temperature equations
by successive substitution method
CONVHC
Calculates convective heat transfer
coefficient
SORCETS
Allows user to provide external heat source to solid node
USRHCF
Allows user to provide new heat transfer correlation
Solver Module/function
User Subroutine/function

## Slide 13: Indexing Subroutine
SUBROUTINE INDEXI (NUMBER, NODE, NNODES, IPN)
or
SUBROUTINE INDEXI (NUMBER, IBRANCH, NBR, IB)
This subroutine determines the pointer of node or branch
Input Variables:
NUMBER: Node or Branch Number
NODE/IBRANCH: Array for storing Node or Branch Number
NNODES/NBR: Number of Nodes or Branches
Output Variable:
IPN/IB: Location of Node or Branch in Array (Pointer)

## Slide 14
Address location of a node (say node number 400).
NUMBER = 400
CALL INDEXI (NUMBER,NODE,NNODES,IPN)
NNODE = 5
NINT = 3
In this Example IPN = 4
P(IPN) = 2557.85
TF(IPN) = 500.25
USE OF SUBROUTINE INDEXI

## Slide 15
SUBROUTINE INDEXA (NUMBER, NODEAM, NAMB, IPAN)
This subroutine determines the pointer of Ambient Node.
SUBROUTINE INDEXS (NUMBER, NODESL, NSOLIDX, IPSN)
This subroutine determines the pointer of Solid Node.
SUBROUTINE INDEXSSC (NUMBER, ICONSS, NSSC, ICSS)
This subroutine determines the pointer of Solid to Solid Conductor.
SUBROUTINE INDEXSFC (NUMBER, ICONSF, NSFC, ICSF)
This subroutine determines the pointer of Solid to Fluid Conductor.
SUBROUTINE INDEXSAC (NUMBER, ICONSA, NSAC, ICSA)
This subroutine determines the pointer of Solid to Ambient Conductor.
SUBROUTINE INDEXSSRC (NUMBER, ICONSSR, NSSR, ICSSR)
This subroutine determines the pointer of Solid to Solid Radiation Conductor.
Indexing Subroutines

## Slide 16
SUBROUTINE INTERPOL (XVALUE, N, XARRAY, YARRAY, YVALUE)
This subroutine linearly interpolates a YVALUE given an XVALUE and XY data. It does not extrapolate, but returns the first or last y-value, as needed.
Input Variables:
XVALUE: x value at which to interpolate y
N: number of points in arrays XARRAY and YARRAY
XARRAY: array of x values, in increasing order
YARRAY: array of y values corresponding to XARRAY
Output Variable:
YVALUE: interpolated y value
Functions to convert units are listed in Appendix 5 of the User Manual. For example:
REAL FUNCTION KW_BTUS (VALUE)
Converts VALUE in kW to BTU/s.
Utility Subroutines and Functions

## Slide 17
Fluid Property Subroutines
CALL PROPS_PT(I_NFLUID, Z_P, Z_T, Z_RHO, Z_H,
+ Z_CP, Z_CV, Z_S, Z_GAMMA, Z_MU
+ Z_K, I_KR, Z_XV)
Input
  I_NFLUID: Fluid ID code (see next slide)
  Z_P: Pressure
  Z_T: Temperature
Output
  Z_RHO: Density
  Z_H: Enthalpy
  Z_CP, Z_CV: Specific heats
  Z_S: Entropy
  Z_GAMMA: Ratio of specific heats
  Z_MU: Viscosity
  Z_K: Thermal conductivity
  I_KR: Fluid phase code (0 unknown; 1 saturated; 2 liquid; 3 gas)
  Z_XV: Quality (vapor mass fraction)
17

## Slide 18
Fluid Property Subroutines
18
ID Number | Gas | ID Number | Gas | ID Number | Gas
1 | GASP He | 51 | GASPAK He | 71 | GASPAK Xe
2 | GASP CH4 | 52 | GASPAK CH4 | 72 | GASPAK R-11
3 | GASP Ne | 53 | GASPAK Ne | 73 | GASPAK R-12
4 | GASP N2 | 54 | GASPAK N2 | 74 | GASPAK R-22
5 | GASP CO | 55 | GASPAK CO | 75 | GASPAK R-32
6 | GASP O2 | 56 | GASPAK O2 | 76 | GASPAK R-123
7 | GASP Ar | 57 | GASPAK Ar | 77 | GASPAK R-124
8 | GASP CO2 | 58 | GASPAK CO2 | 78 | GASPAK R-125
9 | GASP F2 | 59 | GASPAK H2 (para) | 79 | GASPAK R-134A
10 | GASP H2 (para) | 60 | GASPAK H2 (normal) | 80 | GASPAK R-152A
11 | WASP H2O | 61 | GASPAK H2O | 81 | GASPAK N2F3
12 | RP-1 Tables | 62 | GASPAK RP-1 (liq) | 82 | GASPAK NH3
 |  | 63 | GASPAK Isobutane | 84 | GASPAK H2O2
33 | Ideal Gas | 64 | GASPAK Butane | 86 | GASPAK Air
 |  | 65 | GASPAK Deuterium |  | 
37 | User Fluid 1 | 66 | GASPAK Ethane |  | 
38 | User Fluid 2 | 67 | GASPAK Ethylene |  | 
39 | User Fluid 3 | 68 | GASPAK H2S |  | 
 |  | 69 | GASPAK Kr |  | 
 |  | 70 | GASPAK Propane |  | 

## Slide 19
Fluid Property Subroutines
19
Property | English Units
Pressure (P) | Psf
Temperature (T) | °R
Conductivity (k) | BTU/ft-s-R
Density (r) | lb/ft3
Viscosity (m) | lb/ft-s
Specific Heat Ratio (g) | Dimensionless
Enthalpy (H) | BTU/lb
Entropy (S) | BTU/lb-R
Specific Heat (Cp) | BTU/lb-R
Specific Heat (Cv) | BTU/lb-R

## Slide 20
Fluid Property Subroutines
CALL PROPS_PH(I_NFLUID, Z_P, Z_T, Z_RHO, Z_H, Z_CP, Z_CV,
+ Z_S, Z_GAMMA, Z_MU, Z_K, I_KR, Z_XV,
+ Z_RHOL, Z_HL, Z_CPL, Z_CVL, Z_SL, Z_GAMMAL, Z_MUL, Z_KL,
+ Z_RHOV, Z_HV, Z_CPV, Z_CVV, Z_SV, Z_GAMMAV, Z_MUV, Z_KV)
CALL PROPS_PS(I_NFLUID, Z_P, Z_T, Z_RHO, Z_H, Z_CP, Z_CV,
+ Z_S, Z_GAMMA, Z_MU, Z_K, I_KR, Z_XV,
+ Z_RHOL, Z_HL, Z_CPL, Z_CVL, Z_SL, Z_GAMMAL, Z_MUL, Z_KL,
+ Z_RHOV, Z_HV, Z_CPV, Z_CVV, Z_SV, Z_GAMMAV, Z_MUV, Z_KV)
Input
  I_NFLUID: Fluid ID code
  Z_P: Pressure
  Z_H or Z_S: Enthalpy or Entropy
Output
  Similar to PROPS_PT
  If the fluid is saturated (I_KR = 1), properties suffixed in “L” or “V” are the properties of the pure liquid or vapor. The other properties are quality-weighted averages of the two-phase mixture.
20

## Slide 21
Fluid Property Subroutines
CALL PROPS_PSATX(I_NFLUID, Z_P, Z_T, Z_RHO, Z_H, Z_CP, Z_CV,
+ Z_S, Z_GAMMA, Z_MU, Z_K, I_KR, Z_XV,
+ Z_RHOL, Z_HL, Z_CPL, Z_CVL, Z_SL, Z_GAMMAL, Z_MUL, Z_KL,
+ Z_RHOV, Z_HV, Z_CPV, Z_CVV, Z_SV, Z_GAMMAV, Z_MUV, Z_KV)
Input
  I_NFLUID: Fluid ID code
  Z_P: Saturation pressure
  Z_XV: Quality
Output
  Z_T: Saturation temperature
  PROPS_PSATX is for GASP/WASP and GASPAK fluids only.
  If the input saturation pressure is greater than Pcrit, an error message is returned.
21

## Slide 22
Compiling & Linking User Subroutine

## Slide 23: Examples of Typical User Subroutines

## Slide 24
User Subroutine Applications
Example 18 - Simulation of a Subsonic Fanno Flow
User-Prescribed Heat Transfer Coefficient
Thermostatically controlled heater
User-Defined Branch Resistance
  User-Defined Plot Variables

## Slide 25
Problem: To compare with textbook solution, friction factor must be constant. However, GFSSP always solves for friction factor based on Reynolds number.
Solution: Use subroutine KFADJUST to recalculate pipe resistance factor Kf assuming a constant friction factor.
Example 18 - Simulation of a Subsonic Fanno Flow

## Slide 26
C***********************************************************************
SUBROUTINE KFADJUST(I,RHOU,EMUU,RHOUL,EMUUL,RHOUV,EMUUV,ISATU,
& AKNEW)
C PURPOSE: ADJUST RESISTANCE IN A BRANCH
C***********************************************************************
INCLUDE 'COMBLK.FOR'
C**********************************************************************
C ADD CODE HERE
IF (IOPT(I) .EQ. 1) THEN
PIPEL = BRPR1(I)
PIPED = BRPR2(I)
F = 0.002
AKNEW = 8.0 * F * PIPEL / (RHOU * PI**2 * PIPED**5 * GC)
END IF
RETURN
END
VTASC Model & User Subroutine

## Slide 27
C***********************************************************************
SUBROUTINE KFADJUST(I,RHOU,EMUU,RHOUL,EMUUL,RHOUV,EMUUV,ISATU,
& AKNEW)
C PURPOSE: ADJUST RESISTANCE IN A BRANCH
C***********************************************************************
INCLUDE 'COMBLK.FOR'
C**********************************************************************
C ADD CODE HERE
IF (IOPT(I) .EQ. 1) THEN
PIPEL = BRPR1(I)
PIPED = BRPR2(I)
F = 0.002
AKNEW = 8.0 * F * PIPEL / (RHOU * PI**2 * PIPED**5 * GC)
END IF
RETURN
END
User Subroutine Explanation
Including the COMMON block gives us access to all the program variables listed in Appendix 4 of the User Manual.
If the current branch option is a pipe (option 1), then…
Pipe length and diameter are stored in branch parameter arrays.
Set constant friction factor of 0.002
Recalculate KF for this branch
Note that PI and GC are already program constants. Upstream density was passed as argument RHOU.
Argument I is the pointer to the current branch. Output AKNEW is the new value of Kf.

## Slide 28
Branch Parameter Arrays
Branch Option | BRPR1 | BRPR2 | BRPR3 | BRPR4 | BRPR5 | BRPR6
1. Pipe | Length | Diameter | ε/D |  |  | 
2. Restriction | CL |  |  |  |  | 
3. Non-Circular Duct | Length | Height | Width | Type (1-4) |  | 
4. Pipe with Entrance and Exit Losses | Length | Diameter | ε/D | Ki | Ke | 
5. Thin Sharp Orifice | D1 | D2 |  |  |  | 
6. Thick Orifice | Length | D1 | D2 |  |  | 
7. Square Reduction | D1 | D2 |  |  |  | 
8. Square Expansion | D1 | D2 |  |  |  | 
9. Rotating Annular Duct | Length | ro | ri | RPM |  | 
10. Rotating Radial Duct | Length | Diameter | RPM |  |  | 
11. Laby Seal | Radius | Clearance, c | Pitch, m | Number of teeth, n | Multiplier, α | 
12. Parallel Plates (Face Seal) | Radius | Clearance, c | Length |  |  | 
Users have access to branch parameters through the BRPR arrays. Full table is found in Chapter 4 of the User Manual

## Slide 29
User-Prescribed Heat Transfer Coefficient
Diffuser
Liquid
Problem: Heat transfer coefficient between ullage gas and tank dome is not a constant value. It must be evaluated by natural convection correlations based on ullage properties.
Solution: Use subroutine USRHCF to calculate heat transfer coefficient.
Ullage

## Slide 30
User Subroutine to Calculate Heat Transfer Coefficient
C**********************************************************
SUBROUTINE USRHCF(NUMBER,HCF)
C PURPOSE: PROVIDE HEAT TRANSFER COEFFICIENT
C**********************************************************
INCLUDE 'COMBLK.FOR'
C**********************************************************
DATA HL /15.0/
DATA C1, C2 /0.15, 0.33/
NUMF = ICF(NUMBER)
CALL INDEXI(NUMF, NODE, NNODES, IPN)
NUMS = ICS(NUMBER)
CALL INDEXS(NUMS, NODESL, NSOLIDX, IPSN)
BETA = 1.0 / TF(IPN)
DELTAT = ABS(TF(IPN) - TS(IPSN))
GR = HL**3 * RHO(IPN)**2 * G * BETA * DELTAT / (EMU(IPN)**2)
PRNDTL = CPNODE(IPN) * EMU(IPN) / CONDF(IPN)
XNU = C1 * (GR * PRNDTL)**C2
HCF = XNU * CONDF(IPN) / HL
RETURN
END
C**********************************************************
Argument NUMBER is the pointer to the current solid-to-fluid conductor. Output HCF is the heat transfer coefficient.
Including the COMMON block gives us access to program variables such as the node properties used below.
Set characteristic length HL and correlation constants C1 and C2
Get fluid and solid node numbers (NUMF, NUMS) and their pointers (IPN, IPSN)
Having the fluid and solid node pointers (IPN, IPSN) allows us to access fluid and solid node properties such as temperature (TF, TS), density (RHO), viscosity (EMU), Cp (CPNODE), and k (CONDF).
Calculate heat transfer coefficient HCF

## Slide 31
Thermostatically Controlled Heater
Problem: It is desired to simulate a thermostatically controlled heat source in a fluid node. GFSSP’s built-in heat source options are constant-value or time-varying, but not temperature-varying.
Solution: Use subroutine BNDUSER to apply a heat source to a node based on its temperature.

## Slide 32
User Subroutine to Simulate Heater with Thermostat
SUBROUTINE BNDUSER
C PURPOSE: MODIFY BOUNDARY CONDITIONS
C***********************************************************************
INCLUDE 'comblk.for'
C**********************************************************************
C ADD CODE HERE
C Declarations
DATA HEATPOWER /1.0/, THEATOFF /120.0/, THEATON /110.0/
C In every time step, check the temperature of the heated node
C and apply heat if temperature is less than THEATON, or
C set heat to zero if temperature is above THEATOFF.
CALL INDEXI(5, NODE, NNODES, IPN)
TFAHRENHEIT = TF(IPN) - 459.67
IF (TFAHRENHEIT .LT. THEATON) THEN
HSORCE(IPN) = HEATPOWER
ELSE IF (TFAHRENHEIT .GT. THEATOFF) THEN
HSORCE(IPN) = 0.0
END IF
RETURN
END
Subroutine BNDUSER is called at the beginning of each time step. The user can monitor the model and make changes to boundary conditions, heat sources, geometry, etc.
Declare a 1.0 BTU/s heater with temperature limits of 110 and 120 °F.
Get pointer to Node 5
Convert temperature of Node 5 from °R to °F.
If temperature is too low, apply a heat source. If too high, set heat source to zero. (At temperatures in between, HSORCE will retain its value from the previous time step.)

## Slide 33
Problem: The user wishes to model pressure drop in a filter. Test data relating pressure drop to flow rate are available.
Solution: Use the User-Defined Branch Option in VTASC along with subroutine KFUSER.
User-Defined Branch Resistance

## Slide 34
Test Data and Kf
Flow Rate (lb/s) | DP (psf) | Kf
1.0 | 10 | 10
2.0 | 20 | 5
3.0 | 30 | 3.33
4.0 | 40 | 2.5
GFSSP’s momentum equation expresses friction losses in terms of flow rate:

## Slide 35
C***********************************************************************
SUBROUTINE KFUSER(I,RHOU,EMUU,XVU,RHOUL,EMUUL,AKNEW)
C PURPOSE: ADD A NEW RESISTANCE OPTION
C***********************************************************************
INCLUDE 'comblk.for'
C**********************************************************************
C ADD CODE HERE
C Declarations
REAL FILTERMDOT(4), FILTERKF(4)
DATA FILTERMDOT /1.0, 2.0, 3.0, 4.0/
DATA FILTERKF /10.0, 5.0, 3.33, 2.5/
C Executable code.
FILTERFLOW = FLOWR(I)
CALL INTERPOL(FILTERFLOW, 4, FILTERMDOT, FILTERKF, AKNEW)
RETURN
END
User Subroutine Explanation
Filter data (Kf vs. flow rate) stored in arrays.
Get the flow rate in this user-defined branch in the current iteration.
Interpolate KF for this branch

## Slide 36
User-Defined Plot Variables
Problem: The user wants to plot pressurization option heat transfer rates in Winplot.
Solution: Use User-Defined Plot Variables to send extra variables to the Winplot file.

## Slide 37
User Defined Plot Variables
C***********************************************************************
SUBROUTINE BNDUSER
C PURPOSE: MODIFY BOUNDARY CONDITIONS
C***********************************************************************
INCLUDE 'comblk.for'
C**********************************************************************
C ADD CODE HERE
C Turn on user-variables to send to Winplot
USRVAR = .TRUE.
USRVARSNUM = 2
USRPVARNAME(1) = 'QULPRP'
USRPVARUNIT(1) = 'BTU/s'
USRPVARNAME(2) = 'QULWAL'
USRPVARUNIT(2) = 'BTU/s'
C Copy data from pressurization option to user variable
USRPVAR(1) = QULPRP(1)
USRPVAR(2) = QULWAL(1)
RETURN
END
Declare two user variables and set their Winplot names and units
Copy the values of the pressurization option heat transfer rates to the user variables.

## Slide 38
SUMMARY
User Subroutines can be used to add new capabilities that are not available to Users through Logical Options
New capabilities may include:
  Incorporating Design Specification; this may require iterative adjustment
  User Specified Heat Transfer Coefficient
  Incorporating a new physical model such as mass transfer
  Customized output, variable timestep etc.
Checklist for User Subroutines
  Identify subroutines that require modifications
  Select GFSSP variables to be modified
  Make use of GFSSP provided User Variables in your coding

## Slide 39
Demo 3: Tank Blowdown with Heat Transfer
This problem repeats Demo 2, the tank blowdown, but does not neglect heat transfer from the wall.
We will write a user subroutine to calculate the natural convection heat transfer coefficient.

## Slide 40
Demo 3: Prepare Files
Find the original “Demo2.vts” file and make a copy called “Demo3.vts”.
Find the GFSSP installation directory, usually C:\GFSSP701
Find the files “comblk.for” and “userrtn701.for” and copy them to the same directory as the “Demo3.vts” file.
Copy

## Slide 41
Demo 3: Modify VTS File
Rename the input and output files “Demo3.dat” and “Demo3.out”

## Slide 42
Demo 3: Modify VTS File (cont.)
Enable Conjugate Heat Transfer and add Solid Node 3, and Fluid-to-Solid Conductor 31.
The tank is 471 lb of SS304, initially at 80 °F.
The surface area of the tank is 3250 in2.

## Slide 43
Demo 3: Open User Subroutine File
Select Module/Build from the VTASC menu to open the Build Window
Navigate to the blank user subroutine file in your working directory
Edit the file by clicking the “e” button

## Slide 44
Demo 3: Write User Subroutine Code
Type the code above in user subroutine USRHCF
Remember that Fortran statements begin in column 7!

## Slide 45
Demo 3: Build New Executable
Save and close the user subroutine file
Select your Fortran compiler (Compaq, Intel, or G95)
Click the “Build” button

## Slide 46
Demo 3: Verify New Executable
A new executable, “userrtn605.exe”, should now be in your working directory
This executable replaces the standard GFSSP executable on the User Options page

## Slide 47
Demo 3: Compare Results
Run the model and plot the results in Winplot. The old Demo2.WPL file can also be plotted for comparison.
Note that pressure and temperature decrease more slowly when there is heat transfer from the tank wall.

## Slide 48
Demo 3: Compare Results
Plot the temperature of the tank wall and the heat transfer coefficient.
Note that the heat transfer coefficient is not constant over time.