## Slide 1: Fluid Mixture & Two-Phase Flows
Helium
Liquid Oxygen

## Slide 2: CONTENT
Mixture Temperature by Specific Heats
Enthalpy Formulations of Mixture Modeling
Mathematical Formulation
Applications:
  Example 23 – Helium-Assisted Buoyancy-Driven Flow in a Vertical Pipe Carrying Liquid Oxygen with Ambient Heat Leak
  Charging of Pogo Accumulator
Summary

## Slide 3
Calculate Mixture Temperature by Specific Heats
GFSSP’s default is to calculate mixture temperature from a modified Energy Conservation Equation using the specific heats of the individual species instead of enthalpy.
Limitations
Cannot handle phase change of mixture
Assumes specific heats are relatively constant

## Slide 4
Find Temperature from the Total Mixture Enthalpy
GFSSP’s Enthalpy 1 option sums the enthalpies of the individual species to arrive at a Total Mixture Enthalpy.
Using Enthalpy avoids the problem of non-constant Cp
Because the individual species have different reference points, it is not possible to determine the mixture temperature directly. An iterative procedure is used to find the mixture temperature.
Limitation
Cannot handle phase change of mixture

## Slide 5
Feature: Fluid Mixture, Comparison with Textbook Solution
Example 4 - Simulation of the Mixing of Combustion Gases and a Cold Gas Stream

## Slide 6
Ex4 by Mixture Temperature Option

## Slide 7
Ex4 by Enthalpy1 (Total Mixture Enthalpy) Option
Through iteration on temperature, it is found that at 633°F, the enthalpies of H2O and CO2 are 1320 and 474 BTU/lb, respectively.

## Slide 8: Enhanced Mixture Option
The mixture capability in earlier versions of GFSSP does not allow phase change in any constituent of the mixture
In liquid propulsion applications, there are situations where one of the constituent is saturated, i.e. mixture of liquid and vapor in equilibrium
  For example during purging of liquid oxygen by ambient helium, a mixture of helium, LO2 and GO2 exist
Why is there such a limitation?
  Because the energy conservation equation of the mixture is solved in terms of temperature
  For calculating phase change energy equation for each species must be solved in terms of enthalpy

## Slide 9: Mathematical Formulation
Mass Conservation
  Mixture Mass
  Concentration of Species
Momentum Conservation
  Mixture Momentum
Energy Conservation
  Temperature option
    Energy Conservation is formulated in terms of temperature
    Applicable for gas mixture
  Enthalpy 2 option
    Separate Energy Equations are solved for Individual Species
    Applicable for liquid-gas mixture with phase change

## Slide 10: Separate Energy Equation for Individual Species (SEEIS)

## Slide 11: Thermodynamic Properties
Temperature and other properties of individual species is calculated from node pressure and enthalpy of the species:
The nodal properties are calculated by averaging the properties of species:

## Slide 12
Select Mixture Energy Option

## Slide 13
Feature: Phase Change in Fluid Mixture, Buoyancy Driven Flow, Model Import and Conjugate Heat Transfer
Example 23 – Helium-Assisted Buoyancy-Driven Flow in a Vertical Pipe Carrying Liquid Oxygen with Ambient Heat Leak

## Slide 14: Charging of Pogo Accumulator
Problem Considered: An annular shaped pogo accumulator has been wrapped around a liquid oxygen feed line to a rocket engine turbopump. The lower portion of the accumulator communicates to feed line through a series of holes. The accumulator has a dip tube located a few inches above the communication port and connected to the dump line. The accumulator also has a high point bleed and charge port. Initially the accumulator is filled with liquid oxygen. Helium enters into the accumulator through high point bleed and charge port and displaces liquid oxygen to feed line and dump line. Once the liquid oxygen level drops to the location of dip tube, a stable helium bubble is retained in the accumulator that provides desired compliance. The objective of the model is to predict the history of charging process as well as the steady operation of the accumulator during engine run.
Dip Tube
location

## Slide 17: Boundary Conditions
Pressure and Temperature history at the helium supply line
Pressure and Temperature history at the Communication Ports

## Slide 20
Summary
An enthalpy based mixture formulation has been introduced in the code
Energy equation for individual species has been solved to calculate enthalpy of each species
Properties of individual species are computed from pressure and enthalpy
Properties of the mixture are evaluated by averaging properties of the species
New formulation allows calculation of phase change of species