## Slide 1
Tutorial – 6 Modeling an Oxygen Recirculation Line
In this multi-step project, you will:
Model LOx sitting stagnant in a vertical recirculation line
Evaluate the effect of heat transfer on the flowrate
Model a helium injector
Use VTASC’s import option to combine the LOx recirculation and helium injector models
Evaluate the LOx flowrate when both heat transfer and helium bubbling are applied

## Slide 2
Part 1: LOx Sitting Stagnant
VTASC File: Tut6.vts
User Information
  Input File: Tut6.dat
  Output File: Tut6.out
Circuit Options
  Select Gravity
Steady-State
Fluid is Liquid Oxygen

## Slide 3
Build Model on Canvas
The recirculation line is simply a 6’ vertical smooth pipe of 1.87” diameter.
Now would be a good time to save your Tut6.vts file.

## Slide 4
Set Up Steady-State Boundary Conditions
Node 1:
  P = 55.78 psia
  T = -272.5 °F
Node 8:
  P = 53.0 psia
  T = -272.5 °F
The 2.78 psia ∆P corresponds to the hydrostatic head of 6 ft of Lox
At this pressure, the LOx is approximately 1 °F subcooled.

## Slide 5
Set Up Fluid Branches
Branch 12: Inlet
  A = 0.639 in2, CL = 0.424
Branch 23, 34, 45, 56, 67, 78: Pipes
  L = 6 ft / 6 = 1 ft = 12 in
  D = 1.87 in
  Smooth pipe: ε = 0
  Angle = 180° (vertical)

## Slide 6
Result of Stagnant LOx Model
Run the model
Flow rate should be close to zero (< 0.01 lb/s)

## Slide 7
Part 2: Add Heat Transfer to Model
Select Advanced/Enable Conjugate Heat Transfer
Circuit Options
  Add Dittus-Boelter heat transfer correlation

## Slide 8
Update Model on Canvas
Solid Nodes
Fluid-Solid
Convection
Solid-Solid
Conduction
Ambient Node
Solid-Ambient
Convection
Allow 1’ of the pipe to be exposed to ambient. The rest remains insulated.
1.87”
2.32”

## Slide 9
Set Up Solid Nodes
Exposed pipe section is 5.26 lbm of Inconel 718
Nodes 9 & 10
  Guess T = 70 °F
  Mass = 5.26 lbm / 2 = 2.63 lbm
  Material 17
Ambient Node 11
  Tamb = 70 °F

## Slide 10
Set Up Conductors
Fluid-Solid Convection
  Wetted Area:
  GFSSP will calculate h by Dittus-Boelter correlation
Solid-Solid Conduction
  “Average” Area:
  Distance (pipe thickness): 0.225 in
Solid-Ambient Convection
  Exposed Area:
  Natural convection:
    h = 2 BTU/hr-ft2-°F
    = 5.56×10-4 BTU/s-ft2-°F

## Slide 11
Result of LOx Model with Heat Input
Rerun the model
Addition of 0.106 BTU/s of heat has increased flow rate to 0.172 lb/s

## Slide 12
Efficiency of Heat Leak as Pump
Use the values from the output file to determine the following:
Pump Power:
Heat Input:
Efficiency:
Carnot Efficiency:
Flowrate
P1 – P8

## Slide 13
Part 3: Model a Helium Injector
Save current tut6.vts file
Start a new file tut6a.vts
User information
  Input file: Tut6a.dat
  Output file: Tut6a.out
Circuit options
  Inertia
Steady-state
Fluid is helium

## Slide 14
Build Model on Canvas
High Pressure
Helium Supply
Ambient
Now would be a good time to save your Tut6a.vts file.

## Slide 15
Set Up Steady-State Boundary Conditions
Node 1:
  P = 425 psia
  T = 100 °F
Node 4:
  P = 14.7 psia
  T = 60 °F

## Slide 16
Set Up Fluid Branches
Branch 12: Pipe
  L = 12 in
  D = 0.152 in
  Smooth pipe: ε = 0
Branch 23: Restrction
  A = 0.0012566 in2
  CL = 0.6
  Inertia box checked
Branch 34: Pipe
  L = 28 in
  D = 0.152 in
  Smooth pipe: ε = 0

## Slide 17
Result of Helium Injector Model
Run the model
The injector can provide 0.00163 lb/s of helium to ambient pressure

## Slide 18
Part 4: Combine He Injector with LOx Recirc Line
Save current tut6a.vts file, then
Save As tut6b.vts
Select File/Import Model
  Select LOx Recirculation Line model (tut6.vts)
  To prevent conflict with existing nodes/branches, select an offset of 100 and click Apply.
Rearrange the canvas as necessary*
Helium Injector
LOx Recirc Line
Note renumbered nodes and branches on imported model.
*HINT: To move a group of nodes/branches, select multiple items by holding down the CTRL key (or rubber-band them while holding down the SHIFT key). Then drag them across the canvas while holding down the SHIFT key.
NOTE: If the import aborts, close your model, then restart VTASC afresh. This should expunge the gremlins.

## Slide 19
Connect Injector to Recirc Line
Right-click Injector branch 34
Select Change Branch Connection
Change downstream node to Recirc Line node 103
Delete Injector node 4
Branch 34 now connects injector to recirc line node 103

## Slide 20
Set Up User Options
User information
  Input file: Tut6b.dat
  Output file: Tut6b.out
Solution Control
  Mixture Enthalpy2
Circuit options*
  Gravity
  Inertia
  Dittus-Boelter
*NOTE: Many of these options will already be checked after they were imported.

## Slide 21
Set Up User Options (cont.)
Unsteady options
  Unsteady
  Time step: 0.1 sec
  Final time: 100 sec
Fluids are
  Helium
  Oxygen
Winplot binary output

## Slide 22
Complete Transient Boundary Conditions
Node 1:
  P = 425 psia
  T = 100 °F
  He mass fraction: 1.0
  LOx mass fraction: 0.0
Node 101:
  P = 55.78 psia
  T = -272.5 °F
  He mass fraction: 0.0
  LOx mass fraction: 1.0
Node 8:
  P = 53.0 psia
  T = -272.5 °F
  He mass fraction: 0.0
  LOx mass fraction: 1.0*
*Strictly speaking, node 8 will be some mixture of LOx and He. However, because it is downstream, setting the boundary mass fraction to pure LOx will not affect the calculations.

## Slide 23
Complete Internal Node Initial Conditions
Nodes 2 and 3:
  P = 14.7 psia
  T = 60 °F
  He mass fraction: 1.0
  LOx mass fraction: 0.0
Nodes 102, 103, 104, 5, 6, and 7:
  P = 14.7 psia
  T = 60 °F
  He mass fraction: 0.0
  LOx mass fraction: 1.0
*NOTE: Node Volumes can be set to 0.0. GFSSP will calculate the volumes based on the pipe dimensions.
*SHORTCUT: After setting node 102 properties, right-click the node and select Save Properties. Then right-click node 103 and select Apply Properties. Repeat for remaining recirculation line internal nodes.

## Slide 24
Complete Fluid Branches
Branch 12: Pipe
  L = 12 in
  D = 0.152 in
  Smooth pipe: ε = 0
  Gravity angle: 90°
Branch 34: Pipe
  L = 28 in
  D = 0.152 in
  Smooth pipe: ε = 0
  Gravity angle: 90°
*NOTE: Most fluid branches will be already set after the model import. However, the gravity angle must be set in the helium injector pipes.

## Slide 25
Flowrates
With injection of 0.005 lb/s helium, LOx flowrate reaches steady-state at 1.80 lb/s.
Helium
LOx-He mixture

## Slide 26
Mass Fractions
In Node 7, flow is 99.7% LOx, 0.3% He.
Helium
LOx

## Slide 27
Solid Temperatures
Recirculation line chills down in 100 seconds.

## Slide 28
STUDY OF THE RESULTS
Model | Calculated Flowrate (lbm/s)
Stagnant | <0.010
Heat Leak (0.106 BTU/s) | 0.172
Heat Leak and He Injection | 1.80

## Slide 29
Challenge Problem 5
A Deflating Bicycle Tire
This is problem 13.39 of Introduction to Fluid Mechanics, 4th ed., by Fox and McDonald.
Air escapes from a high-pressure bicycle tire through a hole with diameter d = 0.254 mm. The initial pressure in the tire is P = 620 kPa (gage). (Assume that the temperature remains constant at 27 C.) The internal volume of the tire is approximately 4.26x10-4 m3, and is constant. Estimate the time needed for the pressure in the tire to drop to 310 kPa (gage). Compute the change in specific entropy of the air in the tire during this process.

## Slide 30
Challenge Problem 5
A Deflating Bicycle Tire
Hints:
We can assume the temperature remains constant because of heat transfer from the tire walls. In GFSSP we can approximate this with a solid node of a large mass of arbitrary material, initially at 27 C.
At these temperatures and pressures, air behaves as an ideal gas.
Gage pressures should be converted to absolute pressures by adding the ambient pressure of 101 kPa.
Because the pressure in the tire is more than 2x greater than the ambient pressure outside, we can expect choked flow in the hole.
Specific entropy values can be found in the output file. They can also be plotted in Winplot by selecting “Extended Plot Information” on the Output Control Page.

## Slide 31
Challenge Problem 5
http://www.slideshare.net/SubodhKumar27/solution-manual-fluid-mechanics-fox-mcdonald