## Slide 1: Psychrometric Property & Multi-Layer Insulation

## Slide 2: CONTENT
Psychrometric Property
  Definition of Psychrometric Property
  New Subroutines for Psychrometric Property Calculation
  New control parameter for Psychrometric Option
  Modeling Psychrometrics of Air-Water Vapor Mixture (Example 31)
Multi-Layer Insulation (MLI)
  Modified Lockheed Equation
  Solution of Lockheed Equation
  Application of MLI Conductor in modeling Cryogenic Tank (Example 29)

## Slide 3
Definition of Psychrometric Properties

## Slide 4
  New Subroutines for Psychrometric Property Calculation
SUBROUTINE PSAT(T,P)
CALCULATES SATURATION PRESSURE OF WATER AT A GIVEN TEMPERATURE
SUBROUTINE TSATT(P,T,TGUESS)
CALCULATES SATURATION TEMPERATURE OF WATER FROM VAPOR PRESSURE RELATION BY N-R METHOD
SUBROUTINE TWBCAR(TDB,PDP,PAMB,TWB)
CALCULATES WET-BULB TEMPERATURE FROM THE CARRIER EQUATION BY N-R METHOD
SUBROUTINE CARIER(TWB,TDB,PWB,PAMB,PDP)
CALCULATES THE PRESSURE AT THE DEW POINT TEMPERATURE

## Slide 5
  New control parameter for Psychrometric Option
Control Parameter : IOPTPSY
  IOPTPSY = 0: PSYCHROMETRIC PROPERTY INACTIVE
  IOPTPSY = 1: INPUT RELATIVE HUMIDITY (PHI)
  IOPTPSY = 2: INPUT WETBULB TEMPERATURE (TWB)
  IOPTPSY = 3: INPUT HUMIDITY RATIO (OMEGA)
When Psychrometric Option is active, GFSSP reads either PHI, TWB or OMEGA for both steady-state and transient models. Boundary History File requires one of the three property in addition to pressure, temperature and concentration
Uses GASPAK Option for Air and GASP/WASP Option for Water

## Slide 6
  Modeling Psychrometrics of Air-Water Vapor Mixture
  (Example 31)
Cold and dry air enters into an air-conditioning system
  Air is first heated and then humidified
The purpose of the GFSSP model is to calculate the temperature and relative humidity of the air at the exit of the air conditioner

## Slide 7
GFSSP Model
Note the use of Text Option in VTASC

## Slide 8
Activation of Psychrometry in Circuit Option

## Slide 9
Boundary Node Properties for Psychrometrics

## Slide 10
Comparison of GFSSP prediction with hand calculation
Energy conservation between (1) and (2)
GFSSP calculates
For this condition PSYCHRO calculates

## Slide 11
Humidifier
Water mass conservation between (2) and (3)
GFSSP calculates
Energy conservation (2) and (3)
GFSSP calculates
According to PSYCHRO,
Comparison of GFSSP prediction with hand calculation

## Slide 12
MLI Modeling Methodology
Qrad = Q1 = Q2 = Q3
Q2(T1, T2) – Q3(T2, Tc) = 0
Q1(Th, T1) – Q2(T1, T2) = 0
Qrad(Tamb, TH) – Q1 (TH,T1) = 0
Law of energy conservation

## Slide 13
Multi-Layer Insulation
Heat transfer through the MLI calculated by the Modified Lockheed equation
Cs = 2.4  10–4
Cr = 4.944  10–10
Cg = 14,600
q = heat flux through MLI (W/m2)
Tavg= average of hot and cold boundary temperatures (K)
N* = MLI layer density (layers/cm)
Th = hot boundary temperature (K)
Tc = cold boundary temperature (K)
Ns = number of MLI layers
e = MLI layer emissivity (e = 0.031)
P = interstitial gas pressure (torr).

## Slide 14
Multi-Layer Insulation
Radiative heat transfer from the shroud to the outer layer of MLI
Expression assumes radiation between closely spaced parallel planes.
For other situations, user may wish to modify input shroud emissivity.
Concentric cylinders:
Small object in large cavity (eshrd = 1):

## Slide 15
MLI Modeling Methodology
Flowchart of MLI_HEAT_RATE Subroutine

## Slide 16
  Application of MLI Conductor in modeling Cryogenic Tank (Example 29)
Inside blanket first; outside blanket last.

## Slide 17
  Application of MLI Conductor in modeling Cryogenic Tank (Example 29)

## Slide 18
  Application of MLI Conductor in modeling Cryogenic Tank (Example 29)