## Slide 1: Model Integration & Future Developments

## Slide 2: CONTENT
Model Integration
NASP (Network Algorithm for Separated Phases) for Two Phase Flows
Modeling Structural Compliance and Unsteady Friction Factor in Fluid Transient
Adaptive Time Stepping Scheme

## Slide 3: Model Integration
There are two ways GFSSP can handle sub-modeling
  Importing of a new model into an existing one (Tutorial 6)
  Integration of two models by executing another model from the existing one and data transfer between the models
This presentation describes the second approach
  Example 29 (Self-Pressurization of a Cryogenic Propellant Tank Due to Boil-off) demonstrates integration of two GFSSP Models (Tank Model and Thermodynamic Vent System Model)
The advantages of the second approach:
  A transient system model can execute a steady-state component model
  A “coupled” integrated model will be numerically more robust than one large integrated model
  Works around the energy equation trade-offs that normally need to be accepted with mixture models.

## Slide 4
Demonstration of Model Integration
Example 29 - Self-Pressurization of a Cryogenic Propellant Tank Due to Boil-off
GFSSP Model of Self-Pressurization
GFSSP Model of Thermodynamic Vent System (TVS)
Self-Pressurization Model is transient
TVS Model is steady-state
Self-Pressurization model executed TVS model from its User Subroutine

## Slide 5
Integrated Model

## Slide 6
  Demonstration of Model Integration of Tank Model & TVS Model (Example 29)
Self-Pressurization
Pressure Control by TVS

## Slide 7: NASP (Network Algorithm for Separated Phases)
Background
  Separated Flow Modeling will enhance the fidelity of Two Phase Flow Calculations
  Two Phase Flow occur during Propellant Tank Loading, Propellant Transfer and Tank Pressurization
Objective
  A New Algorithm, NASP is under development
  NASP will calculate liquid mass and vapor mass in the node, liquid flow rate and vapor flow rate in the branch to allow interphase slip

## Slide 8
Homogeneous & Separated Flow Model

## Slide 9
=
Mass Conservation Equation of Liquid-Vapor Mixture
Momentum Conservation Equation of Liquid
Momentum Conservation Equation of Vapor
Governing Equations
Liquid Velocity
(8e)
Vapor Velocity
Vapor Area
Av = α Aij
Liquid Area
Al = (1-α) Aij

## Slide 10
Governing Equations
Liquid Compressibility Factor
Vapor Compressibility Factor
Equation of State
Void Fraction

## Slide 11
Energy Conservation Equation
Enthalpy of two-phase mixture can be expressed as:
=
is the mass fraction of vapor.
Governing Equations
Governing Equations to be used | Variable to be calculated
Mass Conservation Equation of Liquid Vapor Mixture | Pressure, p
Momentum Conservation Equation of Liquid | Liquid Flowrate,
Momentum Conservation Equation of Vapor | Liquid Flowrate,
Equation of state | Resident mass, m
Void Fraction in terms of mass fraction & velocities | Void Fraction, α
Energy Conservation Equation of Liquid Vapor Mixture | Enthalpy, h
Mathematical Closure

## Slide 12
Boiling Water Reactor (Example 27)
12
6 ‘ long, 1” dia Water Tube subjected to 130 Btu/lb heat load

## Slide 13: Verification of Steady State Model
Chart: Pipe Length (inches)
| 0 | 7.2 | 14.4 | 21.6 | 28.8 | 36 | 43.2 | 50.400000000000006 | 57.600000000000009 | 64.800000000000011 | 72.000000000000014
Homogeneous | 30 | 29.739 | 29.608 | 29.288 | 28.596 | 27.548 | 26.133 | 24.314 | 22.027 | 19.157 | 14.7
NASP | 30 | 29.739 | 29.487 | 29.198 | 28.791 | 28.126 | 27.07 | 25.488 | 23.233 | 20.101 | 14.7
Chart: Pipe Length (inches)
| 7.2 | 14.4 | 21.6 | 28.8 | 36 | 43.2 | 50.400000000000006 | 57.600000000000009 | 64.800000000000011
Homogeneous | 0 | 0.095148 | 0.23315 | 0.37163 | 0.51038 | 0.64924 | 0.78807 | 0.92674 | 1
NASP (Quality) | 0 | 0.095384 | 0.31205 | 0.42341 | 0.55676 | 0.70459 | 0.85785 | 1 | 1
NASP (Volume Fraction) | 0 | 0.64646 | 0.81632 | 0.89412 | 0.9354 | 0.96213 | 0.9825 | 1 | 1
Chart: Pipe Length (inches)
| 0 | 7.2 | 14.4 | 21.6 | 28.8 | 36 | 43.2 | 50.400000000000006 | 57.600000000000009 | 64.800000000000011
Homogeneous | 62.224 | 59.878 | 0.74647 | 0.30385 | 0.18677 | 0.13145 | 0.098407 | 0.075803 | 0.058782 | 0.039777
NASP | 62.224 | 59.878 | 0.74183 | 0.22666 | 0.16504 | 0.12288 | 0.093727 | 0.072784 | 0.05573 | 0.034466
Chart: Pipe Length (inches)
| 0 | 7.2 | 14.4 | 21.6 | 28.8 | 36 | 43.2 | 50.400000000000006 | 57.600000000000009 | 64.800000000000011
Homogeneous | 80 | 209.99 | 249.59 | 248.97 | 247.61 | 245.5 | 242.54 | 238.53 | 233.14 | 355.53
NASP | 80 | 209.99 | 249.35 | 248.79 | 247.99 | 246.67 | 244.51 | 241.14 | 253.4 | 523.28

## Slide 14: Verification of Steady State Model
Chart: Pipe Length (inches)
| 3.6 | 10.8 | 18 | 25.2 | 32.4 | 39.6 | 46.800000000000004 | 54.000000000000007 | 61.20000000000001 | 68.400000000000006
Homogeneous | 0.7599 | 0.7599 | 0.7599 | 0.7599 | 0.7599 | 0.7599 | 0.7599 | 0.7599 | 0.7599 | 0.7599
NASP(Liquid Flowrate) | 0.7769 | 0.7769 | 0.6416 | 0.5551 | 0.4517 | 0.337 | 0.218 | 0.1006 | 6.788e-11 | 6.84e-11
NASP(Vapor Flowrate) | 7.351e-11 | 7.351e-11 | 0.1353 | 0.2217 | 0.3252 | 0.4399 | 0.5588 | 0.6763 | 0.7769 | 0.7769
Chart: Pipe Length (inches)
| 3.6 | 10.8 | 18 | 25.2 | 32.4 | 39.6 | 46.800000000000004 | 54.000000000000007 | 61.20000000000001 | 68.400000000000006
Homogeneous | 2.239 | 2.327 | 186.6 | 458.5 | 745.9 | 1060 | 1416 | 1838 | 2370 | 3506
NASP (Liquid Velocity) | 2.289 | 2.379 | 5.655 | 9.415 | 13.28 | 16.24 | 17.9 | 17.84 | 0 | 0
NASP (Vapor Velocity) | 0 | 0 | 536.1 | 702.3 | 952.7 | 1259 | 1612 | 2021 | 2556 | 4137
Parametric Study on Inlet Pressure

## Slide 15: Modeling Structural Compliance & Unsteady Friction Factor in Fluid Transient**
The intent of this research is to
  develop numerical algorithm to implement the structural deformation and two-way coupling with fluid flow calculation in GFSSP
  Implement unsteady friction factor for fluid transient calculations
Ex26 – Fluid Transients in Pipes Due to Sudden Opening of Valve was used for this development
Numerical results were compared with Experimental Data
**Summer Faculty Research by Dr. Alak Bandyopadhyay of Alabama A & M University

## Slide 16
Review of Example 26
Schematic of the Pipeline System with ball-valve location.
Two Important Parameters:
a = Lg/LT
PR = pR/p0
Ball Valve Opening
Plexiglass Pipe
PR = 2 to 7
α = 0.45 to 0.05
Ll = 20 ft, D = 1.025 in

## Slide 17
Review of Example 26
Imaginary Control Volume of Air
Variable Volumes
GFSSP predicts higher pressure than experiments
This discrepancy is attributed to rigid pipe assumption

## Slide 18
MODELING APPROACH FOR STRUCTURAL DEFORMATION
STATIC DEFORMATION APPROCH
The pipe is considered as a thin pressure vessel. The stresses are:
Strain in the circumferential direction:
The radial deformation:

## Slide 19
Implementation into GFSSP
Structural deformation was implemented by an implicit scheme
ALGRORITHM STEPS:
The structural deformation of the pipe is computed in user subroutine “padjust” by using static formulation described in the previous slide.
Area and Volume of each branch and volume for each node are recomputed (iteratively) to account for the pipe geometry change.
Under-relaxation factor is used on node volume computation to get results converged.

## Slide 20
Results With Structural Deformation
Chart: pR/pa = 7 a = 0.445
Comparison of computed results on fluid pressure with rigid pipe assumption and deformed pipe with experimental data. (SD: Structural Deformation)

## Slide 21
Results for Shorter Length of Entrapped Air
Chart: PR = 5 a = 0.058

## Slide 22
Unsteady-State Friction Factor Model
GFSSP uses a quasi-steady-state friction factor based on Moody’s chart.
A more accurate model as used by some researchers is the inclusion of unsteady friction factor along with steady-state friction model as:
f = fs + fu
where, fs is the quasi-steady friction factor (Darcy’s friction coefficient)
fu is the unsteady friction coefficient which depends on instantaneous local and convective accelerations as given by Brunone model
, k = C*/2, where C* = 0.00476 for laminar flow and and for turbulent flow.
Where c is the water hammer wave speed, which is the velocity of sound in water.
There is an alternate friction-factor model modified by Vítkovský corrected for back flow as below:

## Slide 23
Results with Unsteady Friction Factor
Chart: Effect of Unsteady Friction Factor and Structural Deformation (PR = 5, α = 0.058)

## Slide 24
Description:
This research focused on enhancing GFSSP’s transient simulation capability by incorporating an algorithm to determine an optimum time step. The determination of the optimum time step size is based on estimation of error indicator and linear feedback control theory. By comparing the error indicator with the desired level of accuracy, GFSSP can adjust the time step size by increasing or decreasing it using a feedback gain factor.
2015 Technical Excellence Initiatives End of Year Reviews
24
Accomplishments:
Linear feedback control algorithm has been successfully modified for time step selection by monitoring the flow physics. The algorithm has been incorporated into GFSSP through User Subroutine . Feasibility and applicability of the algorithm has been demonstrated by predicting pressure surges in pipeline with entrapped air. Numerical experiments show at least 60% reduction in CPU time.
Adaptive Time Stepping Scheme to Enhance Transient Simulation Capability of GFSSP**
** Summer Faculty Research by Dr. S. S. Ravindran of UAH

## Slide 25
Aim:
  Compute with largest possible time step Δt subject to given error bound and stability of the method
Ingredients:
  Sensor for the error (error estimate)
  Controller for Δt (time step adjustment strategy)
  Use control theory model
Adaptive Time-Stepping Scheme

## Slide 26
Example Problem: Waterhammer due to sudden valve opening (Priming)
Schematic of Experimental Set-up (Georgia Tech)
GFSSP Model

## Slide 27
Comparison between GFSSP and Experimental Data

## Slide 28
Comparison between Fixed and Adaptive Time Step

## Slide 29
(Adaptive) ∆tmax | CPU Time (Sec) | # of time steps (istepmax)
0.01 | 89 | 527
0.025 | 25 | 241
0.05 | 15 | 147
0.075 | 13 | 114
(Fixed Time step) | 251 | 1001
Improved Performance of Adaptive Time Stepping Scheme

## Slide 30: Summary
Ongoing development activities include
  NASP (Network Algorithm for Separated Phases) for Two Phase Flows
  Structural compliance and unsteady friction factor during fluid transient
  Adaptive time step
The other planned activities include
  Uncertainty Analysis
  Fluid Structure Interaction
  NASS (Network Algorithm for Separated Species) for fluid mixture
  Fick’s Law of Diffusion in mixture species equation
  Fourier Law of Heat Conduction in energy equation for fluid
  More Choices of Convection Coefficient for Solid-Fluid Conductor