## Slide 1: INPUT/OUTPUT THROUGH A GRAPHICAL USER INTERFACE - VTASC
GFSSP Version 6 Training Course

## Slide 2: Content
Overview
VTASC Description
VTASC Steady State Demonstration
Input/Output Files

## Slide 3: Overview
Visual Thermo-fluid dynamic Analyzer for Systems and Components (VTASC) is a program designed to efficiently build flow network models for use in the GFSSP program.
  Visually Interactive
    “Drag and Drop” Paradigm
    Model Building, Running, and Post-Processing in one environment
  Self-Documenting
    Hard copy of flow network
    JPG image of flow network for inclusion into papers and presentations

## Slide 4: Overview
  Eliminates errors during model building process
    Automatic node and branch numbering
    Save and restore models at any point in the model building process
    Built-in calculator
    Input values can be defined as Symbols that can be easily changed for parametric studies
  Pushbutton generation of GFSSP input file
    Steady and Transient cases
    Advanced features such as Turbopump, Tank Pressurization, and Heat Exchangers
  Run GFSSP directly from VTASC window
    GFSSP Run Manager acts as VTASC/GFSSP interface

## Slide 5: Overview
  Post-processing capability allows quick study of results
    Pushbutton access to GFSSP output file
    Point and click access to output at each node and branch
    Built-in plotting capability for transient cases
    Capable of plotting through Winplot and MultiPlot
  User Subroutines can be developed and integrated
    Editing, compiling, and linking to create a new executable can be done in VTASC Window
    New executable replaces the default executable

## Slide 6: VTASC DEMONSTRATION PROBLEMS

## Slide 7: Build Model on VTASC Canvas

## Slide 8: Determination of Pump Characteristics
Q (GPM) | mdot (lb/s) | Head (ft) | p (psf) | mdot2 (lb/s)2
0 | 0 | 495 | 30,888 | 0
4000 | 556.13 | 485 | 30,264 | 3.093e05
8000 | 1112.3 | 470 | 29,328 | 1.2372e06
12000 | 1668.4 | 450 | 28,080 | 2.784e06
16000 | 2224.5 | 425 | 26,520 | 4.9484e06
20000 | 2781 | 385 | 24,024 | 7.734e06
1.) Manufacturer’s Pump Curve (Head vs. Flowrate)
2.) Convert to lb/s and psf
3.) Plot delP vs. mdot2
4.) Curve fit:

## Slide 9: VTASC DEMONSTRATION PROBLEMS

## Slide 10: INPUT DATA FILE
GFSSP data files are created by VTASC
Structure of the data file are classified into 20 sections
Example 1 will be used to explain the content of input data file
Example 1 Flow System Schematic

## Slide 11
Title Information
Logical Variables
Node, Branch & Fluid Information
Solution Control Variable
Fluid Designation
INPUT DATA FILE

## Slide 12
Node Numbering & Designation
Node Variables
Node Branch Connection
Branch Flow Designation and Resistance Option
Resistance Option Information
Inertia Information
INPUT DATA FILE

## Slide 13
Inertia Information
Restart File
INPUT DATA FILE

## Slide 14: OUTPUT DATA FILE
Output Data File can be classified into following categories:
Title and Data Files
Logical Variables
Node & Branch Information
Fluid Information
Boundary Conditions
Solution Results
Convergence Message

## Slide 15: OUTPUT DATA FILE
1. Titles & Data Files
TITLE :PUMP-SYSTEM CHARACTERISTICS
ANALYST :ALOK MAJUMDAR
FILEIN :ex1.dat
FILEOUT :EX1.OUT
2. Logical Variables
LOGICAL VARIABLES
DENCON = F
GRAVITY = T
ENERGY = T
MIXTURE = F
THRUST = F
STEADY = T
TRANSV = F
SAVER = F
HEX = F

## Slide 16: OUTPUT DATA FILE
3. Node & Branch Information
NNODES = 4
NINT = 2
NBR = 3
NF = 1
NVAR = 5
NHREF = 2
4. Fluid Information
FLUIDS: H2O

## Slide 17: OUTPUT DATA FILE
5. Boundary Conditions
BOUNDARY NODES
NODE P T RHO AREA
(PSI) (F) (LBM/FT^3) (IN^2)
1 0.1470E+02 0.6000E+02 0.6237E+02 0.0000E+00
4 0.1470E+02 0.6000E+02 0.6237E+02 0.0000E+00
6. Solution Results (Nodes)
SOLUTION
INTERNAL NODES
NODE P(PSI) TF(F) Z RHO EM(LBM) QUALITY
(LBM/FT^3)
2 0.2290E+03 0.6003E+02 0.1186E-01 0.6241E+02 0.0000E+00 0.0000E+00
3 0.2288E+03 0.6003E+02 0.1185E-01 0.6241E+02 0.0000E+00 0.0000E+00

## Slide 18: OUTPUT DATA FILE
7. Solution Results (Branches)
BRANCHES
BRANCH KFACTOR DELP FLOW RATE VELOCITY REYN. NO. MACH NO. ENTROPY GEN. LOST WORK
(LBF-S^2/(LBM-FT)^2) (PSI) (LBM/SEC) (FT/SEC) BTU/(R-SEC) LBF-FT/SEC
12 0.000E+00 -0.214E+03 0.191E+03 0.219E+01 0.241E+06 0.183E-02 0.000E+00 0.000E+00
23 0.764E-03 0.193E+00 0.191E+03 0.156E+02 0.644E+06 0.130E-01 0.210E-03 0.848E+02
34 0.591E+00 0.214E+03 0.191E+03 0.156E+02 0.644E+06 0.130E-01 0.162E+00 0.657E+05
8. Convergence Information
***** TOTAL ENTROPY GENERATION = 0.163E+00 BTU/(R-SEC) ******
**** TOTAL WORK LOST = 0.120E+03 HP *****
SOLUTION SATISFIED CONVERGENCE CRITERION OF 0.100E-03 IN 6 ITERATIONS
TAU = 0.100000E+09ISTEP = 1

## Slide 19: SUMMARY
VTASC is a flow network model builder for use with GFSSP
Flow networks can be designed and modified interactively using a “Point and Click” paradigm
Generates GFSSP compatible input files
Winplot and MultiPlot can be activated from VTASC for post processing
User Subroutines can also be developed, compiled, and linked from VTASC