## Slide 1
Tutorial – 1 Simulation of Compressible Flow in a Converging-Diverging Nozzle

## Slide 2
Converging-Diverging Nozzle Geometry
Problem Considered:
One-dimensional pressure and temperature distribution
Flow rates in subsonic and supersonic flow
(This is a simplified version of Example 3 in the GFSSP User’s Manual)

## Slide 3
Program Options
Second Law Option
Input data file : tut1.dat
Output data file : tut1.out

## Slide 4
Program Options (cont.)
Activate INERTIA option globally
  This only means that the inertia term becomes selectable in the branches
  Leave DFLI box checked
Fluid is steam (water)

## Slide 5
Geometry
Branch Geometry
Branch | Area (in2)
12 | 0.3587
23 | 0.2243
34 | 0.1901
45 | 0.2255
56 | 0.3948
67 | 0.7633
78 | 1.2520
89 | 1.6286
Set restriction flow coefficient to 0.0 (isentropic – no friction)
Activate inertia term in each branch

## Slide 6
Geometry
Boundary Conditions
Node 1:
  P = 150 psia
  T = 1000 F
Node 9:
  P = 134 psia
  T = 1000 F*
*Note: We don’t know exit temperature a priori, but because GFSSP uses an upwind scheme for the energy equation, we only need a reasonable guess.

## Slide 7
Run five cases, gradually decreasing the exit pressure.
Results of Parametric Computations
Run | P9 (psia) | F (lbm/s)
1 | 134 | 
2 | 100 | 
3 | 60 | 
4 | 50 | 
5 | 45 | 
How does the choked flowrate compare to the hand-calculated value of 0.327 lbm/s?
How does the throat temperature (T4) compare to the hand-calculated value of 799 °F?

## Slide 8
Study of the Results
Study tut1.out to note the following facts:
  Pressure is decreasing from inlet to throat and increases from throat to exit in subsonic flow (Exit Pressure = 134 psia)
  Temperature follows a similar trend; temperature changes due to expansion and compression
  Entropy remains constant due to isentropic assumption
  With lower exit pressure, flow becomes supersonic in the diverging part and becomes subsonic with the formation of shock wave
  Flowrate remains constant with exit pressure once choked flow rate is reached

## Slide 9
If Time Permits…
Try re-running case 5 with “Energy by First Law”
  Flow rate is slightly different.
  Note that enthalpy (H) is constant, and temperatures remain nearly constant (994 – 1000 F). This is because GFSSP assumes stagnation enthalpy by default.
Now change “Enthalpy Formulation” to “Static” on Circuit Options page.
  Flow rate is slightly different.
  Now temperatures are changing, because the energy equation includes a velocity term.
  In GFSSP, temperatures are associated with nodes, but velocities are associated with branches, introducing some inaccuracy into the calculation of static enthalpies.
  For an isentropic high-speed flow model such as this, the Second Law option is convenient, as it avoids the difficulties of static vs. stagnation enthalpy.

## Slide 10
Challenge Problem 1
Simulation of a Water Distribution Network
Water at room temperature enters the flow network shown below at 50 psia and exits at the given boundary pressures. Each branch of the network is a commercial steel pipe with the dimensions given in the table. The relative roughness (e/D) of the pipes is 0.0018. Determine the mass flow rate of each of the branches.
Branch | Length(inches) | Diameter(inches)
12 | 120 | 6
25 | 2400 | 6
27 | 2400 | 5
57 | 1440 | 4
53 | 120 | 5
56 | 2400 | 4
64 | 120 | 4
68 | 1440 | 4
78 | 2400 | 4
89 | 120 | 5

## Slide 11
Challenge Problem 1
Simulation of a Water Distribution Network
How do your results compare to those determined by calculations using the Hardy Cross method of analyzing pipe networks? The Hardy Cross method assumes a constant friction factor for the network; GFSSP calculates a friction factor for each branch.
Branch | Flow Rate (lb/s) | 
 | Hardy-Cross | GFSSP
12 | 100.16 | 
25 | 63.59 | 
27 | 36.58 | 
53 | 44.43 | 
56 | 29.11 | 
57 | -9.93 | 
64 | 47.07 | 
68 | -17.99 | 
78 | 26.64 | 
89 | 8.66 |