## Slide 1: RESISTANCE & FLUID OPTIONS

## Slide 2: RESISTANCE OPTIONS
GFSSP can model flow in the following passages:
  Circular and non-circular pipes/ducts
  Flow through a restriction
  Thick and thin orifice
  Square expansion and reduction
  Rotating radial and annular ducts
  Labyrinth Seal
  Flow between closely spaced parallel plates (Face Seals)
  Common fittings and valves
  Pump characteristics
  Pump power
  Joule-Thompson device
  Control Valve
  Heat Exchanger Core
  Parallel Tube
  Compressible Orifice
  Fixed Flow
  Two-Dimensional Cartesian Grid

## Slide 3: Friction Term in GFSSP’s Momentum Equation
In classical fluid mechanics, pressure drop can be related to dynamic head by a dimensionless constant K:
GFSSP’s momentum equation expresses friction losses in terms of flow rate:
The relationship between K and Kf is:
Note that Kf is not dimensionless. It will have units of (lbf/ft2)/(lbm/s)2.

## Slide 4
RESISTANCE OPTION 1
For Re > 2300, Friction Factor calculated
from the Colebrook Equation:
Flow Resistance Factor Calculated from:
For Re < 2300, Friction Factor is:
PIPE FLOW

## Slide 5
RESISTANCE OPTION 2
In Classical Fluid Mechanics, Head Loss, H, is Expressed as:
K and CL are Related by:
If the User sets CL to 0, the code will set Kf to 0 (inviscid flow through the branch).
FLOW THROUGH A RESTRICTION

## Slide 6
RESISTANCE OPTION 3
Four cross-sections currently considered:
Poiseuille Number Relationship For Laminar Flow
Po = Cf Re
NON-CIRCULAR DUCT

## Slide 7
NON-CIRCULAR DUCT - CONTINUED
3. Use Effective Diameter & Reynolds Number
in Colebrook Equation:
Flow Resistance Factor Calculated from:
Laminar Flow (ReDh < 2300)
Reynolds Number based upon Hydraulic Diameter Dh (= 4A/P)
Turbulent Flow (ReDh > 2300)
1. Compute Effective Diameter
2. Compute Effective Reynolds Number
RESISTANCE OPTION 3 - CONTINUED

## Slide 8
RESISTANCE OPTION 4
Flow Resistance Factor:
PIPE FLOW WITH ENTRANCE AND EXIT LOSS

## Slide 9
RESISTANCE OPTION 5
Flow Resistance Factor:
Where:
THIN SHARP ORIFICE
Note: this branch is only for incompressible flow.

## Slide 10
RESISTANCE OPTION 6
Flow Resistance Factor:
Where:
THICK ORIFICE

## Slide 11
RESISTANCE OPTION 7
Flow Resistance Factor:
Where:
SQUARE REDUCTION

## Slide 12
RESISTANCE OPTION 8
Flow Resistance Factor:
Where:
SQUARE EXPANSION
Versions 603 and later have the capability to switch between Options 7 and 8 depending upon the flow direction

## Slide 13
RESISTANCE OPTION 9
Flow Resistance Factor:
Where:
ROTATING ANNULAR DUCT

## Slide 14
RESISTANCE OPTION 10
Flow Resistance Factor:
Where:
ROTATING RADIAL DUCT
Note: this branch only models the friction losses in the rotating duct. User must activate centrifugal term in momentum equation separately.

## Slide 15
RESISTANCE OPTION 11
Flow Resistance Factor (Modified Dodge Eqn):
Where:
a = Step Seal Factor (~0.9)
LABYRINTH SEAL

## Slide 16
RESISTANCE OPTION 12
Flow Resistance Factor:
FACE SEAL

## Slide 17
RESISTANCE OPTION 13
Flow Resistance Factor:
K1= K for the fitting at Re =1;
K = K for the fitting at Re = ; (K2 in GFSSP)
D = Internal diameter of attached pipe, in.
Where:
The Following Common Fittings and Valves Can Be Modeled using This Option:
45°, 90°, and 180° Elbows
(Std., Long, & Mitered)
Tees
Valves
(Screwed, Flanged/Welded,
Stub-in-Type)
(Gate/Ball/Plug, Globe [Std., Angle/Y-Type],
Diaphragm [Dam Type], Butterfly, Check
[Lift, Swing, Tilt])
Two-K Method
COMMON FITTINGS AND VALVES

## Slide 18
RESISTANCE OPTION 14
i
j
S
This Option Considers the Branch as a Pump with Given Characteristics. The Pump Characteristics are Expressed in the Pressure Rise:
Where:
Dp = Pressure Rise in lbf/ft2
.
m = Flow Rate in lbm/sec
The Momentum Source Used to Induce the Desired Flow is:
Dp
PUMP CHARACTERISTICS

## Slide 19
RESISTANCE OPTION 15
i
j
S
This Option Considers the Branch as a Pump with a Given Horsepower, P, and Efficiency, h.
The Momentum Source, S, used to Induce the Desired Flow is Expressed as:
PUMP POWER

## Slide 20
RESISTANCE OPTION 16
This Option Considers the Branch as a Valve with a Given Cv.
The Flow Resistance Factor for this Branch is Expressed as:
Cv
VALVE WITH GIVEN CV

## Slide 21
RESISTANCE OPTION 17
This option considers the branch as a Visco Jet which is a specific type of flow resistance with relatively large flow passages with very high pressure drops. The flow rate through the Visco Jet is given by:
Where: w = the flow rate in lbm/hr,
Lohm = the resistance of the fluid device ,
kv = an empirical factor,
S.G. = Specific Gravity,
x = the downstream fluid quality, calculated by the code
and Vf = the viscosity correction factor.
For this option, Kf can be expressed as:
VISCOJET (JOULE-THOMSON DEVICE)

## Slide 22
Pressure monitored at arbitrary point downstream of valve
Valve maintains pressure within user specified tolerance
  Closes when pressure exceeds maximum value
  Opens when pressure drops below minimum value
Flow resistance factor calculated using same equations as Option 2 (Restriction)
CONTROL VALVE
RESISTANCE OPTION 18

## Slide 23
Instantaneous - Valve is either fully open or fully closed at any given time.
Linear - Valve open/close transient is modeled as a linear operation.
Non-linear - Valve open/close transient is modeled as some user specified non-linear operation.
SUB-OPTIONS
RESISTANCE OPTION 18 - CONTINUED

## Slide 24
RESISTANCE OPTION 19
This option allows users to create a new resistance option that is not available in GFSSP library.
Once this option is chosen, user is required to supply the coding for calculating Kf for this option in the User Subroutine
In the preprocessor the user is required to supply the cross-sectional area of the branch.
User has the option of supplying up to six branch parameters via the preprocessor
U
User Defined

## Slide 25
RESISTANCE OPTION 20
Heat Exchanger Core
1
2
As – Wetted Surface Area
Ac – Minimum Free Flow Area
σ – Ratio of Free Flow Area to Frontal Area
Kc- Contraction Loss Coefficient
Ke- Expansion Loss Coefficient
Note: this branch only models the friction loss in the heat exchanger. Heat transfer can be modeled separately with a heat source or the heat exchanger advanced option.

## Slide 26
RESISTANCE OPTION 21
Parallel Tube
This option is an extended version of Resistance Option 1 where n is the numbers of parallel tubes
Assumes flow distribution is approximately uniform.

## Slide 27
RESISTANCE OPTION 22
Compressible Orifice
This option considers branch as an orifice for compressible flow
Flowrate is calculated from a simplified momentum equation
The input to this option is identical to branch option 2 (Restriction)
The flow will choke at the critical pressure ratio (Pdown/Pup):

## Slide 28
RESISTANCE OPTION 22
If :
If (choked flow):
=

## Slide 29
RESISTANCE OPTION 23
a = Step Seal Factor (~0.9)
LABYRINTH SEAL (EGLI Correlation)

## Slide 30
RESISTANCE OPTION 24
Fixed Flowrate
A new branch option has been introduced to fix flowrate in a given branch
The Fixed Flow branch can only be located adjacent to a Boundary Node
For unsteady option, a history file will be needed to specify flow rate and area at all time steps

## Slide 31
System Characteristics
Pump Characteristics
Operating Point
System Characteristics
Pump Characteristics
Operating Point
Algorithm for Fixed Flow Option(Schallhorn)

## Slide 32
RESISTANCE OPTION 25
Linear Cartesian Grid
Multi-dimensional flow calculation capability has been introduced
User can “Enable Grid Generation” under “Advanced” pull down menu option
This will make Linear Cartesian Grid available for drag and drop
By right clicking the image user will have the option to generate the grid

## Slide 33
Generation and display of Two-dimensional Cartesian Grid
Linear Cartesian Grid

## Slide 34: RESISTANCE OPTIONS SUMMARY
Most fluid systems can be modeled using available options
Option 2 can be used as a generic option where CL must be computed from a known pressure drop vs. flowrate characteristics.
User can add new resistance options by User Subroutines
Multi-Dimensional Grid Generation will be expanded to include Cylindrical Polar Co-ordinate

## Slide 35: FLUID OPTIONS
GFSSP requires the following thermodynamic and thermophysical properties of fluids for the solution of the governing equations:
  Density [r(T, p)]
  Absolute Viscosity [m(T, p)]
  Thermal Conductivity [k(T, p)]
  Specific Heat at Constant Pressure [Cp(T, p)]
  Ratio of Specific Heats [g(T, p)]
GFSSP requires these properties at every node at each iteration. These properties are supplied by thermodynamic property programs integrated into GFSSP.

## Slide 36: Integrated Fluid Property Programs
GASP/WASP
  Developed at NASA Glenn Research Center in 1970s
  Uses modified Benedict, Webb, & Rubin (BWR) Equation of State
  Fast and forgiving of out-of-range input
GASPAK
  Developed by Cryodata Inc. as an evolution of MIPROPS/NIST-12.
  Uses variable term Helmholtz equation
  Based on:
    National Institute of Standards and Technology (NIST)
    International Union of Pure & Applied Chemistry (IUPAC)
    National Standard Reference Data Service of the USSR
  Fairly fast, but unforgiving of out-of-range input

## Slide 37
AVAILABLE FLUIDS
ID Number | Gas | ID Number | Gas | ID Number | Gas
1 | GASP He | 51 | GASPAK He | 71 | GASPAK Xe
2 | GASP CH4 | 52 | GASPAK CH4 | 72 | GASPAK R-11
3 | GASP Ne | 53 | GASPAK Ne | 73 | GASPAK R-12
4 | GASP N2 | 54 | GASPAK N2 | 74 | GASPAK R-22
5 | GASP CO | 55 | GASPAK CO | 75 | GASPAK R-32
6 | GASP O2 | 56 | GASPAK O2 | 76 | GASPAK R-123
7 | GASP Ar | 57 | GASPAK Ar | 77 | GASPAK R-124
8 | GASP CO2 | 58 | GASPAK CO2 | 78 | GASPAK R-125
9 | GASP F2 | 59 | GASPAK H2 (para) | 79 | GASPAK R-134A
10 | GASP H2 (para) | 60 | GASPAK H2 (normal) | 80 | GASPAK R-152A
11 | WASP H2O | 61 | GASPAK H2O | 81 | GASPAK N2F3
12 | RP-1 Tables | 62 | GASPAK RP-1 (liq) | 82 | GASPAK NH3
 |  | 63 | GASPAK Isobutane | 84 | GASPAK H2O2
33 | Ideal Gas | 64 | GASPAK Butane | 86 | GASPAK Air
 |  | 65 | GASPAK Deuterium |  | 
37 | User Fluid 1 | 66 | GASPAK Ethane |  | 
38 | User Fluid 2 | 67 | GASPAK Ethylene |  | 
39 | User Fluid 3 | 68 | GASPAK H2S |  | 
 |  | 69 | GASPAK Kr |  | 
 |  | 70 | GASPAK Propane |  | 

## Slide 38
Provision of Using Fluid Not Available in Fluid Library
User can add fluids in the library by providing property tables.
Tables can be used with 1st Law (Enthalpy) energy formulation only.
GFSSP requires the following property tables:
  Thermal Conductivity
  Density
  Viscosity
  Specific Heat at Constant Pressure
  Specific Heat Ratio
  Enthalpy
  Entropy

## Slide 39
No. of Pressure points
No. of Temperature points
Read Statements :
READ(NRP1DAT,*) NP1,NT1
READ(NRP1DAT,*) (T1(J),J=1,NT1)
DO I = 1,NP1
READ (NRP1DAT,*) P1(I),(PHI1(I,J,K),J=1,NT1)
ENDDO

## Slide 40
Units of user-defined fluid tables:
Property | English Unit | SI Unit
P | psia | kPa
T | °R | K
k | BTU/ft-s-°R | W/m-K
r | lbm/ft3 | kg/m3
m | lbm/ft-s | N-s/m2
g | Dimensionless | Dimensionless
H | BTU/lbm | kJ/kg
S | BTU/lbm-°R | kJ/kg-K
Cp | BTU/lbm-°R | kJ/kg-K
To use SI units in fluid tables, SI units must also be enabled in VTASC
The GFSSP installation directory contains a folder with utility programs for converting table units and for converting a REFPROP output file to GFSSP format.

## Slide 41
Saturated Properties of User-Defined Fluids
The seven user-defined fluid property tables are not sufficient for modeling phase change.
The user has the option of adding an eighth file with saturated liquid and vapor properties as a function of saturation pressure.
The GFSSP installation directory contains a folder with utility programs for converting REFPROP saturation properties to GFSSP format.

## Slide 42
Format of the Saturated Property Table
Number of Saturation Pressures
Psat
Tsat
Hliq
rliq
Cpliq
mliq
gliq
kliq
Sliq
Hvap
rvap
Table continues with vapor Cp, m, g, k, and S

## Slide 43: OTHER FLUID OPTIONS
The Constant Property option allows the user to model a fluid with constant density and viscosity. The Energy equation is not solved if this option is used.
The Ideal Gas option allows the user to model an ideal gas with constant viscosity and specific heat.
GFSSP’s default ideal gas is air with viscosity and specific heat given at room temperature.

## Slide 44: USER-CODED FLUID
Beginning in v701, user subroutine PRPUSER allows the user to overwrite any or all fluid properties.
SUBROUTINE PRPUSER(I_GIVEN, I_NFLUID, Z_P, Z_T, Z_RHO, Z_H, Z_CP,
+ Z_CV, Z_S, Z_GAMMA, Z_MU, Z_K, I_KR, Z_XV,
+ Z_RHOL, Z_HL, Z_CPL, Z_CVL, Z_SL, Z_GAMMAL, Z_MUL, Z_KL,
+ Z_RHOV, Z_HV, Z_CPV, Z_CVV, Z_SV, Z_GAMMAV, Z_MUV, Z_KV)
C PURPOSE: ADD NEW FLUID PROPERTY
C I_GIVEN: Inputs are: (1) P/T (2) P/H (3) P/S (4) Psat/X

## Slide 45: USER-CODED FLUID
The user can choose to overwrite just one property (e.g., viscosity), or define a new fluid using their own Fortran-coded property package.
The installation directory includes instructions for calling REFPROP from the user subroutine. The user must have:
  REFPROP installed
  A Fortran compiler (Intel, Compaq, or G95)
Testing has shown that REFPROP agrees well with GASP/WASP, but that models run much slower.

## Slide 46: FLUID OPTIONS SUMMARY
GFSSP considers both gas and liquid as real fluid; liquid is also modeled as compressible fluid.
GASP/WASP/GASPAK provide higher order equation of state to calculate properties of liquid and vapor state over a wide range.
Table look-up provision or user-supplied Fortran code can be used to add new fluid to the library.
The Constant Property and Ideal Gas options can also be used.