## Slide 1
Tutorial – 2 SIMULATION OF FLUID TRANSIENT FOLLOWING SUDDEN VALVE CLOSURE
400 ft
D
= 0.25 inch

## Slide 2
FLUID TRANSIENT SCHEMATIC
Problem Considered:
Time dependent Pressure and Flow rate history during and after valve closure
400 ft
D = 0.25 inch
Liquid Oxygen at 500 psia and 200 R
Flowrate = 0.1 lb/s
Valve closes in 100 milliseconds
450 psia

## Slide 3
Input File: Tut2.dat
Output File: Tut2.out
Check Save Information to save the steady-state solution in the restart files
Fluid is LOx
Part 1: Build Steady State Model

## Slide 4
Build the model on the canvas
Set boundary conditions
Set pipe and restriction parameters
  Assume smooth pipe (ε=0)
Part 1: Build Steady State Model (cont.)

## Slide 5
Run the steady state model
Check that the flowrate is ≈0.1 lbm/s
Note that the results have been saved in the restart files
Part 1: Build Steady State Model (cont.)

## Slide 6
Convert the model to transient
  Time step = 0.02 s
  Run time = 1.0 s
  Check Valve Open/Close Unsteady Option
Part 2: Build Transient Model
  Check Transient Term Active on Circuit Options page

## Slide 7
  Uncheck SAVE restart file box
  Check READ restart file box
  Check Winplot output
  Create history files for both boundary nodes
Part 2: Build Transient Model (cont.)

## Slide 8
Open the Valve Open/Close dialog box from the Advanced menu
To represent the valve closing, the area of Branch 67 will vary as a function of time
Type the name of the valve history file in the dialog box, then press the “e” button to edit
Time (Sec)
Area (in2)
0.00
0.0491
0.02
0.0164
0.04
0.00545
0.06
0.00182
0.08
0.00061
0.10
0.00
Valve Closure History
Part 2: Build Transient Model (cont.)
Don’t forget to click “Accept”!

## Slide 9
Pressure History at Valve

## Slide 10
STUDY OF THE RESULTS
Plot pressure and flowrate history
  Peak pressure approximately 620 psia
Estimate the predicted period of oscillation and compare with the following formula
  Period of Oscillation = 4L/a
  Where L = length of the pipe = 400 ft
  And a = Speed of sound = 2462 ft/sec for LOX
Plot density (RHO6) and compressibility (Z6) history and note variation of compressibility with time

## Slide 11
Challenge Problem 2
Draining a Water Heater
An insulated, electrically heated water heater contains 190 kg of liquid water at 60 °C when a power outage occurs. If water is withdrawn from the heater tank at a steady rate of 0.2 kg/s, how long will it take for the temperature of the water in the tank to drop from 60 to 35 °C? Assume that cold water enters the tank at 10 °C, and that the tank is well insulated.
Fixed flow 0.2 kg/s
A = 5 cm2
Exit restriction
A = 5 cm2, CL = 1.0
Cold Water Source, 10 °C
Water heater, initially 60 °C,
Volume 0.193 m3

## Slide 12
Challenge Problem 2
Draining a Water Heater
Hints:
  SI units can be enabled from the Advanced menu. When entering parameters, you may need to multiply or divide by some power of 10.
  The Fixed Flow branch option can be used to specify the flow rate in this simple system. A reasonable pressure value may be assumed at the boundaries (e.g. 101.3 kPa). The Fixed Flow branch will then act as a pump to raise the driving pressure enough to maintain the specified flow rate of 0.2 kg/s.
  This problem is Example 7.3 of Introduction to Chemical Engineering Thermodynamics, 5th ed. by Smith et al. The answer given in the text is 658.5 seconds, assuming constant properties. How does GFSSP’s answer compare?