## Slide 1: MATHEMATICAL FORMULATION
Node
j = 1
m
ji
.
Node
j = 3
m
ij
.
Node
j = 2
m
ij
.
Node
j = 4
m
ji
.
m
ji
.
m
ij
.
=
-
Single
Fluid
k = 1
Single
Fluid
k = 2
Fluid
Mixture
Fluid
Mixture
Node
i

## Slide 2: Content
Finite Volume Procedure
Mathematical Closure
Governing Equations
Solution Procedure

## Slide 3
Finite Volume Procedure Basics
The Finite Volume Procedure for a fluid network is an extension of single control volume analysis of mass and energy conservation in classical thermodynamics.
Control Volume Analysis
in Classical Thermodynamics
Finite Volume Analysis in Fluid Network

## Slide 4
Finite Volume Procedure Basic Components
Development of governing equations describing the conservation of mass, momentum and energy of fluid and conservation of thermal energy of solid in contact fluid
Use of accurate thermodynamic and thermo-physical properties of fluid and material properties in development of the governing equations
Numerical Solution of the governing equations by an iterative method

## Slide 5
MATHEMATICAL CLOSURE
Problem of a Steady State Flow Network
Given : Pressures and Temperatures at Boundary Nodes
Find : Pressures and Temperatures at Internal Nodes and Flowrates in Branches
Primary Variables
Secondary Variables

## Slide 6
MATHEMATICAL CLOSURE
Problem of an Unsteady Flow Network
Given : Pressures and Temperatures at Boundary Nodes and Initial Values at Internal Nodes
Find : Pressures and Temperatures at Internal Nodes and Flowrates in Branches with Time.
Primary Variables
Secondary Variables

## Slide 7
MATHEMATICAL CLOSURE
Problem of an Unsteady Flow with Conjugate Heat Transfer
Given : Pressures and Temperatures at Boundary Nodes and Initial Values at Internal Fluid Nodes and Solid Nodes
Find : Pressures and Temperatures at Internal Nodes and Flowrates in Branches with Time.
Primary Variables
Secondary Variables

## Slide 8
Mathematical Closure
Unknown Variables Available Equations to Solve
1. Pressure 1. Mass Conservation Equation
2. Flowrate 2. Momentum Conservation Equation
3. Fluid Temperature 3. Energy Conservation Equation of Fluid
4. Solid Temperature 4. Energy Conservation Equation of Solid
5. Species Concentration 5. Conservation Equations for Mass Fraction of Species
6. Mass 6. Thermodynamic Equation of State

## Slide 9
MATHEMATICAL CLOSURE
Secondary Variables:
Thermodynamic & Thermophysical Properties
Unknown Variable Available Equations to Solve
Density
Specific Heats Equilibrium Thermodynamic Relations
Viscosity [GASP, WASP & GASPAK Property Programs]
Thermal Conductivities
Friction Factor Empirical Relations
Heat Transfer Coefficients

## Slide 10: GOVERNING EQUATIONS
Mass Conservation
Momentum Conservation
Energy Conservation of fluid
Energy Conservation of solid
Fluid Species Conservation
Equation of State
Mixture Property

## Slide 11
MASS CONSERVATION EQUATION
Node
j = 1
m
ji
.
Node
j = 3
m
ij
.
Node
j = 2
m
ij
.
Node
j = 4
m
ji
.
m
ji
.
m
ij
.
=
-
Single
Fluid
k = 1
Single
Fluid
k = 2
Fluid
Mixture
Fluid
Mixture
Node
i
GOVERNING EQUATIONS
Note : Pressure does not appear explicitly in Mass Conservation Equation although it is earmarked for calculating pressures

## Slide 12
MOMENTUM CONSERVATION EQUATION
i
j
g
q
w
r
i
r
j
.
m
ij
Axis of Rotation
Branch
Node
Node
GOVERNING EQUATIONS
Represents Newton’s Second Law of Motion
Mass X Acceleration = Forces
Unsteady
Longitudinal Inertia
Transverse Inertia
Pressure
Gravity
Friction
Centrifugal
Shear Stress
Moving Boundary
Normal Stress
External Force

## Slide 13
MOMENTUM CONSERVATION EQUATION
Mass X Acceleration Terms in GFSSP
Unsteady
Longitudinal Inertia
Transverse Inertia
i
j

## Slide 14
MOMENTUM CONSERVATION EQUATION
Force Terms in GFSSP
Pressure
Gravity
Friction
Centrifugal
i
j
g
q
w
r
i
r
j
.
m
ij
Axis of Rotation
Branch
Node
Node

## Slide 15
MOMENTUM CONSERVATION EQUATION
Force Terms in GFSSP
Shear Stress
i
j
u
d
Normal Stress
Moving Boundary

## Slide 16
ENERGY CONSERVATION EQUATION
k = 2
Node
j = 1
m
ji
.
Node
j = 3
m
ij
.
Node
j = 2
m
ij
.
Node
j = 4
m
ji
.
m
ji
.
m
ij
.
=
-
Single
Fluid
k = 1
Single
Fluid
Fluid
Mixture
Fluid
Mixture
Node
i
GOVERNING EQUATIONS
  Energy Conservation Equation can be written in Enthalpy or Entropy
Enthalpy Equation
Rate of Increase of Internal Energy =
Enthalpy Inflow - Enthalpy Outflow + Heat Source
Based on Upwind Scheme
Note: J = 778.17 ft-lbf/BTU

## Slide 17
ENERGY CONSERVATION EQUATION
k = 2
Node
j = 1
m
ji
.
Node
j = 3
m
ij
.
Node
j = 2
m
ij
.
Node
j = 4
m
ji
.
m
ji
.
m
ij
.
=
-
Single
Fluid
k = 1
Single
Fluid
Fluid
Mixture
Fluid
Mixture
Node
i
GOVERNING EQUATIONS
Entropy Equation
Rate of Increase of Entropy =
Entropy Inflow - Entropy Outflow +
Entropy Generation + Entropy Source

## Slide 18
Boundary Node
Internal Node
Branches
Solid Node
Ambient Node
Conductor
Solid to Solid
Solid to Fluid
Solid to Ambient
Solid – Fluid Network for Conjugate Heat Transfer

## Slide 19
Energy Conservation for Solid Node
Conservation Equation
Successive Substitution Form
Solid Node
Ambient Node
Fluid Node

## Slide 20
Heat Transfer Coefficient
Dittus-Boelter Equation for Single Phase
Modified Miropolski Correlation for Two-Phase Flow

## Slide 21
FLUID SPECIES CONSERVATION EQUATION
k = 2
Node
j = 1
m
ji
.
Node
j = 3
m
ij
.
Node
j = 2
m
ij
.
Node
j = 4
m
ji
.
m
ji
.
m
ij
.
=
-
Single
Fluid
k = 1
Single
Fluid
Fluid
Mixture
Fluid
Mixture
Node
i
GOVERNING EQUATIONS
Rate of Increase of Fluid Species =
Fluid Species Inflow - Fluid Species Outflow +
Fluid Species Source

## Slide 22
GOVERNING EQUATIONS
EQUATION OF STATE
For unsteady flow, resident mass in a control volume is calculated
from the equation of state for a real fluid
Z is the compressibility factor determined from
higher order equation of state

## Slide 23
Liquid-Vapor Mixtures
GOVERNING EQUATIONS
If the enthalpy at a given pressure is under the saturation dome, the fluid is considered to be a homogeneous liquid-vapor mixture with a quality (vapor mass fraction).
Saturated fluid properties will be quality-weighted averages of the liquid and vapor properties.

## Slide 24
GOVERNING EQUATIONS
Mixture Property Relations
Mixture Density
Amagat’s Law of Partial Volumes
  GFSSP’s default
  Suitable for liquids and most gas mixtures

## Slide 25
GOVERNING EQUATIONS
Mixture Property Relations
Mixture Density
Dalton’s Law of Partial Pressures
  Activated on Circuit Options page
  Properties are evaluated at the partial pressure of the gas
  Appropriate for gas mixtures at temperatures where at least one gas would be a liquid at the total pressure

## Slide 26
GOVERNING EQUATIONS
Mixture Property Relations
Mixture Density
Example of when Dalton’s Law of Partial Pressures would be appropriate
  Mixture of 76 mol% O2 and 24 mol% He at 45 psia, -277.7 °F
  At total pressure of 45 psia, O2 is a liquid
  At partial pressure of 34.2 psia, O2 is a gas
 | Amagat’s Law | Dalton’s Law
ρO2 (lb/ft3) | 57.73 | 0.5946
ρHe (lb/ft3) | 0.0918 | 0.0221
ρmix (lb/ft3) | 2.336 (Incorrect!) | 0.6167

## Slide 27
GOVERNING EQUATIONS
Mixture Property Relations
Thermophysical Properties
Viscosity, Specific Heat, and Specific Heat Ratio are calculated
by taking Molar Average
Compressibility Factor

## Slide 28
GOVERNING EQUATIONS
Mixture Property Relations
Temperature
Limitations
Cannot handle phase change of mixture
Assumes specific heats are relatively constant
GFSSP’s default is to calculate mixture temperature from a modified Energy Conservation Equation using specific heat instead of enthalpy

## Slide 29: GOVERNING EQUATIONS Summary
Familiarity with GFSSP’s Governing Equations is not absolutely necessary to use the code
However, working knowledge about Governing Equations is helpful to implement various options in a complex flow network
A good understanding of Governing Equations is necessary to introduce new physics in the code

## Slide 30: SOLUTION PROCEDURE
Successive Substitution
Newton-Raphson
Simultaneous Adjustment with Successive Substitution (SASS)
Program sequence
Convergence
Sparse Matrix Solver
Time Step
Relaxation Parameters
Troubleshooting

## Slide 31
SOLUTION PROCEDURE
Non linear Algebraic Equations are solved by
  Successive Substitution
  Newton-Raphson
GFSSP uses a Hybrid Method
  SASS ( Simultaneous Adjustment with Successive Substitution)
  This method is a combination of Successive Substitution and Newton-Raphson

## Slide 32
SUCCESSIVE SUBSTITUTION METHOD
STEPS:
1. Guess a solution for each variable in the system of equations
2. Express each equation such that each variable is expressed in terms of other variables: e. g. X = f (Y,Z) and Y = f (X,Z) etc
3. Solve for each variable
4. Under-relax the variable, if necessary
5. Repeat steps 1 through 4 until convergence
ADVANTAGES:
Simple to program; takes less computer memory
DISADVANTAGES:
It is difficult to make a decision in which order the equations must be solved to ensure convergence
SOLUTION PROCEDURE

## Slide 33
NEWTON-RAPHSON METHOD
STEPS:
1. Guess a solution for each variable in the system of equations
2. Calculate the residuals of each equation
3. Develop a set of correction equations for all variables
4. Solve for the correction equations by Gaussian Elimination method
5. Apply correction to each variable
6. Iterate until the corrections become very small
ADVANTAGES:
No decision making process is involved to determine the order in which equations must be solved
DISADVANTAGES:
Requires more computer memory; difficult to program.
SOLUTION PROCEDURE

## Slide 34
SASS (Simultaneous Adjustment with Successive Substitution) Scheme
SOLUTION PROCEDURE

## Slide 35
GFSSP Solution Scheme
SASS : Simultaneous Adjustment with Successive Substitution
Approach : Solve simultaneously when equations are strongly coupled and non-linear
Advantage : Superior convergence characteristics with affordable computer memory
Mass
Momentum
Energy
Specie
State
Simultaneous
Successive Substitution

## Slide 36
Solution Procedure
Mass Conservation
Momentum
Conservation
Energy Conservation
Equation of State
Heat Conduction
Thermodynamic Property
Mass & Momentum conservation equations and equation of state are solved simultaneously by Newton-Raphson method
Energy & Species conservation equations are solved by successive substitution method
This hybrid practice reduces code overhead while maintains superior convergence characteristics

## Slide 37
Start
READIN - Reads input data from data file generated by VTASC
INIT – Generate Trial Solution
GASP & Wasp or GASPAK – A routine for thermodynamic properties
Obtain a trial solution
Simultaneous (S) solution of pressure, flowrate, and resident maas
NEWTON – Controls the iteration loop of Newton-Raphson scheme
COEF – Constructs the coefficient matrix of the correction equation
SOLVE – Solve correction equation by Gaussian elimination method
UPDATE – After applying corrections update each variable (11)
Successive Substitution (SS) solution of enthalpy & concentration
ENTHALPY – Solves enthalpy by SS method
MASSC – Solves concentration by SS method
Calculate flow resistances
RESIST – Calculates resistances for all branches
DENSITY – Calculates density and other properties
GASP & Wasp or GASPAK – A routine for thermodynamic properties
KFACT1 – KFACT21 Calculates branch resistances
Convergence check
Iteration loop
EQNS – Calculates residuals of three governing equations
Mass conservation
Momentum Conservation
Equation of State
Energy Conservation
Species Conservation
BOUND – Supply Time-dependant boundary conditions
Solution of Temperature of Solid
TSOLID or TSOLIDNR – Solves temperature by SS or S method
Solid Temperature
repeated for each time step
Flow Chart of Solution Algorithm

## Slide 38
Solution of the governing equations involves following steps:
Subdivide the flow domain into fluid nodes and branches
Subdivide the solid domain into solid nodes and conductors
Connect the solid and fluid nodes with solid to fluid conductors
At each fluid node solve mass and energy conservation equation to calculate pressure (p) and enthalpy (h) of fluid and equation of state to compute resident mass (mR) of fluid
Solution Procedure

## Slide 39: Solution Procedure
5. At each fluid branch, solve momentum conservation equations to calculate flow rate ( )
6. From pressure and enthalpy, calculate fluid temperature (TF) and all other thermo-dynamic and thermo-physical properties required in governing equations
7. At each solid node, solve energy conservation equation to calculate temperature of the solid node (TS)
8. Steps 4 through 7 are repeated until convergence
9. Steps 4 through 8 are repeated for each time step

## Slide 40: CONVERGENCE
Numerical solution can only be trusted when fully converged
GFSSP’s convergence criterion is based on difference in variable values between successive iterations. Normalized Residual Error is also monitored
GFSSP’s solution scheme has two options to control the iteration process
  Simultaneous (SIMUL = TRUE)
  Non-Simultaneous (SIMUL = FALSE)

## Slide 41: CONVERGENCE
Simultaneous Option
Single Iteration Loop
  First solve mass, momentum and equation of state by the Newton-Raphson (NR) scheme
  Next solve energy and species conservation equations by Successive Substitution (SS) scheme
  Solution is converged when the normalized maximum correction, max is less than the convergence criterion

## Slide 42: CONVERGENCE
Non-Simultaneous Option
Inner & Outer Iteration Loop
  Mass, Momentum and Equation of state is solved in inner iteration loop by NR scheme
  Energy and Species conservation equations are solved in outer iteration loop by SS scheme
  Convergence of NR scheme is determined by
  Convergence of SS scheme is determined by
max
etc.

## Slide 45: Sparse Matrix Solver
In numerical analysis, a sparse matrix is a matrix in which most of the elements are zero
GFSSP uses matrix method (Gaussian Elimination) to solve the system of correction equations while using N-R method
For large network models, the matrices are usually more sparse
There are iterative and direct methods of solving sparse matrices. GFSSP uses direct method
Sparse matrix solver eliminates multiplications of zero elements and saves processing time

## Slide 46
New Solver Options

## Slide 47: Performance of Sparse Matrix Solver
Problem Description | No. of internal nodes | No. of branches | No. of time steps | CPU time (sec) (non-sparse) | CPU time (sec) (sparse) | % saving
Tank Pressurization (Example 12) | 59 | 64 | 892 | 2214 | 1108 | 50
Transfer Line Chilldown (Example 14) | 31 | 32 | 16000 | 1166 | 1044 | 11
Tank self-pressurization due to boil-off (Example 29) | 6 | 13 | 498500 | 8902 | 8677 | 3
Arc Jet Facility model (LaRC/Hass) | 161 | 238 | 600 | 66443 | 9687 | 85

## Slide 48
Arc Jet Facility model (LaRC/Hass)
An Example where Sparse Matrix Solver brings down solution time by 85%

## Slide 49: Time Step
Systems of differential equations can be solved by explicit or implicit methods.
Explicit methods
  Easier to program
  Time step must be kept small for numerical stability
  Not always easy to determine stable time step a priori
Implicit methods
  Numerically stable regardless of time step
  May still require a small time step for solution accuracy

## Slide 50: Time Step (cont.)
GFSSP uses an implicit solver.
In theory, the solver is numerically stable at any time step.
In practice, negative temperatures and/or pressures will crash the property packages, so very large time steps may not run.
It is still the user’s responsibility to verify time step independence of the solution.
For example, if you have a model running stably with a 0.1 sec time step, make an additional run with a time step of 0.05 sec and compare the solutions of the two runs.

## Slide 51: Non-linearity & Under-relaxation
Under-relaxation is necessary to solve non-linear equations
Let us try to solve a simple non-linear equation:
We can rewrite the equation as:
Suppose , therefore
If we substitute , we get
The solution will oscillate between 2 and 8, will never reach the correct answer
Let us use Under-relaxation of 0.5
Iteration No. 1:
Iteration No.2: = 3.2;
Iteration No.3: = 3.902;

## Slide 52: Relaxation Parameters
GFSSP provides several relaxation parameters to reduce the size of the corrections to the solution variables.
This can prevent the solution “running away” to outrageous values.
However, it can also increase the time needed for the solution to converge.
In general, explicit under-relaxation is employed. The relaxation parameter multiplies the calculated correction by the relaxation parameter before applying it.
For example, if the relaxation parameter is 0.6, only 60% of the calculated correction will be applied in each iteration.

## Slide 53: Relaxation Parameters (cont.)
RELAXNR
  Under-relaxes the Newton-Raphson solver for the mass and momentum equations solving for pressures and flow rates.
  Generally the most effective relaxation parameter on the solution.
RELAXK
  Under-relaxes the change in the factor Kf used in the friction term of the momentum equation.
  May be useful if the model has elements with large swings in Kf; for example, a valve opening and closing.

## Slide 54: Relaxation Parameters (cont.)
RELAXH
  Under-relaxes the change in enthalpy or entropy between iterations.
  If using 1st Law, enthalpy uses inertial relaxation. Weight (or inertia) is given to the enthalpy from the previous iteration. Larger values of RELAXH will apply more relaxation. This is different from the other relaxation parameters.
  If using 2nd Law, entropy is explicitly under-relaxed (i.e., setting RELAXH to 0.6 will apply 60% of the correction).
  The energy equation is fairly linear and usually well-behaved. Problems are most often caused by bad inputs (pressures and/or flow rates) from the solution of the mass and momentum equations. Therefore, RELAXNR is more likely to fix the energy equation than RELAXH.

## Slide 55: Relaxation Parameters (cont.)
RELAXD
  Under-relaxes the change in fluid density between iterations.
  Already set to 0.5 by default. Generally does not need further reduction.
RELAXHC
  Under-relaxes the change in calculated convection coefficient between iterations.
RELAXTS
  Under-relaxes the change in solid temperature between iterations.

## Slide 56: Troubleshooting
Check that input parameters are correct and make sense
Try under-relaxation (especially RELAXNR)
Change time-step
Tighten convergence criteria
Try non-simultaneous solution
If steady-state model won’t converge, convert it to a transient and let it run to steady-state
If a model converges with less severe boundary conditions, try using that solution in a restart file to provide an initial guess
Contact the developers for help

## Slide 57: SOLUTION PROCEDURE Summary
Simultaneous option is more efficient than Non-Simultaneous option
Non-Simultaneous option is recommended when Simultaneous option experiences numerical instability
Non-linearity and strong coupling need under-relaxation
Good initial guess help to overcome convergence problem
A lack of realism in problem specification can lead to convergence problem
Lack of realism includes:
  Unrealistic geometry and/or boundary conditions
  Attempt to calculate properties beyond operating range