## Slide 1: Tank Pressurization, Control Valves, and Relief Valves

## Slide 2: Content
Tank Pressurization
Control Valve
Relief Valve

## Slide 3: TANK PRESSURIZATION
Predict the ullage conditions considering heat and mass transfer between the propellant and the tank wall
Predict the propellant conditions leaving the tank

## Slide 4: TANK PRESSURIZATION ADDITIONAL PHYSICAL PROCESSES
Change in ullage and propellant volume.
Change in gravitational head in the tank.
Heat transfer from pressurant to propellant.
Heat transfer from pressurant to the tank wall.
Heat conduction between the pressurant exposed tank surface and the propellant exposed tank surface.
Mass transfer between the pressurant and propellant (with user subroutine).

## Slide 5: TANK PRESSURIZATION MATHEMATICAL MODELING OF PHYSICAL PROCESSES -1
Change in Ullage and Propellant Volume
Conservation Equation of Volume

## Slide 6: TANK PRESSURIZATION MATHEMATICAL MODELING OF PHYSICAL PROCESSES -2
Change in Gravitational Head in the Tank
Heat Transfer from Ullage to Propellant
Heat Transfer Coefficient (Natural Convection)

## Slide 7: TANK PRESSURIZATION MATHEMATICAL MODELING OF PHYSICAL PROCESSES -3
Heat Transfer from Ullage to Wall
Tank Wall Conduction
Energy Balance on Tank Wall

## Slide 8: TANK PRESSURIZATION MATHEMATICAL MODELING OF PHYSICAL PROCESSES -4
Mass Transfer from Propellant to Ullage
With optional user subroutine
Heat of vaporization (hfg) and saturation temperature (Tsat) determined at current ullage pressure by calling utility subroutine PROPS_PSAT.

## Slide 9: TANK PRESSURIZATION CALCULATION STEPS
For each time step calculate
Ullage and Propellant Volumes
Tank Bottom Pressure
Heat Transfer between pressurant and propellant and pressurant and wall
Wall Temperature
Mass Transfer from propellant to ullage (only with optional user subroutine)

## Slide 10
TANK PRESSURIZATION
EXAMPLE 10 TANK SCHEMATIC AND GFSSP MODEL

## Slide 11
Additional Input for Pressurization Option

## Slide 12
TANK PRESSURIZATION
EXAMPLE 10 PRESSURIZATION OUTPUT
SOLUTION
INTERNAL NODES
NODE P(PSI) TF(F) Z RHO EM(LBM) CONC
(LBM/FT^3)
HE O2
2 0.9138E+02 -0.1347E+03 0.1006E+01 0.1047E+00 0.5144E+01 0.9690E+00 0.0310
4 0.9869E+02 -0.2640E+03 0.2310E-01 0.6514E+02 0.2937E+05 0.0000E+00 1.0000
BRANCHES
BRANCH KFACTOR DELP FLOW RATE VELOCITY REYN. NO. MACH NO. ENTROPY GEN. LOST WORK
(LBF-S^2/(LBM-FT)^2) (PSI) (LBM/SEC) (FT/SEC) BTU/(R-SEC) LBF-FT/SEC
12 0.238E+05 0.362E+01 0.148E+00 0.445E+03 0.156E+06 0.129E+00 0.281E-02 0.127E+04
34 0.000E+00 0.000E+00 0.163E+03 0.899E-01 0.412E+06 0.114E-03 0.000E+00 0.000E+00
45 0.263E+00 0.487E+02 0.163E+03 0.253E+02 0.690E+07 0.323E-01 0.115E+00 0.176E+05
NUMBER OF PRESSURIZATION SYSTEMS = 1
NODUL NODPRP QULPRP QULWAL QCOND TNKTM VOLPROP VOLULG
2 4 1.9642 8.5069 0.0022 196.4447 450.8641 49.1359
SOLUTION SATISFIED CONVERGENCE CRITERION OF 0.100E-02 IN 5 ITERATIONS
TAU = 10.0000 ISTEP = 100
Tank Output Units
QULPROP, Btu/s
QULWAL, Btu/s
QCOND, Btu/s
TNKTM, deg. R
VOLPROP, ft3
VOLULG, ft3

## Slide 13
TANK PRESSURIZATION
EXAMPLE 10 ULLAGE AND TANK BOTTOM PRESSURE HISTORY
Ullage
Tank Bottom

## Slide 14
TANK PRESSURIZATION
EXAMPLE 10 ULLAGE AND TANK WALL TEMPERATURE HISTORY
Tank Wall
Ullage Gas

## Slide 15: TANK PRESSURIZATION EXAMPLE 10 PROPELLANT TO ULLAGE MASS TRANSFER RATE HISTORY

## Slide 16
TANK PRESSURIZATION
COLLAPSE FACTOR CORRELATION
The collapse factor is the ratio of actual pressurant consumption to an ideal pressurant consumption which assumes no heat or mass transfer. It is represented by the following formula (Epstein correlation).

## Slide 17
TANK PRESSURIZATION
COLLAPSE FACTOR CORRELATION DEFINITIONS
C - ratio of wall to gas thermal capacitance
p1-p8 - fitted constants dependent on propellant
Q - ratio of ambient heat input to effective thermal capacitance of gas
S - modified Stanton number
T0 - pressurant inlet temperature
Ts - propellant saturation temperature at initial tank pressure
- ideal pressurant mass consumption

## Slide 18
TANK PRESSURIZATION
PRESSURIZATION MODEL VALIDATION
GFSSP Collapse Factor Prediction: 1.46
Epstein Correlation Collapse Factor Prediction: 1.51
GFSSP Prediction Discrepancy: -3.3%

## Slide 19: TANK PRESSURIZATION SUMMARY
GFSSP’s transient capability further extended to model the pressurization of a propellant tank
User activates this option and supplies additional tank information
Code predicts the history of ullage and propellant conditions
Example 10 illustrates the use of this option and also describes the verification of the numerical prediction

## Slide 20: CONTROL VALVE
Pressure monitored at arbitrary point downstream of valve
Valve maintains pressure within user specified tolerance
  Closes when pressure exceeds maximum value
  Opens when pressure drops below minimum value
Flow resistance factor calculated using same equations as Option 2

## Slide 21: CONTROL VALVE SUB-OPTIONS
Instantaneous - Valve is either fully open or fully closed at any given time.
Linear - Valve open/close transient is modeled as a linear operation.
Non-linear - Valve open/close transient is modeled as some user specified non-linear operation.

## Slide 22: CONTROL VALVE BRANCH INPUTS -1
Sub-option
Flow Coefficient (CL)
Area (A)
Control Node
Valve Initial Position
Pressure Tolerance File Name

## Slide 23: CONTROL VALVE BRANCH INPUTS -2
Linear Sub-option
  Time to open/close
  Number of steps to open/close
Non-linear Sub-option
  Open characteristics file name
  Close characteristics file name

## Slide 24: CONTROL VALVE EXAMPLE 12 SCHEMATIC

## Slide 25: CONTROL VALVE EXAMPLE 12 VTASC CANVAS

## Slide 26: CONTROL VALVE EXAMPLE 12 PROPELLANT TANK PRESSURE HISTORY
LOx Tank Ullage
LOx Tank Bottom
RP-1 Tank Bottom
RP-1 Tank Ullage

## Slide 27: CONTROL VALVE EXAMPLE 12 LOX TEMPERATURE HISTORY
LOx Tank Wall
LOx Tank Ullage

## Slide 28: CONTROL VALVE EXAMPLE 12 HELIUM FLOW RATE HISTORY
To LOx Tank
To RP-1 Tank
To Engine

## Slide 29
APPLICATIONS – Tank Pressurization
LOX Tank
RP-1 Tank
Engine
Interface

## Slide 30
Comparison of LOX Ullage Pressure with Test Data
Engine Cut
APPLICATIONS – Tank Pressurization

## Slide 31: CONTROL VALVE SUMMARY
New Branch Resistance Option added to GFSSP to model a Control Valve
Valid only for transient models
User provides the flow and operational characteristics of the valve
Example 12 demonstrates the operation of the control valve option in GFSSP

## Slide 32: RELIEF VALVE
Distinct from Control Valve
Monitors pressure differential across valve branch
Valve opens when pressure differential exceeds cracking pressure
Can also be used as a check valve if small cracking pressure is used.
Relief valve is an Advanced Option that may be linked to:
  Restriction
  Compressible orifice
  Valve with Cv

## Slide 33: RELIEF VALVE INPUTS
Branch ID number
Valve cracking pressure differential (psid)
Control file determines valve branch flow resistance as function of pressure differential

## Slide 34: RELIEF VALVE CONTROL FILE
Number of lines
Reseating pressure (psid)
Fully-open pressure (psid)
Area (in2) or Cv

## Slide 35: CONTROL VALVE EXAMPLE 24 VTASC CANVAS
Air Supply
35 psia
Tank
10 ft3
Ambient
14.7 psia

## Slide 36: RELIEF VALVE EXAMPLE 24 Tank Pressure History

## Slide 37: RELIEF VALVE EXAMPLE 24 Flow Rate History

## Slide 38: RELIEF VALVE SUMMARY
New Advanced Option added to GFSSP to model a Relief Valve
Valid only for transient models
User provides the cracking pressure and flow resistance characteristics of the valve
Example 24 demonstrates the operation of the relief valve option in GFSSP