## Slide 1
Tutorial – 3 Valve-Controlled Pressurization of a Propellant Tank

## Slide 2
Problem Elements:
Control tank pressure within a specified tolerance
  Use control valve branch option
Use tank pressurization advanced option
Use 2 fluids (oxygen and helium)

## Slide 3
User Information:
  Input File: Tut3.dat
  Output File: Tut3.out
Unsteady Options
  Time step = 0.1 s
  Final time = 200 s
  Check Tank Pressurization option
Set Up Options

## Slide 4
Output Control
  Select Winplot binary output
Set Up Options
Fluid Options
  Select Oxygen first
  Then select Helium

## Slide 5
Build Model on Canvas
He Supply
Control valve
Orifice
Ullage space
Pseudo-boundary
(Pressure on propellant surface)
Pseudo-branch
(Propellant surface)
Propellant
Orifice
Exit boundary

## Slide 6
Node 1 is the helium supply
  P = 95 psia, T = 120 °F
  LO2 mass fraction = 0.0
  He mass fraction = 1.0
Node 4 is a pseudoboundary node
  It separates the He from the LO2
  History file is required, but pressure will be overwritten by Node 3 ullage pressure plus propellant head
  P = 74.76 psia, T = -300 °F
  LO2 mass fraction = 1.0
  He mass fraction = 0.0
Node 6 is the LO2 exit boundary
  P = 50 psia, T = -300 °F
  LO2 mass fraction = 1.0
  He mass fraction = 0.0
Set Up Boundary Nodes

## Slide 7
  Node 3 represents the ullage space
    Initial P = 67 psia, T = -300.0 °F
    Initial Volume = 43,200 in3
    He fraction = 1.0, LOx fraction = 0.0
  Node 5 represents the propellant space
    Initial P = 74.76 psia, T = -300.0 °F
    Initial Volume = 820,800 in3
    LOx fraction = 1.0, He fraction = 0.0
  Node 2 represents the small space between the control valve and the ullage inlet orifice
    Initial P = 79.32 psia, T = 120 °F
    Volume is negligible
    He fraction = 1.0, LOx fraction = 0.0
Set Up Internal Nodes

## Slide 8
Branch 12 is an instantaneous control valve
  A = 0.63617 in2, CL = 0.6
  It is controlled by pressure in Node 3
    70 psia – close
    64 psia – open
  Valve is initially open
  Requires a history file
Branch 23 is the inlet orifice to the ullage
  A = 0.785 in2, CL = 0.6
Branch 45 represents the surface of the propellant
  A = 4015 in2, CL = 0.0
Branch 56 represents the orifice to the exit boundary
  A = 14.25 in2, CL = 0.319
Set Up Branches

## Slide 9
Open Pressurization Dialog from Advanced menu
Click ADD
Cylindrical aluminum tank
Tank Surface Area*: 6431.91 in2
Density: 170. lbm/ft3
Specific Heat: 0.2 Btu/lbm-R
Thermal Conductivity: 0.0362 Btu/ft-s-R
Ullage/Propellant Heat Transfer Area: 4015. in2
Wall Thickness: 0.375 in.
Conv. Heat Transfer Adj. Factor: 1.0
Ttank: -300 °F
Use default convection correlation coefficients
Click ACCEPT, then CLOSE
Tank Pressurization Option
*Tank wall surface area initially exposed to ullage. It will automatically increase as the tank drains.

## Slide 10
Study of the Results
Study tut3.out and plot files to note the following facts:
  Ullage pressure is maintained between 64 and 70 psia by the control valve
  Difference between ullage pressure and tank bottom pressure due to gravitational head
  Tank bottom pressure decreases as propellant is expelled from the tank
If you finish early:
  Re-run the model with increased heat transfer by setting the Heat Transfer Adjustment Factor to 2. What effect does this have on the valve cycling time and the final helium mass in the ullage node?

## Slide 11
Tank Pressure History

## Slide 12
Tank Mass History
For multiple Y-axes in Winplot, select the Multi-Y button, to the left of the Fit-X button.

## Slide 13
Hot and cold water streams enter the system shown below at 50 psia and exit at 25 psia. The hot water enters at 100 °F; the cold, 60 °F. In addition to the 10-inch inlet and exit pipes, the counterflow heat exchanger may be modeled as 10-inch pipes with diameter of 0.25/0.50 inches. The heat exchanger effectiveness is known to be 0.7, and the pipes are assumed to be smooth.
Determine the mass flow rates and exit temperatures of the two streams.
Challenge Problem 3
Simulation of a Flow System Involving a Heat Exchanger

## Slide 14
Hints:
  Because GFSSP’s energy equation uses an upwind scheme, exit boundary temperatures are dummy values.
  The heat exchanger option is activated on the Circuit Options page; the dialog box is accessed from the Advanced menu.
  When the heat exchanger effectiveness is known, the product of the overall heat transfer coefficient and the area (UA) does not need to be specified.
  Answers: Hot: 0.885 lb/s, 72.1 °F Cold: 5.41 lb/s, 64.6 °F
Challenge Problem 3
Simulation of a Flow System Involving a Heat Exchanger