## Slide 1: PRESSURE & FLOW REGULATOR
Flow Regulating Valve

## Slide 2
Modeling Pressure Regulator
GFSSP has two built-in options (algorithms) to model a pressure regulator
  1. Iterative Algorithm
    Applicable for single regulator and longer computation time
    Serves as an example of how to adjust GFSSP solution to satisfy a given boundary condition
  2. Marching Algorithm (Schallhorn-Haas)
    Capable of handling multiple regulators
    Numerically stable and computationally efficient

## Slide 3
Pressure Regulator Option – 1
Iterative Algorithm
Purpose: To control pressure at a given node by adjusting the flow area of the upstream branch
Implementation
  Step 1
    Edit
    Options
    Unsteady Options
      Pressure Regulator
  Step 2
    Advanced
      Pressure Regulator
Application
  Example 16 – Simulation of a Pressure Regulator downstream of a pressurized tank
4
0 35.00
10 35.00
10.01 40.00
1000 40.00
History File
Time in Seconds
Number of lines in the file
Pressure in psia

## Slide 4
Pressure Regulator – Option 2
Marching Algorithm
In Marching Algorithm, area is guessed and adjusted only once in each time step
Adjustment of area is calculated based on difference between calculated and desired pressure
Area adjustment can be done by backward differencing algorithm (Schallhorn-Majumdar) or forward looking algorithm (Schallhorn-Hass)
Schallhorn-Hass Algorithm has been implemented in GFSSP Version 603 as Option 2

## Slide 5: Forward Looking Algorithm
In Forward Looking Algorithm, previous time step result is not used, instead area is calculated from the following expression:

## Slide 6
Application Results
Reference: Forward Looking Pressure Regulator Algorithm for Improved Modeling Performance with the Generalized Fluid System Simulation Program by Paul Schallhorn & Neal Hass, AIAA Paper No. 2004-3667
Air tank
Pressure Regulator
Ambient
Exit

## Slide 7
Comparison between Forward Looking Marching and Iterative Algorithm
Option 1 (Iterative) – Orange
Option 2 (Marching) - Green

## Slide 8
GFSSP Version 603
Forward Looking Pressure Regulator – Option 2

## Slide 9
Pressure History
(Schallhorn & Haas Algorithm)
Tank Pressure
Pressure downstream of regulator

## Slide 10: Applications – Inflatable Re-Entry Vehicle (IRVE3)

## Slide 11: Applications – Inflatable Re-Entry Vehicle (IRVE3)
N2 Tank
Control Valve
Ballutes (x7)
Pressure
Regulator

## Slide 12: Flow Rate
Orange: Flight Data
Green: GFSSP Prediction

## Slide 13: Pressure in Ballute 3
Orange: Flight Data
Green: GFSSP Prediction

## Slide 14: Regulator Pressure
Orange: Flight Data
Green: GFSSP Prediction

## Slide 15
Modeling Flow Regulator
GFSSP has two built-in options (algorithms) to model a flow regulator
  1. Iterative Algorithm
    Applicable for single flow regulator; requires longer computation time
    Serves as an example of how to adjust GFSSP solution to satisfy a given boundary condition
  2. Time-Marching Algorithm
    Adjusts area once per time-step, based on backwards-differencing functional derivative dF/dA
    Capable of handling multiple flow regulators

## Slide 16
Flow Regulator Option – 1
Iterative Algorithm
Purpose: To control flow rate in a given branch by adjusting the branch area
Implementation
  Step 1
    Edit
    Options
    Unsteady Options
      Flow Regulator
  Step 2
    Advanced
      Flow Regulator
Application
  Example 17 – Simulation of a Flow Regulator downstream of a pressurized tank
4
0 0.012
10 0.012
10.01 0.02
1000 0.02
History File
Time in Seconds
Number of lines in the file
Flow rate in lb/s

## Slide 17
Flow Regulator Algorithm
A
The required flow area is determined by the Newton-Raphson scheme with the following steps:
Assume an Area,
Compute the deviation,
Estimate the gradient
4. Estimate the correction in the Area
5. Compute the new Area
6. Repeat steps 2 – 5 until

## Slide 18
Flow Regulator – Option 2
Time-Marching Algorithm
In the Time-Marching Algorithm, area is adjusted only once at the beginning of each time step
Adjustment of area is calculated based on the functional derivative dF/dA and the difference between the calculated and desired flow rate
CAUTION: If other elements of the model have significant effect on the flow rate, calculation of dF/dA by backwards differencing may lead to numerical instability. May require under-relaxation.

## Slide 19
Flow Regulator – Example 17

## Slide 20
Comparison between Iterative and Time-Marching Algorithms
Option 1 (Iterative) – Orange
Option 2 (Marching) - Green
Option 1 running time: 0.031 s
Option 2 running time: 0.016 s

## Slide 21
Example of Multiple Flow Regulators

## Slide 22
Flow Rate History
Spike occurs when inlet pressure is suddenly raised. But desired flow rates are re-achieved within a few time steps.

## Slide 23: Summary
Pressure & Flow Regulator Options have been made available to include in any unsteady flow simulation
Pressure Regulator has two options: Iterative (Option -1) and Marching (Option -2)
Option-2 has the flexibility of using multiple regulators and runs faster
Flow Regulator also has two options: Iterative (Option-1) and Marching (Option-2)
Option-2 has the flexibility of using multiple regulators and runs faster; however, it may require relaxation for numerical stability
Fixed Flow Branch Option can also be used to regulate flow in multiple branches