## Slide 1
Tutorial – 4 Modeling a Pressure Regulator
In this project, you will:
Use GFSSP’s built-in pressure regulator options to model the regulated blowdown of a tank of compressed air
Learn the difference between the two pressure regulator options

## Slide 2
Set Up Options
VTASC File: Tut4.vts
User Information
  Input File: Tut4.dat
  Output File: Tut4.out
Fluid is Ideal Gas
  Defaults to air properties

## Slide 3
Set Up Options (cont.)
Transient run
  Time step: 0.1 s
  Final time: 100 s
  Print Freq: 25
  Select Pressure Regulator option
Output Control
  Select Winplot binary output

## Slide 4
Build Model on Canvas
Air tank
Pressure Regulator
Ambient
Exit

## Slide 5
Set Up Transient Boundary Condition
Node 3:
  P = 14.7 psia
  T = 80.0 °F

## Slide 6
Set Up Internal Nodes
Node 1:
  Initial P = 100.0 psia
  Initial T = 80.0 °F
  Vol. = 10 ft3 = 17280 in3
Node 2:
  Initial P = 14.7 psia
  Initial T = 80.0 °F
  Vol. = 100 in3

## Slide 7
Set Up Fluid Branches
Branch 12: Pressure Regulator
  Initial A = 0.04 in2
  CL = 1.0
Branch 23: Exit
  A = 0.00785 in2
  CL = 1.0

## Slide 8
Set Up Pressure Regulator Option 1
Select Advanced/Pressure Regulator
Make sure the “Option 1” radio button is selected
Click “Add”
Fill in the dialog boxes
Create a pressure history data file: preg_hist.dat
Click “Accept”, “Done”
For each time step, GFSSP will adjust the area of Branch 12 to maintain the desired pressure in the downstream node.
NLines
Time, Pressure

## Slide 9
Result of Pressure Regulator Model
Run the model
Note that in each time step GFSSP is adjusting the area of Branch 12 to meet the desired pressure.
What effect do you think this has on run time?

## Slide 10
Pressure History
Tank Pressure
Pressure downstream of regulator

## Slide 11
Temperature History
Temperature of air inside tank

## Slide 12
Pressure Regulator Area History
Notice that area changes to maintain defined downstream pressure.

## Slide 13
Part 2: Modeling the Forward-Looking Pressure Regulator
Now we will repeat the exercise using a different pressure regulator algorithm
Go to Advanced/Pressure Regulator
Delete the current pressure regulator
Select “Option 2” radio button
Click “Add”
Fill in the dialog boxes
Click “Accept”, “Done”

## Slide 14
Rename the GFSSP Files
On the edit options page, rename the input and output files:
  Tut4a.dat
  Tut4a.out
This will prevent overwriting the results of the first pressure regulator

## Slide 15
Result of Pressure Regulator Model
Run the model
Note that this model runs faster. Why?
  GFSSP’s Option 1 pressure regulator iterates the branch area at every timestep to meet the required pressure. Therefore each timestep is run 10-20 times. It’s like a regulator that reacts instantaneously.
  The Option 2 regulator adjusts the area just once at the beginning of each time step, based on a relation developed by Schallhorn and Haas. It reacts in a finite amount of time, as would a real pressure regulator.
Plot the new Option 2 results (Tut4a.WPL) over the Option 1 results (Tut4.WPL)
Time permitting, try rerunning Option 2 with a different relaxation factor and note its effect on the pressure oscillations.

## Slide 16
Pressure History
Tank Pressure
Pressure downstream of regulator
Note oscillations over time when using Option 2

## Slide 17
Challenge Problem 4
Leakage Flow Past a Piston
A hydraulic system operates at a pressure of 20 MPa. The hydraulic fluid is SAE 10W oil (density = 920 kg/m3, viscosity at 55 °C = 0.018 N-s/m2). A control valve consists of a piston 25 mm in diameter, fitted to a cylinder with a mean radial clearance of 5 microns. Determine leakage flow rate if the pressure on the low-pressure side of the piston is 1.0 MPa. The piston is 15 mm long.

## Slide 18
Challenge Problem 4
Leakage Flow Past a Piston
Hints:
  SI units can be enabled from the Advanced menu. When entering parameters, you may need to multiply or divide by some power of 10.
  The Face Seal branch option can be used to model laminar flow through a tight clearance. Note that it asks for radius, not diameter.
  GFSSP requires at least one internal node between the two boundaries. The single flow resistance can be broken up into two identical branches, each with half the cylinder length.
  This problem is Example 8.1 in Introduction to Fluid Mechanics, 4th ed., by Fox and McDonald. The velocity given in the text is 0.147 m/s, and the volumetric flow rate (mass flow rate / density) is 57.6 mm3/s. How does GFSSP’s answer compare?