## Slide 1: Introduction to the International Space Station (ISS)
Dr. Donna L. Dempsey NASA Johnson Space Center
March 14, 2017
NESC Academy Webcast
Moderated by Dr. Jon Holbrook

## Slide 2
Presenter: Donna L. Dempsey

## Slide 3
Outline
International Partners and Crew
Research Modules and External Payloads
Airlocks and Robotics
More Modules
ISS Video Tour and Assembly Sequence

## Slide 4: International partners and crews
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
Notes: Instructor may pose question: have you encountered other types of students or can you think of other types of students that you may encounter? If yes, awesome. If no, it’s cool – you still made your point.

## Slide 5
NASA (National Aeronautics & Space Administration)
RSA (Russian Space Agency)
CSA (Canadian Space Agency)
JAXA (Japanese Aerospace Exploration Agency)
ESA (European Space Agency)
  Comprised of 22 member states, 11 of which are participating in ISS
International effort of 15 countries
International Partners
United States
Canada
Russia
Europe
Japan
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
Notes: Instructor may pose question: have you encountered other types of students or can you think of other types of students that you may encounter? If yes, awesome. If no, it’s cool – you still made your point.

## Slide 7
Crew Complement
Proportional to IP’s contribution to program’s operation
  The crew compliment in a typical year is:
    6 Russian cosmonauts
    4 NASA astronauts
    1 ESA astronaut
    1 JAXA astronaut
  Every few years, there is
    1 CSA astronaut
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly

## Slide 8: Research modules AND External Payloads
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
Notes: Instructor may pose question: have you encountered other types of students or can you think of other types of students that you may encounter? If yes, awesome. If no, it’s cool – you still made your point.

## Slide 9
US Laboratory
NASA research laboratory
  24 rack locations, 13 designated for payload racks
  Launched with 5 racks
Contains many distributed systems
Built and launched by NASA
aka “Destiny”
LAB
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly

## Slide 10
  LAB Installation
  LAB on Shuttle Remote Manipulator System (SRMS)

## Slide 11
International Standard Payload Racks
  Loading Rack on the Ground
  Rack Installation in LAB
  Rack Shape

## Slide 12
  MELFI Rack
  Exp. 16 Clay Anderson
  Microgravity Science Glove Box Rack
  Exp. 29 Satoshi Furukawa
  Combustion Integrated Rack
  Exp. 30 Dan Burbank
NASA Payload Racks

## Slide 13
Provides attachments points for solar arrays and external payloads
Based on pre-integrated truss design comprised of bulkheads, longerons and diagonals
Built and launched by NASA
Truss
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
TRUSS

## Slide 14
  Truss Segment
  EVA Astronauts on the Truss (Before the addition of the solar arrays)

## Slide 15
  Alpha Magnetic Spectrometer (AMS-02)
  Particle physics payload mounted on the Truss

## Slide 16
Columbus Orbital Facility
ESA research laboratory
  16 rack locations, 10 designated for payload racks
External payload facility on the starboard end cone
Built by ESA, launched by NASA
aka “Columbus”
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
COL

## Slide 17
External Payload Facility on Columbus

## Slide 18
Japanese Experiment Module
  JEM is a multi-component research module:
    JEM Pressurized Module (JPM)
    JEM Exposed Facility (JEF)
    JEM Logistics Module Pressurized Section (JLP)
  JEM includes a robotic arm:
    JEM Remote Manipulator System (JEMRMS)
  Built by JAXA, launched by NASA
  aka “Kibo”
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
JLP
JEMRMS
JPM
JEF
JEM

## Slide 19
JEM Pressurized Module
JAXA research module
  23 rack locations, 10 designated for payloads
Provides payload airlock
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
JPM

## Slide 20
  JPM Outfitting
  STS-124 Ken Ham and Mark Kelly

## Slide 21
  JPM Airlock
  Exp. 19 Koichi Wakata

## Slide 22
JEM Exposed Facility
JAXA external payload facility
Payloads are deployed and retrieved via the JPM airlock
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
JEF

## Slide 23
  JEM Exposed Facility (JEF)

## Slide 24
Mini-Research Module 1
  Russian research laboratory
  Provides Soyuz or Progress docking port
  Built by RSA, launched by NASA
  aka “Rassvet”
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
MRM1

## Slide 25
  MRM 1
  Launched with experiment airlock for MLM and elbow joint for ERA

## Slide 26
  Russian research laboratory
  Provides experiment airlock
  Provides Soyuz or Progress docking port (replacing the Docking Compartment port)
  Built by Russia, launched by Russia NET 2017
  aka “Nauka”
Multipurpose Laboratory Module
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
MLM
Will replace DC

## Slide 27: Airlocks and Robotics
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
Notes: Instructor may pose question: have you encountered other types of students or can you think of other types of students that you may encounter? If yes, awesome. If no, it’s cool – you still made your point.

## Slide 28
  Provides station based spacewalk capability from the Russian segment using Russian Orlan-M suits
  Provides Soyuz and Progress docking port
  Provides two “Strella” cargo booms for moving cargo and cosmonauts
  Built and launched by RSA
  aka “Pirs”
Docking Compartment
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
DC

## Slide 29
  Orlan-M Suit
  Docking Compartment
  As seen from below
  Docking Compartment On the ground

## Slide 30
  Supports EMU-based EVAs and servicing EMUs
  Potential future capability for servicing Orlan-M suits
  Two pressurized, cylindrical chambers
    Equipment Lock
    Crew Lock
  Built and launched by NASA
  aka “Quest”
Joint Airlock
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
Airlock

## Slide 31
  Airlock Installation
  Installed using the SSRMS
  Airlock
  Egressing the Airlock
  EMU Suit

## Slide 32
  Provides station based spacewalk capability from the Russian segment using Russian Orlan-M suits
  Provides Soyuz and Progress docking port
  Built and launched by RSA
  aka “Poisk”
Mini-Research Module 2
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
MRM 2

## Slide 33
  Self-relocatable robotic arm with seven joints and two latching end effectors, and 10 power and data grapple fixtures on ISS
  Pivotal in ISS assembly and maintenance
  Used for module installation, visiting vehicle berthing, and EVA crewmember translation
  Built by CSA, launched by NASA
Space Station Robotic Manipulator System
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
SSRMS

## Slide 34
  SSRMS EVA Translation
  EVA Crewmember on SSRMS
  SSRMS HTV-3 Berthing
  HTV-3 Berthed to Node 2 Nadir

## Slide 35
    Provides a pressurized observation and work area
      Robotics workstation for SSRMS
      External viewing
    Built by the Italian Space Agency for NASA, launched by NASA
Cupola
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
CUP

## Slide 36
  Looking out of Cupola
  Dmitri Kondratyev and Paoli Nespoli
  Looking into Cupola
  Doug Wheelock

## Slide 37
Mobile Transporter
  Provides lateral mobility for the SSRMS
Mobile Base System
  Sits atop the Mobile Transporter and has 4 power and data grapple fixtures
  Provides two attachments locations for external payloads
Built by CSA, launched by NASA
Mobile Transporter and Mobile Base System
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
MT
MBS

## Slide 38
Two armed robot
Built by CSA, launched by NASA
aka “Dextre”
Special Purpose Dexterous Manipulator
SPDM
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly

## Slide 39
  DEXTRE with Payload

## Slide 40
Robotic arm with six joints
  Used to move experimental hardware
  Small fine arm (SFA) can attached to the end of JEMRMS as needed
Built by JAXA, launched by NASA
JEM Robotic Manipulator System
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
JEMRMS

## Slide 41
  Self-relocatable robotic arm
    Launches installed on the MLM NET 2017
    Spare joint stored on MRM1
  Built by ESA, launched by RSA
European Robotic Arm
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly

## Slide 42: More Modules (Crew Support/Nodes/ Logistics)
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
Notes: Instructor may pose question: have you encountered other types of students or can you think of other types of students that you may encounter? If yes, awesome. If no, it’s cool – you still made your point.

## Slide 43
Service Module
Russian critical systems and crew support module
  O2 generation, CO2 removal, galley, toilet, exercise equipment, two каюта (crew quarters)
Provides motion control and reboost capability
Provides Soyuz or Progress docking port
Initially, Russian research laboratory
Built and launched by RSA
aka “Zvezda”
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
SM

## Slide 44
  SM Solar Array Deploy
  ISS Automated Rendezvous and Docking
  SM maintained station keeping orbit

## Slide 45
  Elektron O2 Generation Units in the SM
  Exp. 28 Andrei Borisenko, Aleksandr Samokutyayev, Sergei Volkov

## Slide 46
  Six-way connecting module and passageway to which other modules attach
Crew support module
  Toilet, exercise equipment, water reclamation, O2 generation, CO2 removal
Built by the Italian Space Agency for NASA, launched by NASA
aka “Tranquility”
Node 3
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
Node 3

## Slide 47
  ARED in Node 3
  Exp. 30 Dan Burbank
  (Rotated in 2015, so footplate is now forward)
  WHC in Node 3

## Slide 48
  Six-way connecting module
    Connects Lab to JPM & COL
  Crew support module
    Four crew quarters
  Nadir and zenith ports provide CBM berthing port for cargo visiting vehicles
  In 2015, forward port reconfigured to provide docking port for future manned vehicle. Zenith port will be reconfigured as a backup docking port.
Built by the Italian Space Agency for NASA, launched by NASA
aka “Harmony”
Node 2
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
Node 2

## Slide 49
Crew Quarters in Node 2
Exp. 26 Ron Garan, Paulo Nespoli, Aleksandr Samokutyayev, and Cady Coleman

## Slide 50
  Six-way connecting module and passageway to which other modules attach
  Launched with two pressurized mating adapters (PMAs) attached
In 2015, nadir port upgraded to provide CBM berthing port for cargo visiting vehicles
Built and launched by NASA
  aka “Unity”
Node 1
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
Node 1

## Slide 51
  Node 1

## Slide 52
  Six-way connecting module and passageway to which other modules attach
    (Image shows SPM attached to starboard port on NM, actual port TBD)
  Provides Soyuz or Progress docking ports
  Will launch NET 2017 and attach to MLM nadir
  Built and launched by RSA
Nodal Module
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
NM

## Slide 53
Provides internal stowage for cargo and external propellant storage
First element launched
Provided initial propulsion and power
Built by the Russians for NASA, launched and controlled by RSA
aka “Zarya”
Functional Cargo Block
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
FGB

## Slide 54
  FGB
  First Element Launched

## Slide 55
Provides internal stowage
  8 rack locations
Built by JAXA, launched by NASA
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
JEM Logistics Module Pressurized Section
JLP

## Slide 56
Provides internal stowage
  16 rack locations plus end cone
In 2015, relocated to Node 3 forward
Formerly the reusable Leonardo Multi-Purpose Logistic Module (MPLM)
Built by the Italian Space Agency for NASA, launched by NASA
Permanent Multipurpose Module
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
PMM

## Slide 57
ExPRESS Logistics Carriers (ELCs) attach to the Truss
  Provide mounting surfaces, power, and data connectivity for orbital replacement units (ORUs) and unpressurized payloads
External Logistics
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly

## Slide 58
PMA1 is attached to Node 1
  Connects the USOS to the ROS
PMA2 is attached to Node 2
  Provided Shuttle docking port
  In 2016, installed IDA1 (international docking adapter) to provide new docking port for future manned vehicles
PMA3 is attached to Node 3
  Provided Shuttle docking port for Lab installation
  Will be relocated to Node 2 zenith and will install IDA2 to provide new docking port
Built and launched by NASA
Pressurized Mating Adapters
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
PMA 2
PMA 3
PMA 1

## Slide 59
Temporary 2-year module, berthed to Node 3 aft
Built by Bigelow Aerospace, launched by SpaceX in 2016
Bigelow Expandable Activity Module
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
BEAM

## Slide 60
  BEAM Expansion

## Slide 61: Iss Video Tour and assembly
International Partners
Research Modules
Core Systems
Airlocks/ Robotics
More Modules
ISS Video/ Assembly
Notes: Instructor may pose question: have you encountered other types of students or can you think of other types of students that you may encounter? If yes, awesome. If no, it’s cool – you still made your point.

## Slide 62
ISS Video Tour

## Slide 63
Assembly Sequence

## Slide 64
  Scott Kelly with International Partner Flags
Resource: http://spacestationlive.jsc.nasa.gov/

## Slide 65
Questions?
NESC Academy Webcast