## Slide 1: Introduction to the Theory and Application of Quaternions Part 1 of 2 (“Introduction to Quaternions”)
James R. (Jim) Beaty, PhD - NASA Langley Research Center Vehicle Analysis Branch, Systems Analysis & Concepts Directorate

## Slide 2: Overview
Part 1 of 2 – Introduction to Quaternions
  Definition, mathematical pre-requisites, and quaternion properties
  Comparison with Euler angles and direction cosine matrix (DCM)
  Part 2 of 2 - Working with quaternions
  How quaternions are used for kinematics
  Defining quaternions for a particular coordinate frame rotation
  Using quaternions for coordinate transformations of vectors
  Calculation of DCM from quaternion, and vice-versa
  Time Propagation of quaternions
  Using quaternions for a single axis rotation to align one coordinate frame with another

## Slide 3: What are quaternions?
Quaternions are mathematical abstractions
“Invented” or discovered by several mathematicians in nineteenth century, notably Sir William R. Hamilton, a famous British mathematician
In math terms, a quaternion is a type of tensor. In simple terms, a tensor can be categorized as:
  A rank 0 tensor is a scalar
    Invariant with respect to any particular reference frame
  A rank 1 tensor is a vector
    Dependent on a particular reference frame
    Can be transformed from one frame to another
    Size of the vector (number of elements) is dependent on the application
  A rank 2 tensor is a matrix
    Linear transformation (such as direction cosine matrix) is a rank 2 tensor
    Moment of inertia tensor is a rank 2 tensor
    Size of the matrix (number of rows and columns) is dependent on the application
  A tensor can be covariant, or contravariant, depending on what type of transformation law it “obeys”

## Slide 4: How do quaternions compare with vectors?
Like vectors:
  Quaternions are ordered groups of real numbers (although some people represent quaternion mathematical operations with complex number notation)
  Quaternions have mathematical properties with respect to mathematical operations (commutative, associative, etc.)
  Quaternions can be added, subtracted, multiplied, divided (and more!)
Unlike vectors:
  Quaternions have four elements, instead of three
    Actually, vectors aren’t limited to three elements, but in kinematics and dynamics, we usually think of 3-element vectors to represent 3-dimensional motion

## Slide 5: How are quaternions represented?
Usually, quaternions are expressed as a scalar and a 3-element vector:
  q = ( s , V ) = s + x i + y j + z k or = q0 + q1 i + q2 j + q3 k , where
  i,j,k are basis vectors of some reference frame
  The scalar can represent time or a rotation angle (or anything else!)
    In kinematics use, the scalar part is usually related to a right hand rule rotation angle about the direction specified by the vector part
    In mechanics use, the scalar is usually related to time, and the vector represents position, velocity, or acceleration
Quaternions have virtually unlimited applications
In this presentation, we will concentrate on the kinematics use of quaternions for coordinate transformations, etc.

## Slide 6: How are quaternions used in kinematics?
  q = ( q , V )
  q is rotation of some object, or reference frame about direction specified by vector, V
  A more common way to express q:
    q = [ cos(q/2) , n sin(q/2) ]
    where n is unit vector along V ( or, n = V / | V | )
  Latter form is convenient, in that it is a unit quaternion (its magnitude = 1), which simplifies the mathematics
  In the latter form, the elements of the quaternion are also known as the “Euler parameters” which describe the rotation
x
y
z
q
V
n

## Slide 7: Addition / Subtraction Properties of Quaternions
Quaternion addition / subtraction
  If q1 = ( s1 , V1 ) and q2 = ( s2 , V2 )
  q1 + q2 = ( ( s1 + s2 ) , ( V1 + V2 ) )
  q1 - q2 = ( ( s1 - s2 ) , ( V1 - V2 ) )
  Note that some define subtraction using “scale” factors:
    q1 - q2 = ( ( s1 - s2 ) , ( V1 - V2 ) / 3 )
    This form preserves the holonomic characteristics of quaternions
  Quaternion addition is associative and commutative (subtraction is associative, but not commutative)
    q1 ± ( q2 ± q3 ) = ( q1 ± q2 ) ± q3
    q1 + q2 = q2 + q1
    q1 - q2 ≠ q2 - q1

## Slide 8: Multiplication Properties of Quaternions
Quaternion multiplication is associative, but not commutative
  q1 * ( q2 * q3 ) = ( q1 * q2 ) * q3
  q1 * q2 ≠ q2 * q1
  If q1 = ( s1 , V1 ) and q2 = ( s2 , V2 ), then the product of q1 and q2 is
  q1 * q2 = ( ( s1s2 – V1 · V2 ) , ( s1V2 + s2V1 + V1×V2 ) )
  Other forms for quaternion multiplication are presented later
An interesting fact is that multiplication of two quaternions with zero scalar parts (two pure vectors) produces a quaternion with the negative dot product of the two vectors as its scalar part, and the cross product of the two vectors as its vector part
  Hamilton reportedly used this fact to implement dot and cross products before modern vector algebra was “invented”

## Slide 9: Other Properties of Quaternions
Quaternion conjugate is similar to conjugate of complex numbers
  If q = ( s , V ), the conjugate of q is
  q* = (s , -V )
  The conjugate of the conjugate of a quaternion returns the original quaternion:
  ( q* ) * = (s , +V ) = q
Quaternion magnitude, or norm:
  If q = ( s , V ), where V = xi + yj + zk
  the norm of q is
  | q | = √ s2 + x2 + y2 + z2

## Slide 10: Quaternion Inverse and Conjugate
Product of quaternion and its conjugate:
  q q* = ( (s2 + | V |2 ) , ( s (-V) + sV + V × V ) )
  = ( (s2 + x2 + y2 + z2 ) , 0 ) = | q |2
Quaternion inverse:
  From the equation above, it follows that
  ( q q* ) / | q |2 = 1, or
  q-1 = q* / | q |2
  e.g. – quaternion’s inverse is its conjugate divided by its norm squared
Unit quaternion:
  Defined as | q | = 1
  The inverse of a unit quaternion is its conjugate

## Slide 11: Multiplication of Quaternion by a scalar
Multiplication of quaternion by scalar:
  If q = ( s , V ) , then, k q = ( ks , kV ) = q2 for any real k
Multiplication of quaternion by negative one:
  Consider a special quaternion, qM1 defined as:
  qM1 = ( -1 , 0 n ) = scalar -1, written as quaternion
  Note that qM1 = ( -1 , 0 n ) can be expressed qM1 = ( cos(q/2) , n sin(q/2) ) , where q = ±2pn
  qM1 = [ cos( ±pn ) ) , n sin( ±pn ) ] = [ -1 , 0 ] , where n = 1, 3, 5, …
  Multiplication of any quaternion by -1, (or qM1) gives the same quaternion rotated about its vector direction by ±2pn, so that the orientation defined by the quaternion is unchanged
   Multiplication of a quaternion by -1 does not change the orientation defined by the quaternion
  Quite often, people will multiply a quaternion by -1 if the scalar part is negative

## Slide 12: Quaternion Multiplication
Another way to multiply two quaternions:
  If q1 = ( s1 , V1 ) and q2 = ( s2 , V2 )
  Recall from earlier slide that the product of q1 and q2 can be computed from
  q1 * q2 = ( ( s1s2 – V1 · V2 ) , ( s1V2 + s2V1 + V1×V2 ) )
  This product can be computed manually as follows:
    Define the product of basis vectors i, j, and k as:
      i j = k , j k = i , k i = j
      j i = -k , k j = -i , i k = -j
      i i = -1 , j j = -1 , k k = -1
      Note: these multiplications are NOT commutative
  Compute product q1 * q2 term by term:
    q1 * q2 = ( s1 + x1i + y1j + z1k ) * ( s2 + x2i + y2j + z2k )
    = s1s2 + s1x2i + s1y2j + s1z2k + x1s2i + x1x2(-1) + x1y2k + x1z2(-j) + y1s2j + y1x2(-k) + y1y2(-1) + y1z2i + z1s2k +z1x2j + z1y2(-i) +
    z1z2(-1)

## Slide 13: Quaternion Multiplication - Continued
Another way to multiply two quaternions - continued:
  Group scalar and i, j, k items in term by term product of q1 * q2:
    q1 * q2 = ( s1s2 - x1x2 - y1y2 - z1z2 )
    + i ( s1x2 + x1s2 + y1z2 - z1y2 )
    + j ( s1y2 - x1z2 + y1s2 + z1x2 )
    + k ( s1z2 + x1y2 - y1x2 + z1s2 )
    or
    q1 * q2 = ( s , ( xi + yj + zk ) )
    where
    s = s1s2 - x1x2 - y1y2 - z1z2
    x = s1x2 + x1s2 + y1z2 - z1y2
    y = s1y2 - x1z2 + y1s2 + z1x2
    z = s1z2 + x1y2 - y1x2 + z1s2

## Slide 14: Quaternion Multiplication - Matrix / Vector form
  From expression on previous chart one can express quaternion multiplication as one of the two equivalent matrix / vector products:
  q1 * q2 = Q1 * q2 or = Q2 * q1
    where
  Q1 is referred to as the “quaternion matrix”
  Q2 is referred to as the “quaternion transmuted matrix”
  Note that both are skew symmetric matrices and have the following properties:
    quaternion scalar part down the diagonal
    quaternion in first column and quaternion conjugate in first row
    Shaded part of quaternion matrix is similar to the matrix form of a cross product operation (except the latter has zeros down the diagonal)

## Slide 15: Quaternion Multiplication - Definition of Scalar Part
On the previous page, the quaternions to be multiplied were represented as column vectors with the scalar part as the first element, as follows; If q = ( q0 , q1 i , q2 j , q3 k), then
But, occasionally some people represent quaternions as column vectors with the scalar part as the fourth element as follows; If q = (q1 i , q2 j , q3 k , q4 ), then
If represented in this latter form, the matrix / vector forms for quaternion multiplication shown on the previous page will not be correct

## Slide 16: Euler angles
Euler angles define the orientation of one frame relative to another specified by three sequential rotations about x, y, and / or z axes in any “convenient” sequence, as dictated by the application (or user’s preference)
Provides an “intuitive” representation of the relative orientation of two reference frames
Can’t easily transform vectors directly with Euler angles, must compute DCM or other transformation methods first
Although rarely used, can integrate Euler angle rates to simulate vehicle angular motion
  Requires only 3 state equations for 3-D angular motion
  Usually requires smaller integration step size than propagating DCMs or quaternions, since rate of change of Euler angles is larger than that of DCM elements
  Some orientations, coupled with specific Euler angle sequences can result in singularities in Euler angle rates

## Slide 17: Time Propagation of Euler angles
Euler rates for typical yaw-pitch-roll Euler sequence of a reference frame relative to another frame:
where p, q, r = angular rates of second frame relative to initial frame, measured with respect to the second frame’s axes
The roll Euler angle rate, f-dot, is directly proportional to x-axis angular rate, p, of the vehicle, so that a smaller integration step size required, since it varies rapidly
Singularity in f-dot, y-dot (rates  ∞) for yaw-pitch-roll sequence when cosq = 0 (q = ±90 degrees)

## Slide 18: Direction Cosine Matrices (DCM)
DCMs provide method for transforming vectors from one reference frame to another, usually implemented as matrix multiplication operations
Rows of DCM are direction cosines of the xR-yR-zR axes of the rotated frame relative to those of the reference frame (X-Y-Z):
  = transformation From XYZ frame axes to xRyRzR frame axes
where i,j,k are basis vectors of rotated frame, and I,J,K are basis vectors of the reference frame
DCM is orthogonal: inverse of DCM is same as its transpose, and each row and column of DCM has RSS value of 1  can be used to reduce number of states to be propagated

## Slide 19: Time Propagation of DCMs
DCMs avoid propagation singularities that Euler angles can have
Since DCM is orthogonal its magnitude is invariant, so
where p,q, and r = angular rate of rotated reference frame axes relative to initial reference frame, expressed in the rotated reference frame axes
Allows a larger integration step size than integrating Euler angle rates, since derivatives of DCM are proportional to the angular rates, p, q, and r, multiplied by the elements of the DCM, which are less than or equal to 1 (e.g. – the magnitudes of rate of change of the DCM elements is smaller than the vehicle body axis angular rates)
Requires 9 state equations (actually only 6 if row / column orthogonality constraints are used)

## Slide 20: Multiple axis rotations with DCMs
DCMs usually represent multiple sequential axis rotations:
  DCMs of any Euler angle sequence can be computed by chaining simple 1-axis rotation DCMs in proper sequence:
  Note the order of multiplication of the simple DCMs (is important for comparison with quaternions to follow!)
  For yaw-pitch-roll Euler sequence:

## Slide 21: Singularities in Euler angles from DCMs
  Continuing from the DCM product on the previous page:
  This illustrates the ambiguity possible with Euler angles
    For rotations about three independent axes, if the intermediate (second) rotation is ±90°, the DCM cannot be used to compute unique values of the other two angles
    BUT, the DCM is still valid, and its rates are finite, even at the ±90° angle!
    This ambiguity is consistent with the singularity in the Euler angle rates when q = ±90° (shown a few slides ago)
Note: this equation can only determine
f ± y: there are no unique values

## Slide 22: Introduction to Quaternions Part 1 of 2 Summary
In Part 1, we have covered the following topics
  Definition of quaternions
  Mathematical properties
  Alternate expressions for quaternion multiplication, including matrix/vector forms
  How quaternions differ from DCMs and Euler angles
In Part 2, “Working with Quaternions”, we will cover the following:
  How quaternions are used for kinematics
  Defining quaternions for a particular coordinate frame rotation
  Using quaternions for coordinate transformations of vectors
  Calculation of DCM from quaternion, and vice-versa
  Time Propagation of quaternions
  Using quaternions for a single axis rotation to align one coordinate frame with another