## Slide 1: Introduction to the Theory and Application of Quaternions Part 2 of 2 (“Working with Quaternions”)
James R. (Jim) Beaty, PhD - NASA Langley Research Center Vehicle Analysis Branch, Systems Analysis & Concepts Directorate

## Slide 2: Overview
Part 1 of 2 – Introduction to Quaternions
  Definition, mathematical pre-requisites, and quaternion properties
  Comparison with Euler angles and direction cosine matrix (DCM)
  Part 2 of 2 - Working with quaternions
  How quaternions are used for kinematics
  Defining quaternions for a particular coordinate frame rotation
  Using quaternions for coordinate transformations of vectors
  Calculation of DCM from quaternion, and vice-versa
  Time Propagation of quaternions
  Using quaternions for a single axis rotation to align one coordinate frame with another

## Slide 3: How are quaternions used in kinematics?
Kinematics use of quaternions:
  q = ( q , V )
  q is rotation of some object, or reference frame about direction specified by vector, V
  A more common way to express q as a unit quaternion:
    q = ( cos(q/2) , n sin(q/2) )
    where:
    n is unit vector along V:
    ( n = V / | V | )
  Latter form is convenient, in that it is a unit quaternion (its magnitude = 1), which simplifies the mathematics
  In the latter form, the elements of the quaternion are also known as the “Euler parameters” which describe the rotation
x
y
z
q
V
n

## Slide 4: Definition of unit quaternion to represent rotation about an axis
Quaternions provide another method for transforming vectors from one reference frame to another
  Like DCMs, quaternions for any Euler angle sequence can be computed by multiplying simple quaternions in the proper sequence
    Recall that the most common form of a quaternion representing a rotation is represented as the following UNIT quaternion:
    q = ( cos(q/2) , n sin(q/2) )
    where q is the rotation angle, and n is a unit vector
    in the direction of the rotation (right-hand rule)
    The scalar part of the quaternion is cos(q/2), and the vector part is
    n sin(q/2)

## Slide 5: Defining single axis rotations with quaternions
Like DCMs, simple 1-axis rotations of quaternions can be chained together to represent more complex orientations in specific rotation sequences:
  For single axis rotation of f about x-axis:
  qf = ( cos(f/2) , ( sin(f/2) i + 0 j + 0 k ) ) = (cos(f/2) , sin(f/2) , 0 , 0 )
  For single axis rotation of q about y-axis:
  qq = ( cos(q/2) , (0 i + sin(q/2) j + 0 k ) ) = (cos(q/2) , 0 , sin(q/2) , 0 )
  For single axis rotation of y about z-axis:
  qy = ( cos(y/2) , (0 i + 0 j + sin(y/2) k ) ) = (cos(y/2) , 0 , 0 , sin(y/2) )
  where i,j,k are basis vectors of the x,y, and z axes

## Slide 6: Combining single axis rotations into multiple rotations with quaternions
Simple 1-axis rotations of quaternions can be chained together to represent more complex orientations – continued:
  The quaternion for a yaw-pitch-roll Euler sequence rotation
  q = qy qq qf ,  (note that order of multiplication is opposite that of DCMs)
  where for DCMs
  C = Cf Cq Cy
  The quaternion product, q = qy qq qf can be computed by either of the methods described in Part 1 of this presentation

## Slide 7: Quaternion elements for a yaw-pitch-roll Euler angle sequence:
q = ( q0 , ( q1 i + q2 j + q3 k) ) ≡ ( q0 q1 q2 q3 )
    where
    q0 = cos(f/2)cos(q/2)cos(y/2) + sin(f/2)sin(q/2)sin(y/2)
    q1 = -cos(f/2)sin(q/2)sin(y/2) + sin(f/2)cos(q/2)cos(y/2)
    q2 = cos(f/2)sin(q/2)cos(y/2) + sin(f/2)cos(q/2)sin(y/2)
    q3 = cos(f/2)cos(q/2)sin(y/2) - sin(f/2)sin(q/2)cos(y/2)
This can be computed from the product of 3 individual single axis rotation quaternions:
  q = [ cos((y/2) , sin (y/2) ( 0 0 1 ) ] * [ cos((q/2) , sin (q/2) ( 0 1 0 ) ] * [ cos((f/2) , sin (f/2) ( 1 0 0 ) ]
  E.g. – yaw about z-axis , then pitch about rotated y-axis, then roll about rotated x-axis
Calculation of yaw-pitch-roll Euler angles from this quaternion:
  q = sin-1[ -2*(q1*q3-q0*q2) ]
  y = tan-1[ 2*(q0*q3+q1*q2) / ( q02 + q12 - q22 - q32) ]
  f = tan-1[ 2*(q0*q1+q2*q3) / ( q02 - q12 - q22 + q32) ]
  Care should be taken if q = ±90°, as the denominator of y and f equations will be zero! Euler angle singularity  no unique values for 1st and 3rd Euler angles

## Slide 8: Quaternion elements for a roll-yaw-pitch Euler angle sequence
    q = ( q0 , ( q1 i + q2 j + q3 k) ) ≡ ( q0 q1 q2 q3 )
    where
    q0 = cos(f/2)cos(q/2)cos(y/2) - sin(f/2)sin(q/2)sin(y/2)
    q1 = -cos(f/2)sin(q/2)sin(y/2) + sin(f/2)cos(q/2)cos(y/2)
    q2 = cos(f/2)sin(q/2)cos(y/2) - sin(f/2)cos(q/2)sin(y/2)
    q3 = cos(f/2)cos(q/2)sin(y/2) + sin(f/2)sin(q/2)cos(y/2)
This can be computed from the product of 3 individual single axis rotation quaternions:
  q = [ cos((f/2) , sin (f/2) ( 1 0 0 ) ] * [ cos((y/2) , sin (y/2) ( 0 0 1 ) ] * [ cos((q/2) , sin (q/2) ( 0 1 0 ) ]
  E.g. – roll about x-axis , then yaw about rotated z-axis, then pitch about rotated y-axis
Calculation of roll-yaw-pitch Euler angles from this quaternion:
  y = sin-1[ -2*(q1*q2-q0*q3) ]
  q = tan-1[ 2*(q0*q2+q1*q3) / ( q02 + q12 - q22 - q32 ) ]
  f = tan-1[ 2*(q0*q1+q2*q3) / ( q02 - q12 + q22 - q32 ) ]
  Care should be taken if y = ±90°, as the denominator of q and f equations will be zero! Euler angle singularity  no unique values for 1st and 3rd Euler angles

## Slide 9: Plumb-line frame
Plumb-line frame has X-axis up along local vertical, or plumb line, Z-axis rotated thru azimuth from north about –X axis, Y-axis completes right hand frame
Quaternion elements for plumb-line reference frame relative to Earth Centered Inertial (ECI) frame (lE+lg is longitude plus sidereal “time”, fE is geodetic latitude, y is heading from north of z-axis):
  First rotation of lE+lg about zI-axis:
  q1 = [ cos((lE+lg)/2) , ( 0 i + 0 j + sin((lE+lg)/2) k ) ]
  Second rotation of -fE about rotated y-axis:
  q2 = [ cos(-fE/2) , ( 0 i + sin(-fE/2) j + 0 k ) ]
  Third rotation of -y about rotated x-axis:
  q3 = [ cos(-y/2) , ( sin(-y/2) i + 0 j + 0 k ) ]
  ECI to plumbline quaternion is following quaternion product:
      qECI to PL = q1 q2 q3
  Note that ECI to plumbline quaternion is also a yaw-pitch-roll Euler sequence with yaw = lE+lg,
  pitch = -fE , roll = -y
Meridian
Equinox
X
E
P
Yp
Zp
D
w
E/I
Z
I
, Z
E
Y
E
Y
I
Equatorial
Plane
Greenwich
Vernal
X
I
Local
sidereal
time
l
=
l
g
+
l
E
l
E
l
g
f
E
Xp
y
y

## Slide 10: North-East-Down (NED) frame
North-East-Down (NED) local level frame has X-axis north, Y-axis east, Z-axis down and perpendicular to oblate spheroid
NED reference frame relative to Earth Centered Inertial (ECI) frame defined by lE+lg (geodetic longitude plus sidereal “time”) and fE (geodetic latitude):
  First rotation of lE+lg about ZI-axis:
  q1 = [ cos((lE+lg)/2) , ( 0 i + 0 j + sin((lE+lg)/2) k ) ]
  Second rotation of -90-fE about rotated
  y-axis:
  q2 = [ cos((-90-fE)/2) , ( 0 i + sin((-90-fE)/2) j + 0 k ) ]
  ECI to NED quaternion is following quaternion product:
      qECI to NED = q1 q2
  Note that ECI to NED quaternion is also a
  yaw-pitch-roll Euler sequence with yaw = lE+lg,
  pitch = -90-fE , roll = 0 )
time
Meridian
Equinox
X
E
P
E
N
D
w
E/I
Z
I
, Z
E
Y
E
Y
Equatorial
Plane
Greenwich
Vernal
X
I
Local
sidereal
l
=
l
g
+
l
E
l
E
l
g
f
E

## Slide 11: Quaternion transformation of vectors
Coordinates of a vector in one frame, R, can be transformed with quaternion, q, to coordinates in second frame, r with the following equation:
  r = q* R q
  where
  q is quaternion for orientation of rotated frame relative to the original reference frame
  q* is conjugate of q
  R is vector in original reference frame, written as a quaternion with zero scalar part
  ( R = ( 0 , R ) )
  r is vector transformed from original reference frame to the rotated reference frame, written as a quaternion with zero scalar part ( r = ( 0 , r ) )
After the transformation (calculation of the quaternion product above), discard the scalar component part of the quaternion (it will be zero), and the transformed vector, r, will be contained in the vector part of the quaternion product

## Slide 12: Other “forms” of vector “rotation” equation are sometimes shown
Care should be used when reviewing texts that describe “vector rotations”, using quaternions
  These texts use the following form for the vector rotation equation, r = q R q*, which is not the same as the vector transformation equation shown on the previous slide
  These texts refer to the rotation of the vector R through the angle defined by the quaternion, q, NOT the transformation of the components of a fixed vector, R, in one reference frame into its components, r, in another reference frame
The vector itself is NOT rotated, just the frame that the vector is represented in
  This latter definition is what we mean by quaternion transformations with respect to kinematics applications (e.g. – calculation of coordinates of a fixed vector in two frames rotated relative to each other)
  The equation above represents the inverse (or transpose in DCM terms) of the actual vector transformation shown on the previous page

## Slide 13: How to compute DCM from a Quaternion
Calculation of DCM from a Quaternion:
  If q = [ q0 q1i q2j q3k ] is a quaternion for orientation of a rotated reference frame relative to some original reference frame, the equivalent DCM is:
  This expression can be derived by expanding term-by-term the quaternion transformation
  equation r = q* R q shown previously, and discarding the scalar part (which is identically zero), and then evaluating the remaining vector part
  This is equivalent to the matrix-vector product r = DCM • R

## Slide 14: DCM from Quaternion – an equivalent form
Calculation of DCM from a Quaternion – an equivalent form:
  Note: since the quaternions we usually work with are unit quaternions, some people use this fact to simplify the DCM elements above (or the calculations of Euler angles shown previously)
  Since q is a unit quaternion, q02 + q12 + q22 + q32 = 1, so
  q02 + q12 = 1 – q22 – q32
  q02 + q22 = 1 – q12 – q32
  q02 + q32 = 1 – q12 – q22
   DCM on the previous page is equivalent to:

## Slide 15: How to Compute Quaternion from a DCM
It was just shown that in terms of quaternion elements, a DCM can be written as
The trace of the DCM (sum of diagonal elements) is
  tr( DCM ) = 3q02 – q12 – q22 – q32 = 4q02 – 1 , since 1 = q02 + q12 + q22 + q32
  or, q0 = ½ sqrt( 1 + tr( DCM ) )
Then, the vector components of the quaternion (q1, q2 , q3 ) can be computed from
Care should be taken if the scalar element, q0, is zero (total rotation angle is 180°), as this algorithm is not sufficient (but, another more general form is available)
    Common examples of this situation are single axis rotations of ±180°

## Slide 16: Example: Calculation of Euler angles from a Quaternion:
  If q is a quaternion for orientation of a rotated reference frame relative to some original reference frame, first compute the equivalent DCM from:
  Then, from this DCM, the Euler angles for a particular rotation sequence can be expressed directly. For example, if q corresponds to a yaw-pitch-roll Euler angle sequence, the DCM above can be expressed in terms of those Euler angles as:
  Therefore, tan(f) = DCM23 / DCM33 = 2( qoq1 + q2q3 ) / ( qo2 – q12 – q22 + q32 )
  tan(y) = DCM12 / DCM11 = 2( qoq3 + q1q2 ) / ( qo2 + q12 – q22 - q32 )
  sin(q) = -DCM13 = -2( q1q3 – q0q2 )

## Slide 17: Example: Calculation of Euler angles from a Quaternion:
As a numerical example, consider a yaw-pitch-roll (y,q,f) Euler sequence with
f = -30 °, q = 20 °,y = 10°
  The quaternion for this orientation is computed from the following (or from expressions on page 7):
  q = [ cos((y/2) , sin (y/2) ( 0 0 1 ) ] * [ cos((q/2) , sin (q/2) ( 0 1 0 ) ] * [ cos((f/2) , sin (f/2) ( 1 0 0 ) ]
  or, q = [ cos(5) , 0 , 0 , sin (5 ) ] * [ cos(10) , 0 , sin (10) , 0 ] * [ cos(-15) , sin (-15) , 0 , 0 ]
  q = [ 0.943714 , -0.268536 , 0.144878 , 0.127679 ]
  The DCM for this orientation is computed from from the quaternion above (or traditional methods not covered here):

## Slide 18: Time Propagation of a Quaternion
The time derivative of a quaternion can be computed from Poinsot’s equation
where w is angular rotation rate of the reference frame axes, written as a quaternion with zero scalar part, w = ( 0 , w )
The Poinsot Equation is sometimes written as either of the following matrix / vector products:
Note that Q* in equation to the left above is last three columns of the “quaternion matrix”, Q, used in the matrix-vector product quaternion multiplication representation, and W in the second equation on the right above is the “quaternion transmuted matrix” with zero scalar part, both of which were discussed in Part 1 of this presentation
Quaternion propagation requires 4 states (or, if the unit quaternion constraint is used
( | q | = 1 ), this can be reduced to three)

## Slide 19: Single axis rotation with quaternion
Calculation of quaternion to rotate from one reference frame to another in a single axis rotation:
  If qA is quaternion for orientation of reference frame “A” relative to some base reference frame and qB is quaternion for orientation of another reference frame “B” relative to that same base reference frame
  Dq = (qA-1) qB is quaternion for orientation of reference frame
  “B” relative to reference frame “A”, where qA-1 is inverse of qA
  (if quaternions are unit quaternions, q-1 = q* (conjugate) )
  Since Dq = ( cos(q/2), n sin(q/2) ) = ( q0 , ( q1 i + q2 j + q3 k ) ) the single axis angular rotation to go from frame A to frame B is: qTotal = 2 cos-1( q0 )
  This angle, qTotal, is a right-hand-rule rotation about the unit vector, n, required to align reference frame A with frame B in a single rotation, where n is:
    n = ( q1/sin(qTotal /2) iA + q2/sin(qTotal /2) jA + q3/sin(qTotal /2) kA )
xA
yA
zA
qTotal
n

## Slide 20: Single axis rotation with quaternion - rotations about individual xyz axes
The total right hand rule rotation angle required to rotate with a single rotation frame A to frame B can be expressed as individual, simultaneous rotations about the frame A xyz axes:
  Then, n on the previous slide can be written as:
  The individual rotations about xyz axes that will simultaneously orient the “A” frame with the “B” frame are
  To ensure that the rotation is the “short way around”, or < 180°, make sure that the scalar part of the Dq quaternion is positive (if negative, negate the entire quaternion)

## Slide 21: Introduction to Quaternions Part 2 of 2 Summary
Parts 1 and 2 of this presentation described the mathematical background and use of quaternions for kinematics applications and included:
  Part 1 of 2 – “Introduction to Quaternions”
    Definition, mathematical pre-requisites, and quaternion properties
    Comparison with Euler angles and direction cosine matrix (DCM)
    Part 2 of 2 – “Working with Quaternions”
  How quaternions are used for kinematics
  Defining quaternions for a particular coordinate frame rotation
  Using quaternions for coordinate transformations of vectors
  Calculation of DCM from quaternion, and vice-versa
  Time Propagation of quaternions
  Using quaternions for a single axis rotation to align one coordinate frame with another