## Slide 1
The Representations and Practices of the Discipline of Systems Engineering
Dr. Stephen B. Johnson
Dependable System Technologies, LLC
University of Colorado, Colorado Springs

## Slide 2: Part 2 of 2 Papers
This paper is part two of two papers on the Theory, Representations and Practices of DSE
This paper covers an addition to the theoretical bases and principles, and the strategies, representations, and practices.
Part 1: Stephen B. Johnson, “Theoretical Foundations of the Discipline of Systems Engineering”, AIAA SciTech/Infotech Conference, San Diego, California, 4 January 2016
  Covers Motivation, Approach, Bases, and Principles

## Slide 3: Summary of Paper #1: “Theory of DSE” Motivation & Approach
The Problems with Traditional SE
  Too often, programs fail, slip schedules, overrun budgets
  Complaints that it costs too much, compared to benefits
New approach: model the new “Discipline of SE” on how “Classical Engineering Disciplines” work
  CEDs: theory to model of product, run analyses and compare results to needs, requirements, expectations, in spiral development with product
  Reasons; state-based models and rigor:
    Significantly reduces communication mistakes
    Increases the probability of finding individual mistakes
    This reduces chances of failure and hence reduces cost overruns & schedule slips

## Slide 4: How Do Classical Engineering Disciplines Work?
Physical laws, logical relationships, theory
Theory applied via models to the application/system
System development progressively, iteratively refines the system model and the system design
Discussion, analysis, mainly/significantly through the model to project understanding and expectations of the system
Theory
Applied via model
Generate analysis
results
Compare to
design

## Slide 5: The Bases of DSE (paper 1 summary)
System Basis
  Systems theory applies, particularly concepts of hierarchy and recursion
Value Basis
  Von Neumann-Morgenstern value-utility theory should be used as much as practicable
Model Basis
  Use models instead of natural language documents
State Basis and Functions
  Functions defined as mapping from input state vectors x(t) to output state vector y(t): y(t) = f(x(t))
Goal Basis
  Goals (requirements) are state variables within constraints: g = lower limit < y(t) < upper limit
Control Basis
  Control of state variables is the basis of the system and all of its functions
Knowledge Basis
  Probability theory to model uncertainties in knowledge about the system, environment, internal & external context
Predictive Basis
  Probability theory to model uncertainties in prediction (cost, schedule, performance)

## Slide 6: Strategies of SE (1)
System theory strategies
  DSE shall divide its space of representation into the system, the system’s environment, and the system’s internal and external contexts.
  In hierarchical representations, DSE concepts will typically be applied recursively to each level of the hierarchy.
Value theory strategies
  DSE prefers to construct von Neumann-Morgenstern (vN-M) utility functions whenever possible.
  When it is not possible to construct vN-M utility, other goals, constraints, or uses of the system shall be used to define system goals and preferences.
  Specification of requirements should be delayed as long as practicable during system design and development, in favor of negotiable preferences.
  Note: SBJ skepticism about full applicability of value theory
Model strategies
  DSE shall maximize the use of models to represent, maintain, and generate knowledge.
  DSE system-level representations shall at a minimum include those for value, optimization, intention, design, performance, behavior, and agency.
  DSE shall provide abstract, system-level-compatible representations of discipline models.

## Slide 7: System, Environment, Internal & External Context
 | Controllable by project | Not Controllable by project but influences and can be influenced by system
Operational | System (includes system and orgs/people that operate it) | Environment (immediate operational environment the system interacts with)
Non-Operational | Internal Context (org that designs & builds system) | External Context (orgs, politics, culture, economics)
SE directly develops the system, through the organizations of its “internal context”.
SE must account for the environment.
SE coordinates preferences from the external context to system goals through the value model.

## Slide 8: Strategies of SE (2)
State strategies
  DSE shall maximize, to the extent practicable, the use of state variables in its representations.
  DSE shall define functions as mappings of input states of state variables to output states of state variables, y = f(x).
Goal strategies
  To the maximum extent practicable, DSE shall define goals as constraints on the ranges of output state variables of a function over a specified period of time. Goal = rl < y < rh , where y = f(x) between times t0 and t1.
  DSE shall represent system goals both in terms of operational description and of hierarchy.
Control strategies
  DSE shall deploy passive and active means to control state variables within appropriate constraints so as to achieve the corresponding goal.
  DSE shall use and extend classical control theory concepts of state estimation and state control to assess the system’s ability to achieve goals.
  DSE shall simultaneously with nominal system design also address design of the system to mitigate the failure to achieve goals

## Slide 9: Strategies of SE (3)
Knowledge strategies
  DSE shall use existing sources of knowledge about the system.
  DSE shall accept the variability of human interpretation of acceptable and expected system behaviors.
  DSE shall maximize to the extent that is cost-effective the provision of automated means to cross-check the validity and consistency of information across all representations using different, overlapping knowledge sources.
  DSE shall estimate uncertainties of knowledge about the system, environment, internal context and external context.
Predictive strategies
  DSE shall use predictive models of performance, dependability, cost, and schedule.
  DSE predictive models shall include assessments of uncertainty.

## Slide 10: Loop-Spiral of DSE Representations
Physical Simulation Models
Value-Decision
Model
Concept of
Operations
Model
State Machine Model
Pattern Recognition and Anomaly Detection
Goal-Function
Tree
Fault Tree
Design Model
Failure Propagation Model
Physical Containment Model
Organization Hierarchy Model
Anomaly Investigation
Performance Models
Rounded boxes
are functions,
not models.
Tests
Models of Preference
Models of Intention
Models of Design
Models of Agency
Models of Failure
Models of Behavior
Cost & Schedule Models
Design
Optimization

## Slide 11: Traditional SE Process
Concept of Operations
(ConOps) Document
System Requirements
Document
Interface
Requirements
Documents
Requirements
Traceability
Subsystem
Requirements
Documents
Interface
Control
Documents
V&V Plan
Requirements
Traceability to V&V Plan
V&V
Procedures
Design
Design
Design
Design
Requirements
Traceability to Design
Requirements
Traceability to V&V
Procedures
Build Components
Integrate
Components
To Boxes
Integrate
Boxes to
Subsystems
Integrate
Subsystems
To System
Verify
System
Validate
System
Verify
Subsystems
Verify
Boxes
Verify Components
Verification
Traceability to
Components
Verification
Traceability to
Boxes
Verification
Traceability to
Subsystem
Verification
Traceability to
System
Configuration Management Process Controls ALL Products
Design
Functions
Functions
Disciplines &
Organizations
Disciplines &
Organizations

## Slide 12: Using DSE Models
GFT to Fault Trees
  Logical complement of GFT, then add new failure branches
  Fault trees have more branches than success trees, because failures create new “off-nominal paths” in the system
  More generally, failure space models are the “more complete” system models than success space models
GFT-Functions & Requirements to Organizations and Organization Interfaces
  State variables key
  GFT  Design Model  Physical Containment Model (Configuration Items)  Organization Model
Nominal and Failure Scenarios for Requirement Verification
  Paths from bottom to top of GFTs and Fault Trees, when implemented with state variables
  Test procedures and observables extracted from trees

## Slide 13: Traceability from Functions to Organizations; GFT to Fault Trees
Fcn 1
G(y)
Fcn 2a
Fcn 2b
Fcn 2c
G1(y1)
G2(y2)
G3(y3)
Design 2a
Fail 1
Ḡ(y)
Fail 2a
Fail 2b
Fail 2c
Ḡ1(y1)
Ḡ2(y2)
Ḡ3(y3)
Design 2c
Design 2b
Design 1
Design 3b
y1
y3
x3
y2
y
Logical Complement
GFT
Fault Tree
Fail 2d
Ḡ4(y4)
Design
Design 2a
Design 2c
Design 2b
Design 1
Design 3b
y1
y3
x3
y2
y
Diagnostic Model
Design 2d
y4
System
G(y)
Ele 2a
Ele 2b
Ele 2c
G1(y1)
G2(y2)
G3(y3)
Physical
Containment
Prime
G(y)
SubC 2a
SubC 2b
SubC 2c
G1(y1)
G2(y2)
G3(y3)
Organization
Hierarchy
System, Element, and Interface Requirements
Documents
State variables exist in design & GFT
Failures sometimes create new paths
State variables mostly same for failure as for success
TEAMS Model mostly same as design model, except for new paths
Design includes component interfaces
Interfaces include failure behaviors
Physical interfaces usually match organizational interfaces
Physical interface goals (requirements) extracted to documentation

## Slide 14: Experience with DSE Methods
On NASA SLS, some DSE models developed & used
Goal-Function Tree
  Used for fault management design (coverage of failure detections to protect system goals like crew safety and mission trajectory)
Failure Propagation Model
  Used for analysis of failure effects, criticality, launch commit criteria, fault isolation/diagnostics analysis, latent failure analysis
State Machine models
  Used for debugging / testing algorithms, flight sequences
  Pre-running and assist generation of test scripts
No integration between models so far, but we’re thinking about it!