## Slide 1: NESC GN&C Technical Discipline Team Webcast Series

## Slide 2
Volume Control* | Polls (if any) | Ask a Question | Files (if any)
*Hover your cursor over the speaker icon to access the volume slider.

## Slide 3: Deep Space Mission Design
Dennis Byrnes
Chief Engineer for Flight Dynamics
JPL

## Slide 4: Introduction
So what is Mission Design anyway?
  Is it different from Mission Architecture?
  What about Mission Analysis, Mission Engineering, Navigation?
Mission Design is a systems engineering discipline since it looks at the entirety of the mission. It is also a sub-system since it interacts with other sub-systems (spacecraft, power, comm, etc.)
Mission Design, Navigation and GN&C in general are all part of the field of Astrodynamics

## Slide 5: What do we do?
We always start by asking lots of questions
  What Solar System body are we going to?
  Flyby? Orbiter? Lander? Combination?
  Are the science requirements specified?
    Do they come from a PI? A science group? A decadal survey?
    Do they want mission design feedback/interaction?
  What is the launch timeframe?
  What are the cost limitations?
  What kinds of trajectories are possible?
  Are there limits on total flight time?
  3-axis or spinner? Momentum wheels or thrusters or both? Instrument keep-out zones? Environmental considerations (radiation, dust storms, variable height atmosphere, land in a boulder field, …)
  Planetary protection – Earth and/or target body(ies)
We try to think “out of the box.”
We Do Trades!

## Slide 6: When is Mission Design Done?
We start “pre-pre-Phase-A”
  Brainstorming, studies, “back-of-the-envelope” calculations, concepts, …
Many managers think most mission design is in pre-Phase A and in Phases A&B and nearly complete in Phase C.
NOT TRUE!
Mission design continues right to launch and for many missions up to the completion of an extended mission.

## Slide 7: Orbit Transfers

## Slide 8: Mars Pork Chop

## Slide 9: 2011 Type 1 Launch/Arrival Space
VE-Inertial = 6.1 km/s  VE-Rel = ~5.9 km/s*
VE-Inertial = 6.1 km/s
C3 = 20.1 km2/s2
*VE values correspond to prograde entries and vary as a function of latitude.
Available LD/AD space that meets both injected mass and entry speed requirements
78 days after close of Juno launch period (11/13)
Ls = 170
No LD/AD available with
VE-Rel = ~5.6 km/s in Type 1 region

## Slide 10: 2011 Type 2 Launch/Arrival Space
DLA = 28.5 deg
*VE values correspond to prograde entries and vary as a function of latitude.
78 days after open of Juno launch period (10/22)
VE-Inertial = 5.8 km/s  VE-Rel = ~5.6 km/s*
C3 = 20.1 km2/s2
78 days after close of Juno launch period (11/13)
VE-Inertial = 5.8 km/s
Possible MSL Launch Days
Contingent on Juno’s Launch
Available LD/AD space that meets both injected mass and entry speed requirements
Ls = 170
Available LD/AD space that satisfies injected mass, entry speed, launch pad turn around and Ls constraints
Significant Injected mass degradation
(DLA > 35 deg)

## Slide 11: Type 2 Launch Period (TS1, 25°N – 20°N*)
24 Days
*Includes Mawrth.
78 days after open of Juno launch period (10/22)
78 days after close of Juno launch period (11/13)
VE-Inertial = 5.8 km/s  VE-Rel = ~5.6 km/s**
10/22
11/14
**VE values correspond to prograde entries and vary as a function of latitude.
Ls = 170

## Slide 12: Type 2 Launch Period (TS2, 20°N – 5°N*)
24 Days
78 days after open of Juno launch period (10/22)
78 days after close of Juno launch period (11/13)
VE-Inertial = 5.8 km/s  VE-Rel = ~5.6 km/s**
*Includes Syrtis (possible candidate landing site).
10/22
11/14
**VE values correspond to prograde entries and vary as a function of latitude.
Ls = 170

## Slide 13: Type 2 Launch Period (TS3, 5°N – 27°S*)
24 Days
78 days after open of Juno launch period (10/22)
78 days after close of Juno launch period (11/13)
VE-Inertial = 5.8 km/s  VE-Rel = ~5.6 km/s**
*Includes Gale, Margaritifer (possible candidate landing site), Eberswalde, and Holden landing sites.
10/22
11/14
**VE values correspond to prograde entries and vary as a function of latitude.
Ls = 170

## Slide 14: Type 1B Launch Period (25°N – 27°S*)
*Includes Mawrth, NE Syrtis, Gale, E Margaritifer, Eberswalde, and Holden landing sites.
Contains JPL or Caltech proprietary information; not for public dissemination.
VE-Inertial = 6.1 km/s  VE-Rel = ~5.9 km/s**
78 days after close of Juno launch period (11/13)
11/25
12/18
**VE values correspond to prograde entries and vary as a function of latitude.
24 Days
Max. C3
~ 20.0 km2/s2
Max. Vrel
~ 5.9 km/s
Max. DLA
~ 17.0 deg
Ls = 170

## Slide 15: MRO Aerobraking

## Slide 16: Genesis

## Slide 17: Dawn
A Mission to the two Largest Main Belt Asteroids - Vesta and Ceres

## Slide 19
Final HAMO to LAMO Transfer Design
Greg Whiffen, Dan Parcher, John Smith
11/7/2011

## Slide 23
Thrust Vectors!

## Slide 24: GRAIL (Gravity Recovery and Interior Laboratory)
Or
GRACE at the Moon!

## Slide 25: GRAIL Mission Timeline
Mission Phases
Launch Phase
Trans-Lunar Cruise (TLC) Phase
Lunar Orbit Insertion (LOI) Phase
Orbit Period Reduction (OPR) Phase
Transition to Science Formation (TSF) Phase
Science Phase
Decommissioning Phase

## Slide 26: Orbiter Separation Strategy – 2009 MDNAV PR (1 of 2)
OTM-B1
OTM-B2
TSM-B3
75
85
225
65
Lower bound on separation distance (for science)
Upper bound on separation distance (for multipath and link margin)
Actual multipath constraint

## Slide 27: Galileo
A Mission to Jupiter
Probe (1995)
Orbiter (1995 – 2003)

## Slide 40: The Future

## Slide 41: Thrusts
Efficiently explore multiple encounter tour designs
Design innovative and efficient low energy transfers, captures, and orbits
Close-proximity trajectory design for small-body missions
Design trajectories for missions that involve multiple spacecraft elements

## Slide 42: 14–22 Months of SEP Thrusting Efficiently Increase Energy with Respect to Earth
Exterior and interior leveraging transfers increase the C3 for an outbound or inbound flyby 14–16 mo. after escape
Similar transfers are available 6 mo. earlier, introducing primary and backup launch opportunities

## Slide 43: Gravity-Assist Tours
Used with great success by missions from Mariner 10 through Galileo and Cassini
Enables orbit diversity for minimal propellant
Gravity-Assists are an enabling technology for outer planet missions

## Slide 44: Pathfinding Problem
The possible sequences of flybys quickly becomes overwhelming
Many solutions, but only a few “gems”
Pathfinding is the problem of picking through the possible combinations to find a good tour
Notes: Mention science requiremnts for ‘gems’

## Slide 46
Global Trajectory Optimization Competition:
Worldwide competition sponsored by the Advanced Concepts Team from the European Space Agency
The problem was a low-thrust mission to impact a specified asteroid
Our team from JPL won the competition
MALTO was a key component of our optimization strategy
Winning entry from JPL
Trajectory path:
Earth
Venus
Earth
Earth
Earth
Jupiter
Saturn
Jupiter
Asteroid

## Slide 47: Reference Material
Website: “Basics of Space Flight”
  http://www.jpl.nasa.gov/basics
Encyclopedia of Aerospace Engineering, J. Wiley & Sons, 10th edition. (All NASA sites have institutional access)
  http://onlinelibrary.wiley.com/book/10.1002/9780470686652 (table of contents)
    Dynamics and Control
      Trajectory and Orbital Mechanics
        Orbital Mechanics Fundamentals
        Mission Design and Trajectory Optimization

## Slide 48: Questions? Answers! dennis.v.byrnes@jpl.nasa.gov

## Slide 49: Upcoming NESC GN&C Webcasts
    “Fundamentals of Launch Vehicle Flight Control”, John Rakoczy (MSFC), on 16 May 2012
    “Fundamentals of Spacecraft Attitude Control”, on 18 July 2012
    “Fundamentals of Aircraft Flight Control”, on 19 September 2012
    “Fundamentals of Adaptive Control”, Irene Gregory (LaRC), on 21 November 2012
    “Fundamentals of Spacecraft Attitude Determination”, Prof. John Crassidis (Univ. of Buffalo), on 16 January 2013