## Slide 1: Fundamentals of EMC Mitigation Strategies
John McCloskey
NASA/GSFC Chief EMC Engineer
Code 565
Building 23, room E203
301-286-5498
John.C.McCloskey@nasa.gov

## Slide 2: Topics
Twisted Pairs
Shielding
Method of Images
Balanced Differential Interfaces
Filter Connectors
Radiated Coupling Strategies
Cost/Benefit Analysis

## Slide 3: Twisted Pairs
Emissions
  Provides return current path to cancel culprit current
  Reduced net current reduces net magnetic field
Susceptibility
  Reduced loop area
  Voltages induced on adjacent half-twist loops cancel
  Worst case induced voltage is that induced on loop area of single half twist
VC
RL
CULPRIT CIRCUIT
VICTIM CIRCUIT
RNE
RFE
IC
IC
Total enclosed I 0
Net B  0
+
-
+
-
+
-
+
-
+
-
VHT1
VHT2
VHT3
VHT4
VHT5
I
B
Poynting Vector
Right Hand Rule
H
E
P

## Slide 4: More Twisted Pairs

## Slide 5: Shielding
Purpose of shielding:
  Contain emissions from noisy circuits
  Protect signal carrying conductors from interference
Remember Kirchoff’s Current Law:
  All currents return to their sources following path of least impedance
Shield’s raison d’être:
  Provide return path to the source over the lowest impedance (most desirable) path possible
  Direct current back to source and away from sensitive circuitry

## Slide 6: Cable Shielding - Capacitive Coupling
Emissions
  Culprit current couples to its own shield and returns to its source
Susceptibility
  Any remaining current that makes its way to victim couples to victim’s shield and gets shunted back to source (via ground), protecting victim signal wire
Shields must provide low impedance path back to source
  Includes shield terminations, connector to chassis connections, reference plane to chassis connections, etc.
VC
RL
CULPRIT CIRCUIT
VICTIM CIRCUIT
RNE
RFE
CCV
ICV
IC

## Slide 7: Cable Shielding - Inductive Coupling
Emissions
  Provides return current path to cancel culprit current
  Reduced net current reduces net magnetic field
Susceptibility
  Reduced loop area
  Any remaining B field induces V and I in shield to counter incident field
  Shield must be terminated at both ends to allow current to flow
CULPRIT CIRCUIT
VICTIM CIRCUIT
RNE
RFE
VC
RL
IC
IC
Total enclosed I 0
Net B  0
+
-
VVS
IS
Induced shield voltage/current and resulting B field to counter incident field

## Slide 8: Skin Depth
x
100 mils (2.54 mm) of aluminum provides > 80 dB attenuation above 100 kHz
SKIN DEPTH
ABSORPTION LOSS (ATTENUATION)

## Slide 9: Enclosure Shielding - Seams and Penetrations
Metal chassis provides darned good shielding (previous slide)
Weak point always comes at seams and penetration points
  Poor connections allow ΔV between conductors (antenna)
  ΔV induces common mode current (ICM) across connection impedance
  ICM induces radiated fields
ΔV
ΔV
ICM
ICM
SHIELD
SIGNAL CONDUCTOR

## Slide 10: Enclosure Shielding - Seams and Penetrations (cont.)
Good metal-to-metal contact is essential
  RF gaskets on all seams and penetrations
  360o termination of shield to backshell (NO PIGTAILS!!!)
  Good metal-to-metal contact between backshell and chassis
  Class R bonds
SHIELD
SIGNAL CONDUCTOR
RF gaskets
360o shield termination
Good backshell to chassis connection

## Slide 11: Enclosure Shielding - Seams and Penetrations (cont.)
Reference planes should be bonded to chassis at I/O connector(s)
  Provide low impedance path for currents to return to source
  Minimize ΔV between reference plane and chassis
  Reduce radiated emissions
SHIELD
SIGNAL CONDUCTOR
REF
ΔV → 0
ICM

## Slide 12: Enclosure Shielding - Seams and Penetrations (cont.)
“Pigtail” termination has significant inductance
Allows ΔV between conductors (antenna)
ΔV induces common mode current (ICM) across connection impedance
  ICM induces radiated fields
SHIELD
SIGNAL CONDUCTOR
“PIGTAIL” termination
ΔV
ICM

## Slide 13: Enclosure Shielding - Seams and Penetrations (cont.)
Alternative for panel to panel seams
  Minimum of 2 right angle turns (“labyrinth”)
  Electromagnetic energy has to “work” harder to get through seam

## Slide 14: Demo 8: Twisted Pairs and Shielding

## Slide 15: Demo 8: Twisted Pairs and Shielding (cont.)
TWISTED PAIRS
SHIELDING

## Slide 16: Demo 8: Twisted Pairs and Shielding (cont.)
Equipment
  R&S FSH4 spectrum/network analyzer
  Test fixture
  2 Large coax cables to connect analyzer to fixture
  Single wire fixture with banana-BNC adaptors at each each
  Twisted pair fixture with banana-BNC adaptors at each end
  RG-58 coax with BNC-banana adaptors at each end, plugging into banana-BNC adaptors at each end
  Velcro straps

## Slide 17: Demo 8: Twisted Pairs and Shielding (cont.)

## Slide 18: Demo 8: Twisted Pairs and Shielding (cont.)

## Slide 19: Compiled Data – Pigtails of Varying Lengths

## Slide 20: Pigtail Observations
Quantifiable frequency range: ~ 1 MHz to ~ 20 MHz
  Below 1 MHz, measurements are limited by noise floor of analyzer
  Above ~20 MHz, standing wave effects appear
  l = ~70 cm = λ/4 @ ~110 MHz
Pigtails are reasonably effective at low frequencies, but become less effective as frequency increases
Pigtail of any length (presence of BNC-to-banana adaptors in this case) significantly degrades shield effectiveness above 1 MHz
Curves for longer pigtails rise above noise floor at lower frequency (lower “knee” frequency for longer pigtails)
Shielding effectiveness degrades at 40 dB/decade
  Compared to 20 dB/decade for unshielded wire
  Secondary coupling from shield to center conductor

## Slide 21: Method of Images
Routing cables/traces over ground plane implements the “method of images”
  When a charge is placed over a ground plane, the fields line up to effectively create an image charge of opposite polarity (or cable with opposite potential and current)
  Physically, return current flows back to source on ground plane immediately beneath cable/trace
  Fully enclosed “Faraday cage” not necessary for ground plane to provide benefit
I
+V
-I
-V
E
I
+V
E
B
B
NO GROUND PLANE
Fields radiate
WITH GROUND PLANE
Localized return path for CM current
Fields better contained; partially cancelled by “image”
Reduced loop area reduces susceptibility
THE GROUND PLANE IS OUR FRIEND!

## Slide 22: Method of Images - Crosstalk Data
2 WIRES SEPARATED BY 2 cm
VARYING HEIGHTS ABOVE GROUND PLANE

## Slide 23: Balanced Differential Interfaces
Emissions
  Equal and opposite potentials on (+) and (-) conductors
  Emitted electric fields cancel
Susceptibility
  Incident field couples common current to (+) and (-) conductors
  Common impedance to ground results in common voltage on (+) and (-) conductors
  Differential interface subtracts out common mode voltage
CULPRIT CIRCUIT
VICTIM CIRCUIT
RNE
RFE
RL
VC+
VC-
CCV
CCV
ICV
ICV
+
-

## Slide 24: Differential Interface Examples
RS-422
MIL-STD-1553B
Low Voltage Differential Signal
(LVDS)

## Slide 25: Filter Connectors
Connectors provide capacitor to connector shell
Attenuate high frequencies
Designer must make sure desired frequencies pass
T = 1/f
τr
τf
τ
Frequency content
0 dB/decade
-20 dB/decade
-40 dB/decade
PULSE WIDTH
RISE/FALL TIME
f
Amplitude

## Slide 26: Radiated Coupling – Mitigation Strategies
Shielding, yes, but also:
  Terminate all shields entering or exiting a box to chassis with full 360 degree coverage
  Use EMI gaskets on all chassis seams (connectors, lids, etc.)
  Control common mode currents (Yin/Yang relationship between conducted and radiated coupling)
    Minimize loop areas
    Provide low impedance path for currents back to source
    Route cables/traces over ground plane (“method of images” - next slide)
    On PCB boards, avoid routing traces over split ground planes
In general, same techniques help with both emissions and susceptibility
Icm
Icm
SHIELD TERMINATED TO CHASSIS
REDUCED RADIATED EMISSIONS
CONTROLLED COMMON MODE CURRENTS

## Slide 27: Cost/Benefit Analysis
Cost of implementing recommendations in this presentation:
  Trivial if integrated into design process and implemented early
Cost of EMI problems late in project flow
  Engineer’s salary: ~$1000/day ($125/hr)
  Team of 10 engineers: ~$10,000/day
  10 working days in I&T: ~$100,000
This is very much a “low ball” estimate
  Much direct experience
  Summer 2013: Out of house instrument, larger team, 3 week delay in EMI test campaign
  ~$500 k cost to project
“An ounce (or a few $) of prevention is worth a few $100 k of cure”

## Slide 28: If You Remember Nothing Else From Today…
DO YOU KNOW WHERE YOUR CURRENTS ARE FLOWING?