## Slide 1
Random Vibration

## Slide 2
NASA Engineering & Safety Center (NESC) Academy
Dynamic Concepts, Inc. Huntsville, Alabama

## Slide 3
Tom Irvine
Email: tirvine@dynamic-concepts.com
Phone: (256) 922-9888

## Slide 4
Random Vibration Examples
Turbulent airflow passing over an aircraft wing
Oncoming turbulent wind against a building
Rocket vehicle liftoff acoustics
Rocket engine structural-borne vibration
Earthquake excitation of a building

## Slide 5
Random Vibration Characteristics
One common characteristic of these examples is that the motion varies randomly with time. Thus, the amplitude cannot be expressed in terms of a "deterministic" mathematical function.
Dave Steinberg wrote:
    The most obvious characteristic of random vibration is that it is nonperiodic. A knowledge of the past history of random motion is adequate to predict the probability of occurrence of various acceleration and displacement magnitudes, but it is not sufficient to predict the precise magnitude at a specific instant.

## Slide 6
Optics Analogy
Sinusoidal vibration is a like a laser beam.
Random vibration is a like “white light.” White light passed through a prism produces a spectrum of colors.

## Slide 7
Sample Random Time History

## Slide 9
Random Vibration Examples
Random Vibration Descriptive Statistics | 
Parameter | Value
Duration | 4 sec
Samples | 4000
Mean | 0.00
Std Dev | 0.59 G
RMS | 0.59 GRMS
Kurtosis | 3.04
Maximum | 2.30 G
Minimum | -1.96 G

## Slide 10
RMS and Standard Deviation
 = standard deviation
    [ RMS ] 2 = [  ] 2 + [ mean ]2
RMS =  assuming zero mean

## Slide 11
Peak and RMS values
Pure sine vibration has a peak value that is 2 times its RMS value.
Random vibration has no fixed ratio between its peak and RMS values.
The ratio between the absolute peak and RMS values in the previous example is
2.30 G / 0.59 G = 3.90 (crest factor)

## Slide 12
Peak Level
Random vibration is often considered to have a 3 peak for design purposes.
But higher peaks may occur.

## Slide 14
Histogram Comparison
Sine Vibration has bathtub shaped histogram
  Sine vibration tends to linger at its extreme values
Random Vibration has a bell-shaped curve histogram
  Random vibration tends to dwell near zero
  But also has some high peaks

## Slide 15
Probability Values for Random Signal
Normal Distribution
Statement | Probability Ratio | Percent
- < x < + | 0.6827 | 68.27%
-2 < x < +2 | 0.9545 | 95.45%
-3 < x < +3 | 0.9973 | 99.73%

## Slide 16
More Probability
Normal Distribution
Statement | Probability Ratio | Percent
¦ x ¦ >  | 0.3173 | 31.73%
¦ x ¦ > 2 | 0.0455 | 4.55%
¦ x ¦ > 3 | 0.0027 | 0.27%

## Slide 17
Using Probability Values
The probability tables can be used as follows.
Suppose that a random vibration time history has a total duration of 60 seconds. For what amount of time will the amplitude exceed 1 in terms of absolute value?
    (60 sec)(0.3173) = 18.22 sec
Suppose the same time history is digitized such that it consists of 200,000 points. How many points will exceed 2 in terms of absolute value?
    ( 200,000 )( 0.0455 ) = 9100 samples

## Slide 18
Probability Exercise
Use program: stats.exe
Select: Normal Distribution
Select “Calculate probability for a given Z value.” Note that Z represents s assuming a zero mean.
Click on –Z to +Z
Input Z=4 which is equivalent to 4s
What is the probability that a random time history will have points greater than 4s in terms of absolute value?
Given a time history with 100,000 points, how many will exceed 4s in terms of absolute value?

## Slide 19
Program stats.exe

## Slide 21
Probability of Exceeding
Probability of exceeding 4s
= 6.33E-05
Assume a time history with 100,000 points.
100,000 x 6.33E-05 = 6.3 points exceeding 4s

## Slide 22: SDOF System Subject to Base Excitation
The natural frequency is

## Slide 23
Rayleigh Distribution
Consider a lightly damped, single-degree-of-freedom system subjected to broadband random excitation.
The system will tend to behave as a bandpass filter.
The bandpass filter center frequency will occur at or near the system’s natural frequency.
The system response will thus tend to be narrowband random.
The probability distribution for its instantaneous values will tend to follow a Normal distribution, which is the same distribution corresponding to a broadband random signal.
The absolute values of the system’s response peaks, however, will have a Rayleigh distribution.

## Slide 24
Rayleigh Probability Table
Rayleigh Distribution Probability for Response Peaks | 
 | Prob [ A >  ]
0.5 | 88.25 %
1.0 | 60.65 %
1.5 | 32.47 %
2.0 | 13.53 %
2.5 | 4.39 %
3.0 | 1.11 %
3.5 | 0.22 %
4.0 | 0.034 %
Thus, 1.11 % of the peaks will be above 3 sigma for a signal whose peaks follow the Rayleigh distribution.

## Slide 25
Exercise: generate.m - White noise
>> generate
generate.m version 2.7 November 1, 2010
By Tom Irvine Email: tomirvine@aol.com
Enter the signal type
1=sine
2=cosine
3=damped sine
4=sine sweep
5=white noise
6=terminal sawtooth pulse
7=half-sine pulse
8=versed sine pulse
9=wavelet
5
Enter the duration (sec) 50
Enter the sample rate (samples/seconds) 2000
Enter the standard deviation 2
The time history is renamed as "white_noise"

## Slide 26
100,000 Samples.
The 4s level is 8 G.
There are 7 peaks which exceed 4s.
The number of expected peaks was 6.3
(Your time history may be different based on random number generator)

## Slide 27
signal_stats.exe
>> signal_stats
signal_stats.m
ver 3.1 November 10, 2010
by Tom Irvine Email: tomirvine@aol.com
This program gives statistics and plots for
PSD, SRS and time history functions.
Select function:
1=PSD
2=SRS
3=VRS
4=SPL
5=time history
5
The time history must be in a two-column matrix format:
Time(sec) & amplitude

## Slide 28
Select file input method
1=external ASCII file
2=file preloaded into Matlab
3=Excel file
2
Enter the matrix name: white_noise
Time Stats
start = 0 sec end = 50 sec duration = 50 sec
number of samples = 100001
Time Step
dtmin = 0.0005 sec
dt = 0.0005 sec
dtmax = 0.0005 sec
Sample Rate
srmin = 2000 samples/sec
sr = 2000 samples/sec
srmax = 2000 samples/sec

## Slide 29
Amplitude Stats
number of points = 100001
mean = -1.37e-016 std = 2 rms = 2
max = 8.203 at = 9.063 sec
min = -9.527 at = 47.22 sec
crest factor = 4.764
skewness = -0.01831 kurtosis = 2.992
positive zero crossings = 24991
negative zero crossings = 24992
number of positive peaks = 29259
number of negative peaks = 29229
total peaks = 58488
Plot time history file?
1=yes 2=no 2
Plot histogram?
1=yes 2=no 1
Enter the number of bars 21
(Your time history may be different based on random number generator)

## Slide 30
The histogram of white noise signal, which is to be used as a base input to an SDOF system.

## Slide 31
SDOF Response Exercise
Apply the white noise time history as a base acceleration input to an SDOF system with fn = 200 Hz and Q=10.

## Slide 32
Maximum Expected Level
where
fn= natural frequency (Hz) T = duration
The is equation is derived from the Rayleigh distribution.
Consider the response of a SDOF system to base excitation.
The maximum expected response is ls
where

## Slide 33
peak_response_random.exe
Given a duration of 50 seconds and fn=200 Hz, what is the maximum expected peak? 4.29s

## Slide 34
>> arbit
arbit.m ver 2.5 November 11, 2010
by Tom Irvine Email: tomirvine@aol.com
This program calculates the response of a single-degree-of-freedom
system to an arbitrary base input time history.
The input time history must have two columns: time(sec) & accel(G)
Select file input method
1=external ASCII file
2=file preloaded into Matlab
3=Excel file
2
Enter the matrix name: white_noise

## Slide 35
Time Step
dtmin = 0.0005 sec
dt = 0.0005 sec
dtmax = 0.0005 sec
Sample Rate
srmin = 2000 samples/sec
sr = 2000 samples/sec
srmax = 2000 samples/sec
Enter the natural frequency (Hz) 200
Enter damping format: 1= damping ratio 2= Q 2
Enter the amplification factor (typically Q=10) 10

## Slide 36
Acceleration Response
peak =
14.9437
maximum = 14.94 G
minimum = -15.38 G
overall = 3.60 GRMS
mean = 0.00 G
std dev = 3.60 G
crest factor = 4.27
kurtosis = 2.96
Relative Displacement Response
maximum = 0.00376 inch
minimum = -0.00358 inch
overall = 0.000877 inch RMS
(Your time history may be different based on random number generator)

## Slide 37
std dev = 3.60 G Max Absolute Peak is 15.4 G Highest expected peak from Rayleigh distribution is 4.29s or 15.4 G

## Slide 38
There are about 40 positive peaks in 0.2-second interval. Thus, response frequency is 200 Hz. The response is narrowband random.

## Slide 39
The histogram of the SDOF response has a normal distribution.
Accel (G)

## Slide 40: Program & Data Summary for this Unit
Programs
stats.exe
peak_response_random.exe
generate.m
signal_stats.m
arbit.m
Data
Only synthesized data.