## Slide 1
Introduction to On-Orbit Thermal Environments
Part 2

## Slide 2
Part 2 Roadmap
Thermal Radiation Basics
Orbits
Solar Flux
Albedo Flux
Planetary Infrared Flux
Albedo and Planetary Flux Combinations
Beta Angle
Consequences of Beta Angle Variation
Putting It All Together
Other Heating Environments
Solar Zenith Angle
Form Factor
The Celestial Inertial Coordinate System
Projected Area
Time Constant

## Slide 3
Albedo Flux

## Slide 4
Albedo Heating
Partially Illuminated Earth as Seen from Apollo 12
(NASA Photo)
Albedo heating is solar energy reflected from the planet and its atmosphere;
It is not a point source -- it subtends a solid angle and has non-uniform area intensity.

## Slide 5
A Simplified Albedo Model
Analysis of albedo is complicated by its non-uniform area intensity;
We can, however, gain an understanding of the contribution of albedo heating by making some simplifying assumptions;
Corrections to this will be discussed.

## Slide 6
Assumptions for the Simplified Albedo Model
Simplifying assumptions:
Low altitude, circular orbit -- restricts planet viewing to local regions with similar illumination conditions;
Constant albedo factor planet-wide -- uniform albedo factor, with diffuse reflection, is the easiest to model.

## Slide 7
The expression for the simplified albedo flux is formed by considering the following:
intensity of the sunlight striking the planet, qsol;
fraction of sunlight reflected, r (i.e., the albedo factor is just 1 - a);
scaling of intensity from orbit noon (i.e., solar zenith angle, );
local form factor to the planet, FF.
Simplified Albedo Flux Calculation
.

## Slide 8
Aside: Solar Zenith Angle, 
b
q

The solar zenith angle, , is a measure of angular distance from orbit noon;
If orbit angle, q is measured from orbit noon and b is measured from a plane containing the sun, an increase in either parameter results in an increase in .

## Slide 9
Aside: Solar Zenith Angle, 
for:
Mathematically,  is expressed as:
We'll explore b in detail in Part 3.
b
q


## Slide 10
Aside: The Form Factor
A form factor describes how well one object can "see" another object;
The form factor may take on a value from zero to unity.

## Slide 11
Aside: Form Factor
The Nusselt Sphere technique is one of many ways to calculate form factors;
The form factor from dA1 to Surface 2 is calculated as the projected area, AP, divided by the area of the hemisphere's circular base.
Surface 2
dA1
AP

## Slide 12
Aside: Form Factor
Let's use the Nusselt Sphere technique for calculating the form factor to the planet from an orbiting plate, at altitude h above the planet, whose surface normal faces the nadir direction.
Planet
dA1
re
AP
h
re

## Slide 13
Aside: Form Factor
Planet
dA1
re
AP
h
re
re
We see that we can construct a right triangle (in green) with a short side measuring re and a hypotenuse measuring re+h;
We define the angle f by noting:
f

## Slide 14
x
Aside: Form Factor
Planet
dA1
re
AP
h
re
re
Similarly, we can construct a right triangle (in red) with a hypotenuse measuring unity and the angle f, already defined;
We define the distance x by noting:
f
r = 1

## Slide 15
Aside: Form Factor
Planet
dA1
re
AP
h
re
re
Projecting x down to the base, we see that the ratio of the projected circular area to the total area of the base is:
We'll come back to this result in our heating calculations.
f
r = 1
x

## Slide 16
Aside: Form Factor
The forward (east)-, aft (west)-, north- and south-facing surfaces have a different view to the planet due to their orientation.
For these "perpendicular" surfaces, the form factor is presented in Ref. 5 and shown here, without derivation.

## Slide 17
The equation for a nadir-facing plate is:
Simplified Albedo Flux Calculation
re

h
r
Intensity of sunlight striking the planet
Fraction of the sunlight reflected
Scaling of intensity from orbit noon
Local Form Factor to the planet
For:

## Slide 18
Our simplified model isn't perfect but there's a way to correct for albedo by applying this formula:
Note that this correction was derived from data restricted to latitudes of +30° to -30°.
Solar Zenith Angle Corrections
to Albedo (Ref. 6)

## Slide 19
Solar Zenith Angle Corrections
to Albedo (Ref. 6)
Albedo Correction Term, r()
Solar Zenith Angle,  (°)

## Slide 20
Solar Zenith Angle Corrections to Albedo
Solar Zenith Angle,  (°)
Albedo Flux (W/m2)
Corrected Model
Simplified Model
Assumptions:
r = 0.3
qsol = 1367 W/m2
.
Note: Raw flux value with no form factor correction.

## Slide 21
Planetary Infrared Flux

## Slide 22
Planetary Infrared Heating
Thus far, we've discussed natural heating components using illumination in the solar spectrum;
But there is another heating source incident on a spacecraft when in proximity to a planet/moon;
And the heating is concentrated in the infrared portion of the spectrum -- it's called planetary infrared or outgoing long-wave radiation (OLR);

## Slide 23
Simplifying Assumptions for Earth Infrared
We can learn much by examining a simplified representation of Earth's heat balance;
For this analysis, we'll assume that Earth's atmosphere and relatively rapid rotation with respect to the sun results in uniform temperatures over the entire globe; Earth is at thermal radiation equilibrium; and, Earth's albedo is constant over the entire surface.

## Slide 24
The Overall Planetary Heat Balance
The overall planetary heat balance assumes steady state heat transfer -- the amount of heat absorbed by the planet must equal the amount radiated:
Let's take a closer look at each of these terms.

## Slide 25
The Overall Planetary Heat Balance
The heat absorbed is the amount of incoming solar flux times the area that intercepts the flux times the fraction absorbed:
But what is meant by the projected area (Aproj)?

## Slide 26
Aside: Projected Area
The entire planetary sphere is not illuminated;
Only half is illuminated at any given instant and even that illumination is not uniform;
But it's easy to visualize how much sunlight is intercepted by the planet, even with this non-uniform illumination.
Earth as Seen from Apollo 8
(NASA Photo)

## Slide 27
Incoming Solar Heating
(Assumed Parallel)
Aside: Projected Area
Imagine that you could lower a white screen behind an illuminated planet and observe from afar;
How much sunlight would be missing?
re

## Slide 28
Aside: Projected Area
Looking at the screen head-on, we see that a circle of sunlight is missing;
The projected area of a sphere is simply that of a circle.
re

## Slide 29
The Overall Planetary Heat Balance
The heat emitted is assumed uniform over the entire planet;
We can express the heat rejected using the familiar Stefan-Boltzmann law:
where is recognized as the surface area of the planetary sphere.

## Slide 30
The Overall Planetary Heat Balance
Next, we equate the outgoing and incoming energy, and substituting for the projected area:
Solving for the planetary temperature, T yields:

## Slide 31
The Overall Planetary Heat Balance
We can also find the flux emitted by the planet at temperature, T:
For a mean solar flux of 1367 W/m2, albedo of 0.3 and an assumed Earth emittance of 1.0:
255 K
239 W/m2

## Slide 32
The Overall Planetary Heat Balance
The flux incident on the spacecraft is scaled by the local form factor to the planet for a nadir-facing plate:
re
h
r

## Slide 33
Why Won't This Calculation Work for the Moon?
Recall our simplifying assumptions:
Earth has an atmosphere to transport heat over the globe -- the Moon does not;
Earth rotates rapidly with respect to the sun when compared to the Moon.
Moon as Seen from Apollo 11
(NASA Photo)
Hot
Cold

## Slide 34
Why Won't This Calculation Work for the Moon?
Because of this, assuming the Moon is isothermal is not a good assumption.
Moon as Seen from Apollo 11 as it was Homeward Bound
(NASA Photo)

## Slide 35
Albedo and Planetary Flux Combinations

## Slide 36
Combination of Natural Environmental Parameters
The previous developments were used to show how reasonable estimates of natural environmental parameters could be obtained using some simplifying assumptions;
Now, it's time to explore "reality".

## Slide 37
Local Variation vs. the Planet-Wide Heat Balance
Our earlier derivation for planetary OLR assumed a planet-wide heat balance;
This isn't necessarily true for local conditions;
Seasonal variation in vegetation, snow cover, cloud cover, etc., can all affect local albedo and OLR components.
So how do engineers account for this?

## Slide 38
Local Variation vs. the Planet-Wide Heat Balance (Ref. 7)

## Slide 39
Earth Radiation Budget Experiment (ERBE)
Earth Radiation Budget Satellite (ERBS)
The Earth Radiation Budget Experiment (ERBE) used a new generation of instrumentation to make accurate regional and global measurements of the components of the radiation budget. (Ref. 8)

## Slide 40
Albedo and Planetary OLR Data (Ref. 9)
Albedo
Albedo
Albedo
Albedo
51.6° Inclination
16 s Data
51.6° Inclination
895 s Running Means
51.6° Inclination
3600 s Running Means
51.6° Inclination
5400 s Running Means

## Slide 41
Albedo vs.Planetary OLR (Ref. 9)
High Inclination Orbits, 128 Second Averaged Data

## Slide 42
Aside: Time Constant
As the thermal environment changes, so does an object's temperature;
Objects with low thermal inertia react faster than objects with a higher thermal inertia;
Objects with high heat transfer to or from the environment will react more rapidly than those with lower heat transfer.

## Slide 43
Aside: Time Constant
The effect of thermal inertia and heat transfer into and out of an object may be understood through investigation of the time constant, t.
Mathematically, for a mass, m, the time constant, t is given by:
where Cp is the specific heat and G is conductance or a linearized conductance.

## Slide 44
Aside: Time Constant
Real-life problems require more than a single set of environmental parameters:
Objects with short time constants react to short-term changes in the thermal environment -- examples: components such as radiators and insulation surfaces;
Objects with longer time constants react more slowly to changes -- examples: massive components with small area and insulated structure.

## Slide 45
Albedo vs. OLR (Ref. 9)
Engineering Extreme Cases for High Inclination Orbits

## Slide 46
Albedo and OLR Combinations (Ref. 10)

## Slide 47
Albedo and OLR Combinations (Ref. 10)
Design Hot Case Thermal Environment Profile

## Slide 48
Albedo and OLR Combinations (Ref. 10)
Design Cold Case Thermal Environment Profile

## Slide 49
Conclusion of Part 2