## Slide 1: PSPICE Circuit Simulation Overview: Part 3 Using PSPICE and the Probe Viewer Dr. Chris Iannello Deputy, Power Technical Fellow NASA Kennedy Space Center 321-861-3276 chris.iannello@nasa.gov

## Slide 2: Discussion Topics
PSPICE Overview
  Part 3: PSPICE and Probe Viewer
    Guided Tour of simulation and visualization of results
      Getting Started
        Simulation Profile Settings
        Time domain, transient sims
        Adding plots, cursors
        Presentation of data
        AC Sweep and Bias Point Solution
      Common pitfalls
    Probe Setup Options

## Slide 3: Discussion Topics
PSPICE Overview
  Part 3: PSPICE and Probe Viewer
  Convergence Tips and Tricks
    “Virtual Snubber”
    reltol=.01
    Auto convergence

## Slide 4: Buck Converter CCM Open Loop Transient Simulation
Time
0s
2ms
4ms
6ms
8ms
10ms
V(L1:2)
0V
20V
40V
60V
SEL>>
I(L1)
-10A
0A
10A
20A
30A
Time
9.9800ms
9.9840ms
9.9880ms
9.9920ms
9.9960ms
9.9772ms
10.0000ms
I(L1)
1.0A
2.0A
3.0A
4.0A
SEL>>
V(V2:+)
0V
1.0V
2.0V
V(L1:2)
24.44V
24.45V
24.46V
24.47V

## Slide 5: What is SPICE/PSPICE?
  Normal SPICE Calculation flow:
    SPICE is generally used to model nonlinear circuits
    Both large signal, time domain analyses and small signal (frequency domain) analyses are often preceded by a quiescent point calculation.
    In the case of the AC analysis, the circuit is linearized about that operating point.
    In the case of large signal analyses, the solution is iteratively solved for using various numerical methods with a variable timestep.
    Analysis at various temperatures was done by automatically updating semiconductor model parameters for temperature, allowing the circuit to be simulated at temperature extremes.