## Slide 1
Sample Rate & Nyquist Frequency
for Data Acquisition & Telemetry Systems

## Slide 2
NASA Engineering & Safety Center (NESC) Academy
Dynamic Concepts, Inc. Huntsville, Alabama

## Slide 3
Tom Irvine
Email: tirvine@dynamic-concepts.com
Phone: (256) 922-9888

## Slide 4
Data Collection
Engineers collect accelerometer data in a variety of settings.
Examples include:
1. Aerospace vehicle flight data
2. Automotive proving grounds
3. Machinery condition monitoring
4. Building response to seismic excitation
5. Modal testing of structures
This Unit gives guidelines for choosing the sampling rate. It also briefly covers amplitude resolution.

## Slide 5
Analog-to-Digital Conversion
The accelerometers measure the data in analog form.
The analog signal is sent through a signal conditioner. The signal conditioner may have an analog lowpass filter. Filtering will be covered more extensively in Unit 18.
An understanding of sample rate criteria requires some preliminary consideration of filtering, however.
Lowpass filtering of the analog signal is necessary to prevent an error source called aliasing. Aliasing is covered in Unit 17.
Eventually, the accelerometer data is passed through an analog-to-digital converter. The proper sampling rate must be selected to ensure that the digitized data is accurate.

## Slide 6
Sampling Rate, First Requirement
The first requirement is that the sampling rate must be greater than the maximum analysis frequency.
Industry guidelines:
minimum sample rate > N (maximum analysis frequency) | 
Analysis Type | N
Frequency Domain | 2
Time Domain | 10

## Slide 7
Conservative Rule
The frequency domain requirement in the previous table is based on the fact that at least two time-domain coordinates per cycle are required to resolve a sine wave for analytical purposes.
The Nyquist frequency is equal to one-half the sampling rate. The frequency domain analysis thus extends up to the Nyquist frequency.
Note that some conservative sources specify a value of N = 2.5 for frequency domain analysis.

## Slide 8
Reference
IEST-RP-DTE012.1 Handbook for Dynamic Data Acquisition and Analysis, Institute of Environmental Sciences, Illinois.
www.iest.org

## Slide 9
SRS Rule-of-Thumb
Unlike other spectral quantities evolving from the discrete Fourier transform computations, the SRS is essentially a time domain quantity.
The digital sampling rate given by Rs=1/(delta t), introduces errors beyond those associated with aliasing about the Nyquist frequency.
Rs must be high enough to accurately describe the response of the SRS oscillators.
To minimize potential error, it is recommended that the SRS computations be performed with a sampling rate of Rs > 10 fh, where fh is the highest natural frequency of the SRS computation.

## Slide 10
The shock response spectrum is calculated in the time domain.
Pyrotechnic shock is typically analyzed up to 10 KHz.
Thus use a minimum sample rate of 100 KHz.
SRS Q=10 CH 1 X-axis S2/3 Separation
Natural Frequency (Hz)
Peak
Accel (G)

## Slide 11
Sampling Rate, Second Requirement
The second requirement is that the sampling rate must be greater than the maximum frequency present in the source energy at the measurement location.
This requirement is necessary to prevent aliasing.
Actual
Measured
Time (sec)
Amp.

## Slide 12
Sample Rate, Second Requirement (cont.)
Shannon’s sampling theorem states that a sampled time signal must not contain components at frequencies above the Nyquist frequency.
The Nyquist frequency is equal to one-half the sampling rate.
Shannon's theorem applies to frequency domain analysis.
minimum sample rate > M (maximum frequency in source energy) | 
Analysis Type | M
Frequency Domain | 2
Time Domain | 10

## Slide 13
Lowpass Filter
In many cases, the maximum expected frequency is unknown.
Thus, analog lowpass filtering can be used as a precaution to ensure compliance with the second requirement.
Filtering will be covered in Units 17 and 18.

## Slide 14
Summary of Rules
Note that the maximum source energy frequency may be independent of the maximum analysis frequency.
Thus, the first and second requirements may be independent.
minimum sample rate > N (maximum analysis frequency)
minimum sample rate > M (maximum frequency in source energy)
N = M = 2 for frequency domain
N = M = 10 for time domain

## Slide 15
An accelerometer must be mounted on a rocket engine for a static fire test.
The resulting vibration data will be transformed into power spectral density curves with an upper frequency of 2000 Hz.
The highest energy component in the data is expected to be 5000 Hz, however.
What is the minimum sampling rate per the guidelines given in this Unit?
Answer: 10,000 samples per second.
(Still need to use analog anti-aliasing filter in case there is energy above 5000 Hz)

## Slide 16
SRS Example
A segment of data from the engine test on the previous slide will be converted to a shock response spectrum.
A time domain calculated is required to form this spectrum.
The spectrum will have an upper frequency of 10,000 Hz.
What is the recommended minimum sampling rate?
Answer: 100,000 samples per second.
(Still need to use analog anti-aliasing filter in case there is energy above 5000 Hz)

## Slide 17
Amplitude Resolution
Analog-to-digital conversion systems have amplitude resolution, which is measured in bits.
The amplitude resolution is one part in 2^(number of bits).
Thus, a 12-bit system has a resolution of one part in 4096.
Consider a 12-bit system set up to measure a full scale amplitude of 10 V peak-to-peak. The resolution is ( 10 V / 4096) = 2.4 mV.
This example is shown in the next table, along with two other cases.

## Slide 18
Bit Examples
Amplitude Resolution, 10 V peak-peak | 
Bits | Voltage Resolution (mV)
8 | 39.1
12 | 2.4
16 | 0.15
A higher bit resolution yields a smaller voltage increment.

## Slide 19
Telemetry Bits
Note that telemetry data is given in terms of bits, where the bits are in integer format. The user must apply a scale factor to the bit values. The scale factor might convert the bit values to volts, or to some engineering unit.
The voltage resolution is proportional to the G level for an accelerometer. For example, consider the following configuration:
An accelerometer has a 10 V peak-peak range ( + 5 V zero-peak)
The accelerometer sensitivity is 10 G/volt ( 0.010 G /mV)
The accelerometer signal is applied to a 12-bit acquisition system
2^12 = 4096 amplitude steps
10 V / 4096 = 2.4 mV
2.4 mV (0.010 G /mV) = 0.024 G amplitude bit resolution
So the available amplitudes (G) are: 0, +0.024, +0.048, +0.072, ….. , +50

## Slide 20
Bit Conversion to G
Some actual flight telemetry data is given in file: T_flight.txt
The data has two columns: time (sec) and amplitude (bits)
Note that it represents a transient event which occurred during the burnout of a solid, upper-stage motor.
The amplitude resolution is: 0.2 G/bit
Convert the amplitude column to G units and plot the data

## Slide 21
signal_functions.m
>> signal_functions
signal_functions.m
ver 1.7 January 31, 2011
by Tom Irvine Email: tomirvine@aol.com
This program performs post-processing on a time history signal.
The time history must be in a two-column matrix format:
Time(sec) & amplitude
Select file input method
1=external ASCII file
2=file preloaded into Matlab
3=Excel file
1
Filename: T_flight.txt

## Slide 22
Select option
1=add constant to time column
2=multiply time column by scale factor
3=add constant to amplitude column
4=multiply amplitude by scale factor
5=remove mean
6=extract segment
7=reverse time history
8=linear interpolation
9=normalize
10=zero pad at start
11=zero pad at end
12=sort time history for ascending time
13=std dev time history
14=amplitude filter
15=cubic spline
16=view stats & plot time history option
17=Output Processed Time History File as ASCII text
18=exit
4
Enter scale factor 0.2
(Then use option 16 to plot the scaled data)

## Slide 23
Time (sec)
Accel (G)
Matlab filename: signal_post

## Slide 24
fourier.m
>> fourier
fourier.m ver 2.5 November 22, 2010
by Tom Irvine Email: tomirvine@aol.com
This program calculates the Fourier transform of a time history which is pre-loaded into Matlab.
The time history must have two columns: time(sec) & amplitude(units)
Select file input method
1=external ASCII file
2=file preloaded into Matlab
3=Excel file
2
Enter the matrix name: signal_post

## Slide 25
Select output option
1=plot only 2=plot & output text file 1
mean removal?
1=yes 2=no 1
Select Window
1=Rectangular 2= Hanning 1
1183 samples
SR = 3943.68 samples/sec dt = 0.00025357 sec
Plot Fourier Transform
Fourier transform overall level = 2.28311
Peak occurs at 313.63 Hz

## Slide 26
Peaks at 70, 83, 316 Hz
Frequency (Hz)
Fourier Magnitude
Accel
(G)

## Slide 27
signal_functions.m - spline
>> signal_functions
Select external file: INS.dat
Data is sampled at 100 samples/sec
Use option 15 to plot cubic spline with 500 samples/sec

## Slide 28
Time (sec)

## Slide 29
Time (sec)

## Slide 30
Time (sec)

## Slide 31
Program Summary
Data
T_flight.txt
INS.dat
Program
signal_functions.m
fourier.m