## Slide 1: New Developments in Portable Backscatter Systems
Seth Van Liew
July 15, 2014

## Slide 2: AS&E product lines
NETWORKING
ASE Connect
Product Areas & Offerings
CARGO & VEHICLE INSPECTION
PARCEL INSPECTION
PERSONNEL INSPECTION
ZBV Line
Mobile
Sentry Portal
Z Portal
Portal
Gantry
Gemini Line 6040, 7555, 100100
SmartCheck
OmniView Gantry
SmartCheck HT

## Slide 3: AS&E at a glance
ORPORATE HEADQUARTERS / Billerica, MA  FOUNDED / 1958  EMPLOYEES 362 BUSINESS / X-ray Screening & Inspection  FY13 Revenue / $183M  STOCK / ASEI
Unique and Flexible Solutions
50+ Years of Experience to Draw From
Over 600 ZBVs sold worldwide (US state department has about 200)
World’s #1 supplier in vehicle detection systems
2002 Nobel prize for extraterrestrial x-ray detection

## Slide 4: Transmission X-rays & Backscatter X-rays
Target
Core Technology
TRANSMISSION X-RAY
Core Technologies
Detector
X-ray Source
Detector
Z BACKSCATTER X-RAY OF THE SAME SUITCASE
BACKSCATTER X-rays detect by reflecting an X-ray beam from a target to a detector on the near side, creating an image that is easy to interpret and understand.
TRANSMISSION X-rays detect by passing an X-ray beam through a target to a detector on the far side.
Notes: 4
Z Backscatter provides additional information about the scanned object

## Slide 5: Portable / Mobile Backscatter Products
Decreasing Size
Decreasing Penetration
Increasing portability
Increasing time to scan a large object
 | ZBV | AXISS Family | Portable | Handheld
Energy | 225 keV | 140keV | 70 keV | 70 keV
Steel Penetration | 8mm | 3-5 mm | 1-3 mm | none
Viewing Distance | 4 m | 3 m | 1 m | 15 cm
Notes: New products won’t replace ZBV – Each has applications that might be better at

## Slide 6: Modular Backscatter imager

## Slide 7: Motorized Cart Configuration
Powered Cart: push cart, powered by battery
Powered lift raises imager up to 104” (264 cm) high
Size (with imager): 30” (w) x 54” (l) x 52” (h) (lowest level)
76 cm (w) x 137 cm (l) x 132 cm (h)
Total weight (cart and imager): ~950 lbs (430 kg)
Fits through 32” door (81 cm)
At lowest lift position
At highest lift position - 2.6m (104”) high

## Slide 8: Inspecting Vehicles Entering Secure Facilities

## Slide 9: VBIED: Rental Truck with 55 Gallon Drums of ANFO simulant

## Slide 10: VBIED – 25 Lbs Threat Material in Passenger Door ( 24” from Target )

## Slide 11: VBIED – 25 Lbs Threat Material in Trunk (Side View) ( 24” from Target )

## Slide 12: AXISS Family

## Slide 13: AXISS (Advanced X-ray imaging, Single Sided) Family
Small Backscatter Imaging System
Flexible solutions for the detection of explosives, drugs, currency and other organic threats and contraband
Depending on conveyance platform, fits through doors
Sees into objects that are inconvenient to open or difficult to x-ray with transmission systems like bicycles, panel trucks, trunks, planes, boxes, etc.
More portable than a ZBV
30” (76 cm)
25” (64 cm)
32” (81 cm)
Standard Imaging Module Can be used in Multiple Configurations
AXISS Family Imager

## Slide 14: AXISS Systems Imaging Information
X-ray source 140 keV, 600 W
Scan time: Capable of taking quick scan that is lower resolution (as quick as 15s) or a higher resolution scan (as long as 2 minutes)
System provides its own scan motion through Curvilinear Scanning: Turret rotates horizontally while scanning
Field of View: Vertical +/- 42º
Maximum distance to object being scanned: 12 feet (3.6m)
Middle:
Main viewing angle
Bottom:
Useful for looking at objects close up (<3 feet (1m)) that are on the ground (e.g. suitcase)
Top:
Useful for looking at very tall objects (e.g. truck trailer)

## Slide 15: AXISS Family Images: Flexible Scanning
10 ft away
18”
12” High Resolution scan
Potential progression of scanning a suspect vehicle:
Whole view of vehicle, closer view of suspicious area, detailed view of suspicious item
Notes: 1) Steel walled van 10 feet scan distance, 6 minute scan, 4mm apertures, Adaptive Contrast Applied on Raw Filters & Edge Preserving Smoothing
2) Steel walled van Filtered Image: 18” scan distance 5 minute scan, 2mm apertures
3) High Resolution – IED Simulant 12” 90 sec Axiss
<30 seconds PortBx, Lab IED Simulant. 4x1mm aperture. Represents 5 lbs of TNT with timer and battery

## Slide 16: AXISS Family
One Imager – Many Uses

## Slide 17: AXISS Family
Three programs / three prototypes
  Base Configuration
    Mounted on a motorized handcart
    Prototype developed under DHS S&T contract: Modular Bx
  Aviation Scanner
    Mounted on a specialized platform for scanning general aviation aircraft
    Backscatter imaging ideal for scanning planes for explosives or contraband such as narcotics
    Prototype developed under DHS S&T contract: Aviation Scanner
  AXISS Robot:
    Smaller than regular AXISS
    Remote operation for EOD applications
    Prototype developed under CTTSO/TSWG contract: AXISS
Modular Backscatter
Aviation Scanner
Prototype AXISS RT
AXISS Robot

## Slide 18: AXISS Robot Towed (RT) Configuration
Slightly different imager (smaller but 3x slower)
Weight of box: ~300 lbs (135 kg)
Scan time: varies 45s to 2 minutes
Size: 25” x 28” x 25” (64 cm x 71 cm x 64 cm)
Designed for Bomb Squad use
  Analysis of potential VBIEDs
Towable by a bomb squad robot
Provides remote imaging capability
50 lb bags Fertilizer – ANFO Simulant

## Slide 19: Aviation Scanner

## Slide 20: General Aviation Scanner
Scans executive and private planes
Mounted on a rugged platform that includes:
Omni-directional wheels that allow for precise control and maneuverability
Motorized lift that can lift imager up to 17 ft (5.2m) high to see under and over wings and fuselage
Full battery powered operation

## Slide 21: General Aviation Scanner: Contraband Inside Aircraft
Pair of 5 gallon containers of liquid organic simulant
Chain of 0.50 cal. cartridges with simulated gunpowder (2nd from right has empty case)
‘stripper clip’ of ten 0.223 cal. cartridges with simulated gunpowder
9mm handgun in plastic case
Simulated cash, two stacks of 200 bills
2 lb organic simulant
5 lb organic simulant

## Slide 22: General Aviation Scanner: Aircraft Scan at Various Distances
2 feet
8 feet
4 feet

## Slide 23
General Aviation Scanner: Small Plane with Contraband
= Contraband
Fuel Tank
Fuel Tank
Notes: Standard Scan @ 7 ft. horizontal, 6 ft. Vertical @ 140 KEV 4 ma With Contraband

## Slide 24: Aviation Scanner Changes Height and Viewing Angle
Imager in lowered position with the X-ray source tilted upwards so that it looks into the bottom of the aircraft
Imager raised and with the X-ray source tilted downwards so that it looks into the upper section of the aircraft

## Slide 25: Portable backscatter imager

## Slide 26: Portable Backscatter
70 keV, 300 W system that is highly portable
Scans both vertically and horizontally and any angle in between
Lift assembly for viewing at different heights
No exclusion zone, operator safe
  Standard wall power or battery operated
  Can be mounted on any platform
  Can penetrate drywall, fiberglass, aluminum, thin steel
  Safe for scanning personnel and baggage
  Weight: Imager 70 kg, Lift 60 kg
  Detectors can be removed for repositioning

## Slide 27: Imaging Head Two-Man Carry

## Slide 28: Scans Horizontally or Vertically

## Slide 29: Vehicle Scanning
270 degree panorama scan of internal rear passenger area
Imaging head fits completely inside vehicle
Hidden organics (drug and explosive simulants) identified

## Slide 30: NASA tiles

## Slide 31: MINI Z

## Slide 32: Handheld device can see through non-metallic objects and produces images of potential threats and contraband
Narcotic simulant in bumper
Narcotic simulant concealed in tire

## Slide 33: MINI Z Specs
Scanner Dimensions
Length: 11.5 in (29.2 cm)
Width: 9.8 in (24.9 cm)
Height: 7.6 in (19.3 cm)
Weight: 9.2 lbs (4.2 kg)
Energy: 70 kV
Power: 10 W
Operating Time: 4 hrs per battery charge (typical, based on 25% duty cycle)
Scan Speed: 6 in (15 cm) per second (typical)
Operating Environment: IP 54 Rated
Operating Temperature: 0° C to 45 C (32 F to 113 F)

## Slide 34: Imaging of objects
Narcotic simulant in a car seat
Can scan at any distance and any speed, allowing for increased detection capability or fast scan times
  Examination of walls, vehicle interiors, airplane interiors, pleasure boats, packages, space stations, spacecraft, etc.
  Closer scan distances increase image quality

## Slide 35: Versatility
Image organic materials and aluminum
  The MINI Z produces a real-time image of the scan target, highlighting organic materials and thin aluminum
  Does not require physical set-up: enabling immediate operation
  Battery operated, wireless communications (Wi-Fi)
  Intuitive operation: as an operator scans a target, an image appears in real-time on the system’s dedicated tablet.

## Slide 36: NASA tiles – 3 mm hole

## Slide 37: Capabilities and image analysis

## Slide 38: High resolution backscatter imaging

## Slide 39
AXISS Family
Distance: 6ft (1.8 m)
Time: 60 seconds (Modular Backscatter)
Time: 180 s (AXISS RT)
ZBV
Distance: 5 ft (1.5 m)
Time: 10 seconds
ZBV vs. AXISS Family Imaging
AXISS systems are smaller than ZBV, but slower
Notes: Contents unknown: Probably 4 lbs of sugar
X-ray Energy: 225 keV vs. 140 Kev
“The difference in X-ray energy is made up by extending the time to scan”

## Slide 40: Image Trade-offs
Faster scan speed….
  Faster but grainier
Slower scan speed….
  Slower but sharper
60s (Modulat Bx configuration)
180s (AXISS RT configuration)
15s (Modular Bx configuration)
45s (AXISS RT configuration)

## Slide 41: Image Trade-offs
Further away from object……
  Wider field of view, decreased spatial resolution due to beam divergence
Closer to object……
  Smaller field of view, better resolution
10 feet (3m)
18 inches (.5m)

## Slide 42: GUI and Operator Control Unit (OCU)
AXISS family systems are controlled by the OCU via radio

## Slide 43: Conclusions
MINI Z (handheld): 70 kV, 10 W, 8.5 lbs, unparalleled portability and versatility
Portable Backscatter: 70 kV, 70 kg unit, excellent portability with good imaging
AXISS: 140 kV, larger than PBx but with excellent imaging up close and penetration of steel
Aviation Scanner: AXISS mounted on a 360 degree platform with telescoping arm capable of imaging a plane or other object from variety of angles
Modular Backscatter: 140 kV, larger but can image at a distance through steel and is still portable
Capabilities: Backscatter imaging devices capable of fast scan times (car speeds) and high resolution (sub-mm), though usually not at the same time.
Pick your application and we likely have a solution!