## Slide 1: Space Flight Ionizing Radiation Environments
ES4/Dr. Steve Koontz, ISS System Manager for Space Environments NASA Johnson Space Center, 2101 NASA Parkway, Houston, Texas, 77058, USA, 281-483-8860 Email: steven.l.koontz@nasa.gov
June 29, 2017

## Slide 2: Presentation Outline
Space Radiation Environments: What, Where, When, and How Much?
  Some general characteristics of space radiation environments – directionality, energy spectra, randomness
  Energetic photons – primarily solar X-rays and extreme UV (not enough gamma rays to matter)
  Radiation Belts – trapped protons and electrons (relatively “soft” kinetic energy spectra)
  Solar Particle Events – mostly protons and electrons (with some heavier nuclei); “harder” energy spectra
  Galactic Cosmic Rays (GCR) – extremely “hard” spectra and significant heavy nuclei content
How does space radiation interact with matter (i.e., us and our stuff)?
  Direct ionization/excitation (particle tracks)
  Nuclear reactions and secondary particle showers (leading to more nuclear reactions and particle tracks)
  Displacement Damage Dose (optoelectronics, solar cells, LEDs, photodiodes) disrupting crystal structure
Space Station Zero – space radiation shielding specification and performance, in perspective, with humanities oldest (and lowest cost) spacecraft
  Shielding mass and geomagnetic field
  Shielding performance – surface environments
  Shielding performance – commercial and military aircraft environments
International Space Station – space radiation shielding specification and performance
  Spacecraft shielding mass and geomagnetic field
  Shielding performance – internal to pressurized elements
  Shielding performance – surface materials
Beyond GEO – the interplanetary radiation environment – GCR and Solar Particle Event (SPE)
  GCR and SPE
  Shielding mass, shielding materials, total dose and LET Spectra
  Environments definitions for design and verification
  Interplanetary environment, models, and spacecraft measurements
Some space radiation nuclear reaction and transport analysis tools
Summary
Back-up and References

## Slide 3: Space Radiation Environments: What, Where, When, and How Much

## Slide 4: Some General Features of Space Radiation
Definitions and Units – Particle (ion, electron, photon) energy
  In physics, the electron volt (eV) is a unit of energy equal to approximately 1.602×10−19 joule. By definition, it is the amount of kinetic energy gained by the charge of a single electron moving across an electric potential difference of one volt.
Definitions and Units – Total Ionizing Dose (TID)
  TID reported for a specified material; TID (H20) ≠ TID (Si)
  Original Unit of absorbed dose – rad = 100 ergs/gram
  SI unit of absorbed dose – grey (Gy) = 1J/kg = 100 rads, so 1 rad = 1 cGy
Definitions and Units – Shielding mass/path length as areal density
Shielding mass thickness reported as grams/cm2
  Same units for particle path length through target
  Thickness (cm) x density(g/cm3) = g/cm2
Definitions and Units – Linear Energy Transfer (LET)
  Quantifies energy deposition, by ionization/excitation production, along the charged particle track when high-energy charged particles move through a specific material composition; e.g., dE/dx (Si)
  Essential for microelectronic single event environment effects assessments and crew dose evaluations
  Energy deposition along the track can be orders of magnitude greater than the average dose for the object
  Units – keV/μ or MeV cm2/mg
Definitions and Units – Non-Ionizing Energy Loss (NIEL) and Displacement Damage Dose (DDD)
  DDD = ∫ NIEL [dΦ(E)/d(E)] d(E); NIEL units keVcm2/g or MeVcm2/g and DDD units keV/g or MeV/g

## Slide 5: Some General Features of Space Radiation
In free space, charged particle flux is approximately isotropic, or nearly so, in all cases, so no shadow shielding (except by planets, asteroids, moons, etc.)
  Fraction of 4π steradians covered by shielding mass is important
    Any area on a sphere, totaling the square of its radius and observed from its center, subtends precisely one steradian.
Energetic photons are not isotropic: line-of-sight to source
  Shadow shielding can work for solar X-ray flares
Low-energy particles/photons are much more abundant than high-energy particles/photons
    Penetration of active or passive shielding depends on particle energy:
    high energy => greater penetration so we have,
  High spacecraft skin dose – and rapidly decreasing dose as shielding mass increases
    Greatest % reduction in the first 1 to 10 g/cm2
    Much lower % reduction as shielding mass increases beyond 10 g/cm2
  How and where the dose is distributed in a particular object (Dose/Depth for spacecraft, asteroids, moons, planetary surfaces, and atmospheres, etc.) depends on the ionizing radiation environment and how that environment interacts with that object’s configuration and materials.
ISS Design Environment – electron and proton dose to the center of an aluminum sphere, of radius = shielding thickness, in mils (1 mil = 0.025 mm)

## Slide 6: Some General Features of Space Radiation: Randomness, Probability, and Particle Counting Statistics
The number of cosmic ray particles arriving in a counter or target material in some time interval, t, is a random (Poisson) process characterized by:
  Event probability is independent of previous or subsequent events
  An average event count, nave= µ, averaged over for many (>>t) time intervals
  The uncertainty (standard deviation) in any nt is equal to , where nt is a sample estimate of nave = µ
  So, the fractional uncertainty in nt becomes smaller with increasing nt; ( /nt )
  Note that µ can be constant for long periods (homogeneous Poisson process) or variable in time (inhomogeneous Poisson process)
As an example, just because you see an event at high latitude or in the SAA, the high radiation likelihood location doesn’t, by itself, prove it was a radiation event.
Similarly, you can’t conclude that an event observed in a low radiation likelihood location, like the western Pacific or southeast Asia, isn’t a radiation event.
Note that the most probable count for a
low likelihood event is 0

## Slide 7: Some General Features of Space Radiation: Charged Particle Populations

## Slide 8: Energetic Photons
TID depends on the material mass adsorption coefficient, i.e. on how much mass the energy is deposited into – consider 1 m2 (104 cm2) of material facing the sun (yes, there is a cosine and solar exposure time factor here)
  If 90% of the energy (10-4 W/m2) is adsorbed in the top 10μ (10-3 cm) of a solid of density 1 then we have 1 cGy/sec
  If 90 % of the energy (10-4 W/m2) is deposited in the top 10 cm then the dose rate is 10-4 cGy/sec
  Example - solar x-rays contribute about 20% to total ISS external surface dose
  http://www.swpc.noaa.gov/products/goes-x-ray-flux

## Slide 9: Radiation Belts
Confined to planetary radiation belts
Origin – uncertain at this time – some contribution from decay of neutrons produced by GCR interactions with Earth’s atmosphere and some from capture of solar particle event protons and electrons
Composition – protons and electrons for the most part
Flux and fluence – up to 106 to 108 per cm2/sec
Energy and spectrum – 10 MeV to 100 MeV
http://propagation.ece.gatech.edu/ECE6390/project/Fall2012/Team06/Webpage%20Folder/Webpage%20Folder/riskmitigation.html
TID (Si) under 4 mm Al vs. altitude
ESA SPENVIS
http://www.swpc.noaa.gov/products/goes-electron-flux

## Slide 10: Solar Particle Events
Origin – solar flares and coronal mass ejections
Composition – mostly protons/electrons with small percentage of heavier ions
Flux and fluence – 102 to 103 protons/(cm2sec) at E > 100MeV
SPEs are of short duration; 2 to 3 days typically
Energy and spectrum – 10 MeV to > 1 GeV
SPEs show a high degree of event-to-event variability
  How to select a worst-case design environment?
http://www.swpc.noaa.gov/products/goes-proton-flux

## Slide 11: Solar Particle Events
ESA SOHO Spacecraft
NASA Image Spacecraft

## Slide 12: Galactic Cosmic Rays: 1 AU Spectrum, Composition, and Solar Cycle Modulation
Origin – outside the solar system, but inside the Milky Way galaxy for the most part (supernovae & other extreme events)
Composition – atomic nuclei (and a few electrons and gamma rays) – all the elements of the periodic table are represented – 87% protons, 12% He nuclei, 1% heavier nuclei, smaller flux of energetic gamma ray photons
Flux and fluence (abundance) – about 0.1/(cm2 sec) at the top of earth’s atmosphere and about 0.5/(cm2 sec) in interplanetary space (geomagnetic shielding)
GCR flux modulated significantly by the 11-year solar cycle
Energy spectrum – Most energetic charged particle population – relativistic or ultra-relativistic, – Most in the energy range between 100 MeV to >> 100 GeV
Little or no change of the 1 AU flux/spectrum between the orbit of Mercury and the asteroid belt
R. A. Mewaldt, Cal Tech, JPL

## Slide 13: GCR Spectra

## Slide 14: Galactic Cosmic Rays (GCR): Heliosphere modulation/shielding
https://www.nasa.gov/topics/solarsystem/features/ray_surge.html
Attenuation of
Interstellar GCR
by the solar wind
and estimated local
Interstellar spectra
Voyager 1 (interstellar, solid circles) and Pamela (earth orbit. dots) measurements compared to GCR transport and solar wind attenuation model (solid line)
Ptuskin, V. S., Seo, E. S., Zirakashvili, V. N.; “Interpretation of Voyager 1 data on low energy
cosmic rays in the galactic wind model,” 24th European Cosmic Ray Symposium (ECRS2014),
Journal of Physics: Conference Series 632 (2015) 012022

## Slide 15: How does space radiation interact with matter (i.e., us and our stuff)?

## Slide 16: The Electromagnetic Force – Direct Ionization & Excitation (Electromagnetic Force) of Target Substance
High-speed charged particles decelerate by losing energy to target substance electrons during columbic collisions (with electrons) leaving an ionization/excitation damage track
  Nuclear collisions make little contribution to deceleration except at the lowest kinetic energies near end of track (displacement damage), but are the cause of secondary particle showers and limit the distance traveled by very high-energy primary CR particles
  http://pdg.lbl.gov/2010/reviews/rpp2010-rev-passage-particles-matter.pdf
dE/dx is the rate of energy transfer: keV/micron or MeV-cm2/mg in a particular target substance
  Linear and nearly constant over most of the particle range – hence the term linear energy transfer (LET)
  Nonlinear near end of track – most of the energy is deposited near the end of track in the “Brag Peak;” basis of accelerator hadron therapy for certain cancers
  More info and some look-up tables
    http://holbert.faculty.asu.edu/eee460/IonizationRange.pdf
    http://www.kayelaby.npl.co.uk/atomic_and_nuclear_physics/4_5/4_5_1.html
Quantified by the relativistic Bethe-Bloch equation
Projectile (space radiation particle) dependencies
β = v / c; v = velocity of the particle; E = energy of the particle; x = distance travelled by the particle in the target; c = speed of light; z = particle charge; ε0 = vacuum permittivity
Target substance dependencies
I = mean excitation potential of the target = 10eV(Z), n = electron density of the target = (NA Z ρ)/A Mμ ; ρ = density of the target; Z = target atomic number; A = target atomic mass number; NA = Avogadro number; and Mu = Molar mass constant = 1 in Si units; e = charge of the electron; me = rest mass of the electron

## Slide 17: The Electromagnetic Force – Direct Ionization & Excitation (Electromagnetic Force) of Target Substance

## Slide 18: The Strong and Electroweak Forces – Nuclear Reactions and Secondary Particle Showers
Inelastic Nuclear collisions attenuate the primary flux exponentially and generate secondary particle showers via nuclear reactions
  N(l) = N(0) exp(-l/λ)
    λ = inelastic collision length (grams/cm2)
    l = thickness in g/cm2
  http://pdg.lbl.gov/2010/reviews/rpp2010-rev-atomic-nuclear-prop.pdf
    λ ranges from 42 g/cm2 to 118 g/cm2 for protons in various materials
      λ increases with target atomic number
    At fixed target mass, number of collisions decreases with increasing atomic weight (i.e., fewer target nuclei per gram)
    λ Scales as (projectile atomic number) -0.77
<nevent> = average number of secondary particles per single collision event
<nevent> is proportional to A(projectile) x A(target) x (average nuclear thickness function) and collision energy
<nshower> is proportional to primary projectile energy
Neutrons are an important secondary particle shower productsas are pions, muons, and γ rays
GCR secondary particle shower schematic
Mg nucleus cosmic ray emulsion “star,” i.e., nuclear reaction event- Albert Lim (2000) http://astro.com.sg/articles/ Difference_%20btw_Gamma_n_Cosmic_Rays/DiffRays_image001.jpg

## Slide 19: The Strong and Electroweak Forces – Nuclear Reactions and Secondary Particle Showers
Video by Cosmus using AIRES (AIRshower Extended Simulations) to simulate what happens when a proton with 1Tev (1 trillion electron volts) of energy hits the atmosphere about 20 km above the ground. The shower is in a 20km x 5km x 5km box. Different particles are given different colors, electrons and positrons are green, muons are red and gamma rays are cyan. Source- http://http://astro.uchicago.edu/cosmus/projects/aires/

## Slide 20: The Strong and Electroweak Forces – Nuclear Reactions and Secondary Particle Showers

## Slide 21: The Strong and Electroweak Forces – Nuclear Reactions and Secondary Particle Showers
And it looks like this when it hits the ground…

## Slide 22: Displacement Damage
J. Knaster, A. Moeslang, T. Muroga; Nature Physics 12, 424–434 (2016)

## Slide 23: Space station zero – space radiation shielding specification and performance (in perspective) with humanities oldest and lowest cost spacecraft

## Slide 24: This One

## Slide 25
Shielding Specification and Performance Summary
Structural shielding mass
Diameter = 12,756.3 km
Mass = 5.9736 x 1024 kg
Composition – silicate rock with iron core (slightly radioactive from naturally occurring radioisotopes)
At surface, blocks all space radiation over ~ 2π steradians (under your feet)
Atmospheric shielding mass
Thickness = ~100 km (1033 g/cm2) measured along a radius
Mass = 5.1480×1018 kg
Composition – 77% nitrogen, 21% oxygen, with traces of argon, carbon dioxide and water (note – low Z elements)
Accounts for most space radiation shielding effect for the remaining 2π Sr (overhead) and the production of cosmogenic radioisotopes
Geomagnetic field – At the Earth's surface ranges from 25 to 65 microteslas (0.25 to 0.65 gauss). Effectively blocks solar wind. Mitigates GCR and SPE in an altitude, latitude, and particle kinetic energy dependent manner.

## Slide 26
Shielding performance – Surface environments
Earth surface ionizing radiation dose environments are dominated by natural radioisotope decay and man-made radiation source
  Radon gas is the most important contributor
2 to 8 mSv (~0.2 to 0.8 rad) annual dose at the surface
Space radiation contributions on the order of 10% of the total
http://www.world-nuclear.org/info/inf05.html

## Slide 27
Shielding Performance – Commercial and Military Aircraft Environments
The Pfotzer Maximum: GCR + Earth’s Atmosphere

## Slide 28
Shielding Performance – Commercial and Military Aircraft Environments
Average ISS hourly crew dose rates are on the order of 20 µSv/hr, comparable to commercial aircraft rates (polar route flights)
Want to experience space radiation? Buy a plane ticket for a polar route flight
Current polar route GCR/SPE dose environments can be viewed here
  http://sol.spacenvironment.net/nairas/Dose_Rates.html
Estimate you flight dose at the FAA CARI on-line calculator
  http://jag.cami.jccbi.gov/cariprofile.asp

## Slide 29
Shielding Performance – Solar Cycle Modulation of GCR Flux: Monitoring GCR Secondary Particle Shower Neutrons
http://neutronm.bartol.udel.edu/

## Slide 30: International Space Station – Space radiation shielding specification and performance

## Slide 31
Geomagnetic Field
Latitude dependence of ISS LA-1 MDM-16 DRAM single event upset rate reported by system EDAC firmware
Higher magnetic latitude => reduced geomagnetic shielding
Higher magnetic latitude => greater similarity to interplanetary GCR environment
Latitude dependence of GCR spectrum for ISS orbit
AMS-01/STS-91
Higher magnetic latitude => reduced geomagnetic shielding
Higher magnetic latitude => greater similarity to interplanetary GCR environment
Bobik, P., Boschini, M., Gervasi, M., Grandi, D., Kudela, K., Micelotta, E.; In: Solar variability as an input to the Earth's environment. International Solar Cycle Studies (ISCS) Symposium, 23 - 28 June 2003

## Slide 32
Geomagnetic Field
AMS-01 STS-91 He++ GCR fluxes:
Low latitude region -
Mid latitude region -
High latitude region -
Interplanetary at 1 AU -
ISS enjoys significant geomagnetic GCR shielding at low latitude and almost none at high latitude (too bad about that SAA region)
At high latitude, ISS is in a GCR environment very similar to the interplanetary GCR environment
ISS can be used as a flight demonstration platform for exploration hardware with a high degree of confidence
P. Bobik, G. Boella, M.J. Boschini, M. Gervasi, D. Grandi, K. Kudela,
S. Pensotti, P.G. Rancoita; “Fluxes and nuclear abundances of cosmic rays inside the
magnetosphere using a transmission function approach”, Advances in Space Research 43 (2009) 385–393

## Slide 33
Geomagnetic Field
4 years of ISS AMS-02 data Veronica Bindi, Physics and Astronomy Department University of Hawaii at Manoa, NASA Advisory Committee, Human Exploration and Operations, NASA HQ, April, 7 2016

## Slide 34
Shielding Performance – Internal to Pressurized Elements
ISS Space Radiation Control Design Requirements (SSP-41000) - None
  Primary/secondary structure determined by launch loads and dynamics, pressure vessel safety, thermal, and MM/OD protection
  Materials and avionics to meet performance/safety requirements for the life of the vehicle without special shielding mass considerations
    Natural Environment Definition for Design – SSP-30512, 500 km/51.6o
      Worst-Case – we don’t fly above 420 km (Soyuz/Progress certification limits)
      Worst-Case solar minimum GCR environment
    ISS must “fail safe” and recover from the worst-case SPE defined in SSP-30512 and operate nominally otherwise
  Crew Radiation dose administrative limits enforced by tracking accumulated crew dose and limiting crew exposure time (i.e., limiting stay time on ISS to limit total dose per expedition – “number of safe days in space”
    Stay time must be compatible with planned crew change out flight rate
    Safety requirements (SSP-50021) limits crew dose to less than 40 cSv per year
So, how did this approach work?
  No space radiation induced materials or avionics hard failures to date and none expected before end of program
  No documented exception to expedition crew dose limits (that I know of – check with the SA/SD - JSC/SRAG on this)

## Slide 35
ISS Shielding Performance – Internal to Pressurized Elements
Shielding mass distribution functions with ranges from 10 g/cm2 to more than 100 g/cm2 (aluminum with cargo, avionics and consumables) with median values of 20 to 50 g/cm2 (e.g. US Lab module)
Pre-flight annual dose estimates (using the SSP-30512 Design/Verification Environment) for the US Lab module range from 8 rads (Si) to 21 rads (Si) with a median value of about 14 rads (Si) depending on location of the dose point
  Variable environment – altitude, solar activity, and solar cycle effects
  The design environment specifies 500 km altitude as a worst-case to compensate for any uncertainties
In-flight TLD measurements during solar max ranged from 4.5 rads (Si) to 8.2 rads (Si) per year.
DOSTEL (particle hodoscope) measurements averaged to 7.1 rads Si per year (Reitz et al., AIAA 2001-4903)
In-flight solar max measurements (Kodiara et al., 2013) 11.1 rads (H2O)/year ~ 8.6 rads (Si)/year

## Slide 36
ISS Shielding Performance
Internal to Pressurized Elements
Secondary Neutrons
Mission | Date | Solar Cycle | Altitude (km) | Inclination | Shielding (g/cm2) | Neutron Detector
STS-28 | 8/8/1989 | 22 | 302 | 57° | 20-50 | Bonner Ball
STS-36 | 2/28/1990 | 22 | 246 | 62° | 20-50 | Bonner Ball
Mir | 1990-1992 | 22 | 354-374 | 51.6° | 40 | Fission Foil
ISS | 2001 | 23 | - | - | 20-50 | Bonner Ball
Good agreement from 0.01 MeV to 100 MeV
Unknown whether agreement will continue at higher energies
STS neutron flux consistently lower than ISS and Mir
  May be a result of detector locations and less shielding at those locations
Some uncertainty in vehicle thickness and neutron detector locations from the experimental data
Kristina Rojdev, NASA-JSC, Brandon Reddell, NASA-JSC Steve Koontz, NASA-JSC,
William Atwell, Boeing Technical Fellow, Retired, Paul Boeder, Boeing Research & Technology (Now with JPL); “Investigation of Secondary Neutron Production in Large Space Vehicles for Deep Space,” AIAA Space 2016, Conference Proceedings

## Slide 37: GCR Nuclear Collisions: Secondary Particle Showers and Shielding Effectiveness

## Slide 38
Shielding Performance – External Surfaces
Shielding mass distribution functions are highly anisotropic and median ranges from zero to more than 10 g/cm2
Trapped radiation (protons and electrons) dominates (SAA and high latitude regions) – GCR contribution negligible is compression
  Highly variable environment – altitude, solar activity, and solar cycle effects
Boeing Radiation Effect Lab thermo-luminescent dosimeter measurements on MISSE-1, 2, and 3 ISS payloads (Wert, Normand, Perry, Pippin, Bartholet; NSMMS, June 2010)
  Median shielding mass ranges 0.0 to 0.9 g/cm2
  4-year doses range from 3 x 103 rads (Si) at 0 g/cm2 to 102 rads (Si) at 0.9 g/cm2
  All well below the annual worst-case Design/Verification Environment (SSP-30512) doses at the corresponding shielding thicknesses (106 rads (Si) @ 0.0 g/cm2, and 3 x 105 rads (Si) @ 0.9g/cm2)

## Slide 39
Shielding Performance – External Surfaces
STP-H4 MARS radiation detectors – channel 9 – lower shielding mass
Applied Space Environments Conference, May 2017, ISS Miniature Array of Radiation Sensors Dosimeter Measurements and Modeling, Andrew Nicholas (US Naval Research Laboratory), Mike Xapsos (NASA Goddard Space Flight Center), Peter, Walker (Computational Physics Inc), Craig Stauffer (AS&D), Joseph Minow (NASA Marshall Space Flight Center)

## Slide 40
Shielding Performance – External Surfaces
STP-H4 MARS radiation detectors – channel 2 – higher shielding mass
Applied Space Environments Conference, May 2017, ISS Miniature Array of Radiation Sensors Dosimeter Measurements and Modeling, Andrew Nicholas (U.S. Naval Research Laboratory), Mike Xapsos (NASA Goddard Space Flight Center), Peter, Walker (Computational Physics Inc), Craig Stauffer (AS&D), Joseph Minow (NASA Marshall Space Flight Center)

## Slide 41
A Graphic Example of How Different it is on ISS: CR-39 Plastic Nuclear Track Detectors – 925 Days Inside the ISS U.S. Lab
Ground Control Plastic Nuclear Track Detectors (PNTD)
Flight PNTD
Flight PNTD surface in contact with 0.005 cm Pb foil
High Z elements, like Pb, produce more secondary particle shower products than low Z elements
The obvious differences between the flight-PNTD and the Pb-foil-flight PNTD are expected as a result of nuclear reactions, caused by space radiation primary and secondary particles, in the Pb foil with smaller contribution from trace (ppm level) Th and U impurities in the Pb foil itself. Ag, Hf, and W foils produced many fewer nuclear reaction products in their PNTDs. Track area increases with increasing particle LET.

## Slide 42: Beyond GEO – The interplanetary radiation environment – GCR and SPE

## Slide 43: GCR and SPE
Two important radiation environments
  GCR – continuously present
    Varies slowly over 11-year solar cycle
      No sudden increases in the observational record
    Solar Max Environment << Solar Min Environment
    Little radial dependence (< 10%/AU) between the orbit of Mercury and the Asteroid belt
    “Hard” spectra – difficult to manage with shielding, active or passive
    Total Ionizing Dose (TID) effects on materials and avionics largely negligible
    Prime cause of avionics SEE effects
  SPE – A few days at a time, about once or twice a year on average
    During events, SPE particle flux >> GCR particle flux
    “Softer” spectra, so more manageable with shielding
    TID effects are significant and are reduced with shielding mass
    Radial dependence is significant and highly variable
      Peak intensities often fall off as R-3 while total event dose falls off as R-2, but you can’t count on it
      CMEs are efficient charged particle accelerators and examples exist of SPEs that were more severe at Mars than at Venus or Earth
      See the ESA SPE modeling, analysis and data archive web page - http://dev.sepem.oma.be/
https://settlement.arc.nasa.gov/75SummerStudy/figure2.6.gif

## Slide 44: GCR: Solar Max, Solar Min, Shielding Mass and Shielding Material
NASA HZETRN 2010 estimates of crew dose vs. shielding mass for a 3-year interplanetary mission assuming solar maximum and solar minimum GCR environments, no SEP event contributions, and both the 10 cSv and 100 cSv dose limits

## Slide 45: GCR: LET Spectra Under Aluminum Shielding
Detector Si Shell | SiDet1 | SiDet2 | SiDet3 | SiDet4 | SiDet5 | SiDet6 | SiDet7 | SiDet8
Detector Shell Radius (cm) | 5037.4 | 5037.3 | 5037.1 | 5035.6 | 5033.7 | 5030.0 | 5018.9 | 5000.0
Si Detector Median Al Shielding Mass in g/cm2 | 0.15 | 0.81 | 1.6 | 7.9 | 15.6 | 31.1 | 77.5 | 156.2
Solar Min-ISS Orbit
Solar Min-Interplanetary-1 AU

## Slide 46: SPE: Spectra Model, Shielding Materials and Shielding Mass
TID vs polyethylene shielding mass and two different SPE spectra models needed to during the July 2000 and November 2001 SPEs
Event dose at 0.1 g/cm2 ~ 104 cGy for both events
The Band model shows higher dose at low and high shielding mass and is more consistent with Earth surface neutron monitor data

## Slide 47: SPE: Spectra Model, Shielding Materials and Shielding Mass
Shielding mass of four different materials needed to reduce TID to 1 cGy and 10 cGy during the July 2000 SPE using the Band spectrum model
Event dose at 0.1 g/cm2 ~ 105 cGy
Shield material | 1cGy Band | 10 cGy Band
Polyethylene | 30 g/cm2 | 10 g/cm2
Carbon | 37 g/cm2 | 12 g/cm2
Aluminum | 40 g/cm2 | 13 g/cm2
Titanium | 43 g/cm2 | 15 g/cm2

## Slide 48: Environments Definitions (Models) for Design Development and Test
ISS: SSP-30512; Space Station Ionizing Radiation Design Environment
  Revision C effective date: June 3, 1994
  Applicable to ISS orbits only
    Orbital inclination = 51.6 degrees
    Altitude = 500 km (worst case, ISS altitude < 420 km at all times)
    NASA/GSFC AP8/AE8 trapped radiation models
      No plans to update to DoD/Aerospace Corp. AP9/AE9 at this time, but we are considering it
    Solar Minimum CREME-96 solar minimum GCR environment with a space weather index of M=4, (Moscow State University GCR model), worst case for GCR (until last minimum anyway)
    SPE model – October 1989 SPE
    Epoch 1964 geomagnetic field for both GCR and SPE
SLS-SPEC-159; Cross-Program Design Specification for Natural Environments
  Revision D, effective date: November 4, 2015
  Revision E, in work
    Presently applicable to SLS and MPCV (Orion)
    Recommended for Future Capabilities Team (FCT)/Deep Space Gateway (DSG)
    NASA/GSFC AP8/AE8 trapped radiation models
      No plans to update to DoD/Aerospace Corp. AP9/AE9 at this time, but we are considering it
    October 1989 solar particle event
    CRÈME-96 GCR with near Earth/interplanetary option
  Includes ascent, LEO, radiation belt transit, interplanetary GCR and SPE design environments with definition of design reference mission (DRM) trajectories

## Slide 49: Interplanetary Spacecraft Measurements
Lunar Reconnaissance Orbiter (LRO) (Solar Minimum Conditions)
  “The total dose for the LRO mission over the first 333 days was only 12.2 cGy behind ~3.3 mm of aluminum (because of the delayed rise of solar activity in solar cycle 24 and the corresponding lack of intense solar energetic particle events) => ~17 cGy per year in free space.
  “The dose rate in a 50 km lunar orbit was about 30 percent lower than the interplanetary rate, as one would expect from lunar obstruction of the visible sky.”
Mars Science Laboratory (Curiosity Rover) interplanetary
  ~ 15 cGy per year during 2011-2012 – weak Solar Max (much higher during SPEs)
Mars Science Laboratory (Curiosity Rover) on Martian surface
  ~ 8 cGy per year during 2012-2013 – weak Solar Max (much higher during SPEs)

## Slide 50: Interplanetary Spacecraft Measurements: LRO
Mazur, J. E., C. Zeitlin, N. Schwadron, M. D. Looper, L. W. Townsend, J. B. Blake, and H. Spence (2015), Update on Radiation Dose From Galactic and Solar Protons at the Moon Using the LRO/CRaTER Microdosimeter, Space Weather, 13, 363–364, doi:10.1002/2015SW001175.
millirad/hr x 240 =
microGray/day

## Slide 51: Interplanetary Spacecraft Measurements: Curiosity interplanetary cruise
https://mars.nasa.gov/multimedia/images/index.cfm?ImageID=5321h

## Slide 52: Interplanetary Spacecraft Measurements: Curiosity Martian Surface
http://authors.library.caltech.edu/42648/1/RAD_Surface_Results_paper_SCIENCE_12nov13_FINAL.pdf

## Slide 53: Some space radiation nuclear reaction and transport analysis tools

## Slide 54: Space Radiation Nuclear Reaction and Transport Tools
Monte Carlo vs. “Deterministic” computer codes
  Monte Carlo methods (or Monte Carlo experiments) are a broad class of computational algorithms that rely on repeated (step-by-step) random (most often “pseudo random”) sampling of physical probability distributions (i.e., reaction probability as cross sections) to obtain numerical results.
    Digital simulation of real experiment – one particle at a time
    Examples – FLUKA, MCNP, PHITS and others….
    Long execution times and massive computational resource requirements (multiprocessor blade servers, supercomputers)
  “Deterministic” methods describe how a variety of different types of particles travel through a material using statistical averages of reaction probabilities (cross sections) and look-up tables. It is generally considered the most accurate description of the statistical average density of particles in a system, as long as the particles do not interact with themselves. Operates like a deterministic calculation.
    Quick execution, modest computational resources
    Easy to install and run on your PC or Mac (or use the on-line web page)
    Examples – Novice, CREME-96, HZETRN 2010, 2015, and Oltaris
Code comparison and validation (see references)
  The codes (both Monte Carlo and “deterministic”) have been extensively validated against both ground-based accelerator and space flight data.

## Slide 55: Space Radiation Nuclear Reaction and Transport Tools
FLUcuating KAskades (FLUKA) is a fully integrated particle physics Monte Carlo simulation package. It has many applications in high-energy experimental physics and engineering, shielding, detector and telescope design, cosmic ray studies, dosimetry, medical physics and radio-biology.
  http://www.fluka.org/fluka.php
Monte Carlo N-Particle Transport Code (MCNP) is a software package for simulating nuclear processes. It has been developed by Los Alamos National Laboratory since at least 1957[3] with several further major improvements. It is distributed within the United States by the department of energy Radiation Safety Information Computational Center in Oak Ridge, TN and internationally by the Nuclear Energy Agency in Paris, France.
  https://mcnp.lanl.gov/
NOVICE (Deterministic/Monte Carlo) – commercial product of EMPC.
  http://empc.com/novice-software/
CREME-96 (Deterministic) – primarily an avionics single event effects and total ionizing dose code developed at the Navel Research Lab in the late 1990s – now maintained by Vanderbilt University and available as an on-line tool.
  https://creme.isde.vanderbilt.edu/
  https://creme.isde.vanderbilt.edu/CREME-MC/help/how-to-run-creme96
NASA/LARC/HZETRN (Deterministic).
  https://software.nasa.gov/software/LAR-18803-1
  https://spaceradiation.jsc.nasa.gov/irModels/
NASA/LARC/Oltaris (Deterministic) – On-line version of HZETRN.
  https://oltaris.nasa.gov/

## Slide 56: Summary

## Slide 57: Summary
Energetic photons (X-rays) are a threat to relatively thin surface layers of exposed materials. The X-ray energy flux can be as high a 10-3 W/m2 during solar flares. The natural gamma ray flux is low enough to be a non-issue.
SPEs are transient events (localized in time), seldom lasting more than a week, that can increase particle flux, TID rates, and SEE rates by orders of magnitude; however, “soft” energy spectra make management with shielding mass practical.
Trapped radiation is localized in space, consists primarily of energetic electrons (electron belt) and protons (proton belt), and can drive annual dose rates as high a 105 cGy through 4 mm Al near GEO. Shielding is effective, even at 1 to 2 cm Al, but costly (up-mass). The very high flux of lower energy particles can determine surface dose of exposed materials.
GCRs are most important for long-term (> few weeks or months) crew dose and the avionics single event environment. The much harder spectra makes management with shielding mass impractical. The avionics part of this problem is workable with reasonable cost and schedule constraints by selecting radiation resistant components and fault-tolerant, redundant system architectures.
Shielding mass processes (modifies) the natural environment so shielding mass effects must be accounted for when assessing the real space radiation environment to which spacecraft hardware and crew are exposed.
  Remember the secondary neutrons produced by space radiation in any material.

## Slide 58: Back-up and References

## Slide 59: References On-line tools
http://www.swpc.noaa.gov/ National Oceanic and Atmospheric Administration Space Weather Prediction Center (space radiation events)
https://nepp.nasa.gov/ NASA Electronic Parts and Packaging Program home page (SEE/TID effects, testing and analysis
https://srag.jsc.nasa.gov/ JSC Space Radiation Analysis Group (Human Health)
https://software.nasa.gov/software/LAR-18803-1 HZETRN 2015 home page
http://www.fluka.org/fluka.php FLUKA home page
https://creme.isde.vanderbilt.edu/ CREME-96 home page (avionics SEE/TID)
http://tec-ees.esa.int/ProjectSupport/ISO/CREME96.html ESA CREME-96 page
https://www.spenvis.oma.be/ ESA space environments modeling and analysis tools home page
http://dev.sepem.oma.be/ ESA Solar Particle Event modeling and analysis home page
http://holbert.faculty.asu.edu/eee560/see.html Arizona State university space flight environments effects and analysis home page
http://lansce.lanl.gov/ DOE Los Alamos National Laboratory atmospheric Neutron and High Energy Proton Testing Facility home page

## Slide 60: General References
Holmes-Siedle, Andrew, Adams, Len; Handbook of Radiation Effects Second Edition, Oxford University Press, Oxford, New York, 2007.
Hastings, Daniel, Garrett, Henry; Spacecraft-Environment Interactions, Cambridge University Press, Cambridge, New York, 1996
Beringer, J., et al. (Particle Data Group), “Cosmic Rays,” Physical Review, Vol. D86, No.010001, 2012, pp. 1–21.
Friedlander, M. W., A Thin Cosmic Rain: Particles from Outer Space, Harvard University Press, Cambridge, 2000.
Longair, M. S., High Energy Astrophysics Volume 1: Particles Photons and their Detection, Cambridge University Press, Cambridge, 1992.
Gaisser, T., K.; Cosmic Rays and Particle Physics, Cambridge University Press, Cambridge, New York, 1990.
Steven L. Koontz , Kristina Rojdev, Gerard D. Valle, John J. Zipay; “Estimating the Effects of Astronaut Career Ionizing Radiation Dose Limits on Manned Interplanetary Flight Programs,” Proceedings of the AIAA 43rd International Conference on Environmental Systems, 14 - 18 July 2013, Vail, Colorado.
Steve Koontz, Brandon Reddell, Kristina Rojdev, Paul Boeder, and William Atwell; “Spacecraft SPE Shielding: SPE environment models and materials performance in an Enhanced Cygnus Pressurized Cargo Module (PCM)-based Exploration Augmentation Module (EAM),” Proceedings of the AIAA 45th International Conference on Environmental Systems, 12 - 16 July 2015, Bellevue, Washington.
Durante, M., Cucinotta, F. A., “Physical Basis of Radiation Protection in Space Travel,” Reviews of Modern Physics, Vol. 83, 2011, pp. 1245-1281.
Cucinottaa, F. A., Kim, M-H.Y., Ren, L., “Evaluating Shielding Effectiveness for Reducing Space Radiation Cancer Risks,” Radiation Measurements, Vol. 41, 2006, pp. 1173–1185.
John W. Wilson, F. A. Cucinotta, Judy L. Shinn, and Lisa C. Simonsen; “Overview of HZETRN and BRNTRN space radiation shielding codes,” Proc. SPIE, Vol. 2811, 51 (1996); Online Publication Date: 22 March 2005.
Hastings, D., Garrett, H., Spacecraft Environment Interactions, Cambridge University Press, Cambridge, New York, 1996.
Usoskin, I. G., Solanki, S. K., Schussler, M., Mursula, K., Kovaltsov, G. A., “A Physical Reconstruction of Cosmic Ray Intensity since 1610,” Journal of Geophysical Research, Vol. 107, No. A11, pp. SSH 13-1 – SSH 13-6, 2002.
Wiedenbeck, M.E., David, A. J., Leske, R. A., Binns, W. R., Cohen, C. M. S., Cummings, A. C., et. al., “The Level of Solar Modulation of Galactic Cosmic Rays from 1997 to 2005 as Derived from ACE Measurements of Elemental Energy Spectra,” 29th International Cosmic Ray Conference, Vol. 00, Pune, 2005, pp. 101–104.

## Slide 61: References Space Radiation Environments Models and Measurements
Usoskin, I. G., Solanki, S. K., Schussler, M., Mursula, K., Kovaltsov, G. A., “A Physical Reconstruction of Cosmic Ray Intensity since 1610,” Journal of Geophysical Research, Vol. 107, No. A11, pp. SSH 13-1 – SSH 13-6, 2002.
Wiedenbeck, M.E., David, A. J., Leske, R. A., Binns, W. R., Cohen, C. M. S., Cummings, A. C., et. al., “The Level of Solar Modulation of Galactic Cosmic Rays from 1997 to 2005 as Derived from ACE Measurements of Elemental Energy Spectra,” 29th International Cosmic Ray Conference, Vol. 00, Pune, 2005, pp. 101–104.
Patrick M. O'Neill; “Badhwar–O'Neill 2010 Galactic Cosmic Ray Flux Model—Revised,” IEEE Transactions on Nuclear Science ( Volume: 57, Issue: 6, Dec. 2010 ).
Pat M. O'Neill, Myung-Hee Y. Kim; "BADHWAR-O’NEILL 2011 GALACTIC COSMIC RAY MODEL UPDATE AND FUTURE IMPROVEMENTS“, https://www.hou.usra.edu/meetings/hrp2014/pdf/3015.pdf.
Myung‐Hee Y. Kim , Patrick M. O’Neill , Tony C. Slaba; “Implementing Badhwar‐O’Neill Galactic Cosmic Ray Model for the Analysis of Space Radiation Exposure,” https://ntrs.nasa.gov/archive/nasa/casi.ntrs.nasa.gov/20140009922.pdf.
Nymmik R.A.; “Radiation environment induced by cosmic ray particle fluxes in the International Space Station orbit according to recent galactic and solar cosmic ray models,” Adv Space Res. 1998;21(12):1689-98.
N. V. Kuznetsov, H. Popova, M. I. Panasyuk; “Empirical model of long-time variations of galactic cosmic ray particle fluxes.” Journal of Geophysical Research, Space Physics, Volume 122, Issue 2, February 2017, pp.1463–1472.
M. A. Dayeh, M. I. Desai, K. Kozarev, N. A. Schwadron, L. W. Townsend,M. PourArsalan, C. Zeitlin, and R. B. Hatcher; “Modeling proton intensity gradients and radiation dose equivalents in the inner heliosphere using EMMREM: May 2003 solar events,” SPACE WEATHER, VOL. 8, S00E07, doi:10.1029/2009SW000566, 2010 .
D. Lario, A. Aran, R. G´omez-Herrero, N. Dresing, B. Heber, G. C. Ho1, R. B. Decker, and E. C. Roelof; “LONGITUDINAL AND RADIAL DEPENDENCE OF SOLAR ENERGETIC PARTICLE PEAK INTENSITIES: STEREO, ACE, SOHO, GOES, AND MESSENGER OBSERVATIONS,” The Astrophysical Journal, 767:41 (18pp), 10 April 2013.
F.B. McDonald, Z. Fujii, B. Heikkila, N. Lal, and R.E. McGuire; “The Radial Distribution of Galactic Cosmic Rays in the Heliosphere at Solar Minimum and Solar Maximum,” Proceedings of the 23rd International Cosmic Ray Conference, 2003, Tsukuba, Japan, http://inspirehep.net/record/632683.
O. G. Morales-Olivares and R. A. Caballero-Lopez; “Radial intensity gradients of galactic cosmic rays in the heliosphere at solar maximum: 1D no-shock simulation,” Geofísica Internacional 48 (2), 237-242 (2009).

## Slide 62: Models and Analysis Tools References
Code comparison and validation
R. A. Reed, R. A. Weller, A. Akkerman, J. Barak, W. Culpepper, S. Duzellier, C. Foster, M. Gaillardin, G. Hubert, T. Jordan, I. Jun, S. Koontz, F. Lei, P. McNulty, M. H. Mendenhall, M. Murat, P. Nieminen, Member, IEEE, P. O’Neill, M.Raine, B. Reddell, F. Saigné, G. Santin, L. Sihver, H. H. K. Tang, P. R.Truscott, and F. Wrobel; “Anthology of the Development of Radiation Transport Tools as Applied to Single Event Effects.”
John H. Heinbockel, Tony C. Slaba, Steve R. Blattnig, Ram K. Tripathi, Lawrence W. Townsend, Thomas Handler, Tony A. Gabriel, Lawrence S. Pinsky, Brandon Reddell, Martha S. Clowdsley, Robert C. Singleterry, John W. Norbury, Francis F. Badavi, Sukesh K. Aghara; “Comparison of the transport codes HZETRN, HETC and FLUKA for a solar particle event,” Advances in Space Research 47 (2011) 1079–1088.
John H. Heinbockel, Tony C. Slaba, Steve R. Blattnig, Ram K. Tripathi, Lawrence W. Townsend, Thomas Handler, Tony A. Gabriel, Lawrence S. Pinsky, Brandon Reddell, Martha S. Clowdsley, Robert C. Singleterry, John W. Norbury, Francis F. Badavi, Sukesh K. Aghara; “Comparison of the transport codes HZETRN, HETC and FLUKA for a solar particle event,” Advances in Space Research 47 (2011) 1079–1088.
S. Koontz, Reddell, B., Boeder, P.; “Calculating Spacecraft Single Event Environments with FLUKA: Investigating the Effects of Spacecraft Material Atomic Number on Secondary Particle Showers, Nuclear Reactions, and Linear Energy Transfer (LET) Spectra, Internal to Spacecraft Avionics Materials, at High Shielding Mass,” Radiation Effects Data Workshop (REDW), 2011 IEEE DOI: 10.1109/REDW.2010.6062528, Publication Year: 2011, pp.188-195.
T.T. Böhlen, F. Cerutti, M.P.W. Chin, A. Fassò, A. Ferrari, P.G. Ortega, A. Mairani, P.R. Sala, G. Smirnov and V. Vlachoudis, "The FLUKA Code: Developments and Challenges for High Energy and Medical Applications“ Nuclear Data Sheets 120, 211-214 (2014)
A. Ferrari, P.R. Sala, A. Fasso`, and J. Ranft,"FLUKA: a multi-particle transport code" CERN-2005-10 (2005), INFN/TC_05/11, SLAC-R-773
G. Battistoni, S. Muraro, P.R. Sala, F. Cerutti, A. Ferrari, S. Roesler, A. Fasso`, J. Ranft; "The FLUKA code: Description and benchmarking,“ Proceedings of the Hadronic Shower Simulation Workshop 2006, Fermilab, 6-8 September 2006, M. Albrow, R. Raja eds., AIP Conference Proceeding 896, 31-49, (2007).

## Slide 63: Poisson Processes
The Poisson distribution is an appropriate model if the following assumptions are true.
  n is the number of times an event occurs in an interval and n can take values 0, 1, 2, …
  The occurrence of one event does not affect the probability that a second event will occur. That is, events occur independently.
  The rate at which events occur is constant. The rate cannot be higher in some intervals and lower in other intervals.
  Two events cannot occur at exactly the same instant.
  The probability of an event in a small interval is proportional to the length of the interval.
  The actual probability distribution is given by a Binomial distribution and the number of trials is sufficiently bigger than the number of successes one is asking about.
If these conditions are true, then n is a Poisson random variable, and the distribution of n is a Poisson distribution.
Poisson equation
  P(n) = (µn/n!)µ is the long-term average value of n
  µ = λ t where λ is the long-term average count per unit time, so
  P(r) = ((λt)n/n!)
  For the Poisson distribution, µ = mean(n), µ = variance(n), = Std Dev(n)
  In the limit of large n, this becomes the Gaussian distribution
  Event counts are described by Poisson distribution, but time between events in a real random processes are described by an exponential distribution
  P(Δt, λ) = (λt)

## Slide 64: GCR Environment Characterization Data Sources
http://www.srl.caltech.edu/personnel/dick/cos_encyc.html
http://pdg.lbl.gov/2010/reviews/rpp2010-rev-cosmic-rays.pdf
Mark E. Wiedenbeck, Jet Propulsion Laboratory, California Institute of Technology mark.e.wiedenbeck@jpl.nasa.gov

## Slide 65: GCR Nuclear Collision and Secondary Particle Showers

## Slide 66: GCR: Calculating LET Spectra Under Aluminum Shielding with FLUKA
Detector Si Shell | SiDet1 | SiDet2 | SiDet3 | SiDet4 | SiDet5 | SiDet6 | SiDet7 | SiDet8
Detector Shell Radius (cm) | 5037.4 | 5037.3 | 5037.1 | 5035.6 | 5033.7 | 5030.0 | 5018.9 | 5000.0
Si Detector Median Al Shielding Mass in g/cm2 | 0.15 | 0.81 | 1.6 | 7.9 | 15.6 | 31.1 | 77.5 | 156.2
The differential LET spectra [#/(cm2 week LET)] at various shielding depths in a concentric spherical shell model spacecraft (50 meter radius, 37.4 cm thick).
LET spectra are calculated, using the FLUKA Monte Carlo radiation transport code, as the number of particles entering each of the Si detector shells placed at various depths in the concentric spherical shell model (see the table below).
All secondary particle shower processes are enabled and the full shielding mass distribution function for each Si shell is used in a fully three-dimensional calculation.
Radial distance of Si detector shells in cm from the center of the sphere (determines Si shell shielding depth as measured from the external surface) – Each concentric shell is a FLUKA “region” with specific boundary surfaces

## Slide 67: GCR Nuclear Collisions: Secondary Particle Showers and Shielding Effectiveness
Dose vs shielding mass including human body shielding mass
(Cucinotta, Space Radiation Cancer Risk Projections and Uncertainties, 2010)
Point dose vs. shielding mass calculations excluding human shielding mass http://srag.jsc.nasa.gov/Publications/TM104782/techmemo.htm
Point dose calculations make differences between shielding materials look better than they really are.
Note that liquid hydrogen isn’t a simple shielding material. It is a shielding system because maintaining a cryogenic liquid adjacent to a manned crew cabin for several years implies liquid containment and an as yet TBD thermal control system, neither of which will be weightless. Also, the density of LH2 is 0.07 g/cc => 7 meters of LH2 at 50 g/cm2 shielding mass.

## Slide 68: Estimated Mars Surface Radiation Dose Map (Confirmed by MRO and Curiosity)
Martian Surface Cosmic Ray Environment map – This map was produced based on cosmic radiation data by the Mars radiation environment experiment (MARIE), an instrument on NASA's Mars 2001 Odyssey spacecraft. Those data were combined with Mars altimetry from the MOLA instrument aboard MGS (Mars Global Surveyor. Lowest elevations are anticipated to have lowest radiation levels because more atmosphere exists above them to prevent penetration to the surface. The color scale is 10 rems (dark blue) to 20 rems (dark red). Astronauts on the International Space Station in Earth orbit encounter radiation equivalent to an annual rate of 20-40 rems. JPL Press Release, March 1, 2002. Credit: NASA/JPL/JSC

## Slide 69
Origin of GCRs confirmed
The first direct evidence that galactic cosmic rays are accelerated within supernova remnants has been provided by observations by the Fermi Large Area Telescope collaboration. The results make use of four years of data collected by the telescope observing two supernova remnants – IC 443 and W44 – within our galaxy. The observations fit very neatly with predictions of neutral pion decay. http://physicsworld.com/cws/article/news/2013/feb/14/supernova-origin-of-galactic-cosmic-rays-confirmed

## Slide 70
GCRs in the galaxy
The Fermi LAT 60-month image, constructed from front-converting gamma rays with energies greater than 1 GeV. The most prominent feature is the bright band of diffuse glow along the map's center, which marks the central plane of our Milky Way galaxy. The gamma rays are mostly produced when energetic particles accelerated in the shock waves of supernova remnants collide with gas atoms and even light between the stars. Hammer projection.
Image credit: NASA/DOE/Fermi LAT Collaboration

## Slide 71: Natural radioisotope decay chains

## Slide 72: Acronyms & Abbreviations
Ag Silver
Al Aluminum
AMS Alpha Magnetic Spectrometer
AU Astronomical Unit (mean radius of earth’s orbit
CARI The CARI-7 computer program, developed at the FAA's Civil Aerospace Medical Institute, calculates the effective dose of galactic cosmic radiation received by an individual (based on an anthropomorphic phantom) on an aircraft.
cGy centi Gray
cm centimeter
CME Coronal Mass Ejection
CR Cosmic Ray
cSv centi Sievert, a unit of biological “equivalent” ionizing radiation dose
DDD Displacement Damage Dose
dE/dx energy loss per unit length in reference to linear energy transfer (LET)
DoD Department of Defense
DOSTEL Dose Telescope (ISS flight experiment)
DSG Deep Space Gateway
EDAC Error Detection And Correction
ESA European Space Agency
eV electron Volt
FAA Federal Aviation Agency
FCT Future Capabilities Team
FLUKA FLUktuierende KAscade
g/cm2 grams per square cm
GEO Geosynchronous/Geostationary Orbit
GCR Galactic Cosmic Rays
GeV giga (109) electron volts
GSFC Goddard Space Flight Center
Hf Hafnium
HQ Headquarters
ISS International Space Station
JPL Jet Propulsion Laboratory
keV kilo (103) electron volt
km kilometer
LED Light Emitting Diode
LEO Low Earth Orbit
LET Linear Energy Transfer

## Slide 73: Acronyms & Abbreviations
LH2 Liquid Hydrogen
LRO Lunar Reconnaissance Orbiter
MCNP Monte Carlo N-Particle Transport Code
MeV mega (106) electron Volt
Mg Magnesium
MM/OD Micro Meteoroid/Orbital Debris
MOS/CMOS Metal Oxide Semiconductor/Complimentary Metal Oxide Semiconductor
MPCV Multi Purpose Crew Vehicle (Orion)
NIEL Non-Ionizing Energy Loss
Pb Lead
PHITS Particle and Heavy Ion Transport code System
PNTD Plastic Nuclear Track Detector
ppm parts per million
SAA South Atlantic Anomaly
sec second
SEE Single Event Environments (Effects)
SEP Solar Energetic Particle
SEU Single-Event Upset
Si Silicon
SLS Space Launch System
SOHO Solar Heliospheric Observatory
SPE Solar Particle Event
SPENVIS Space Environment Visualization System
TBD to be determined
TeV trillion (1012) electron Volts
Th Thorium
TID Total Ionizing Dose
TLD Thermo Luminescent Detector
U Uranium
UV Ultraviolet Light
W Tungsten