## Slide 1: THERMAL TESTING and VERIFICATION

## Slide 2: Introduction
This lesson provides an introduction to spacecraft thermal testing and a comparison of the thermal test requirements and practices of different government organizations, including NASA’s Goddard Space Flight Center (GSFC), the Jet Propulsion Laboratory (JPL), and the Department of Defense (DoD). GSFC, JPL, and DoD specifications provide well documented and detailed requirements for spaceflight hardware testing.

## Slide 3: Overview of Thermal Testing
This lesson will explain the various kinds of thermal testing performed on spaceflight hardware and the objective of each type of test.
The interdependencies of thermal testing and the spacecraft thermal design analysis process will be explored.
Test facilities, test planning, and lessons learned will also be discussed.

## Slide 4: Lesson Breakdown
Part 1 – Purposes of thermal testing, test levels, and margins
Part 2 – Unit, development and subsystem level testing
Part 3 – Spacecraft level testing
Part 4 – Thermal Test Facilities and Methods
Part 5 – Test Planning, Lessons Learned and Checklist

## Slide 5: Lesson Roadmap
Test Purposes and
Industry Practices
Test Types
Test Levels
Test Margins
Unit
Testing
Thermal Cycling
Thermal Vacuum
Unit Test Requirements
Development Testing
Subsystem Testing
Spacecraft Level Testing Objectives
Test Temperatures
Spacecraft Thermal Balance
Math Model Correlation
Space Environment Simulation
Test Planning
Lessons Learned
Testing Checklist

## Slide 6
Fundamentals of Thermal Testing
Part 1

## Slide 7: Part 1 Roadmap
Test Purposes and
Industry Practices
Test Types
Test Levels
Test Margins
Unit
Testing
Thermal Cycling
Thermal Vacuum
Unit Test Requirements
Development Testing
Subsystem Testing
Spacecraft Level Testing Objectives
Test Temperatures
Spacecraft Thermal Balance
Math Model Correlation
Space Environment Simulation
Test Planning
Lessons Learned
Testing Checklist

## Slide 8: Introduction
This lesson discusses the purposes of thermal testing and how various types of tests address those needs.

## Slide 9: Overview
The key objectives of thermal testing will be outlined and the types of testing typically found in industry will be described.
The concepts of acceptance, qualification, and protoflight testing will be introduced.
The important role that margin plays in establishing test temperature levels will be discussed.

## Slide 10: Test Purposes and Practices

## Slide 11: Purpose of Thermal Testing
Increase confidence in the design and workmanship.
Ensure successful operation in flight.
    Demonstrate robustness of design.
    Verify performance within specification in flight-like environment.
    Measure critical performance parameters (e.g. power dissipations).
Confirm thermal modeling assumptions.
Perform bake-out and verify contamination requirements.

## Slide 12: Industry Test Standards and Practices
Thermal test philosophies vary within the aerospace community.
NASA, DoD, and Commercial practices have been developed that have been successful in meeting the needs of these respective organizations.
While organizational test practices share much in common, there are differences driven by mission environments, unique vs. high production hardware, risk tolerance, and historical experience.

## Slide 13: Industry Test Standards and Practices (cont.)
Understanding how test requirements are driven by customer test philosophy is necessary to ensure a successful test.
  Test terminology
  Cycling requirements
    Number of thermal cycles
    Levels
    Dwell time
  Thermal balance criteria

## Slide 14: Types of Thermal Tests
Thermal tests are comprised of multiple phases.
  Environmental stress screening
  Performance verification
  Turn-on demonstration
  Thermal hardware verification
  Thermal balance testing (operational and survival cases)
  Bake-out

## Slide 15: Test Types

## Slide 16: Environmental Stress Screening
Subjects hardware to physical stresses that force latent defects to become observable failures.
  Allows component to be repaired or replaced.
  Involves environments more severe than flight.
    Soaks hardware at survival levels.
    Cycles temperatures to plateaus more extreme than expected in actual usage.
Thermal is usually last in environmental test sequence.
Exposes defects incurred during vibration, acoustic, and shock testing.

## Slide 17: Performance Verification
Demonstration that a unit, subsystem or space vehicle operates within specifications in a flight-like environment
  Accomplished during functional tests in which equipment is exercised over operational scenarios.
  Realistic environment is maintained during the test.
  Varies voltage and power dissipation over flight ranges.
  May include environmental variations for “day-in-the-life” simulations.

## Slide 18: Turn-on Demonstration
The verification that a unit can be activated in a severe thermal environment.
  Powers on unit under severe temperatures, changing temperatures, thermal gradients and/or extreme voltage conditions.
  Typically performed at hot/cold survival conditions.
  In-spec performance not required until returned to the operational range.

## Slide 19: Thermal Balance
Verifies the thermal model’s capabilities for predicting flight temperatures.
  Hot, cold, and transient environments simulated.
  Temperature data gathered.
  Heater duty cycle data gathered.
  Data used to adjust thermal math models.

## Slide 20: Bake-Out
Outgassing of unit until contamination criteria are met.
  Typically performed in vacuum.
  Temperatures may be elevated to accelerate bake-out.
  Contamination certification may be done at bake-out or less extreme temperature levels.

## Slide 21: Test Levels

## Slide 22: Test Levels
Testing is performed at different stress levels.
  Qualification testing
  Acceptance testing
  Protoflight qualification testing
  Development Testing

## Slide 23: Qualification Testing
Emphasis of qualification testing is on verification of the hardware design and manufacturing process, not the workmanship.
Testing is performed at environmental conditions more severe than expected in flight.
Performed on non-flight equipment.

## Slide 24: Acceptance Testing
Emphasis is on verification of workmanship and demonstration of flight-worthiness.
Demonstrates the acceptability of each deliverable item.
Performed after qualification testing.
Notes: Emphasis of acceptance testing is on verification of workmanship and demonstration of flight-worthiness.

## Slide 25: Protoflight Qualification Testing
Qualification testing done on flight hardware.
Reduces schedule time and cost of building qualification hardware.
Also known as protoqual testing or flight-proof testing.
Thermal environment is typically between that of acceptance and qualification levels.
Notes:   Thermal environment is typically between that specified for acceptance testing and qualification testing

## Slide 26: Development Testing
Engineering tests used to gain information about the design.
Can occur at any point in the test sequence, but typically before formal qualification testing and before unit level testing.

## Slide 27: Hardware Levels
Testing is performed at various hardware levels:
  Unit Level
  Subsystem or Payload Level
  Spacecraft Level

## Slide 28: Thermal Tests
Three main types of thermal tests are performed:
  Thermal cycle (TC) test
  Thermal vacuum (TV) test
  Thermal balance (TB) test

## Slide 29: Thermal Cycle Test
Rapid temperature cycling at atmospheric pressure.
Primarily for environmental stress screening.
Includes burn-in testing.

## Slide 30: Thermal Vacuum Test
Thermal cycling performed in vacuum.
Primarily for performance demonstration.
May be substituted for Thermal Cycle testing.

## Slide 31: Thermal Balance Test
Normally part of thermal vacuum test.
Performed for thermal model correlation and verification of thermal design.

## Slide 32: Consider the Thermal Environment!
Vehicle build – factory
Shipping – plane, truck
Launch pad and ascent
Mission – on orbit
Test conditions must envelope thermal environments hardware will see in use.
Battery cooling during ground test and on launch pad
Heat pipes inoperative in non-horizontal configuration
Lubricant integrity after storage
Solar cell inspection after test environment
Transfer orbit environments can be highly stressing on power systems
Special Considerations
Pressure
Thermal Cycling
Humidity
Temperature

## Slide 33: Example - Thermal Test Profile
HS, FF
Temperature.
HS, AF
CS, AF
FF
HS, AF
CS, FF
FF
FF – Full Functional Performance Test
AF – Abbreviated Functional Test
HS – Hot Starts
CS – Cold Starts
Time
FF
CS
HS
FF

## Slide 34: Test Margins

## Slide 35: Application of Thermal Test Margins
Bounding analytic predictions consider worst realistic combinations of:
Orbit environments
Spacecraft Orientation
Articulation/deployment configuration
Interface Conductance
Voltage
Power dissipation
Eclipse conditions
Surface finish degradation
Ascent or transfer orbit conditions
Hot margin provides assurance that hardware is robust and that test temperatures will not be exceeded in flight.
Cold margin provides assurance that hardware is robust and that test temperatures will not be exceeded in flight.

## Slide 36: Acceptance Test Temperature Range
The acceptance temperature range is established based upon thermal model predictions plus margin OR a default minimum temperature range.
  Default minimum acceptance ranges are typically driven by need to adequately stress hardware in thermal cycle tests.

## Slide 37: Acceptance Test Temperature Range (cont.)
If a unit was previously qualified for another program, the existing acceptance range is generally retained and the spacecraft designed to maintain the unit within that range.

## Slide 38: Acceptance Test Temperature Range (cont.)
Margin between analysis and test temperature maintained through uncertainty margin and/or Allowable Flight Temperature (AFT) limits.
  DoD typically applies 11°C analysis uncertainty margin between predictions and acceptance test temperatures per MilStd 1540. (1,2)
  NASA typically applies AFT limits that maintain 5°C margin between AFT and acceptance. (3)
    GSFC adds another 5°C margin for analysis uncertainty (4)
    Analysis predictions allowed to go to AFT at JPL, with additional margin as a goal. (5)
Notes: Margin between analysis predictions and acceptance test temperature maintained through analysis uncertainty margin and/or by Allowable Flight Temperature (AFT) limits.

## Slide 39: Qualification Temperature Range
Qualification testing is conducted beyond expected service temperatures on non-flight hardware.
  Serves as the minimum design temperature range for the hardware.
  Ensures design robustness.
  Proves the design by exposing design defects.
  Demonstrates tolerance to degradation (fatigue, wear).
  Proves compatibility with acceptance test tolerances.

## Slide 40: Qualification Temperature Range (cont.)
Qualification temperature range is established based upon the acceptance temperature range plus a qualification margin.
  10°C margin for DoD (1)
  10°C for GSFC (3)
  15°C (cold) and 20°C (hot) for JPL (5)
Some organizations specify a default minimum qualification range.
  –34 to + 71°C for DoD (1)
  –35 to + 70°C for JPL (5)

## Slide 41: Qualification Temperature Range (cont.)
Qualification hardware is usually not flown because it has been exposed to excessive environments during test.

## Slide 42: Protoflight Qualification Temperature Range
A compromise in the test sequence in which qualification testing is performed on flight equipment.
Protoflight test temperature range typically in between acceptance and qualification ranges.
  The qualification margin over acceptance is reduced from 10°C to 5°C for GSFC and DoD. (3,1)
  The qualification margin is not reduced for protoqualification tests at JPL. (5)

## Slide 43: Survival Temperature Range
Temperature range over which the hardware must survive.
  In-spec performance not required.
  Operating (unit “on”) and non-operational (unit “off”) survival temperature limits.
  Set at the beginning of the program based on hardware limitations.

## Slide 44: Turn-on Temperature
Usually, the cold temperature at which the unit can safely be turned on.
  Frequently, this is the cold operating survival temperature, otherwise the unit will need to be warmed to this temperature by heaters prior to turning on electronics.
  In-spec performance not required until hardware reaches operational temperature range.
Usually set at the beginning of the program.
Restricts unit operation.

## Slide 45: Predicted Flight Temperatures are Uncertain
Difficulties in accurately capturing complex view factors, radiation environments.
Directional reflectance and emittance of real surfaces not modeled.
Imperfect knowledge of surface properties.
Cables and harnesses typically not included in model.
Joint and interface conduction hard to predict accurately.
Multi Layer Insulation (MLI) effective emissivity is difficult to predict accurately.
Nodalization patterns chosen by analyst can introduce error.
Ground test simulation not perfect.

## Slide 46: THERMAL UNCERTAINTY DROPS AS DESIGN MATURES
Thermal Uncertainty
Concept definition to Preliminary Design Review
Trade studies with simple models
Requirements being defined
Identifying potential development problems
Preliminary to Critical Design Review
  Thermal models developed or refined
  More analysis cases being analyzed
  Requirement verification
Critical Design Review to thermal balance test
  Updates to analysis
  Problem areas well understood
Thermal balance test to launch
  Correlation of thermal model to test data
  Final flight predictions
Launch and on-orbit operations
Correlation of thermal model to flight data
High
Medium
Low

## Slide 47: Margin Covers Thermal Uncertainties
For NASA, 5°C is maintained between Allowable Flight Temperature (AFT) and Acceptance.
  GSFC requires an additional 5°C margin between analysis and AFT while JPL suggests that as a goal. (4)
  For elements that are thermally controlled by active means, a 30% excess control authority may be substituted for temperature margin, i.e., predictions can equal the acceptance test temperature. (4)

## Slide 48: Margin Covers Thermal Uncertainties (cont.)
For DoD, 11°C is maintained between analysis predictions and Acceptance temperature after models have been correlated to Thermal Balance test data. (1)
  An additional 6°C margin is required prior to Thermal Balance test, where practical. (1)
  Where active thermal control is used, a 25% excess control authority may be substituted for the 11°C. (1)

## Slide 49: Margin Covers Thermal Uncertainties (cont.)
Commercial programs typically apply 5°C between analysis predictions and Acceptance.
  Willingness to accept higher risks.
  Less one-of-a-kind hardware, more space heritage.
  Orbits and thermal environments that are common throughout their product line.

## Slide 50: Basis for DoD Thermal Uncertainty Margin
Intent of the MilStd 1540 thermal uncertainty margin is to have 95% confidence that acceptance temperatures will not be exceeded in the hottest and coldest flight conditions.
  Margin to be applied to realistic worst-case hot and cold analysis cases.
  No extra “pad” to be applied to analysis parameters.
  Parameters to be stacked only if such stacking will occur in flight, e.g., end of life optical properties with hottest orbit beta angle and winter (highest) solar flux.

## Slide 51: Basis for DoD Thermal Uncertainty Margin (cont.)
DoD (MilStd 1540) thermal uncertainty margin is based upon a report written by R. Stark5 in 1971.
  Compared analysis predictions to test and flight temperature data for several spacecraft.
    Found 11°C (2-sigma or 95%) prediction error for programs that used a thermal balance test to verify analytic predictions.
    Found 17°C (2-sigma or 95%) prediction error for programs that did not use a thermal balance test.
  D. Gluck6 (1987) and J. Welch7 (2009) gathered data for 9 additional missions and found similar prediction uncertainty.

## Slide 52: Thermal Uncertainty Margin for Cryogenic Equipment
For cryogenic systems, margins are often applied as a percentage of the design heat load and decrease as the design matures. (1)
Milestone | Program Go-Ahead | PDR | CDR | Qualification | Flight Acceptance
Power Margin (%) | 50 | 45 | 35 | 30 | 25

## Slide 53: Thermal Uncertainty Margin for Cryogenic Equipment (cont.)
As the temperature drops toward absolute zero, each degree represents an increasingly large percentage of the thermal balance, so margins expressed in degrees are reduced. (1)
 | Thermal uncertainty margin (K) | 
Predicted temperature (K) | Pre-validation | Post-validation
Above 203 | 17 | 11
203 to 186 | 16 | 10
185 to 168 | 15 | 9
167 to 150 | 14 | 8
149 to 132 | 13 | 7
131 to 114 | 11 | 6
113 to 96 | 9 | 5
95 to 78 | 8 | 4
77 to 60 | 6 | 3
59 to 42 | 4 | 2
41 to 23 below 23 | 2 1 | 1 1

## Slide 54: Margin – The Big Picture*
The figure depicts an integrated picture of JPL’s margin.
The goal is to keep all piece parts in limits with reasonable unit AFT range.
Other organizations follow similar margin processes.
*Courtesy of Jeffery Nunes, JPL

## Slide 55: Concluding Remarks for Part 1
Thermal testing helps ensure a successful mission by increasing confidence in the design and workmanship.
Temperature cycling screens for workmanship defects.
Functional testing demonstrates hardware operates within specifications in a flight-like environment.
Thermal balance test validates thermal math models.
Margin is applied to predicted flight temperatures to account for uncertainties and ensure robust design.

## Slide 56: Conclusion of Part 1