## Slide 1
Spacecraft Level Testing and Verification
Part 3

## Slide 2: Part 3 Roadmap
Test Purposes and
Industry Practices
Test Types
Test Levels
Test Margins
Unit
Testing
Thermal Cycling
Thermal Vacuum
Unit Test Requirements
Development Testing
Subsystem Testing
Spacecraft Level Testing Objectives
Test Temperatures
Spacecraft Thermal Balance
Math Model Correlation
Space Environment Simulation
Test Planning
Lessons Learned
Testing Checklist

## Slide 3: Introduction
This lesson will describe the thermal tests that are typically performed at the spacecraft level.

## Slide 4: Overview
Thermal vacuum, thermal balance and thermal cycle testing of spacecraft will be described along with government requirements for such tests.
The process by which appropriate test temperatures are established based on the allowable temperature ranges of spacecraft components will be discussed.
The process by which thermal math models are correlated to thermal balance test data will be outlined.

## Slide 5: Spacecraft Level Testing
Also known as “system level”.
Emphasis is different that at the unit or subsystem level.
  Final ground verification of system and unit performance in a flight-like environment.
  Focus is not on individual unit functionality, but rather on end-to-end performance verification of subsystems.
    Interfaces between units and subsystems.
    Continuity of mission objectives.
    Compatibility of different subsystem requirements.
    Flight-worthiness of vehicle.

## Slide 6: Spacecraft Level Thermal Tests
Qualification
  Thermal vacuum
    Functional performance test demonstrating the ability of vehicle to meet design requirements under vacuum and at prescribed temperature extremes plus a margin.
  Thermal balance
    Part of thermal vacuum test.
    Thermal model correlation and verification of thermal design and hardware.
  Thermal cycling
    Environmental stress screening for detection of design and manufacturing process defects.

## Slide 7: Spacecraft Level Thermal Tests (cont.)
Acceptance
  Thermal vacuum
    Functional performance tests to prove workmanship and flight-worthiness.
  Thermal cycling
    Environmental stress screening exposes workmanship defects.

## Slide 8: Spacecraft Level Thermal Test Objectives
Primary focus: thermal vacuum test.
  Emphasizes proving flight-worthiness and system performance in a flight-like environment.
    Thermal vacuum environment provides the most realistic flight conditions.
    Thermal gradients and temperature extremes will be most accurately represented.

## Slide 9: Spacecraft Level Thermal Test Objectives (cont.)
Secondary focus: thermal cycling.
  Emphasizes stress screening to detect problems.
    This should have been completed at a lower level of assembly.
    Problems are extremely costly to fix at the system level.
  Rapid rates of temperature change can be difficult (impossible) to achieve with the full spacecraft.
  Environmental stress screening is not as perceptive.

## Slide 10: Meeting Spacecraft Level Thermal Test Objectives
Qualification testing with a non-flight spacecraft rarely performed due to cost.
  Protoqual testing typical at spacecraft level for most programs.
  Acceptance testing typical for second and subsequent spacecraft in a block buy.

## Slide 11: Spacecraft-level Protoqual/Acceptance Testing
Demonstrates system performance in vacuum at or near maximum and minimum expected flight temperatures plus applicable margin.
Detect material, process and workmanship defects.
  Emphasis is on mounting, cabling, connectors and unit and subsystem interactions.

## Slide 12: Spacecraft level Protoqual/Acceptance Testing (cont.)
Functional verification of thermal control hardware.
  Abbreviated test during one cycle.
  Heater control circuit hardware function and control authority.
  Heat pipe performance.
  Propulsion thermal performance.
Test objectives accomplished during functional testing at temperature plateaus and during temperature transitions.

## Slide 13: Thermal Subsystem Verification in Acceptance Tests
Spacecraft thermal design previously verified by thermal balance test on qual/protoqual vehicle, but build-to-build variations can have thermal impacts.
Installation quality of thermal control hardware is highly sensitive to individual technician’s performance.

## Slide 14: Thermal Subsystem Verification in Acceptance Tests (cont.)
Some manufacturing processes are difficult to control:
  Interface materials (contact conductance).
  Wrapping of tapes and heater elements (overlap, tension).
  MLI wraps (compression, seams, overlaps).
  Mounting of Optical Solar Reflectors (gap between mirrors).
  Attachment of thermostats, sensors and patch heaters.
  Thickness and area of optical coatings (paints).
  Installation effect on optical properties.
Defects seem to concentrate at higher levels of assembly.
  Unresolved defects are pushed up to higher levels.

## Slide 15: Test Requirements for Spacecraft
Temperature range:
Acceptance, Protoflight and Qualification temperature ranges are the same as applied at unit level.
Actual spacecraft temperature cycle range is limited by units within the spacecraft that reach their allowable limits first.

## Slide 16: Test Requirements for Spacecraft (cont.)
Number of cycles, dwell duration, thermal balance: (1,3)
*Qualification testing rarely performed at spacecraft level
** JPL limits spacecraft level thermal tests to Acceptance temperature levels
*** GSFC allows 2 cycles for spacecraft that sees <10°C temperature variation on orbit
Organization | Test Level | Number of cycles | Dwell at plateaus (hours) | Thermal Balance phases
GSFC | Acceptance | 4*** | 24 with 2 hot and 2 cold starts | 3 or more
 | Protoflight | “ | “ | “
 | Qualification* | “ | “ | “
JPL | Acceptance | Not specified | Not specified | 2 or more
 | Protoflight** | N/A | N/A | N/A
 | Qualification** | N/A | N/A | N/A
DoD | Acceptance | 4 | 8 first and last cycle, 4 on other cycles | Not required
 | Protoflight | 4 | “ | 3 or more
 | Qualification* | 8 | “ | “

## Slide 17: Example - Spacecraft Thermal Vacuum Test Profile
0 Pumpdown 9 TB Phase 9 19 Cold 3 trend
1 TB Phase 1 ascent 10 TCS htr A funct 20 Cold to hot 3
2 TB Phase 2 heater/survival 11 Cold 1 trend 21 Hot 3 trend
3 TB Phase 3 pre op pre heat 12 Cold to hot 1, 22 Hot to cold 3
4 TB Phase 4 cold op/eclipse 13 Hot 1 trend 23 TCS htr B funct
5 TB Phase 5 14 Hot to cold 1 24 Cold funct 4
6 TB Phase 6 cold to hot 15 Cold 2 trend 25 Cold to hot 4
6A Outgas/functional tests 16 Cold to hot 2 26 Hot funct 4
7 TB Phase 7 hot 17 Hot 2 trend 27 Power down,
8 TB Phase 8 hot 18 Hot to cold 2

## Slide 18: Test Temperatures

## Slide 19: Establishing Space Vehicle Level Test Temperatures
Objective is to get as many units as possible to their individual protoqual or acceptance temperatures.
  More benign test temperature plateaus may be established to demonstrate in-spec performance.
Vehicle is divided into thermal control zones.
  Equipment panel, individual heater control zone.
Unit nearest its temperature limit is used for control of that zone.
  Do not want to exceed test temperature limits for any units.

## Slide 20: Establishing Space Vehicle Level Test Temperatures (cont.)
First thermocouple in a zone to reach the test temperature establishes when the entire zone is at the test temperature.
  Results in most units within a zone being tested at a less stressing temperature than in unit level test.
  Illustrates the importance of complete unit level testing.

## Slide 21: Example – Establishing Vehicle Level Test Temperatures
Unit acceptance test range
  A: -24°C to +61°C (85°C range)
  B: -10°C to +70°C (80°C range)
  C: -34°C to +50°C (84°C range)
Vehicle level temperature predictions (without 11°C margin)
  A: -5°C to +45°C (50°C range)
  B: -5°C to +52°C (57°C range)
  C: -5°C to +35°C (40°C range)
Vehicle level temperature predictions (with margin)
  A: -5°C to +56°C (61°C range)
  B: -5°C to +63°C (68°C range) -5°C to +46°C (51°C range)
  C: -5°C to +46°C (51°C range)
Test tolerance (±3°C) and test margin of safety (±3°C)
  -5°C to +40°C (45°C range)
Functional testing begins when first unit in zone reaches temperature
  Results in an even less stressful temperature range for most units (~35°C range)
A
C
B
3 electronic units on a common panel in the same thermal test zone
}

## Slide 22: Example - Space Vehicle Level Test Temperatures

## Slide 23: Thermal Vacuum Test Functional Testing
Perform functional test prior to chamber door closure.
Full functional tests desirable during first and last cycle at hot and cold temperature limits.
  Required by MilStd 1540, optional for NASA. (1,3)
Abbreviated functional tests performed at hot and cold temperature limits for intermediate cycles.
Final functional test performed after test is completed and chamber door opened.

## Slide 24: Thermal Vacuum Test Functional Testing (cont.)
Operational status of spacecraft:
  Equipment operational during all portions of the test and should be programmed through various operational modes with perceptive parameters being monitored (recorded).
  Only exception to this is during transitions from hot to cold.
  Operating times should be divided approximately equally between primary and redundant circuits.

## Slide 25: Spacecraft Thermal Balance Test

## Slide 26: Thermal Balance Test Objectives
Performed as part of the system qualification thermal vacuum test.
Provides test data for correlation of thermal model.
  Temperature data (steady-state and transient).
  Heater power usage.
  Electronic box power dissipations.

## Slide 27: Thermal Balance Test Objectives (cont.)
Verifies spacecraft thermal design.
  Components remain within allowable temperature limits.
  Interface temperature requirements are met.
  Thermal gradients are as expected.

## Slide 28: Thermal Balance Test Objectives (cont.)
Shows thermal hardware works over full temperature range.
  Heater operation: measure current draw, demonstrate margin.
  Thermostat operation: verify location and primary/backup functionality.
  Radiator sizing is adequate.
  Heat pipe operation, sizing and location.
  Louvers, phase change materials, interface materials, cryocoolers function as expected.
  Flight temperature sensor accuracy.
  Thermal software control and commanding.

## Slide 29: Thermal Balance Test Objectives (cont.)
Example - Solar Array Damper Heater Verification

## Slide 30: Thermal Balance Test Phases
A minimum of three test phases are usually required.
  Hot operational equilibrium phase.
  Cold operational equilibrium phase.
  Cold non-operational equilibrium phase (typically cold “survival”).
    Heater verification.
  Additional phases, as necessary, for further correlation, transients, eclipse conditions, software verification, etc.
  .

## Slide 31: Thermal Balance Test Phases (cont.)
Test phases are usually specified for worst case conditions.
  Need not be the absolute worst case condition, but similar to thermal design cases.
    Combination of seasons, equipment duty cycles, solar angles and eclipses.
  Component internal dissipation, voltage, and environment typically held constant.
    “Pseudo” steady-state is achieved for components cycling on thermostats.
Notes:   Test phases are usually specified for worst case conditions.
    Need not be the absolute worst case condition, but should be significantly different than ambient conditions and similar to driving thermal design analysis cases. Combination of seasons, equipment duty cycles, solar angles and eclipse conditions.
  Component internal dissipation, voltage, and environment typically held constant to provide steady-state conditions.
    “Pseudo” steady-state (repeatable transient behavior) is achieved for components cycling on thermostats.

## Slide 32: Example - Spacecraft Thermal Balance Test Profile

## Slide 33: Thermal Balance Test Data Collection
Temperatures for all test thermocouples and flight thermistors are recorded once all have reached equilibrium.
  Thermal engineer decides when equilibrium has been achieved.
    Guideline, such as “≤0.5°C/hr”, should be established prior to test.
  No cycling of equipment or environmental heaters during equilibrium phases.
  Balance may be approached from a more extreme condition for conservatism.
Notes:   Hot balance may be approached from a hotter condition, or cold balance from a colder condition, for conservatism

## Slide 34: Thermal Balance Test Data Collection (cont.)
Heater duty cycle data also taken for model correlation and heater subsystem verification.
For transient phases, temperatures are taken from a known equilibrium state through the entire transition.
  End point need not be an equilibrium phase, but component power should be held constant until the transient phase is completed.

## Slide 35: Functional Performance During Thermal Balance
Important to exercise all important heat flow paths.
  Across critical box to mounting surface interfaces, especially for high power units.
  Across heat pipe interfaces.
  Verify spreading of heat onto radiator surfaces.
  Thermal gradients on equipment panels.
  Requires that time be spent before the test to identify all critical heat flow paths and that test phases be implemented to verify them.

## Slide 36: Functional Performance During Thermal Balance (cont.)
Important to obtain operational responses of temperature-sensitive and mission critical equipment.
  May require dedicated test phase to impose specific environment.

## Slide 37: Thermal Math Model Correlation

## Slide 38: Thermal Model Correlation Process
Prior to test, spacecraft temperatures and heater power usage are predicted for planned test configuration and environment.
During each phase of thermal balance testing, temperatures and heater duty cycle data are recorded for comparison to the thermal model predictions.

## Slide 39: Thermal Model Correlation Process (cont.)
Test configuration information are recorded.
  Spacecraft bus voltage, electronic box operating modes, chamber cold plate temperatures, test heater power, etc. needed to confirm test conditions were as assumed in pre-test predictions.
Thermal model predictions are updated with as-run test configuration prior to start of model correlation .

## Slide 40: Thermal Model Correlation Process (cont.)
Correlation of thermal model:
  Model parameters adjusted within reasonable range to bring predictions into agreement with test data.
    Conduction and radiation heat transfer paths often adjusted.
    Spacecraft geometric model is rarely modified.
    All changes must be justifiable and reasonable.
  Each thermal balance test phase is correlated to model predictions separately.
  With each new correlation phase, care must be taken so as not to destroy correlation achieved in previous case.

## Slide 41: Thermal Model Correlation Process (cont.)
Correlation criteria vary from organization to organization, but ±3 to 5°C is typical.
  Correlation criteria for heater power not generally specified, but criteria of ±10% has been used.

## Slide 42: Thermal Model Correlation Process (cont.)
Following correlation, final flight temperature and heater duty cycle predictions are made.
    Compliance with thermal uncertainty or Allowable Flight Temperature (AFT) margin requirements demonstrated.
    Heater power control authority demonstrated.
    Any non-compliances require hardware or operational changes to maintain margin, or a waiver after appropriate review of risk.
Despite test correlation, math model still has inherent uncertainties.

## Slide 43: Residual Flight Temperature Uncertainties
Temperature and heater power correlation deviations remain.
Test unknowns:
  Spurious heat sources in chamber.
  Limited number of test cases.
  Absorbed heating is an indirect technique.
  Instrumentation inaccuracy.
  Individual component dissipation accuracy.
  End-of-life thermophysical properties cannot be tested.
  Test cable and support structure losses.
  Test equipment interference.

## Slide 44: Residual Flight Temperature Uncertainties (cont.)
Design changes as a result of testing are rarely verified by re-test.
Other vehicle hardware changes such as box change-outs, addition of flight equipment that could not be tested in chamber, etc.

## Slide 45: Concluding Remarks for Part 3
While defects in individual units may be discovered in spacecraft level test, emphasis is on interfaces and end-to-end verification of the system.
Goal is to bring as many units as possible to their target temperature by setting up thermal control zones.
Vacuum thermal cycling required on most programs, most commonly for 4 cycles.
Thermal balance test required to correlate math model and verify thermal design.

## Slide 46: Conclusion of Part 3