## Slide 1
Unit, Development and Subsystem Level Thermal Testing
Part 2

## Slide 2: Part 2 Roadmap
Test Purposes and
Industry Practices
Test Types
Test Levels
Test Margins
Unit
Testing
Thermal Cycling
Thermal Vacuum
Unit Test Requirements
Development Testing
Subsystem Testing
Spacecraft Level Testing Objectives
Test Temperatures
Spacecraft Thermal Balance
Math Model Correlation
Space Environment Simulation
Test Planning
Lessons Learned
Testing Checklist

## Slide 3: Introduction
In this lesson, the various types of tests performed at the unit and subsystem level will be discussed.

## Slide 4: Overview
We will start with a definition of a “unit” and show how margins are applied to predicted flight temperatures to establish unit test temperature ranges.
Thermal cycle, thermal vacuum, and burn-in tests will be described along with government requirements for such testing.
The unique aspects of development and subsystem level testing will be discussed.

## Slide 5: Unit Level Testing

## Slide 6: What is considered a “unit”?
“Unit” defined as a functional item that is viewed as a complete and separate entity for purposes of manufacturing, maintenance, or record-keeping.
    Examples: Electronic box, battery, solar array, valve, electrical harness.

## Slide 7: Approaches to Unit Test Temperatures
Thermal Model Temperature Prediction Range
MIL-STD-1540
JPL
Commercial Programs (Different Contractors)
Qualification Margin
Acceptance Margin
Thermal Uncertainty Margin
GSFC
Flight Allowable Margin
Notes: Different organizations have different approaches to defining analysis and test margin. For government programs, the total temperature margin between analytical flight predictions and qualification (the temperature to which the hardware is designed) is essentially the same for DoD and NASA, with JPL adding another 5 degrees C of margin in the hot case.
The commercial comsat industry does tend to carry a bit less margin than found on government programs. This reflects the greater importance of cost for customers who view the satellite as an insured commodity product that is just adding a bit more capacity to their fleet and the widespread use of standard spacecraft designs that have lots of flight history. Government programs, on the other hand, tend to be one-of-a-kind vehicles whose failure could result in compromised national security or the loss of invaluable scientific information.

## Slide 8: Establishing Unit Level Test Temperatures
Design
Test
------------
-----------
Qualification
Hot
Qualification
Cold
Protoqual Hot
Protoqual Cold
Acceptance Hot
Acceptance Cold
5 to11°C
5 to 11°C OR 25 to 30% control authority
Min/Max Model Temperature Predictions
Thermal uncertainty and/or
Allowable Flight margin
Acceptance
Margin
Protoqual Margin
(5 to 10°C)
Qualification Margin
(10 to 20°C)

## Slide 9: Unit Thermal Cycling Test

## Slide 10: Unit Thermal Cycling Overview
Rapid temperature cycling in ambient air or gaseous nitrogen.
  Fans for circulation
  Heating elements and cooling coils

## Slide 11: Unit Thermal Cycling Overview (cont.)
Functional tests are performed at hot and cold plateaus, but primary emphasis is environmental stress screening.
Types of failures found in thermal cycling of electronic equipment:
  Loose connectors
  Defective solder joints
  Inadequate stress relief
  Performance drift
  Material deficiencies

## Slide 12
Example - Unit Thermal Cycle Profile

## Slide 13: Hot and Cold Temperature Plateau
Most organizations define “Dwell” as the total time at plateau temperature.
MilStd 1540 defines Dwell as time at plateau temperature to allow unit internal temperatures to equilibrate and Soak as the total time at plateau temperature. (1)
Thermal Soak
Thermal Dwell
Hot Operational Soak
Functional
Test
Thermal Stabilization
Hot
Start
Test
Tolerance
Unit
Operating
Time
Temperature
Cold
Start
Functional
Test
Unit Not
Operating
Test
Tolerance
Temperature
Time
Thermal Soak
Thermal Dwell
Thermal Stabilization
Notes: The survival temperature may be more extreme than the operational qualification temperature.

## Slide 14: Unit Thermal Vacuum Test

## Slide 15: Unit Thermal Vacuum Overview
Demonstrates the ability of the unit to perform in an appropriate thermal environment (temperature and vacuum).
Basic difference between Thermal Cycle and Thermal Vacuum is the vacuum environment.
  The vacuum environment is realistic of flight conditions because convection is eliminated.
  Parts will reach hotter temperatures.
  Thermal gradients will be accurate.
  Vacuum-sensitive parts will be appropriately stressed.

## Slide 16: Unit Thermal Vacuum Overview (cont.)
Although temperature cycles are performed, the primary emphasis of thermal vacuum testing is performance verification.
  Demonstrates that unit performance is within specification in hot and cold thermal environments.
  Accomplished through extensive functional tests performed at hot and cold temperature plateaus.
  Testing is also performed during temperature transitions.

## Slide 17: Unit Thermal Vacuum Test Configuration
For conduction cooled equipment…
  Generally hard mounted to a thermally controlled heat sink.
  Component covered with a thermal blanket.
For radiation-cooled or conduction/radiation-cooled equipment….
  Conduction heat transfer to thermally controlled heat sink and radiation heat transfer to surrounding environment should be controlled to the same proportion as calculated for the flight environment.

## Slide 18: Unit Thermal Vacuum Test Configuration (cont.)
Chamber vacuum capability of 10-5 Torr or lower
Heating and cooling capability controlled on chamber walls and cold plates

## Slide 19: Unit Test Requirements

## Slide 20: Test Requirements for Electronic Units
Temperature range: (1,3,5)
*Active design must have capacity margin of 30% for GSFC, 25% for DoD
Organization | Test | Minimum margin over flight predictions (°C) |  | Minimum Range (°C)
 |  | Passive design | Active design* | 
GSFC | Acceptance | 10 | 5 | None
 | Protoflight | 15 | 10 | None
 | Qualification | Same as Protoflight |  | 
JPL | Acceptance | 5 | 5 | -25 to +55
 | Protoflight | +20/-15 | +20/-15 | -35 to +70
 | Qualification | Same as Protoflight |  | 
DoD | Acceptance | 11 | 0 | -24 to +61
 | Protoflight | 16 | 5 | -29 to +66
 | Qualification | 21 | 10 | -34 to +71

## Slide 21: Test Requirements for Electronic Units (cont.)
Number of cycles, transitions, and dwell duration: (1,3,5)
*GSFC allows ambient pressure testing with 50% cycle increase plus PF margin of 25C or acceptance margin of 20C and 6 hour soaks at plateaus
Organization | Test | Number of cycles | Dwell at plateaus (hours) | Transition rate (°C/min)
GSFC | Acceptance | 8 at unit level or 4 unit+4 subsystem* | 4 | 1 to 2 typical
 | Protoflight | “ | “ | “
 | Qualification | “ | “ | “
JPL | Acceptance | Min of 3, Max of 10 | 2 | ≤ 5
 | Protoflight | “ | “ | “
 | Qualification | “ | “ | “
DoD | Acceptance | 10 TC and 4TV or 14 TC | 7 first and last cycle 1 on other cycles | 1 to 5
 | Protoflight | 23 TC and 4 TV or 27 TC | “ | “
 | Qualification | “ | “ | “

## Slide 22: Test Requirements for Electronic Units (cont.)
Important for unit to be “on”.
  Effective screening only accomplished with unit operating.
  Functional tests at hot and cold plateaus for performance verification.
  Operation during transitions to plateaus to test workmanship over full temperature range.
  Hot and cold starts after non-operational soak period.

## Slide 23: Test Requirements for Electronic Units (cont.)
Burn-in testing is a continuation of thermal cycling without functional testing.
  Often performed as part of thermal cycling.
  Objective is to accrue additional hours under thermal stress.
GSFC(3) | JPL | DoD(1)
1000 hours total “on” time for unit level and spacecraft level testing, including 200 hours at hot/cold plateaus in vacuum. Last 350 hours must be failure free. | 1000 hours “on” time for unit level and spacecraft level testing, including 72 hours at hot and 24 hours at cold plateaus in vacuum. | 200 hours under thermal vacuum or thermal cycle conditions at unit level with last 100 hours failure free.
Notes: Burn in is a continuation of thermal cycling without functional testing.
  Usually performed as part of thermal cycling.
  Objective is to accrue additional hours under thermal stress.
  GSFC requires 1000 hours “on” time total for unit level and spacecraft level testing, including 200 hours at hot/cold plateaus in vacuum. Last 350 hours must be failure free.

## Slide 24: Example of Tailored Temperature Requirements
-200 -180 -160 -140 -120 -100 -80 -60 -40 -20 0 20 40 60 80 100 120
Temperature (Degrees C)
Cold turn-on at -18C
<5C cell-to-cell
<1C slice-to-slice
<0.1C internal gradient
<1.25C/24-hr distortion
Survival Temperature Range
Operating Temperature Range
Data Handling & TT&C Subsystem
Electrical Power Distribution Unit
Main Computer
Mass Memory Unit
Stabilization & Control Subsystem
Inertial Reference Unit
Dipole Ring Array Antenna
Cone Antenna
Solar Array
Solar Array Dampers
Payload 1
Payload 2
Batteries (Ni-Cd)
Batteries (Ni-H2)
Trickle Charge
Maximum Discharge
Propulsion Subsystem
Demodulator Unit
Cesium Clock

## Slide 25: Testing of Non-electronic Units
With some modifications, the approach to thermal testing of electronic units applies to other units:
  Moving mechanical assemblies
  Antennas
  Solar arrays
  Batteries
These items have special requirements that demand careful test planning.

## Slide 26: MilStd 1540 Test Requirements for Various Units (1)

## Slide 27: Unit Testing of Moving Mechanical Assemblies
Moving mechanical assemblies can be extremely temperature sensitive and may be sensitive to temperature gradients.
JPL and DoD require thermal vacuum testing at the qualification and acceptance levels. (1)
  Motion performance should be demonstrated at hot and cold temperature extremes.

## Slide 28: Unit Testing of Moving Mechanical Assemblies (cont.)
Motion performance should also be demonstrated during severe thermal gradients or transitions.
  Particularly deployment mechanisms and bearing assemblies.
  For deployment mechanisms, possible clearance/binding problems at temperature extremes and under temperature gradient conditions.
  For bearing assemblies, friction can be highly dependent on temperature gradients.

## Slide 29: Unit Testing of Antennas
Antennas are externally mounted components that experience wide temperature excursions and rapid rates of temperature change.
JPL requires thermal vacuum testing at Qual/Protoflight, and Acceptance levels.
DoD only requires thermal vacuum testing at qual/protoqual level for performance verification and demonstration of design.

## Slide 30: Unit Testing of Antennas (cont.)
Antenna testing recommendations:
  Test high power antennas with transmitter power on.
  Subject all antenna components to vacuum and temperature-induced stresses.
  Monitor perceptive RF performance parameters, if practical.
  For some designs, shape of reflectors must be measured.

## Slide 31: Unit Testing of Solar Arrays
Solar arrays also experience wide temperature extremes and rapid rates of temperature change on orbit.
Typical life test for a geosynchronous 10-year satellite:
  Test conducted on coupon.
  1700 cycles.
  -175°C to +55°C.

## Slide 32: Unit Testing of Solar Arrays (cont.)
DoD requires thermal vacuum at qual/protoqual level. (1)
  Thermal vacuum or thermal cycle optional at acceptance level.
DoD permits thermal vacuum only, but thermal cycle testing may be beneficial for workmanship screening. (1)
  Rapid rate of temperature change subjects the material, honeycomb, substrates, films, cells, wiring, backside paint to temperature induced stresses.

## Slide 33: Unit Testing of Batteries
Batteries are extremely temperature sensitive.
  At hot temperatures, performance and life can degrade.
  At cold temperatures, electrolytes can freeze, batteries can explode.
Notes: Extremely temperature sensitive.
  At excessive hot temperatures, performance and life can degrade.
  At excessive cold temperatures, electrolyte can freeze, batteries can explode.
Cold, tight temperature control often required.
  Entirely controlled by heaters, except during high discharge or charging periods.
  Thermal uncertainty temperature margin may not be applied to batteries because margin is large compared to allowable temperature range.
    Equivalent margin may be achieved by cold-biasing the design and using oversized heaters to control within desired range.

## Slide 34: Unit Testing of Batteries (cont.)
Tight temperature control at low temperature often required.
  Typical design uses radiators with heaters or variable conductance heat pipes.
  Analysis uncertainty temperature margin may be large compared to allowable temperature range.
    Equivalent margin achieved with cold-biased design and oversized heaters or variable conductance heat pipes.

## Slide 35: Unit Testing of Batteries (cont.)
Cell-to-cell temperature gradients must be controlled.
  Battery packs often have complex designs with many thermal interfaces.
  Thermal conductances across these interfaces should be verified during unit level tests.
DoD requires thermal vacuum test at qualification and acceptance level. (1)
  Thermal cycling not required.

## Slide 36: Unit Level Thermal Testing Summary
Three tests:
  Thermal vacuum
  Thermal cycling
  Burn-in
Three functions:
  Environmental stress screening
  Performance verification
  Survival and turn-on capability demonstration
Two test levels:
  Qualification verifies the design
  Acceptance verifies the workmanship and flight-worthiness
Thermal cycling is effective for environmental stress screening.
Thermal vacuum is effective for demonstrating performance and survival/turn-on capabilities.

## Slide 37: Development Testing

## Slide 38: Development Testing
Also known as engineering tests.
Required to:
  Validate new design concepts or the application of proven concepts to new configurations.
  Assist in the evolution of designs from the conceptual to operational phase.
  Reduce risks associated with new flight hardware.
  Investigate problems or concerns that arise after successful qualification.

## Slide 39: Development Testing
Objectives:
  Identify problems early in the design phase so that any required actions can be taken prior to starting formal qualification testing.
  Confirm structural and performance margins, manufacturability, testability, maintainability, reliability, life expectancy, and compatibility with system safety.

## Slide 40: Development Testing (Cont’d)
Test requirements depend upon subsystem maturity, operational requirements, and the intent of the test.
  Tests should be conducted over a range of conditions exceeding design limits to identify marginal capabilities and design “features”.
Common Thermal Development Tests:
  Unit/subsystem thermal balance testing.
  Deployment mechanism testing.
  Heat pipe tests.

## Slide 41: Thermal Balance Development Test
Two objectives:
  To obtain thermal data for the verification of analytical thermal models.
  To verify the thermal control subsystem and hardware.

## Slide 42: Thermal Balance Development Test (cont.)
Performed in a thermal vacuum chamber on flight or flight-like equipment.
  Individual units
  Full spacecraft
Several conditions are simulated:
  Hot operational, cold operational, cold non-operational, and transitions.
Equilibrium temperatures and repeatable heater cycling data are taken.

## Slide 43: Deployment Mechanism Development Test
Deployment mechanisms are critical to mission success.
They are also mounted external to the vehicle where thermal environments are extreme.

## Slide 44: Deployment Mechanism Development Test (cont.)
It is common for deployment tests to be specified for deployment mechanisms to show operation.
  Vacuum conditions
  Hot and cold environment
  Changing temperature environment
Special fixtures may be needed to support deployed mass during test in gravity environment.
Concerns:
  Differential expansion of materials causing failure to deploy.
  Thermal gradients causing binding.
  Material, adhesive or lubricant degradation at extreme temperatures.

## Slide 45: Heat Pipe Development Tests
Development testing contributes to heat pipe reliability.
  Checks for leaks.
  Verifies weld integrity.
  Demonstrates functional performance.
A primary consideration is that heat pipes must be in a level orientation for performance verification.
  Not always possible at higher levels of assembly.

## Slide 46: Typical Heat Pipe Development Test Program
Development Testing
Heat Pipe Level Testing
Qualification:
Burst Pressure Test
(2270 psig, 70C 100 psig increments)
Acceptance:
Radiographic Inspection of Welds
Proof Pressure Test (850 psig, 5 minutes)
Helium Leak Test
Functional Performance Test (100 Watts,
60C, 0.12” Tilt, reservoir wick at 7 watts)
Aliveness Test
In Gravity Characterization Test
Qualification:
Functional Performance Test
(Including heat pipe performance, heater
resistance check, and temperature
sensor check)
Static Load Test
Acoustic Test
Thermal Vacuum Test
Pallet Level Testing
Acceptance:
Gas Charge Verification
Full Tube Leak Test
Functional Performance Test
Acoustic Test
Thermal Vacuum Test

## Slide 47: Subsystem Testing

## Slide 48: Subsystem or Payload Testing
Subsystem/payload level testing is performed after unit level testing but before spacecraft level testing.
The objective is to satisfy spacecraft level requirements in a configuration or environment dedicated to the subsystem under test.

## Slide 49: Subsystem or Payload Testing (cont.)
Advantages of testing at payload or subsystem level include:
  Test can be accomplished in a smaller chamber.
  Environment can be tailored to the subsystem only.
  No interference from adjacent subsystems.
  Boundary conditions are well understood.
  Easier to obtain data for model correlation.
  Easier to isolate problems.
  Instrumentation can be significantly more thorough than at spacecraft level.
  Can reduce overall program costs because problems are resolved without impacting the schedule critical path.

## Slide 50: Test Requirements for Electronic Subsystems
Temperature range:
Acceptance, Protoflight and Qualification temperature ranges are the same as applied at unit level.
Actual subsystem temperature cycle range is limited by units within the subsystem that reach their allowable limits first.

## Slide 51: Test Requirements for Electronic Subsystems (cont.)
Number of cycles, transitions, and dwell duration: (1,3)
Organization | Test | Number of cycles | Dwell at plateaus (hours) | Transition rate (°C/min)
GSFC | Acceptance | 4 | 12 with two hot and 2 cold starts | 
 | Protoflight | “ | “ | 
 | Qualification | “ | “ | 
JPL | Acceptance | 3 to 10 | Total of 60 hot and 8 cold operating, 6 hot and 6 cold non-operating | ≤5
 | Protoflight | “ | Total of 72 hot and 24 cold operating, 6 hot and 6 cold non-operating | “
 | Qualification | “ | “ | 
DoD | Acceptance | 4 | 8 first and last cycle, 4 on other cycles | Max expected flight
 | Protoflight | “ | “ | “
 | Qualification | 8 | “ | “

## Slide 52: Subsystem Test Example – MILSTAR EHF Antenna
EHF Antenna
SHF Antenna
Spot Beam Antennas (2)
Crosslink Antenna
UHF Antenna
Spot Beam Antenna
Photo courtesy of US Air Force
EHF Antenna
Constant Conductance Heat Pipe (X-Y Plane)
MLI Blanket
Variable Conductance Heat Pipes (Y-Z Plane)
Radiator
Fibrous Refractory Composite Insulation Tile
EHF Test Issues
Close proximity to other payloads
  Performance requirements could not be verified
  EHF heater lamps would interfere with other payloads
Heat pipes are not level
  Variable conductance heat pipes are vertical
  No flight-like demonstration of heat pipe performance
Limited instrumentation
  Thermal model correlation would be difficult
  Visibility to thermal behavior difficult
Limited functional testing

## Slide 53
EHF Subsystem-Level Test Issue Solution
Constant Conductance Heat Pipe
Variable Conductance Heat Pipes
Radiator Panel
High Thermal Conductance Bracket (Test Only)

## Slide 54: EHF Subsystem-Level Thermal Test Hardware
Test-only MLI over Panel Opening
Test-only MLI over Variable Conductance Heat Pipes
Liquid Nitrogen Cold / Heater Plates
Liquid Nitrogen Cold / Heater Plates

## Slide 55: Concluding Remarks for Part 2
Principal test at unit level is temperature cycling in air or vacuum.
Margins are applied to expected flight temperatures to establish acceptance and qualification test ranges.
Development and subsystem tests reduce program risk by identifying problems earlier.
Government agencies have minimum temperature range, number of cycles, and total test time requirements.

## Slide 56: Conclusion of Part 2