## Slide 1: Unit 16
General Method for Calculating the Vibration Response Spectrum
Vibrationdata

## Slide 2
Determine the response of a single-degree-of-freedom system subjected to base excitation, where the excitation is in the form of a power spectral density.
Vibrationdata
SDOF System, Base Excitation
The natural frequency fn is
Do this for a family of natural frequencies. Plot results as Vibration Response Spectrum (VRS).

## Slide 3
Recall that he general method gives a more accurate response value than the Miles equation.
General Method Equation
Vibrationdata
where f is the base excitation frequency and fn is the natural frequency

## Slide 4
Consider the base input vibration test level from MIL-STD-1540C.
This level is used to test avionics components on shaker tables.
>>load webinar_16_data_files.mat Array name: m1540
Frequency (Hz) | Accel (G^2/Hz)
20 | 0.0053
150 | 0.04
600 | 0.04
2000 | 0.0036

## Slide 5
Use: vibrationdata > power spectral density > SDOF Response to Base Input Save each response
Plot family of curves using: vibrationdata > Miscellaneous Functions > Plot Utilities > Multiple Curves

## Slide 6
GRMS Values for Response Curves
Vibrationdata
Natural Frequency (Hz) | Response Acceleration (GRMS)
100 | 6.4
200 | 11.1
300 | 13.7
Vibration Response Spectrum Q=10

## Slide 7
vibrationdata > Power Spectral Density > Vibration Response Spectrum (VRS)
Base Input is the MIL-STD1540C level. Duration is 60 seconds.
6.4 G
11.1 G
13.7 G

## Slide 8
Plot family of curves using: vibrationdata > Miscellaneous Functions > Plot Utilities > Multiple Curves
Actual Case History
The accelerometer was mounted near the component in flight.
The component natural frequency is unknown.
Was the component under-tested?
PSD Arrays:
flight_data test_spec

## Slide 9
Calculate VRS for both flight_data & test_spec
Duration = 60 seconds (but does not matter for this calculation)
Save each VRS, 1-sigma (1-sigma = GRMS for zero mean)
Plot the two VRS curves using:
vibrationdata > Miscellaneous Functions > Plot Utilities > Multiple Curves
VRS Calculation
Vibrationdata

## Slide 10
The SDOF response to the Test Spec is greater than that of the Flight Data across all natural Frequencies, with margin to spare.
So the component was not under-tested!
Assumptions:
SDOF Response, Q=10
Both PSDs are stationary with normal distribution.
PSD Durations:
Test > Flight

## Slide 11
Flight Accelerometer Data
Vibrationdata
Task: Derive a simplified envelope using four coordinates. This envelope will then be used to specify a design and test level after uncertainty margin has been added.
Matlab array name:
sub_bulkhead

## Slide 12
Vibrationdata
Envelope Derivation, Method 1
Dark red line is a candidate envelope.
Overall level = 10.3 GRMS
Too Conservative!

## Slide 13: Envelope Derivation Method
Vibrationdata
Allow the envelope PSD to clip the flight data peaks as long as the envelope VRS meets or exceeds the flight data VRS
Use trial-and-error to derive the least possible PSD which meets the VRS requirement
This only cover GRMS response – fatigue will be covered in a future Webinar
Matlab >> vibrationdata > Power Spectral Density > Envelope PSD via VRS

## Slide 14
PSD Comparison
Vibrationdata
Frequency (Hz) | Accel (G^2/Hz)
10 | 0.0022
241 | 0.081
482 | 0.081
2000 | 0.0095
Envelope
The Envelope allows for peak clipping.

## Slide 15
VRS Comparison
Vibrationdata
The Envelope is greater than or equal to the Flight Data Input across all natural frequencies.
Assumptions:
SDOF Response, Q=10
Both PSDs are stationary with normal distribution.
PSD Durations:
Envelope > Input

## Slide 16
Conclusions
Vibrationdata
The Vibration Response Spectrum (VRS) is a useful tool for comparing the effects of different PSDs on a SDOF system, where the natural frequency and amplification factors are independent variables
The VRS can be used to determine whether a component previously tested to one PSD specification needs to be re-testing for a new specification
The VRS can be used for deriving envelopes for measured PSDs
The VRS will be extended to fatigue damage in future webinars