## Slide 1: Rationale for Selected MIL-STD-1540E Thermal Test Requirement
John W. Welch
The Aerospace Corporation
TFAWS 2012
13-17 August 2012

## Slide 2: Introduction
MIL-HDBK-340 – guidance for planning and executing ground testing of military spacecraft based on MIL-STD-1540 requirements
  Update of MIL-HDBK-340 in work providing justification and rationale for test requirements and parameters
Four specific test parameters reviewed in this presentation
  These four selected based on the their relative importance in meeting test objectives and frequency requests for clarification and discussion
    Thermal uncertainty margin
    Unit-level thermal vacuum test exemption criteria
    Unit-level thermal test temperature range and number of cycles
    Vehicle-level thermal test temperature range and number of cycles

## Slide 3: Thermal Uncertainty Margin
Temperature margin between worst-case analytic predictions and acceptance temperature range
  Accounts for inherent design uncertainties
  Passive thermal control (conduction/radiation): ±11°C temperature margin
  Active thermal control (heaters): 25% control authority
  Cryogenic systems: gradation of temperature and power margins
The ±11°C thermal uncertainty margin is the result of extensive comparisons between preflight predictions and flight measurements
  95% of flight temperatures within ±11°C of temperature predicted by correlated analytic thermal models
    1971, 1987, 2006
    US military, NASA, commercial, European flight data reviewed

## Slide 4: Thermal Uncertainty Margin Flight Data
High priority military program launched in 1994 showed an required margin of 10.5°C
ESA (Thales Alenia) flight data from 1990s across several programs indicated a 95% confidence level required a 11.5°C margin
  Recommendation for a 90% probability of compliance at ±10°C
  Recommendation for a 95% probability of compliance at ±12°C
±11°C margin shown to be necessary to ensure high confidence that flight temperatures will not exceed predicted values for low-risk, high-priority space programs
±11°C
Welch, J. W., “Assessment of the Thermal Uncertainty Margin from Flight Data Comparison with Thermal Model Predictions,” Proceedings of the 24th Aerospace Testing Seminar, April 2008

## Slide 5: Unit-Level Thermal Vacuum Test Exemption
MIL-STD-1540E provides criteria to assess whether an electronic unit is sensitive to vacuum conditions
  When a unit is proven to be vacuum insensitive, the unit-level thermal vacuum test may be waived and all unit-level thermal testing performed in an ambient thermal cycle environment
  Criteria serve as an example for consideration for determining vacuum-sensitivity
    Proven flight heritage, design and performance robustness, thermal design margins, etc.
  Applicable to electronic units only
    Mechanical and electro-mechanical units require TV environment to demonstrate performance in a flight-like environment
    TC testing not required for mechanical units per MIL-STD-1540E
  Applicable for acceptance units only
    Protoqualification and qualification units require TV environment to demonstrate vacuum-insensitivity for any unit of new design

## Slide 6: Unit Thermal Test Requirements for Electronic Units
MIL-STD-1540E Requirements
  Temperature Ranges
    Acceptance: maximum predicted or -24°C to +61°C
    Protoqualification: 5°C beyond acceptance or -29°C to +66°C
    Qualification: 10°C beyond acceptance or -34°C to +71°C
  Duration
    Acceptance: 10 TC and 4 TV (14 cycles total)
    Protoqualification: 23 TC and 4 TV (27 cycles total)
    Qualification: 23 TC and 4 TV (27 cycles total)

## Slide 7: Establishing Unit Test Temperature Levels

## Slide 8: Rationale for Unit Test Temperature Range
Acceptance temperature range
  Rationale for the ±11°C thermal uncertainty margin already discussed
  85°C range based upon part manufacturer’s practice for screening
  50°C maximum model prediction was the result of an industry survey of spacecraft manufacturers
Qualification temperature range
  The qualification margin was the result of consulting unit manufacturers and aerospace contractors about common practices for qualifying hardware design
  Agreement was reached that an additional 10°C margin should be included in the acceptance temperature range for qualification
Protoqualification
  Compromise in the qualification margin where unit design test objectives are still met, but on flight hardware
  Margin is half of the qualification margin (5°C)

## Slide 9: Rationale for Unit Thermal Test Cycles
Basis of 14 and 27 cycles is a continued emphasis of environmental stress screening (ESS) at the unit level were defects are more perceptible and less costly to repair or replace
Test effectiveness data as a function of cycles is difficult to obtain and many times the results are subjectively interpreted
One study, based upon the work reported in MIL-HDBK-344 and Aerospace data
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30
 | 0.18904 | 0.34234 | 0.46667 | 0.56749 | 0.64925 | 0.71555 | 0.76933 | 0.81293 | 0.8483 | 0.87697 | 0.90023 | 0.91909 | 0.93439 | 0.94679 | 0.95685 | 0.96501 | 0.97162 | 0.97699 | 0.98134 | 0.98486 | 0.98773 | 0.99005 | 0.99193 | 0.99345 | 0.99469 | 0.99569 | 0.99651 | 0.99717 | 0.9977 | 0.99814
 | 0.2006 | 0.36096 | 0.48916 | 0.59163 | 0.67355 | 0.73904 | 0.79139 | 0.83324 | 0.86669 | 0.89343 | 0.91481 | 0.9319 | 0.94556 | 0.95648 | 0.96521 | 0.97219 | 0.97777 | 0.98223 | 0.98579 | 0.98864 | 0.99092 | 0.99274 | 0.9942 | 0.99536 | 0.99629 | 0.99704 | 0.99763 | 0.99811 | 0.99849 | 0.99879
 | 0.21154 | 0.37832 | 0.50983 | 0.61352 | 0.69527 | 0.75973 | 0.81056 | 0.85063 | 0.88223 | 0.90714 | 0.92678 | 0.94227 | 0.95448 | 0.96411 | 0.9717 | 0.97769 | 0.98241 | 0.98613 | 0.98906 | 0.99138 | 0.9932 | 0.99464 | 0.99577 | 0.99667 | 0.99737 | 0.99793 | 0.99837 | 0.99871 | 0.99898 | 0.9992
Qualification
Protoqualification
Acceptance
Cycles
Test Effectiveness
Test effectiveness at 27 cycles for qualification testing = 99.8%
Test effectiveness at 14 cycles for qualification testing = 94.7%
Welch, J. W., “Investigation of the Relative Importance of Thermal Test Parameters as Specified in MIL-HDBK-344,” Proceedings of the 25th Aerospace Testing Seminar, October 2009.
Wright , C. P., “Test Effectiveness of SMC-S-016 Unit Acceptance Thermal Testing,” Proceedings of the 26th Aerospace Testing Seminar, March 2011.

## Slide 10: Vehicle TV Test Requirements
MIL-STD-1540E Requirements
  Qualification: 10°C beyond acceptance temperatures for 8 cycles
  Protoqualification: 5°C beyond acceptance temperatures for 4 cycles
  Acceptance: maximum predicted temperature range for 4 cycles
Unlike unit-level test temperatures, there is no default temperature range at the vehicle level
  Primary purpose of vehicle-level testing is not ESS, but rather demonstration of performance requirements in a flight-like environment
  Acceptance temperature range includes the ±11°C thermal uncertainty margin at both hot and cold temperature levels
    Heater power typically keeps cold test temperatures at flight values
    Use of thermal zones in which only one location within a hardware area achieves the test temperature means that most areas of the vehicle will not see the test margin at test temperatures
    Emphasizes the importance of rigorous unit-level test program
  Protoqualification and qualification test temperature ranges use the same margins as discussed for unit-level testing

## Slide 11: Vehicle TV Test Requirements - Cycles
Vehicle-level cycles require the same number of cycles for protoqualification as required for acceptance
  Trend is different than seen at the unit level where protoqualification cycles are the same as qualification cycles
    Result of a goal for accruing more screening at the unit level of assembly
    At the vehicle level, performance verification is primary emphasis, not ESS
Four cycles for acceptance and protoqualification is consistent with industry practice
Ambient
SP
Temp.
SP
FT
FT
FT
FT
FT
FT
SP – Specification Performance Test (Full Functional)
FT – Functional Test (Abbreviated Functional)
Time
SP
SP
First cycle:
Verifies initial performance and detects early defects
Middle cycles:
Adds thermal stresses to hardware and interfaces
Final cycle:
Demonstrates flightworthiness, assesses integrity after thermal stresses, and provides trending data to first cycle

## Slide 12: Conclusions
MIL-STD-1540E was written to ensure that high-priority military spacecraft are tested to levels and environments that increase the likelihood of mission success
MIL-HDBK-340 provides the application guidelines and rationale for test parameters and procedures specified in MIL-STD-1540E
Testing to MIL-STD-1540E requirements over the past decades has demonstrated its value in support of military programs:
  Identifying design workmanship problems early in the build process
  Providing realistic flight environments where performance and functional requirements can be verified
  Demonstrating flight-worthiness