## Slide 1: Antimonide Based Infrared Detectors and Focal Plane Arrays for NASA Applications
May 15th 2018
NASA Webinar
Sanjay Krishna
Professor and George R Smith Chair in Engineering,
Department of Electrical and Computer Engineering
The Ohio State University
Email: krishna.53@osu.edu
https://kind.engineering.osu.edu
https://discovery.osu.edu/

## Slide 2: Outline
Motivation and Application Need
  Mid-infrared Imaging and Sensing
  Driving Application Need for NASA
Technology Background
  Antimonide Based Semiconductors
  Historical Perspective of Superlattices
  Physics of Superlattices
Engineering Band-diagrams and Band-structures
  Band-diagram Engineering: Unipolar Barrier Detectors
  Band-structure Engineering: Superlattice Avalanche Photodiodes
Technology Status and Future Directions
  Job security for Physicists, Chemists, Material Scientists and Engineers!!!

## Slide 3
Reflective and Thermal Infrared
25mm
Infrared is generally considered to span the wavelength between 0.7mm-25mm*
* Various research communities use different semantics
The wavelength range between 1.7mm-25mm is referred to as Mid-Infrared*

## Slide 4: Mid-Infrared Sensing and Imaging
Stand-off Chemical Sensing
Seeing Through Objects
Thermal Imaging
Modified from http://www.resrchintl.com/Gas_Detection.html
Absorption Finger Print
Three scientific phenomenology enabled in the infrared
Various applications exploit these phenomenology

## Slide 5
Growth in Mid-Infrared Sensing Market
Key Messages:
IR Sensing and imaging are fast growing multi-billion dollar markets
Significant growth expected in the commercial market
DoD/NASA could benefit from innovations in the commercial sector

## Slide 6: NASA Applications
Space-Based Lidar
CubeSat Infrared Atmospheric Sounder (CIRAS)
Hyperspectral Thermal Emission Spectrometer (HyTES)
SLI-T: Long Wavelength Infrared FPA for Land Imaging
Earth Science Applications
https://www.jpl.nasa.gov/cubesat/missions/ciras.php
Weather, gas detection, pollution monitoring, ocean and ice changes, deforestation, forest fires, soil moisture, geology, plant health etc

## Slide 7: History of Infrared Detectors
A Rogalski et al 2016 Rep. Prog. Phys. 79 046501 doi:10.1088/0034-4885/79/4/046501

## Slide 8: Outline
Motivation and Application Need
  Mid-infrared Imaging and Sensing
  Driving Application Need for NASA
Technology Background
  Antimonide Based Semiconductors
  Historical Perspective of Superlattices
  Physics of Superlattices
Engineering Band-diagrams and Band-structures
  Band-diagram Engineering: Unipolar Barrier Detectors
  Band-structure Engineering: Superlattice Avalanche Photodiodes
Technology Status and Future Directions
  Job security for Physicists, Chemists, Material Scientists and Engineers!!!

## Slide 9: 6.1 Å Semiconductor Materials
Kroemer, The 6.1A family (InAs,GaSb, AlSb) and its heterostructures: A selective review, Phyisica E 20, (2004)
Two application drivers:
High Speed, Low Power Electronic Devices (Field effect transistors, Resonant Tunneling Diodes etc)
Mid-Infrared Photonic Devices (Infrared lasers and detectors)

## Slide 10: InAs/(In)GaSb Type-II Superlattices (T2SL)
Key Historical Papers: Sai-Halasz, G. A., Tsu, R., and Esaki, L. (APL 1977): “A new semiconductor superlattice”
Frensley and Kroemer (1977); Schulman and McGill (MCT superlattice, APL, 1979); Smith and Mailhiot (InAs/InGaSb strained layer superlattces, JAP, 1987); Osbourn (InAsSb SLS, JAP 1982/JVSTB 1984)
Good Review Articles and Recent References:
Super-lattice

## Slide 11: Physics of Bulk and Superlattice Bandstructures
73.2 Å InAs/
19.7 Å InAs0.55Sb0.45
Growth-axis ->
<- In-plane
T=77 K
Hg0.77Cd0.23Te
  Key Differences:
  Anisotropy in bandstructure and transport
  Reduced k-vector due to periodicity of superlattice
  Additional degrees of freedom for iso-gap structures
Smith, D. L., and C. Mailhiot. "Theory of semiconductor superlattice electronic structure." Reviews of Modern Physics 62, no. 1 (1990): 173.
  Modeling by Chris Grein, UIC

## Slide 12: From Theory to Practice: Materials Development
42 Å
STM by Michael Weimer (Texas A & M)
Growth by Solid Source Molecular Beam Epitaxy by Dr. Ron Kaspi
TEM by Paul Rotella (UNM)

## Slide 13: Outline
Motivation and Application Need
  Mid-infrared Imaging and Sensing
  Driving Application Need for NASA
Technology Background
  Antimonide Based Semiconductors
  Historical Perspective of Superlattices
  Physics of Superlattices
Engineering Superlattice Band-diagrams and Band-structures
  Band-diagram Engineering: Unipolar Barrier Detectors
  Band-structure Engineering: Superlattice Avalanche Photodiodes
Technology Status and Future Directions
  Job security for Physicists, Chemists, Material Scientists and Engineers!!!

## Slide 14: Unipolar Barrier Engineering
  A unipolar barrier* blocks one type of carrier and allows the transport of the other carrier
  Anthony White, Infrared Detector Patent, 1987
*Term Coined by David Ting, JPL

## Slide 15: Unipolar Barrier Detectors
2006
nBn (with InAs) [1]
W-structure [2]
2007
nBn
(with T2SL) [3]
M-structure [4]
2008
2009
CBIRD [6]
2010
pBiBn [7]
2011
pBp [10]
2012
Interband Cascade (ICIP) [9]
N-structure [11]
XBn
[5]
2014
nBn [13]
2016
Ga-free W-nBn [14]
Ga-free nBn [12]
pBn [8]
[1] Maimon and Wicks, Appl. Phys. Lett. 89, 151109, 2006
[2] Vurgaftman et al, Appl. Phys. Lett. 89, 121114, 2006
[3] Rodriguez et al, Appl. Phys. Lett. 91, 043514, 2007
[4] Nguyen et al, Appl. Phys. Lett. 91, 163511, 2007
[5] Klipstein, Proc. SPIE 6940, Infr. Tech. Appl., 2008
[6] Ting et al, Appl. Phys. Lett. 98, 023508, 2009
[7] Gautam et al, Appl. Phys. Lett. 96, 231107, 2010
Reduction in dark current by use of current blocking layers
[8] Hood et al, J. Electron Mat., 39.7 (2010): 1001-1006.
[9] Yang et al, Journal of Applied Physics 107.5 (2010): 054514
[10] Plis et al, IEEE Photonics Journal 3, 234, 2011
[11] Salihoglu et al, Appl. Phys. Lett. 101, 073505, 2012
[12] Kim et al, Applied Physics Letters 101.16 (2012): 161114.
[13] Soibel et al, Appl. Phys. Lett., 105, 023512, 2014
[14] Olson et al, Applied Physics Letters 108.25 (2016): 252104
[15] Soibel et. Al, Appl. Phys. Lett. 112, 041105 (2018).
2018
HOT nBn [15]
Notes: Philip Klipstein ""XBn " barrier photodetectors for high sensitivity and high operating temperature infrared sensors", Proc. SPIE 6940, Infrared Technology and Applications XXXIV, 69402U (April 23, 2008); doi:10.1117/12.778848;
Klipstein, Proc. SPIE 6940, Infrared Technology and Applications, 2008

## Slide 16: nBn Detector: The Concept
1/T
Log I
Standard diode
nBn
G-R
Diff
S. Maimon and G. W. Wicks, Appl. Phys. Lett. 89, 151109 (2006)
3 m N-Absorber
100 nm Unipolar Barrier
Metal
50 nm N-Contact
500 nm N-Contact
Metal
Modeled Band diagram for nBn structure
Growth direction
T1
T2
T2 > T1
I2
I1
I2 < I1
Higher Topwith the same performance
Better performance at the same Top

## Slide 17: InAs/GaSb Superlattices based Detectors and FPAs
T=77K
320x256
f4 optics, NETD=23.8mK
Kim et al, Appl. Phys. Lett. 92, 183502 (2008)

## Slide 18
Khoshakhlagh et al, (APL,263504, 2007)
N-SLS
(1)
N-SLS
(2)
Barrier
Vbias
N-SLS
(2)
N-SLS
(1)
Barrier
Vbias
Dual-color detection using nBn based T2SL detectors
2 Color nBn Superlattice Detectors

## Slide 19: Dual Color (LW/LW) pBp Detectors
The detector was designed to operate with l50%, blue = 9.5 µm and l50%, red 11.5 µm
LWIR1
Barrier
LWIR2
Top
Bottom
P+ GaSb
P+ InAs/GaSb Contact
p- InAs/GaSb “Blue” LWIR Abs. (4µm)
p- InAs/AlSb Barrier
p- InAs/GaSb “Red” LWIR Abs. (4µm)
P+ InAs/GaSb Contact
p
B
p
Notes: Double Check

## Slide 20: Band-Structure Engineering
Potential benefits of superlattices over bulk alloys:
Eg= -type resonance can be engineered into either conduction or valence band, giving rise to engineered impact ionization coefficients (/<<1 or / >>1) or reduced Auger recombination
Eg and  are independently adjustable  resonance can occur at desired wavelength in broad spectral range: SWIR to VLWIR
Resonant band has high density of states  can benefit from resonance even in high fields
Large growth-axis effective masses  lower dark currents
Superlattice Based Avalanche Photodiodes:
/ enhancement in AlAs/GaAs (Mon and Hess, 1982)
Bandstructure engineering can only be done in superlattices and quantum confined materials

## Slide 21: Engineering Impact Ionization in Superlattices
ElectronAPD
Hole APD
Mallick, S., Banerjee, K., Ghosh, S., Plis, E., Rodriguez, J. B., Krishna, S., & Grein, C. (2007). Ultralow noise midwave infrared InAs–GaSb strain layer superlattice avalanche photodiode. Applied Physics Letters, 91(24), 241111.
Banerjee, K., Ghosh. S, Mallick.S, Plis E, Krishna S. and Grein C "Midwave infrared InAs/GaSb strained layer superlattice hole avalanche photodiode." Applied Physics Letters 94, no. 20 (2009): 201107.

## Slide 22: Impact Ionization and Avalanche photodiode (APDs)
Excess noise

## Slide 23: Design of Low Noise APD
For a desired gain value.
Output
noise
noise
Internal gain
Random process
Excess noise
Excess noise
factor (F) or k value
Multiplication
(M)
: electron ionization coefficient
: hole ionization coefficient
Figure of Merits
Stochastic process
Notes: We need to get a good materials which has low-k value and high multiplication.
k value depends on a material that we will use.
This excess noise is Inevitable because in order to use APD we need a internal gain which create excess noise!
Unfortunately, the excess noise can degrade the S/N ratio

## Slide 24: Outline
Motivation and Application Need
  Mid-infrared Imaging and Sensing
  Driving Application Need for NASA
Technology Background
  Antimonide Based Semiconductors
  Historical Perspective of Superlattices
  Physics of Superlattices
Engineering Superlattice Band-diagrams and Band-structures
  Band-diagram Engineering: Unipolar Barrier Detectors
  Band-structure Engineering: Superlattice Avalanche Photodiodes
Technology Status and Future Directions
  Job security for Physicists, Chemists, Material Scientists and Engineers!!!

## Slide 25: State of Superlattice Technology
Thanks to US DoD investments, Significant Advances Made in the T2SL Technology (Especially in MWIR )
Ting et al. IR Tech and Applications XLIII. Vol. 10177 2017.
Vurgaftman, I., et al APL 108.22 (2016): 222101.
Ariyawansa, Gamini, et al. APL 108.2 (2016): 022106.
B. V. Olson et al, Phys. Rev. Appl. 7, 24016 (2017).
Sundaram, M. SPIE Proc. XLIII, 10177-33, 2017
Razeghi et al Optics letters 43, no. 3 (2018): 591-594.
* Customers have different product requirements with varying price points
Technology Readiness Level
Wavelength
Customer Requirement*
DoD
Commercial
Antimonide Superlattice Technology (2018)
DoD Vista Push
Space

## Slide 26: Scientific Challenges for Superlattices
Key drift-diffusion parameters for vertical transport are not fully understood
    Effect of localization, Sb segregation, interfacial roughness, hole-mixing, on minority carrier diffusion length and vertical mobility
Passivation of p-type superlattice material
Behavior of hot carriers at edge of Brillouin Zone
Reduction of noise to achieve high operating temperature long wave infrared
Reduced modulation transfer function (MTF – array contrast) in small pixel, high fill factor, large format nBn format focal plane array (FPA) – due to lateral collection

## Slide 27: New Materials Platform: 6.3 Å Metamorphic Antimonides
Lattice constant vs. wavelength in III-V semiconductors
LWIR
InAs1-xSbx
Starting substrate
LWIR (8 -14 μm):
Wavelength range with the most available thermal imaging cameras.
According to Planck’s law, terrestrial targets emit mainly in the LWIR.
Available substrate
as
Lattice constant as < ae
Epitaxy layer
ae
Requires virtual substrate of same lattice constant
Svensson, S. P., et al Physical Review B 86, no. 24 (2012): 245205
Dahiya et al, JVSTB, 2018.

## Slide 28: Field Programmable Avalanche Photodiodes
Singh et al, IEEE JST AEORS, 2018
Objective: Replace two detectors with a single field programmable detector

## Slide 29: Krishna INfrared Detector (KIND) Laboratory
Graduate Students
Dr. Chris Ball (Res. Scientist)
Dr. TJ Ronningen (Sr. Researcher)
Dr. Alireza Kazemi (Postdoc)
Dave Hollingshead (Res. Engg)
Sen Mathews (Res. Scientist)
Senior Researchers
Grassman/Ringel/Rajan/Carlin/ Rodriguez-Saona/Heremans/Myers (OSU)
Grein (UIC)/Campbell (Uva)
Grbic (Michigan)
Maria (NC State)
Schehing/Reyner/Ariyawansa/Duran (AFRL-RY)
Cowan/Steenbergen/Morath(AFRLRV))
SK Infrared LLC
Lee/Kim (KRISS)
Raytheon Vision Systems
Collaborators
Past Group Members
www.krishnairlab.com
https://kind.engineering.osu.edu/
Research Faculty/Postdocs (8): Dr. A.Amout (Emcore), Dr. P. Dowd (ASU), Dr. J. Brown (Micron), Dr. J.B. Rodriguez (Montpellier), Dr. T. Vandervelde, (Tufts); Dr. M. Naydenkov (Lightspin); Dr. Y.D. Sharma (OSI); Dr. J.O. Kim (KRISS); Dr. Plis (Assurance); Dr. Winckel (SNL); Dr. Tian, Dr. Klein (SNL);
PhDs (26): Dr. Winckel, (UNM); Dr. Zhu, (DC); Dr. Plis, UNM; Dr. Attaluri, Lehigh Univ.; Dr. Newmann, Emcore; Dr. Andrews, NRL; Dr. Wilcox NRL, Dr. Khoshakhlagh (JPL), Dr. Kim (UCB), Dr. Shenoi (RPI), Dr. Ramirez (Skinfrared), Dr. Shao (Purdue); Dr. Barve (UCSB); Dr. Gautam (UCSB); Dr. Jang (AFRL/RY), Dr. Myers (Skinfrared); Dr. Kutty; Dr. Fiorante (Universidade de São Paulo); Dr. F. Santiago (SNL); Dr. Brianna Klein (UNM);. Dr. Sebastian Godoy (Concepcion); Dr.Montoya (Duke); Dr. Schuler-Sandy (UNM); Dr. Kazemi (OSU); Dr. Zarmiri (UW) Dr. Cowan (AFRL);
M.S. (16) : C. Kadlec (SNL), M. Malone T. Specht, K. Knobel (AFRL), J. Oberling, A. Scott (AFRL), N. W. Bernstein (LANL), J. Shelton, (SNL), G. Bishop (SNL), E. Varley (SNL), D. Jepson (AFRL); M. Lenz, (SNL), K. Posani (Qualcomm), C. Wilcox, (NRL), S. Annamalai (Triquint), M. Serna (Oxford), S.Raghavan
* At UNM
, HEL-JTO, DARPA/AFRL , MDA,
Funding Agencies
Spring 2018
Teressa Specht (PhD)
Vinita Dahiya (PhD)
Seung Hyun Lee (PhD)
Sri Harsha Kondati (PhD)
Lilian Acosta (PhD)*
Zahra Taghipour (PhD)*
Undergraduate Students
Brett Ringel
Rudy Fink
Aashita Kawatra
Quentin Shu