## Slide 1
Data package for HyMAX
Krishna Talluru, Liam McQuellin & Andrew Neely
Hypersonics group, UNSW Canberra.
Email for correspondence: k.talluru@adfa.edu.au

## Slide 2
Input data
HyMAX
Run #
Freestream conditions
Facility operation
Geometry
Sensor locations
Cantilever plate, static shock generator at 2 degrees (mandatory) and 10 degrees (optional)
Total pressure : 980 40 kPa
Total temperature: 580 2 K
Freestream pressure: 755 5 Pa
Freestream temperature: 75 2 K
Model wall temperature: 300 2 K
Mach number: 5.8 0.06
Unit Reynolds number: 7.1 x 106
Ludwieg tube at University of Southern Queensland (TUSQ), Australia
Test flow: Free jet
Test gas: Compression heated air
Flow start: Bursting of diaphragm
Flow duration: 0.2 0.01 seconds
(Time series data of freestream pressure fluctuations will be provided on request.)
Refer to page 3.
Refer to page 4.
Notes: STP files
Drawing sheets – 2D sketches

## Slide 3
Geometry
Shock generator
Note: All dimensions are in mm.
Variable | Value
a | 130 mm
b | 80 mm
h | 2 mm
a | -3o
qw | 5o
Q = a + qw | 2o
See the next page for the locations of pressure transducers, strain gages and thin film gages.
CAD files will be provided on request.
Details of the wedge geometry can be found in Currao et al., “Hypersonic Oscillating Shock-Wave/Boundary-Layer Interaction on a Flat Plate”, vol. 59, AIAA 2021.
Resultant wedge angle
Notes: STP files
Drawing sheets – 2D sketches

## Slide 4
Sensor locations
Note: All dimensions are in mm.
(Bolted joint)
1. Spatial pressure distribution history (Pressure Sensitive Paint).
2. High-speed schlieren video history (flow field structure).
3. High-speed displacement history (image tracking of schlieren).
4. Heat flux measurements from four thin film gauges on the panel.
5. Laser scanner measurements on the centerline of the cantilever plate.
6. Pressure histories from discrete sensors at four locations on the panel.
7. Strain gage measurements at two locations near the hinge line.
Data sets available:
Notes: STP files
Drawing sheets – 2D sketches

## Slide 5
Sample data/results
Figure 1: Timeseries of displacement of the trailing edge using laser scanner, image tracking and 2D laminar simulation.
Figure 2: Power spectral density of (a) trailing edge displacement and (b) pressure fluctuations at four locations on the panel.
(a)
(b)
Notes: STP files
Drawing sheets – 2D sketches

## Slide 6
schlieren visualization
2o Static shock generator
Cantilever plate
Notes: STP files
Drawing sheets – 2D sketches